## Slide 1: Global Used Oil and Re-Refined Lubricants:
Market Analysis and Opportunities
January 2022
Base Year: 2020 and 2021
Table of Contents

## Slide 2: Global Used Oil and Re-Refined Lubricants: Market Analysis and Opportunities
Global Used Oil and Re-Refined Lubricants: Market Analysis and Opportunities
This report and the survey on which it is based were conducted under the direction of: MILIND PHADKE Vice President, Energy Practice Kline Research +1-973-435-3379 Copyright © 2022 Kline & Company, Inc. Access to this report is restricted to employees of subscribing companies and subsidiaries in which these companies hold more than a half interest. Its contents must not be disclosed to any other persons or organizations before January 1, 2025.

## Slide 3: Foreword
Global Used Oil and Re-Refined Lubricants: Market Analysis and Opportunities summarizes the results of Kline & Company’s comprehensive syndicated analysis of the global used oil and re-refined lubricants industry in the wake of record low crude oil prices and low basestocks demand due to COVID-19. With crude oil prices rising yet again and improvements in basestocks demand, the industry is expected to recover quickly. Our report will focus on key trends, developments, changes, challenges, and business opportunities. This report assists used oil collectors, re-refiners, lubricants blenders, and marketers in identifying opportunities within the global used oil re-refining industry.
The results of this study will provide subscribers with a comprehensive, accurate, and independent appraisal of business opportunities, including:
Developing business strategies by understanding the trends and developments that are driving the used oil re-refining market
Identifying end-use markets and applications with high potential for growth and the challenges and barriers for catering to these opportunities
Recognizing key competitors and evaluate their market position
For a more focused analyses, Kline can also provide assistance through its custom, strategic consulting capabilities. Having served the lubricants industry since the 1970s, the company has undertaken numerous consulting assignments that have involved growth forecasts, competitive intelligence, market and brand analyses, and market research. In addition to these analyses, Kline has completed various other engagements for industry-leading clients, including:
Acquisition screening and assessment
Industry/Category/Brand assessment
Strategic analyses
New business development
Competitive intelligence
Customer satisfaction
We would like to remind you that your subscription to the study includes one day of strategic planning assistance with members of the project team, to be used at your discretion within six months of receipt of this report. We also invite all subscribers to notify us of any errors so that we may correct them in any future editions of this survey.
Lenka G. Contreras
Senior Vice President, Kline Research
+1-973-435-3407
Lenka.Contreras@klinegroup.com

## Slide 4: Special Notice
Each company subscribing to Global Used Oil and Re-refined Lubricants: Market Analysis and Opportunities, including those companies subscribing to sections of the survey, has agreed that for three years from their dates of issue, they will:
Restrict access to these reports to its own employees, and those of subsidiaries in which it has more than a half interest, or of parent organizations which have more than a half interest in the subscribing company.
Take all reasonable precautions to prevent the disclosure of the contents of these reports to any other persons or organizations.
Accordingly, online login details to the Global Used Oil and Re-refined Lubricants: Market Analysis and Opportunities report, and circulation of its hardcopies, must be restricted to employees of subscribing companies and their subsidiaries, as defined above, until January 1, 2025. Similarly, all sections of the survey are so restricted for three years from their dates of issue. Failure to prevent unauthorized disclosure before these dates will result in legal action against the subscriber and the receiver.
Kline & Company, Inc.

## Slide 5: Table of Contents
Global Used Oil and Re-Refined Lubricants: Market Analysis and Opportunities
This report summarizes the findings and conclusions from Kline & Company’s comprehensive study of the global used oil collection and re-refining business.
Introduction
Executive Summary
Country Profiles
  Brazil
  China
  India
  Mexico
  Russia
  USA and Canada
  Western Europe

## Slide 6
Introduction

## Slide 7: Scope
Global Used Oil and Re-Refined Lubricants: Market Analysis and Opportunities focuses on key lubricant-consuming regions, such as North America (Canada, the United States, and Mexico); Western Europe (DACH, France, Italy, United Kingdom, Iberia, and Benelux); Asia-Pacific (China, India, Indonesia, Japan, Malaysia, South Korea, and Thailand); Brazil; and Russia. The base year for the study’s data is 2020; however, initial estimates for 2021 have been provided.
Forecasts have been provided for 2025 and 2030.

## Slide 8: Coverage
For the reader’s convenience, this report is organized into three main sections.
Chapter 1 is the introduction, which provides the scope, methodology, and organization for this report.
Chapter 2 is the executive summary providing the key highlights of the report.
Chapter 3 is sub-divided into 12 chapters. Each chapter is an independent profile for the 12 regions/countries covered in the study. Each profile outlines the used oil material flow, regulatory scenario, used oil generation, collection, and handling practices, re-refining business and its attractiveness in the different markets. Each profile covers:
  Used oil material balances in terms of used oil generated, collected, and disposed of in different markets
  Various routes to disposal of used oils
  Regulations
  Re-refining of used oil to basestocks
  Consumption of re-refined basestocks
  Major re-refiners of used oil
  Market trends and outlook for re-refined basestocks

## Slide 9: Methodology
The report is based primarily on a series of interviews with approximately 250 individuals, including used oil collectors and processors including re-refiners, automotive garages and workshops, and government agencies globally. It also draws on an analysis of statistical data from government, trade, and industry associations; and non-confidential information from Kline’s database.
This analysis also draws on secondary sources such as: (1) product literature and websites of re-refiners; (2) data from various environmental regulation authorities; (3) an analysis of statistical data from government, trade, and industry organizations; and (4) non-confidential data from Kline & Company’s previous work in this industry, including syndicated studies.
Unless otherwise specified, all volumes are provided in tons or kilotons while prices are provided in U.S. dollars per Kg (USD/Kg).
Forecasts are provided for 2025 and 2030.
The data presented in this report is as accurate as possible within the general scope of the survey but may vary by product and application. Overall, we believe that the data presented is within 10% to 15% of the true values.

## Slide 10
Executive Summary

## Slide 11: Introduction
This chapter summarizes key findings from Kline & Company’s comprehensive study of the market for used oils and the market for re-refined basestocks in seven regions or countries. It also summarizes regulations related to used oil collection, transportation, disposal, and re-refining in the additional four countries covered briefly in this study.
Finished lubricants are unique among refinery products, as they are not consumed during their use. Most lubricants are not destroyed during their service life. They degrade and accumulate contaminants during operation, causing them to lose their efficacy as lubricants. At the end of their service life, lubricants have to be replaced, and the original lubricant that is drained from a vehicle or a piece of industrial equipment is referred to as “used oil.” The amount of used oil generated and the type of contaminants that it contains are dependent on the lubricant type and service conditions.
The U.S. Environmental Protection Agency (EPA) defines used oil for regulatory purposes as “any oil that has been refined from crude oil or any synthetic oil that has been used and, as a result of such use, tends to get contaminated by physical and chemical impurities.”
Three main criteria determine if a substance is a “used oil” or not: origin, use, and contaminants. The oil should have origins in crude oil or synthetic materials; hence, animal and vegetable oils are not classified as used oils. Secondly, the oil has to be used in operation. Unused waste oils, such as bottom clean-out waste from virgin fuel storage tanks and virgin fuel oils which are spilled, are not classified as used oils. Thirdly, the oil has to be contaminated due to use with physical (wear metals, sludge, and soot) and chemical (solvents, halogens, water, and fuel) contaminants. Also excluded from the EPA definition of used oil are products such as antifreeze, kerosene, and various solvents. This definition of used oils is followed in the study.

## Slide 12: Used Oil Life Cycle Stages
Generated used oil: All lubricant that is sold will eventually return as used oil with the exception of the volume that is consumed in service (for example, rubber process oil that is part of the final product), lost due to combustion, or leakages. The volume of lubricant that returns as used oil is defined as generated used oil.
Collected used oil: The generated used oil can be disposed of by the generator in a number of ways, or it can be sent to a used oil collector. The used oil volume that generators sell or give to collectors is called collected used oil.
Reclamation: The generator of the used oil may filter, dewater, and re-additize and re-use the used oil as a lubricant. This is defined as reclamation. This definition covers all instances when the used oil returns as a lubricant with minimal re-processing.
  Other avenues of disposal for the generator, such as sending used oil to landfill, incineration of used oil, and combustion of used oil for fuel value, are straightforward and do not need elaboration. The generator may or may not clean the oil before disposing of it in any of the previously mentioned routes.
Re-refining: Used oil can be re-refined into basestocks that can be used to produce lubricants. Re-refiner can collect used oil themselves or get it from used oil collectors. Re-refining includes a broad spectrum of technologies, some of which are rudimentary. Re-refining in this report covers technologies such as thin-film evaporation, acid/clay treatment, solvent extraction, and hydrotreatment.
Continued…

## Slide 13: Used Oil Life Cycle Stages
USED OIL GENERATION, COLLECTION, AND DISPOSAL

## Slide 14: Used Oil Regulations: Brazil
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | In Brazil, federal regulations govern the disposal of used oil. The Ministry of Mines and Energy and the Ministry of Environment are co-responsible for developing and enforcing laws throughout the entire country. These ministries are backed up by the Brazilian National Agency of Petroleum, Natural Gas and Biofuels (ANP), the Brazilian Environment and Natural Resources Institute (IBAMA), and the National Environment Council (CONAMA), which are ultimately responsible for enforcing regulations.
2. How is used oil classified i.e., hazardous waste, special waste etc.? | Hazardous waste
3. Are there any requirements on who can collect used oil? | Used oil collectors must have collection contracts with one or more producers or importers and sales contracts with one or more basestock re-refiners or any other party that can ensure that the used oil is only used for recycling.
4. Does country have an association(s) managing the collection and disposal of used oil? | Brazilian Institute JOGUE LIMPO is an association of lubricants producers and importers, and it is the managing entity responsible for carrying out the reverse logistics of plastic packaging used in finished lubricants as well as used/contaminated lubricating oil.
5. Is a levy charged on sales of lubricants to support used oil collection associations? | CONAMA’s resolution states that lubricant blenders/importers are directly responsible for the collection of used oil or should at least cover the cost of used oil collection by third parties.
6. Are there any requirements for how used oil generators manage used oil? | Same requirements as question 7 (next in this table).
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | Used oil generators are required to: Store used oil properly to avoid environmental contamination, enabling collection Adopt proper measures to avoid used oil contamination with chemical products, water, fuels or anything else that might prevent used oil recycling Transfer used oil exclusively to a regular collector Provide the regular collector with information on possible contamination due to oil usage Keep documents on the used oil collection and sale However, if the generator is working with lubricants that lead to the generation of non-recyclable used oil, then they are required to dispose of the used oil as per the law in an environmentally friendly way.
Continued…

## Slide 15: Used Oil Regulations: Brazil
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
8. Do any requirements/legislation exist around different types of used oil? |  | No.
9. Does the country have requirements or regulations regarding the export or import of used oil? |  | Both exports and imports of used oils are not authorized.
10. Does the country have any legislation that requires used oil to be re-refined? |  | Brazilian legislation predicts that all used oil collected must be recycled/re-refined.
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? |  | There is no obligation, but as Brazilian market is a large importer re-refined basestocks are important in the overall supply for lubricants market.
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? |  | All these end-uses are considered illegal.
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | Both used or contaminated lubricant oils can not be used as fuel for burning in Brazil.
14. Is used oil allowed to be placed in a landfill? |  | The disposal of used oils in the soil, underground, territorial waters, and sewage and effluents systems is prohibited.
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | There is mandate but not subsidies.
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | No.
 | ii. Blending with crude oil at a refinery | No.
 | iii. Dust suppressant | No.
17. Are there companies/associations advocating in used oil category? |  | Not for used oils but SINDIRREFINO (National Syndicate of the Mineral Oil Re-refining Industry) and AMBIOLUC (Environmental Association for Collection, Management and Re-refining of used oils) are private associations representing basestocks re-refiners in Brazil

## Slide 16: Used Oil Regulations: China
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | Yes
2. How is used oil classified i.e., hazardous waste, special waste etc.? | Hazardous waste
3. Are there any requirements on who can collect used oil? | Yes
4. Does country have an association(s) managing the collection and disposal of used oil? | Yes, China Recycling Oil Committee of China National Resources Recycling Association
5. Is a levy charged on sales of lubricants to support used oil collection associations? | No
6. Are there any requirements for how used oil generators manage used oil? | Yes
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | No
8. Do any requirements / legislation exist around different types of used oil? | Yes, National standard for used engine oil, used gear oil, used hydraulic fluids etc. and required to be stored separately
9. Does the country have requirements or regulations regarding the export or import of used oil? | Yes, export of used oil is allowed but import is fully banned since 2020
10. Does the country have any legislation that requires used oil to be re-refined? | Encouraged but not mandatory, used oil can also be incinerated, placed in a landfill or processed as raw materials and fuel
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No, related regulations only exist for eligibility of tax benefits
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | No, used oil need to be processed/pre-treated before burning as fuel
Continued…

## Slide 17: Used Oil Regulations: China
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | No, they share same set of air emissions requirements, but energy recovery equipment is encouraged by the government for burner to increase total energy efficiency
14. Is used oil allowed to be placed in a landfill? |  | Yes, but pre-treatment is required to remove the ignitability and reactivity of used oil
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | Yes, exemption of consumption tax and 50% VAT refund for qualified processors and re-refiners, and reduced income tax rate for collectors, processors and re-refiners
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | No such regulations to prohibit
 | ii. Blending with crude oil at a refinery | 
 | iii. Dust suppressant | 
17. Are there companies/associations advocating in used oil category? |  | Yes
Continued…

## Slide 18: Used Oil Regulations: China
Key Used Oil Regulations
i. Administration Policies
National Hazardous Waste Catalogue (2021 version)
Solid Waste Pollution Prevention and Control Law of People’s Republic of China (2020 Amendment)
Announcement on Comprehensive Solid Waste Import Ban 2020
Management Measures on Hazardous Waste Export Approval 2008 (2019 Amendment)
Administrative Measures on Hazardous Waste Operating Permit 2004 (2016 Amendment)
Hazardous Waste Disposal Fee System 2003
Management Measures for Hazardous Waste Transfer Forms 1999
ii. National Standards
Technical Guides for Collection and Re-refining of Used Oil (GB/T17145-1997)
Technical Specifications for Pollution Control of Used Mineral Oil Recovery, Recycle and Reuse (HJ607-2011)
Standard for Pollution Control on Hazardous Wastes Storage (GB 18597-2001)
Standard of Pollution Control on the Hazardous Waste Landfill (GB 18598-2019)
Standard of Pollution Control on Hazardous Waste Incineration (GB 18484-2020)
iii. Tax Benefits
Announcement on Policy Issues Regarding Corporate Income Tax of Third-party Enterprises Conducting Pollution Prevention 2019
Catalogue of Value-Added Tax Benefits for Products and Services of Resources Comprehensive Utilization 2015
Notice of State Taxation Administration and Ministry of Finance on Exemption of Consumption Tax on Re-refining Products of Waste Mineral Oil 2013
i. Generation
Use oil generators should entrust an entity licensed with Hazardous Waste Operation Permit to collect and dispose of used oil. Generators are allowed to conduct re-refining or disposal themselves only if Comprehensive Operation Permit is granted.
ii. Classification (Hazardous Waste)
Used oil is classified as hazardous waste
iii. Collection
Hazardous Waste Operation Permit is a must for used oil collection. Two types of Operation Permit are available, one is Collection Operation Permit, for use oil collection from automobile maintenance sector only, and the other one is Comprehensive Operation Permit, for collection, storage and disposal (re-refining) of used oil from all sources.
iv. Transportation and Storage
Hazardous Waste Transfer Form should be filled out and submitted to county/provincial-level Environment and Ecology Authority before transfer
Vehicles to be licensed with Road Transport Permit for Dangerous Goods and storage facility to be licensed with Hazardous Waste Operating Permit
v. Disposal – Re-Refining
Re-refiners should obtain Hazardous Waste Comprehensive Operation Permit and meet requirements of re-refining capacity, facilities and environmental protection
vi. Disposal – Fuel
Used oil is not legally allowed to be used as fuel for any industry, however it is allowed to burn diesel and other types of oil processed from used oil
vii. Disposal – Other
Other major disposal ways are burning and landfill, which should be operated with Hazardous Waste Comprehensive Operating Permit

## Slide 19: Used Oil Regulations: India
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for Used Oil? | Yes. used oil is covered under Hazardous Waste Management Handling & Transboundary Movement Rules, 2016.
2. How is Used Oil classified i.e., hazardous waste, special waste etc.? | Hazardous waste
3. Are there any requirements on who can collect Used Oil? | Yes, used oil collectors should be authorized from the Central Pollution Control Board( CPCB) and State Pollution Control Board (SPCB).
4. Does country have an association(s) managing the collection and disposal of Used Oil? | No
5. Is a levy charged on sales of lubricants to support Used Oil collection associations? | No
6. Are there any requirements for how Used Oil generators manage Used Oil? | Yes, proposed operating practices have been developed to help generators of used oil to manage their wastes in environmentally safe manner, as per the Hazardous Waste Management Handling & Transboundary Movement Rules, 2016.
7. Are there requirements for oil manufacturers, marketers or retailers to take back Used Oil? | No
8. Do any requirements / legislation exist around different types of Used Oil? | No
9. Does the country have requirements or regulations regarding the export or import of Used Oil? | Yes. As per Rule 12 of Hazardous Waste Management Handling & Transboundary Movement Rules, 2016, import of hazardous waste is not allowed for disposal. However, it is permitted to be re-refined or regenerated as per Rule 13 as specified in Part A & Part B of Schedule III.
10. Does the country have any legislation that requires Used Oil to be re-refined? | No
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | Yes, Indian government has passed mandate of utilizing 25% re-refined basestocks for lubricants by 2023.
Continued…

## Slide 20: Used Oil Regulations: India
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? |  | Nothing has been given regarding usage of used oil as a fuel. However, oil that is categorized as a waste oil such as tank bottom slugged of crude oil, or mixtures containing synthetic oil can be burned as fuel as per specification laid down in Schedule V Part B of Hazardous Waste Management Handling & Transboundary Movement Rules, 2016
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | Yes, As per HW rule 2016, waste oil burner shall comply with prescribed standards for particulate matter, HCl, SO2, CO, HF, NOx (NO and NO2 expressed as NO2), Hydrocarbons, Dioxins/Furans, Cd +Th (and its compounds), Hg (and its compounds), Sb + As + Pb + Cr + Co + Cu + Mn + Ni + V (and their compounds).
14. Is used oil allowed to be placed in a landfill? |  | Yes, only authorized Treatment Storage Disposal Facility (TSDF) are allowed to place used oil in a landfill after meeting specification laid down in Schedule - I, II (Part A, B and C of the Hazardous Waste Management Handling & Transboundary Movement Rules, 2016.
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | No
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | No information has been given
 | ii. Blending with crude oil at a refinery | No information has been given
 | iii. Dust suppressant | No information has been given
17. Are there companies / associations advocating in Used Oil category? |  | Yes, Public sector OMCs such as IOCL, HPCL and BPCL

## Slide 21: Used Oil Regulations: Indonesia
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | Yes. Laws such as Indonesian Law No. 23/1997, Indonesian Law No. 32/2009 (EPMA), Government Regulation No. 101 of 2014 on Management of Hazardous and Toxic Waste (B3), and Government Regulation No. 22 of 2021: Management of B3 Waste and Non-B3 Waste (Articles 274 – 470).
2. How is used oil classified i.e., hazardous waste, special waste etc.? | Hazardous and Toxic Waste or B3 Waste
3. Are there any requirements on who can collect used oil? | No.
4. Does country have an association(s) managing the collection and disposal of used oil? | No.
5. Is a levy charged on sales of lubricants to support used oil collection associations? | No.
6. Are there any requirements for how used oil generators manage used oil? | Yes.
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | No.
8. Do any requirements / legislation exist around different types of used oil? | No.
9. Does the country have requirements or regulations regarding the export or import of used oil? | Yes.
10. Does the country have any legislation that requires used oil to be re-refined? | No.
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No.
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | Yes.
Continued…

## Slide 22: Used Oil Regulations: Indonesia
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | No.
14. Is used oil allowed to be placed in a landfill? |  | Yes.
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | No.
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | Yes
 | ii. Blending with crude oil at a refinery | No.
 | iii. Dust suppressant | No.
17. Are there companies / associations advocating in used oil category? |  | Yes.

## Slide 23: Used Oil Regulations: Japan
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | Yes – Waste Disposal Law for industrial waste which includes used oil.
2. How is used oil classified i.e., hazardous waste, special waste etc.? | Used oil can be categorized under either regular industrial waste or special waste under the Fire Service Act.
3. Are there any requirements on who can collect used oil? | Yes – only certified list of companies are able to collect, process and transport used oil.
4. Does Japan have an association(s) managing the collection and disposal of used oil? | Japan Oil Recycling Co-operative, Japan Federation of Industrial Waste Management and Recycling Associations
5. Is a levy charged on sales of lubricants to support used oil collection associations? | No levy is charged
6. Are there any requirements for how used oil generators manage used oil? | Yes – waste generators need to properly dispose industrial waste. If the generators cannot process the waste internally, they must make contracts with an approved disposal company.
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | Yes, requires approval
8. Do any requirements / legislation exist around different types of used oil? | Yes, used oil with a flash point of 70 degrees Celsius or less are classified as “specifically controlled industrial waste” due to their high combustion.
9. Does the country have requirements or regulations regarding the export or import of used oil? | Yes, both exports and imports require permission by the environment ministry for it
10. Does the country have any legislation that requires used oil to be re-refined? | No, there is nothing any regulation to re-refine as barely any used oil are re-refined in Japan
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No, there is nothing any regulation on that
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | Yes – they are often used in cement kilns, industrial boilers, and power plants.
Continued…

## Slide 24: Used Oil Regulations: Japan
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | Partially yes – users of fuel must report to the Ministry of Environment through their local municipalities to notify their activities and sizes (boilers with a heat transfer area of 10m2 or more/combustion capacity of 50litres/hour or more). However, used oil burners (processors) are not obligated to install additional pollution control equipment (although this is encouraged).
14. Is used oil allowed to be placed in a landfill? |  | Yes – they are used in landfills and must be incinerated as a preliminary step. Incineration does not consume everything and the leftover waste which is then disposed of in landfill.
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | No, there is nothing to encourage to re-refining, processing, etc. of used oil.
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | Yes – no regulations prohibit this use
 | ii. Blending with crude oil at a refinery | Yes – no regulations prohibit this use
 | iii. Dust suppressant | Yes – no regulations prohibit this use
17. Are there companies / associations advocating in used oil category? |  | Yes – Japan Oil Recycling Association

## Slide 25: Used Oil Regulations: South Korea
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | Yes, under the Act on the Promotion of Saving and Recycling of Resources (known as the ‘Recycling Act’). South Korea introduced an Extended Producer Responsibility (EPR) system in 2000. (See slide 8)
2. How is used oil classified i.e., hazardous waste, special waste etc.? | No, it is not classified as hazardous waste; it is included in the greater category of all recycling products including Batteries, Tire, Lubricant, Fluorescent lamps, Styrofoam floats
3. Are there any requirements on who can collect used oil? | Yes, under Article 66 of the Act Regulations, local government must provide authorization for collection vehicles.
4. Does country have an association(s) managing the collection and disposal of used oil? | Private, non-profit Producer Responsibility Organization (PRO); for used oil the PRO is the Korea Lubricant Oil Industrial Association.
5. Is a levy charged on sales of lubricants to support used oil collection associations? | There is no levy applied to the products; producers/importers of used oil however will subsidize local government collection via the establishment of a PRO (Producer Responsibility Organization)
6. Are there any requirements for how used oil generators manage used oil? | Yes, storage and management facilities must meet approval from local government
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | Yes, under terms of the act, producers or importers are required to collect and recycle any EPR designated product, which includes lubricants.
8. Do any requirements / legislation exist around different types of used oil? | No, used oil/lubricant types are not delineated within the act.
9. Does the country have requirements or regulations regarding the export or import of used oil? | Lubricant waste export is not listed as a method of recycling by the Ministry of Environment, with the proportion of waste being exported considered at only 0.1%.
10. Does the country have any legislation that requires used oil to be re-refined? | No
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No, this is not required in any legislation.
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | Yes, it is permitted to use used oil as fuel in cement kilns or furnaces.
Continued…

## Slide 26: Used Oil Regulations: South Korea
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | There are no listed requirements for additional pollution control equipment when burning used oil.
14. Is used oil allowed to be placed in a landfill? |  | Used oil or lubricants may not be placed in landfills in South Korea.
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | No, as re-refining is currently not done in South Korea there is no special incentive targeting it, nor for fuel burning or use in landfills.
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | Not officially regulated under the current Act.
 | ii. Blending with crude oil at a refinery | Not applicable in South Korea
 | iii. Dust suppressant | Not officially regulates under the current Act.
17. Are there companies / associations advocating in used oil category? |  | Companies in South Korea are not recognized as heavily advocating for used oil recycling. Organizations such as Korea Petroleum Quality & Distribution Authority (KPETRO), Korea Environment Corporation (KECO), and the Korea Lubricant Oil Association do promote used oil recycling domestically.

## Slide 27: Used Oil Regulations: Thailand
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | Yes. Regulations such as Factory Act, B.E. 2535 (1992), Industrial Estate Act, B.E. 2522 (1979), Public Health Act, B.E.2535 (1992), The Enhancement and Conservation of National Environment Quality Act, B.E. 2535 (1992), Industrial Estates Act 1992, and Hazardous Substance Act 1992
2. How is used oil classified i.e., hazardous waste, special waste etc.? | Hazardous Waste
3. Are there any requirements on who can collect used oil? | No. There is no concrete regulatory framework in Thailand to support proper collection of used oil. However, there is permission granted by DIW for collection of hazardous waste in Thailand.
4. Does country have an association(s) managing the collection and disposal of used oil? | Yes.
5. Is a levy charged on sales of lubricants to support used oil collection associations? | No.
6. Are there any requirements for how used oil generators manage used oil? | Yes.
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | No.
8. Do any requirements / legislation exist around different types of used oil? | No.
9. Does the country have requirements or regulations regarding the export or import of used oil? | Yes.
10. Does the country have any legislation that requires used oil to be re-refined? | No
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No.
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | Yes
Continued…

## Slide 28: Used Oil Regulations: Thailand
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | No.
14. Is used oil allowed to be placed in a landfill? |  | Yes
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | No.
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | No. However, a license type 106 (Ror. Ngor. 4) from the DIW and the Ministry of Industry is required to carry out a process to make substitute fuell from used oil for burning. In addition, the Department of Energy Business, Ministry of Energy also provide license for operating a fuel storage facility.
 | ii. Blending with crude oil at a refinery | No.
 | iii. Dust suppressant | No.
17. Are there companies / associations advocating in used oil category? |  | Yes.

## Slide 29: Used Oil Regulations: Mexico
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | No. However, the General Law for Prevention and Management of Waste (LGPGIR) defines hazardous waste, that includes used oils.
2. How is used oil classified i.e., hazardous waste, special waste etc.? | Hazardous waste
3. Are there any requirements on who can collect used oil? | Yes. All professional services rendered in relation to the recollection, storage, transport, and final disposal of hazardous waste must have the prior authorization of SEMARNAT.
4. Does country have an association(s) managing the collection and disposal of used oil? | No
5. Is a levy charged on sales of lubricants to support used oil collection associations? | No
6. Are there any requirements for how used oil generators manage used oil? | Yes. Generators of used oils must be registered in SEMARNAT and need to have an authorized management program.
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | No
8. Do any requirements / legislation exist around different types of used oil? | No
9. Does the country have requirements or regulations regarding the export or import of used oil? | No
10. Does the country have any legislation that requires used oil to be re-refined? | No
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | Yes
Continued…

## Slide 30: Used Oil Regulations: Mexico
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | There is not extra regulations on the type of fuel burner emission.
14. Is used oil allowed to be placed in a landfill? |  | No
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | No
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | Yes
 | ii. Blending with crude oil at a refinery | Yes
 | iii. Dust suppressant | Yes
17. Are there companies / associations advocating in used oil category? |  | No

## Slide 31: Used Oil Regulations: Canada
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | Yes
2. How is used oil classified i.e., hazardous waste, special waste etc.? | Hazardous Waste
3. Are there any requirements on who can collect used oil? | Yes
4. Does country have an association(s) managing the collection and disposal of used oil? | Yes
5. Is a levy charged on sales of lubricants to support used oil collection associations? | Yes
6. Are there any requirements for how used oil generators manage used oil? | Yes
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | Extended producer responsibility principle applied​
8. Do any requirements / legislation exist around different types of used oil? | No
9. Does the country have requirements or regulations regarding the export or import of used oil? | Yes
10. Does the country have any legislation that requires used oil to be re-refined? | Yes
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | Yes, but only if used oil is pre-treated and its contaminants are reduced below certain levels
Continued…

## Slide 32: Used Oil Regulations: Canada
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | Yes​
14. Is used oil allowed to be placed in a landfill? |  | No
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | Yes
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | No
 | ii. Blending with crude oil at a refinery | No
 | iii. Dust suppressant | No, all the provinces and territories except Alberta have banned the usage of used oil as dust suppressant
17. Are there companies / associations advocating in used oil category? |  | Yes

## Slide 33: Used Oil Regulations: USA
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | Yes
2. How is used oil classified i.e., hazardous waste, special waste etc.? | Special Waste, not Hazardous Waste
3. Are there any requirements on who can collect used oil? | Yes
4. Does country have an association(s) managing the collection and disposal of used oil? | NORA represents the industry, but does not manage collection or use
5. Is a levy charged on sales of lubricants to support used oil collection associations? | Not at the Federal level
6. Are there any requirements for how used oil generators manage used oil? | Yes
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | No
8. Do any requirements / legislation exist around different types of used oil? | Yes
9. Does the country have requirements or regulations regarding the export or import of used oil? | Not specific to UO
10. Does the country have any legislation that requires used oil to be re-refined? | No
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | Yes
Continued…

## Slide 34: Used Oil Regulations: USA
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | Not at the Federal level
14. Is used oil allowed to be placed in a landfill? |  | No
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | Not at the Federal level
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | Allowed
 | ii. Blending with crude oil at a refinery | Allowed
 | iii. Dust suppressant | Prohibited
17. Are there companies / associations advocating in used oil category? |  | Yes

## Slide 35: Used Oil Regulations: Russia
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | No, used oil is categorized as a hazardous waste under National standard “Waste treatment. Elimination of used petroleum products.”
2. How is used oil classified i.e., hazardous waste, special waste etc.? | According to Russian environmental legislation, oil waste is subject to mandatory disposal and processing and is classified as III-IV hazard class.
3. Are there any requirements on who can collect used oil? | Yes. Operators licensed by The Ministry of Natural Resources and Environment (Rosprirodnadzor)
4. Does country have an association(s) managing the collection and disposal of used oil? | Waste Recycling Association
5. Is a levy charged on sales of lubricants to support used oil collection associations? | No
6. Are there any requirements for how used oil generators manage used oil? | Yes, (GOST 2146-a) regulates standards under which used oil generators manage the waste in environmentally safe manner.
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | No
8. Do any requirements / legislation exist around different types of used oil? | No
9. Does the country have requirements or regulations regarding the export or import of used oil? | No
10. Does the country have any legislation that requires used oil to be re-refined? | Yes. Technical regulation of the Customs Union 030/2012 “Requirements for lubricants, oils and special liquids"
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | Burning of used oils is carried out only in cases that are allowed by the National standard “Waste treatment. Elimination of used petroleum products.” Legal burning of used oils implies that the contaminants need to be removed from used oil before burning it.
a- Russian Technical Regulations Certificate (GOST) Standards were developed in Soviet Union, however, still in use in Russia.
Continued…

## Slide 36: Used Oil Regulations: Russia
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | Yes, waste oil burner should comply with the National standard: Resources saving. Best available techniques. Used oils must not be burned unless hazardous substances are removed from it, according to the standard.
14. Is used oil allowed to be placed in a landfill? |  | No. According to the restrictions on waste disposal as per the Industry Development Strategy for the processing, utilization, and disposal of production and consumption of waste it is illegal to dispose of the used oil in the landfill.
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | No
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | Yes, Russian legislation does not contain a direct prohibition on burning of used oil as fuel. However, used oil is allowed to be burned only in specially equipped installations approved by Rosprirodnadzor.
 | ii. Blending with crude oil at a refinery | No
 | iii. Dust suppressant | No
17. Are there companies / associations advocating in used oil category? |  | Yes. Waste Recycling Association is the main public organization for the re-refining industry in Russia advocating for the recycling of used oil.

## Slide 37: Used Oil Regulations: Western Europe
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | Yes. European Regulation 1013/2006 and EU Directive 2018/851 are the main legislative instruments at a European level specifically regulating used oil.
2. How is used oil classified i.e., hazardous waste, special waste etc.? | Hazardous
3. Are there any requirements on who can collect used oil? | Yes. They have to either apply for a license or become part of a public consortium.
4. Does country have an association(s) managing the collection and disposal of used oil? | In Italy, Portugal, Spain, and Denmark.
5. Is a levy charged on sales of lubricants to support used oil collection associations? | In Italy and Portugal.
6. Are there any requirements for how used oil generators manage used oil? | Yes. Used oil is classified as a hazardous waste and needs to be collected and stored separately.
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | Yes. There are requirements for all collectable used oil to be collected.
8. Do any requirements / legislation exist around different types of used oil? | Yes. There is a hierarchy of waste oil.
9. Does the country have requirements or regulations regarding the export or import of used oil? | Yes. Importers-exporters have to follow the requirements for the export and import of used oil.
10. Does the country have any legislation that requires used oil to be re-refined? | Yes. Re-refining is encouraged by EU legislation.
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No.
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | Yes.
Continued…

## Slide 38: Used Oil Regulations: Western Europe
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | The fuel burner is subject to the same carbon emission requirements for burning used oil as for using fuel.
14. Is used oil allowed to be placed in a landfill? |  | No.
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | Yes. For re-refining.
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | Yes.
 | ii. Blending with crude oil at a refinery | Used oil can be blended with virgin basestock in a refinery.
 | iii. Dust suppressant | No.
17. Are there companies / associations advocating in used oil category? |  | Yes. GEIR is the main trade association for the re-refining industry at a European level advocating for the recycling of used oil.

## Slide 39: Global Lubricant Demand 2020 and 2021
Chart: 
| USA | China | Western Europe | India | Russia | Japan | Brazil | Indonesia | South Korea | Canada | Thailand | Mexico | Malaysia | Rest of World
2020 | 7373.3 | 6517.3 | 3107.6 | 2516.7 | 1477.3 | 1303.1 | 1201.5 | 854.2 | 830.9 | 698 | 635.9 | 640 | 238.8 | 9421
2021 | 7450.7 | 6967.4 | 3281.6 | 2594.3 | 1506.7 | 1305.6 | 1222.7 | 888.5 | 847.2 | 696.8 | 655.5 | 689.2 | 55.8 | 9800.7
In 2020, overall lubricant demand declined by around 10.5% due to impact of COVID-19. Lubricant demand in all regions except Africa and the Middle East declined in the 10%-11%. In Africa and the Middle East, lubricant demand declined by 7.8%. This is mainly due to lower impact of COVID-19 in Africa and the Middle East compared to other regions.
Industrial is the biggest segment with 47.8% share. The commercial and the consumer segments account for 29% and 23.8%, respectively, in 2020.
In terms of market segments, lubricant demand in the consumer segment showed the highest decline at 13.3% in 2020. This is because personal mobility was hampered as countries started imposing lockdowns to control the spread of COVID-19. Lubricant demand in the industrial segment experienced decline of 8.9% in 2020. This is because industries, especially industries such as pharmaceutical, food, etc., continued working due to which decline in the lubricant demand in the industrial segment was lower than other segments.
The key markets covered in this study account for close to two-thirds of the global lubricant demand.
GLOBAL LUBRICANT DEMAND 2020 AND 2021

## Slide 40: Global Used Oil Material Balance 2020
Chart: USED OIL RE-REFINING, 2020
| Basestock | All other
Sales | 0.64 | 0.36
Total: 5,426.6 Kilotonnes
Chart: USED OIL GENERATION, 2020
| Used oil generated | Lubricant lost
Sales | 0.55 | 0.45
Total: 36,815.6 Kilotonnes
Chart: USED OIL COLLECTION, 2020
| Collected | Not collected
Sales | 0.67 | 0.33
Chart: USED OIL DISPOSAL, 2020
| Fuel | Re-refined-a | All other-b
Sales | 0.52 | 0.4 | 0.08
Total: 20,248.6 Kilotonnes
Total: 13,566.5 Kilotonnes
Total estimated global lubricant demand was 36,815.6 kilotonnes in 2020. Around 20,248.6 kilotonnes or 55% this is generated as used oil. The remaining 45% is lost in consumption/handling or collected on-site and reused as lubricant. Losses can be due to technical losses such as evaporation, combustion, leakages, and handling losses. Some categories of lubricants, such as white oils, selected metalworking fluids, and most grease are consumed totally during the industrial processes.
  Overall generation rate is similar to the generation rate seen in the 12 key markets covered in this study.
Collected used oil accounts for 13,566.5 kilotonnes in 2020 or 67% of the total generated used oil. The overall collection rate is lower than the collection rate seen in the 12 key markets, where the collection rate is around 73%. This is mainly due to better collection infrastructure and implementation of regulations in markets such as Canada, Western Europe, and China, where collection rate is more than 80%. In the US and Japan, the collection rate is 72% and 70%, respectively, leading to higher collection ate in the 12 key markets.
Used oil is mainly disposed as fuel as shown in the pie-chart above. In the 12 key markets, disposing used oil as fuel is the largest disposal method. However, in the 12 key markets, disposal as fuel has 46% share, which is 6% lower than the global market. This is mainly due to lower re-refining capacity outside these 12 key markets.
a- Includes re-refining to VGO/MDO and transformer oil regeneration.
b- Includes landfill, dust suppressant, etc.
Note: Includes re-refining to VGO/MDO and transformer oil regeneration.

## Slide 41: Global Used Oil Material Balance 2021
Chart: USED OIL RE-REFINING, 2021
| Basestock | All other
Sales | 0.64 | 0.36
Chart: USED OIL GENERATION, 2021
| Used oil generated | Lubricant lost
Sales | 0.55 | 0.45
Total: 37,962.7 Kilotonnes
Chart: USED OIL COLLECTION, 2021
| Collected | Not collected
Sales | 0.68 | 0.32
Chart: USED OIL DISPOSAL, 2021
| Fuel | Re-refined-a | All other-b
Sales | 0.52 | 0.4 | 0.08
Total: 20,879.5 Kilotonnes
Total: 14,198.0 Kilotonnes
Total: 5,679.2 Kilotonnes
In 2021, total used oil generation grew by 3.1%, which is same as the growth in lubricant demand. In 2021, the used oil collection grew by 4.7%, which is slightly higher than the growth in the used oil generation. The slightly higher growth in used oil collection is due to higher demand from re-refineries. Used oil re-refining grew by 4.7% in 2021 as demand for basestocks grew in 2021.
Overall share of fuel, re-refining, and other disposal methods in the disposal of used oil remained stable in 2021, same as 2020.
a- Includes re-refining to VGO/MDO and transformer oil regeneration.
b- Includes landfill, dust suppressant, etc.
Note: Includes re-refining to VGO/MDO and transformer oil regeneration.

## Slide 42: Used Oil Material Balance in Key Markets
USED OIL MATERIAL BALANCE IN KEY MARKETS, 2020 |  |  |  |  |  | 
COUNTRY/REGION | LUBRICANT DEMAND (KT) | USED OIL GENERATION (KT) | USED OIL COLLECTION (KT) | DISPOSAL (KT) |  | 
 |  |  |  | RE-REFINING | FUEL | ALL OTHER-a
USA | 7,373.3 | 4,155.3 | 2,996.7 | 1,804.3 | 1,164.6 | 30-b
China | 6,517.3 | 3,361.2 | 2,740.6 | 1,189.7 | 1,131.4 | 419.5
Western Europe | 3,282.5 | 1,872.7 | 1,560.0-c | 974.4 | 567.3 | 18.3
India | 2,516.7 | 1,179.5 | 752.8 | 105.6 | 502.0 | 145.2
Russia | 1,477.3 | 817.6 | 410.1 | 62.6 | 226.1 | 121.6
Japan | 1,303.1 | 635.8 | 441.0 | 6.1 | 419.7 | 15.2
Brazil | 1,201.5 | 657.8 | 452.5 | 400.4 | 52.3 | -
Indonesia | 854.2 | 473.1 | 314.8 | 121.4 | 179.0 | 14.4
South Korea | 830.9 | 473.1 | 325.2 | - | 325.2 | -
Canada | 698.0 | 460.7 | 419.3-c | 250.3 | 125.4 | 43.6
Thailand | 635.9 | 361.9 | 237.5 | - | 222.9 | 14.6
Mexico | 639.9 | 356.4 | 220.6 | 2.3 | 189.2 | 29.2
Malaysia | 238.8 | 129.7 | 86.7 | 19.0 | 53.6 | 14.1-b
a- Includes land filling, dust suppressant, etc. b- Export volume of used oil. c- Includes import of used oil. |  |  |  |  |  | 
Continued…

## Slide 43: Used Oil Material Balance in Key Markets
USED OIL MATERIAL BALANCE IN KEY MARKETS, 2021 |  |  |  |  |  | 
COUNTRY/REGION | LUBRICANT DEMAND (KT) | USED OIL GENERATION (KT) | USED OIL COLLECTION (KT) | DISPOSAL (KT) |  | 
 |  |  |  | RE-REFINING | FUEL | ALL OTHER-a
USA | 7,450.7 | 4,203.3 | 3,031.7 | 1,830.8 | 1,176.8 | 30-b
China | 6,967.4 | 3,605.8 | 2,993.8 | 1,362.6 | 1,169.2 | 462.0
Western Europe | 3,366.2 | 1,919.0 | 1,596.6-c | 989.5 | 587.5 | 19.6
India | 2,594.3 | 1,216.6 | 776.6 | 100.9 | 517.9 | 157.8
Russia | 1,506.7 | 835.2 | 419.2 | 64.0 | 231.0 | 124.2
Japan | 1,305.6 | 635.0 | 439.9 | 6.7 | 418.4 | 14.8
Brazil | 1,222.7 | 668.6 | 468.8 | 410.5 | 58.6 | -
Indonesia | 888.5 | 492.4 | 327.5 | 126.4 | 186.3 | 14.8
South Korea | 847.2 | 479.9 | 329.4 | - | 329.4 | -
Canada | 696.8 | 458.8 | 417.5-c | 248.9 | 125.1 | 43.5
Thailand | 655.5 | 373.2 | 244.8 | - | 231.1 | 13.7
Mexico | 689.2 | 383.8 | 237.6 | 2.5 | 203.5 | 31.6
Malaysia | 255.8 | 140.0 | 93.6 | 19.9 | 60.2 | 13.-b
a- Includes land filling, dust suppressant, etc. b- Export volume of used oil. c- Includes import of used oil. |  |  |  |  |  | 

## Slide 44: Used Oil Generation in Key Markets
Chart: 
| Canada | South Korea | Western Europe | Thailand | USA | Brazil | Russia | Mexico | Indonesia | Malaysia-a | China | Japan | India
Series 1 | 0.66 | 0.57 | 0.57 | 0.57 | 0.56 | 0.55 | 0.55 | 0.56 | 0.55 | 0.54 | 0.52 | 0.49 | 0.47
USED OIL GENERATION RATES IN KEY MARKETS, 2020 AND 2021
Used oil generation rates are generally in the range of 52%-57%. Canada is an exception with 66% generation rate. This is because Canada has relatively higher share of automotive lubricants that have higher generation rates than industrial lubricants. In Canada, share of automotive lubricants is around 55%, which is 10%-15% higher than markets such as the US, Japan, Western Europe, South Korea, etc., leading to higher used oil generation rate in Canada.
Japan and India have relatively lower used oil generation rates.
  In Japan, share of MWF and rubber process oils in total lubricant demand was around 21% while it is around 16.4% in the US in 2020. It is to be noted that rubber process oils do not generate any used oil while MWF is generally reclaimed at site and generate small amount of used oil. Further, grease that do not generate any used oil accounts for around 4.8% of total lubricant demand in Japan in 2020. The corresponding share for the US is 2%. As a result, the used oil generation rate in Japan is low.
  In India, white oils, rubber process oils, and grease that do not generate any used oil is around 25% in total lubricant demand in the country in 2020. The corresponding share in the US is around 22.3%. There is also a possibility of used oil being generated is not recorded resulting in lower generation rates. As a result, the used oil generation rate is lower in India.
a- Generation rate is 55% in 2021. The increase is due to higher growth in automotive lubricants demand in 2021. Automotive lubricants generate more used oil as compared to industrial lubricants.

## Slide 45: Used Oil Collection in Key Markets
Chart: 
| Canada-a | China-b | Western Europe | USA | Japan | Brazil-c | South Korea | Indonesia | Malaysia | Thailand | India | Mexico | Russia
Series 1 | 0.85 | 0.82 | 0.79 | 0.72 | 0.69 | 0.69 | 0.69 | 0.67 | 0.67 | 0.66 | 0.64 | 0.62 | 0.5
USED OIL COLLECTION RATES IN KEY MARKETS, 2020 AND 2021
Used oil collection rates are generally in the range of 64%-70%.
  Canada, China, and Western Europe are exceptions with collection rates either more than or close to 80%. This is due to well developed collection infrastructure. For example, in Canada, collection of used oil is managed by individual used oil associations in provinces in Canada leading to higher collection rates. Similarly, in Western Europe, many countries have government authorized bodies/associations that manage the used oil collection leading to high used oil collection. Western Europe also has well developed re-refining industry, which is also involved in used oil collection. This also leads to higher used oil collection.
  In China, strict implementation of regulations, have led to high used oil collection rates. In 2020, total collection rate of used oil increases to 82%, up by 7% compared to 2018, as governments tighten up regulations and enhance enforcement mechanism for hazardous waste collection.
Russia is on the other side of the spectrum with low collection rates. This is mainly due to two reasons:
  Logistics. Russia is the largest country by area in the world due to which collectors need to travel long distances to collect used oil. As a result, collectors tend to transport only large volumes of used oil to make profit. In case when collectors have to drive long distances for collecting small volumes of used oils, the costs can be covered by the generator. This results in low collection.
  Collection by grey/black market for which no proper records are maintained leading to lower reported used oil collection in the country.
a- Collection rate is 84% in 2021
b- Collection rate is 83% in 2021.
c- Collection rate is 70% in 2021.

## Slide 46: Used Oil Disposal in Key Markets
Chart: 
| Canada | China | Western Europe | USA | Japan | Brazil | South Korea | Indonesia | Malaysia | Thailand | India | Mexico | Russia
Re-refining | 0.57 | 0.46 | 0.62 | 0.6 | 0.02 | 0.88 | 0 | 0.38 | 0.25 | 0 | 0.13 | 0.01 | 0.15
Fuel | 0.32 | 0.39 | 0.37 | 0.39 | 0.95 | 0.12 | 1 | 0.57 | 0.75 | 0.94 | 0.67 | 0.86 | 0.55
All other-a | 0.11 | 0.15 | 0.01 | 0.01 | 0.03 | 0 | 0 | 0.05 | 0 | 0.06 | 0.2 | 0.13 | 0.3
USED OIL DISPOSAL RATES IN KEY MARKETS, 2020
Used oil disposal varies across countries/regions with fuel being the by far the largest disposal method in some countries/regions while re-refining being the largest disposal method in some countries/regions.
  Countries/Regions such as the US, Western Europe, Canada, China, and Brazil with well-developed re-refining capacity have higher share of re-refining in disposal of used oil.
  On the other hand, countries such as Japan, South Korea, Thailand, and Mexico that have no re-refining capacity or small re-refining capacity have almost entirely used oil disposed as fuel.
  Other countries such as Indonesia, India, Malaysia, and Russia have moderate to significant share of re-refining as disposal route for used oil. However, lower share of re-refining than fuel is due to not sufficient re-refining capacity as in Indonesia, where used oil fed to re-refineries accounts for more than 90% of re-refining capacity or disposal of used oil as fuel is more profitable.
In 2021, used oil disposal has remained same as 2020 in most regions/countries except in few countries/regions such as China and India.
  In China, share of re-refining has increased from 44% in 2020 to 46% in 2021 while share of fuel has declined by 1% in 2021. This is mainly driven by improved collection amid growing demand for basestocks in China.
  In India, share of re-refining has declined 14% in 2020 to 13% in 2021. This is because disposal of used oil as fuel or other ways such as blending it with superior kerosene oil, which is sold as replacement for light diesel oil is more profitable.
a- Used as dust suppressant, disposed in landfill, etc.

## Slide 47: Used Oil Re-Refining
ESTIMATED GLOBAL RE-REFINED BASESTOCKS CAPACITY, 2020 |  |  |  | 
 | KILOTONNES |  |  | 
REGION | GROUP I | GROUP II | GROUP III | TOTAL
Asia Pacific | 1,661.1 | - | - | 1,661.1
North America | 60.0 | 954.0 | 17.0 | 1,031.0
Europe-a | 667.2 | 179.0 | 50.0 | 896.2
South America | 198.0 | 159.0 | - | 357.0
Middle East and Africa | 583.0 | - | - | 583.0
Total | 3,179.3 | 1,396.0 | 67.0 | 4,642.3
a- Includes Russia and Eastern Europe. |  |  |  | 
In 2020, China, and the United States and Canada led the re-refined basestock capacity among the 12 regions/countries covered in the study. This is not surprising given that these two markets generate the most amount of used oil in the markets covered in the study.
They are followed by Western Europe and Brazil, which have well-established re-refining industry as well as reasonably well-enforced regulations that have allowed the industry to grow in these two regions.
India, Mexico, Indonesia, Russia, and Malaysia have small re-refining capacity, as the availability of used oil as well as demand for re-refined products is low in these markets. For the same reason, Mexico and Japan have less than 10 KT of re-refining capacity.
Thailand and South Korea have no re-refining capacity and the used oil is mostly used as fuel in these two countries.
The re-refining industry is mostly focused on producing Group I re-refined basestocks. The global re-refined basestock capacity is around 4,642.3 kilotonnes with Group I accounting for around 68% of the total re-refining capacity. Group II accounts for around 30% while Group III accounts for more than 1%.
The re-refining industry is shifting toward Group II and III basestocks as can be seen from the fact that the share of Group I has declined from 71% in 2018 to 68% in 2020. At the same time, share of Group II capacity has increased from 28% in 2018 to 30% in 2020.
Further, in Europe, Group III capacity has increased from 50 KT to 100 KT in April 2021 after Puraglobe upgraded its Group II re-refinery to Group III re-refinery in Germany.

## Slide 48: Attitudes Toward Re-Refined Lubricants
Generally, the lubricants made from re-refined lubricants are considered to be of lower quality compared to lubricants made from virgin basestocks. As a result, lubricants made from re-refined basestocks have low demand in the market. Usually, small local blenders who are price-driven look to use re-refined basestocks for blending their products. Local blenders acquire both virgin and re-refined basestocks and blend them to reduce the cost of raw materials.
As of 2020, most of the re-refined basestocks are used for producing HDMO, hydraulic fluid, and PCMO, especially in monograde with lower API classification. In the United States and Canada, and Brazil, 80%-85% of re-refined basestocks is used to produce HDMO, MCO, PCMO, and hydraulic fluids. The corresponding share for China is around 60%. The usage of re-refined basestocks is not clear in Western Europe as information availability is limited, however, it is estimated that 50% of re-refined basestocks are used to produce automotive lubricants, while the remaining 50% are used to produce industrial lubricants. In countries such as India, Russia, and Mexico, the re-refined basestocks are probably used for producing industrial lubricants for small enterprises.

## Slide 49: Finished Lubricant Market Outlook
Chart: PROJECTED GLOBAL FINISHED LUBRICANT DEMAND, 2020-2030
| Industrial | Commercial | Consumer
2020 | 17606.7 | 10571.7 | 8637.2
2021 | 18052.8 | 10942.6 | 8967.3
2025 | 19391.3 | 11498.3 | 9778.9
2030 | 19884.2 | 11536.3 | 9755.1
The overall market demand of finished lubricant is expected to see a significant growth of 4.3% to an estimated 37,991.0 KT in 2021 because of sharp decline in lubricant demand in 2020. The next decade is anticipated to witness a moderate growth at a CAGR of 2.2% per year between 2020 and 2025, and then at a CAGR of 0.3% during 2025- 2030.
During 2020-2025, consumer segment is expected to grow the fastest at a CAGR of 2.6% while both the industrial and the commercial segments are expected to grow at a CAGR of 2.1%.
During 2025-2030, consumer segment is expected to witness a decline at an annual rate of 0.1% while the industrial and the commercial segments are expected to grow at a CAGR of 0.2% and 0.4%, respectively.
During 2020-2025, Africa and the Middle East, and South America are expected to be the two fastest growing regions growing at a CAGR of 3.4% and 3.2%, respectively. They will be followed by Europe and Asia Pacific growing at a CAGR of 2.5% and 2%, respectively. North America is expected to grow the slowest at a CAGR of 1.5% during the same period.
During 2025-2030, Africa and the Middle East, and South America are expected to grow at a CAGR of 2% and 1.6%, respectively while North America and Asia Pacific are expected to show a decline. Decline in Asia Pacific is expected due to decline in the lubricant demand in China during 2025-2030.

## Slide 50: Global Used Oil Industry 2025
Chart: USED OIL GENERATION, 2025
| Used oil generated | Lubricant lost
Sales | 0.56 | 0.44
Total: 40,668.5 Kilotonnes
Chart: USED OIL COLLECTION, 2025
| Collected | Not collected
Sales | 0.68 | 0.32
Chart: USED OIL DISPOSAL, 2025
| Fuel | Re-refined | All other
Sales | 0.51 | 0.42 | 0.07
Chart: USED OIL RE-REFINING, 2025
| Basestock | All other
Sales | 0.64 | 0.36
Total: 22,774.4 Kilotonnes
Total: 15,486.6 Kilotonnes
Total: 6,504.4 Kilotonnes
In 2025, used oil generation rate is expected to grow from 55% in 2020 to 56% in 2025 driven by the faster growth in automotive lubricants during 2020-2025. It is estimated that automotive lubricants will grow at a CAGR of 2.1% during 2020-2025. During the same period, industrial lubricants are expected to grow at a CAGR of 2%. As automotive lubricants generate more used oil compared to industrial lubricants, used oil generation rate is expected to grow from 55% in 2020 to 56% in 2025.
Used oil collection is expected to grow from 67% in 2020 to 68% in 2025 due to better implementation of regulations.
Share of re-refining in disposal of used oil is expected to rise from 40% in 2020 to 42% in 2025 as new re-refining capacity is commissioned in the key markets such as the US, Western Europe, and China. As a result, share of fuel as disposal route is expected to decline during 2020-2025.
  It should be noted that decline in share of fuel as disposal route does not mean the decline in volume of used oil disposed as fuel. The volume of used oil disposed as fuel is expected to increase during 2020-2025.
Note: Global forecast is estimated after assuming that used oil industry do not undergo a major change outside the 12 key markets during the forecast period.

## Slide 51: Global Used Oil Industry 2030
Chart: USED OIL GENERATION, 2030
| Used oil generated | Lubricant lost
Sales | 0.56 | 0.44
Chart: USED OIL COLLECTION, 2030
| Collected | Not collected
Sales | 0.69 | 0.31
Chart: USED OIL DISPOSAL, 2030
| Fuel | Re-refined | All other
Sales | 0.47 | 0.46 | 0.07
Chart: USED OIL RE-REFINING, 2030
| Basestock | All other
Sales | 0.64 | 0.36
Total: 41,175.6 Kilotonnes
Total: 23,058.3 Kilotonnes
Total: 15,910.3 Kilotonnes
Total: 7,318.7 Kilotonnes
In 2030, used oil generation rate is expected to remain stable at 56%, same as 2025. During 2025-2030, automotive lubricant demand growth is expected to show a small growth leading to same generation rate in 2030 as 2025.
Used oil collection is expected to grow from 68% in 2025 to 69% in 2030 due to better implementation of regulations and improvement in collection infrastructure.
Share of re-refining in disposal of used oil is expected to rise from 42% in 2025 to 46% in 2030 mainly driven by rise in re-refining in China. In China, improved quality of used oil as a result of growing usage of better-quality lubricants is expected to drive the growth in re-refining as disposal route for used oil. Share of re-refining is expected to rise from 55% in 2025 to 74% in 2030 in China. As a result, share of fuel as disposal route is expected to decline during 2025-2030.
Note: Global forecast is estimated after assuming that used oil industry do not undergo a major change outside the 12 key markets during the forecast period.

## Slide 52: Used Oil Re-Refining Outlook
ESTIMATED GLOBAL RE-REFINED BASESTOCKS CAPACITY, 2020, 2025, AND 2030 |  |  | 
 | KILOTONNES |  | 
REGION | 2020 | 2025 | 2030
Asia Pacific | 1,661.1 | 1,828.7 | 1,828.7
North America | 1,031.0 | 1,283.0 | 1,283.0
Europe-a | 896.2 | 981.2 | 981.2
South America | 357.0 | 357.0 | 357.0
Middle East and Africa | 583.0 | 583.0 | 583.0
Total | 4,642.3 | 5,032.9 | 5,032.9
a- Includes Russia and Eastern Europe. |  |  | 
During 2020-2025, re-refining capacity is expected to be added in Asia, Europe, and North America.
  Capacity is expected to be added in China, the US, and Germany.
  In China, Group I capacity will be added while in the US and Germany, Group III capacities will be added.

## Slide 53: Market Evaluation
Opportunities
Growth opportunities for re-refiners as countries around the world focus on reducing waste and move toward circular economy. This is expected to drive the demand for re-refined basestocks.
Further, as the demand shift toward Group II and Group III basestocks, re-refiners with Group II and Group III capacity are expected to have better growth prospects.
Better implementation of regulations along with fiscal incentives are also expected to drive the growth in volume of used oil collection as well as improvement in quality of the used oil collected leading to more used oil available for re-refining. This is also expected to drive the growth in re-refining industry.
Perceptions of quality regarding re-refined basestocks oil are improving with consumers looking at re-refined lubricants more favorably. This is also expected to drive the demand for re-refined basestocks during the forecast period.
Challenges
In some countries, there is insufficient used oil feedstock to cover the whole of the re-refining capacity and feedstock needs to be imported from abroad to make up the shortfall. There are logistical and administrative difficulties in importing used oil, since they are classified as a hazardous waste in several countries.
Grey/Black market of used oil in some countries reduces the available used oil for re-refining. Lax implementation of regulations also increases this issue.
Logistics is another challenge in big countries such as Russia or the US due to which it is financially unviable to collect used oil over large distances. Further, in some countries such as Canada or Germany, where the used oil collection is already above 80%, collecting further used oil could become very expensive leading to rise in operating cost for the re-refining industry.
The global basestock market is shifting away from API Group I basestocks in favor of higher quality basestocks, such as API Group II and Group III. This represents a challenge for the used oil re-refining industry, as most re-refineries are geared toward Group I basestocks production and may not have enough suitable used oil feedstock to produce Group II and III basestocks.

## Slide 54
Country Profiles

## Slide 55: Country Profiles
In this study, Kline has covered following countries/regions:
  Brazil
  China
  India
  Mexico
  Russia
  USA and Canada
  Western Europe

## Slide 56
Brazil

## Slide 57: Brazil Market Synopsis
Chart: USED OIL MATERIAL BALANCE IN BRAZIL, 2021-2030 (MILLION TONS)
| Finished Lube Demand | Used Oil Generated | Used Oil Collected | Used Oil Re-refined | RRBO produced
2021 | 1205.1 | 665.1 | 466.2 | 408.1 | 257.1
2025 | 1311.2 | 734.3 | 514 | 467.7 | 294.7
2030 | 1424.2 | 811.8 | 568.3 | 528 | 334
Used Oil Regulations
The key used oil regulations in Brazil are:
  Resolutions of ANP (Brazilian National Agency of Petroleum, Natural Gas and Biofuels), nº 19/99 and nº 20/99
  CONAMA Resolution n. 362/2005
  National Solid Waste Policy (Law 12,305/2010)
All used oil must be collected and destined for recycling, through re-refining. The combustion or incineration (burning) of waste for any purpose is expressly prohibited.
Collectors must have collection contracts with lubricant marketers and sales contracts with re-refiners to ensure used oil is only used for recycling.
Used Oil Material Balance
Used oil generation increased by 1.6% in 2021, which is in line with 1.8% increase in lube demand in 2021. In 2020, used oil generation declined by 5%.
The used oil collection was not affected as much as used oil generation due to COVID-19 as the mandatory collection increased by 1%-3% in different provinces of Brazil.
Used oil collection to be around 70% for 2025 and 2030. Since the collection rate was more than 50% in 2021, which is more than minimal percentage of collection for 2025 and 2030, used oil collection is not expected to grow beyond 70% by 2025 and 2030.
It is estimated about 10% of used oil not collected was illegally burned as industrial fuel in 2021 in Brazil. This is expected to decline to 8.6% and 7% by 2025 and 2030, respectively.
MAJOR USED OIL RE-REFINERS IN BRAZIL, 2021-2030 |  |  | 
 | RE-REFINED BASESTOCKS CAPACITY (KILOTONNES) |  | 
COMPANY | 2021 | 2025 | 2030
Lwart-a | 135.0 | 135.0 | 135.0
Lubrasil | 39.0 | 39.0 | 39.0
Petrolub | 39.0 | 39.0 | 39.0
Proluminas | 27.0 | 27.0 | 27.0
All other | 93.0 | 93.0 | 93.0
Total | 334.0 | 334.0 | 334.0
a- Group II re-refinery, all other refiners produce Group I. |  |  | 
Used Oil Re-refining
The yield of re-refineries in Brazil is around 63%.
Re-refined basestocks are mainly used to produce HDMO, PCMO, and hydraulic fluids in Brazil. Grease is also another major lubricant made from re-refined basestocks in Brazil.
It is not possible to assess consumers’ views about using lubricants made from re-refined basestocks as lubricant brands in Brazil do not disclose if a lubricant is made from virgin or re-refined basestocks.
No significant changes in the overall Brazilian re-refining capacity are expected in the foreseeable future.
Opportunities
As Brazil is expected to remain a net importer of basestocks, there is business opportunity for re-refiners to market re-refined basestocks to reduce Brazil’s dependence on imports.
In this sense, re-refining industry opportunities are two-fold; however, re-refiners need to be seen as a reliable supply alternative for finished lubricants blenders:
  Usage of used oil as fuel needs to be controlled to increase used oil’s availability for re-refining.
  Investments need to be made in used-oil processing technology to ensure a better quality of re-refined Group I basestocks.
Challenges
Used oil collection is a challenge due to the lack of inspection from the main regulators to prevent used oil's usage as a fuel in the country.

## Slide 58: Economic Background
SELECTED ECONOMIC CHARACTERISTICS OF COUNTRY, 2020 AND 2021 |  | 
KEY INDICATOR | 2020 | 2021
Population (Million) | 211.8 | 213.3
GDP at current prices (USD Billion) | 1443 | 1609
GDP per capita, current prices (USD) | 6,816 | 7,543
GDP growth rate, constant prices (Annual % change) | -4.1 % | 5 %
Inflation, average consumer prices (Annual % change) | 4.5 % | 9.3 %
Current account balance (% Of GDP) | -1.7 % | -0.9 %
Gross debit (% Of GDP) | 88.8 % | 82.1 %
Net debit (% Of GDP) | 62.7 % | 59.5 %
Exchange rate BRL/USD (end year) | 5.19 | 5.50
Interest rate (SELIC, end year) | 2 % | 9.25 %
Industrial production (annual % change) | -4.5 % | 5.3 %
Share in Real GDP |  | 
Services (%) | 62.9 % | 63.5 %
Industry (%) | 17.6 % | 19 %
Agriculture (%) | 5.9 % | 6.5 %
Before COVID-19 pandemic, the Brazilian economy was in a slow recovery process during 2017-2019. The GDP was growing at 1.5% after a painful economic slowdown during 2014-2016, when GDP declined at an average annual rate of 2.1%.
Brazil has been strongly impacted by the COVID-19 pandemic and since February 2020 to October 2021, the death toll reached about 610,000.
Brazilian GDP declined by 4.1% in 2020. The fall would have been higher without a huge fiscal stimulus package from government which accounted for more than 8% of GDP in 2020. This massive fiscal stimulus package moderated the impact of COVID-19 on Brazilian economy which could be regarded as one of the most resilient performing markets in Latin America, but this has now left investors and market analysts on edge over the sustainability of Brazilian debt.
IMF (World Economic Outlook, Update October 2021) is forecasting a GDP growth of 5.2% in 2021 and a CAGR of around 2.0% for GDP during 2022-2026 for Brazil.

## Slide 59: Vehicle Population
Chart: VEHICLE SALES BY TYPE IN BRAZIL, 2019-2021
| PC-a | MC-b | Trucks | Tractors | Ag/Constr-c | Buses
2019 | 2.67 | 1.12 | 0.1 | 0.034 | 0.01 | 0.021
2020 | 1.95 | 0.95 | 0.09 | 0.036 | 0.011 | 0.013
2021 | 2.1645 | 1.14 | 0.1035 | 0.03852 | 0.01177 | 0.01495
Million units
Chart: VEHICLE PRODUCTION BY TYPE IN BRAZIL, 2019-2021
| PC-a | MC-b | Trucks | Tractors | Ag/Constr-c | Buses
2019 | 2.8 | 1.1 | 0.118 | 0.04 | 0.0132 | 0.03
2020 | 2.4 | 0.96 | 0.095 | 0.037 | 0.0111 | 0.02
2021 | 2.904 | 1.22 | 0.1349 | 0.04551 | 0.011877 | 0.0284
Million units
The Brazilian automotive industry has been considerably impacted by COVID-19 pandemic.
In general, all automotive vehicles registered significant drops in 2020 except tractors and agricultural/construction vehicles.
Among major automotive categories, passenger cars was the most impacted as its sales dropped almost 30% in 2020.
Other significant sales drops in 2020 in the Brazilian market were: buses 33%, motorcycles 16%, trucks 12%.
Sales of electric vehicles in Brazil broke a new record in 2020, with a 66.5% increase compared to 2019. The market jumped from 11,900 units in 2019 to 19,700 units in 2020.
Forecasts to 2021 by ANFAVEA (Brazilian Automotive Industry Association) and ABVE (Brazilian Association of Electric Vehicles) suggests better outlook for both sales and production in all automotive categories.
Major forecasts for the year 2021:
  Automotive vehicles (including passenger cars, trucks and buses): Sales +11%, production +22%
  Motorcycles: Sales +20%, production +27%
  Electric vehicles (BEV/HEV/PHEV): Sales 30-32 thousand units
Some major challenges for automotive industry recovery in the next years include cost pressures from increasing exchange rate, inflation and concerns about credit availability as interest rates are expected to increase during the next five years, OEMs’ supply chain disruptions and lack of key components for OEMs’ assembly lines (e.g., semiconductors).
a – Passenger cars, b – Motorcycles, c – Agricultural and construction vehicles
a – Passenger cars, b – Motorcycles, c – Agricultural and construction vehicles

## Slide 60: Finished Lubricants Market
Chart: OVERALL LUBRICANT DEMAND IN 2020
| Commercial | Industrial | Consumer
Sales | 0.37 | 0.37 | 0.26
Total: 1,201.5 Kilotonnes
Chart: OVERALL LUBRICANT DEMAND BY TYPE IN 2020 AND 2021
| HDMO | PCMO/MCO | Process Oils | Hydraulic fluids | MWF | Industrial engine oils | All other-a
2020 | 338.2 | 265.5 | 164 | 107.6 | 46.1 | 27.9 | 252.2
2021 | 342.2 | 269.4 | 168.5 | 110.2 | 47.8 | 28.5 | 256.1
KT
Brazil’s lubricants demand in 2020 declined by 5.7% to reach around 1,201.5 kilotonnes in 2020.
The impact of COVID-19 on the Brazilian finished lubricant market was severe in April and May 2020. During these months, Brazilian total lubricant demand registered a drop of about 36% and 22%, respectively, in comparison to the corresponding months in 2019.
From June onwards, lubricants demand recovered at a good pace, specially for industrial lubricants, mainly due a huge fiscal package stimulus by the Brazilian government and despite many future concerns about macroeconomics and political-economic issues, the mid- and long-term growth prospects for finished lubricant demand growth in Brazil remain positive.
Market preliminary data and Kline analysis point out to a recovery of Brazilian finished lubricants in the first half of 2021. Based on main market fundamentals, Kline forecasts an overall growth of around 1.8% to reach about 1,222.7 kilotonnes in 2021.
a - Includes gear oils, greases, compressor oils, refrigeration fluids, turbine oils, and other automotive and industrial applications

## Slide 61: Lubricant Blenders
Chart: 
| Iconic | Vibra Energia | Moove | Shell | Petronas | All other-a
Series 1 | 0.20262 | 0.19214 | 0.14354 | 0.10306 | 0.090022 | 0.26863
FINISHED LUBRICANT MARKET SHARE
IN BRAZIL BY COMPANY, 2020
Total: 1,201.5 kilotonnes
According to ANP (Brazilian National Agency of Petroleum, Natural Gas and Biofuels), by February 2020, the Brazilian lubricant market consisted of over 120 finished lubricant blenders, 3 Petrobras' refineries for producing virgin basestocks, 13 re-refiners of used oils, and 24 used oil collectors.
The five largest lubricant blenders – Iconic (a JV between Ipiranga [controlled by Ultra Group] and Chevron), Vibra Energia (former BR/Petrobras Distribuidora), Moove (Cosan Group), Shell, and Petronas – accounted for 73% of Brazilian finished lubricant market in 2020.
Brazilian finished lubricants demand was estimated at 1,184.5 kilotonnes in 2020, which was 5.7% lower than 2019.
Overall Brazil’s finished lubricants demand is forecast to grow at a CAGR of 2.1% over the next 10 years to reach about 1,458.1 kilotonnes by 2030.
Brazilian basestock demand also dropped in 2020, in line with the declining demand for finished lubricant to about 22.2 KBD, a decline of 5.5% over 2019.
Local basestocks supply was another big concern for Brazilian blenders in 2020 mainly because of reduced basestock availability owing to 20% decline in production by Petrobras.
Petrobras is the sole local producer of virgin Group I basestocks, but small and mid Brazilian re-refiners also play an important role in the whole basestock supply chain.
Re-refined basestocks local supply including API Group I and Group II also registered a drop of about 6% in 2020.
a – Includes YPF, TotalEnergies, BP Castrol, Energis 8, Ingrax, Quaker Houghton, Ultrax, Fuchs Petrolub, and many other small and mid lubricant blenders.

## Slide 62: Regulations
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | In Brazil, federal regulations govern the disposal of used oil. The Ministry of Mines and Energy and the Ministry of Environment are co-responsible for developing and enforcing laws throughout the entire country. These ministries are backed up by the Brazilian National Agency of Petroleum, Natural Gas and Biofuels (ANP), the Brazilian Environment and Natural Resources Institute (IBAMA), and the National Environment Council (CONAMA), which are ultimately responsible for enforcing regulations.
2. How is Used Oil classified i.e., hazardous waste, special waste etc.? | Hazardous waste
3. Are there any requirements on who can collect used oil? | Used oil collectors must have collection contracts with one or more producers or importers and sales contracts with one or more basestock re-refiners or any other party that can ensure that the used oil is only used for recycling.
4. Does country have an association(s) managing the collection and disposal of used oil? | Brazilian Institute JOGUE LIMPO is an association of lubricants producers and importers, and it is the managing entity responsible for carrying out the reverse logistics of plastic packaging used in finished lubricants as well as used/contaminated lubricating oil.
5. Is a levy charged on sales of lubricants to support used oil collection associations? | CONAMA’s resolution states that lubricant blenders/importers are directly responsible for the collection of used oil or should at least cover the cost of used oil collection by third parties.
6. Are there any requirements for how Used Oil generators manage used oil? | Same requirements as question 7 (next in this table)
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | Used oil generators are required to: Store used oil properly to avoid environmental contamination, enabling collection Adopt proper measures to avoid used oil contamination with chemical products, water, fuels or anything else that might prevent used oil recycling Transfer used oil exclusively to a regular collector Provide the regular collector with information on possible contamination due to oil usage Keep documents on the used oil collection and sale However, if the generator is working with lubricants that lead to the generation of non-recyclable used oil, then they are required to dispose of the used oil as per the law in an environmentally friendly way.
Continued…

## Slide 63: Regulations
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
8. Do any requirements/legislation exist around different types of used oil? |  | No.
9. Does the country have requirements or regulations regarding the export or import of used oil? |  | Both exports and imports of used oils are not authorized.
10. Does the country have any legislation that requires used oil to be re-refined? |  | Brazilian legislation predicts that all used oil collected must be recycled/re-refined.
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? |  | There is no obligation, but as Brazilian market is a large importer re-refined basestocks are important in the overall supply for lubricants market.
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? |  | All these end uses are considered illegal.
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | Both used or contaminated lubricant oils can not be used as fuel for burning in Brazil.
14. Is used oil allowed to be placed in a landfill? |  | The disposal of used oils in the soil, underground, territorial waters, and sewage and effluents systems is prohibited.
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | There is mandate but not subsidies.
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | No.
 | ii. Blending with crude oil at a refinery | No.
 | iii. Dust suppressant | No.
17. Are there companies/associations advocating in used oil category? |  | Not for used oils but SINDIRREFINO (National Syndicate of the Mineral Oil Re-Refining Industry) and AMBIOLUC (Environmental Association for Collection, Management and Re-Refining of Used Oils) are private associations representing basestocks re-refiners in Brazil
Continued…

## Slide 64: Regulations
iii. Collection/Transportation/Storage/Disposal (continued)
Collectors must also present to IBAMA and other regulatory entities information on the volume of used oil collected for each producer/importer, and volume delivered to each re-refiner.
Collectors need to guarantee safe storage, handling, and transportation, including avoiding the contamination of used oil with chemical products, solvents, water, etc.
iv. Disposal – Re-refining
All used oil must be collected and destined for recycling, through re-refining.
v. Disposal – Fuel/Others
The combustion or incineration (burning) of waste for any purpose is expressly prohibited.
Regulatory Enforcement
i. Responsible Agencies
The ANP is responsible for regulating and inspecting the collection, transport and re-refining activities of used or contaminated oil.
ii. Enforcement Mechanisms
The regulations also mention the penalties for the non-fulfillment of the obligations on the part of producer/importers, collectors, and re-refiners. The enforcement of the regulation and the application of penalties are done by IBAMA and other state and/or municipal environmental bodies.
iii. Effectiveness of Regulations Enforcement
Although legislation predicts that all used oil collected must be recycled, it is estimated around 20% of used oil is burned as industrial fuel or send to other illegal disposals.
Key Used Oil Regulations
Resolutions of ANP (Brazilian National Agency of Petroleum, Natural Gas and Biofuels), nº 19/99 and nº 20/99
CONAMA Resolution n. 362/2005
National Solid Waste Policy (Law 12,305/2010)
i. Generation
Used oil generators are required to:
  Store used oil properly to avoid environmental contamination, enabling collection
  Adopt proper measures to avoid used oil contamination with chemical products, water, fuels or anything else that might prevent used oil recycling
  Transfer used oil exclusively to a regular collector
  Provide the regular collector with information on possible contamination due to oil usage
  Keep documents on the used oil collection and sale
  However, if the generator is working with lubricants that lead to the generation of non-recyclable used oil, then they are required to dispose of the used oil as per the law in an environmentally friendly way.
ii. Classification of Used Oil
According to the above-mentioned regulations OLUC is considered a Class I hazardous waste.
iii. Collection/Transportation/Storage/Disposal
Collectors must have collection contracts with one or more producers/importers and sales contracts with one or more re-refiners or any other party that can ensure that the used oil is only used for recycling.
Key Influencers
i. Public Sector
Ministry of Economy
Ministry of Mines and Energy
Ministry of Environment
ANP (Brazilian National Agency of Petroleum, Natural Gas and Biofuels)
IBAMA (Brazilian Environment and Natural Resources Institute)
CONAMA (National Environment Council)
ii. Private Sector
ABD (Brazilian Downstream Association)
JOGUE LIMPO, the Brazilian Institute
SINDIRREFINO (National Syndicate of the Mineral Oil Re-refining Industry)
AMBIOLUC (Environmental Association for Collection, Management and Re-Refining of Used Oils)
Impact of Current Regulations
Due to current regulations in the period of 2016-2020, around an average of 400 kilotonnes was collected per year of used oils fully disposed and processed in the Brazilian re-refining industry.
Probable Future Regulations
There are no new regulations, amendments or changes to current regulations expected in a foreseeable future.
Continued…

## Slide 65: Regulations
MINIMUM PERCENTAGE OF USED OIL COLLECTION TO LUBRICANTS SALES IN BRAZIL BY REGION, 2012–2021 |  |  |  |  |  | 
 | BRAZILIAN REGION |  |  |  |  | 
YEAR | NORTHEAST | NORTH | CENTRAL-WEST | SOUTHEAST | SOUTH | BRAZIL
2012 | 26% | 26% | 32% | 42% | 36% | 36.9%
2013 | 28% | 28% | 33% | 42% | 36% | 37.4%
2014 | 30% | 30% | 34% | 42% | 37% | 38.1%
2015 | 32% | 31% | 35% | 42% | 37% | 38.5%
2016 | 33% | 32% | 36% | 42% | 38% | 38.9%
2017 | 34% | 33% | 36% | 42% | 38% | 39.2%
2018 | 35% | 35% | 37% | 42% | 39% | 39.7%
2019 | 36% | 36% | 38% | 42% | 40% | 40.1%
2020 | 37% | 37% | 38% | 45% | 42% | 42.0%
2021 | 38% | 38% | 39% | 48% | 45% | 44.0%
2022 | 39% | 39% | 39% | 50% | 48% | 45.5%
2023 | 40% | 40% | 40% | 52% | 50% | 47.5%
Chart: % of collection
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
% Coleta | 0.381 | 0.385 | 0.389 | 0.392 | 0.397 | 0.401 | 0.42 | 0.44 | 0.455 | 0.475
MINIMUM % OF USED OIL COLLECTION IN BRAZIL
(COUNTRY NATIONAL AVERAGE)
The percentage of finished lubricants that are to be collected as used oil is determined by the Inter-ministerial Ordinance number 100 dated April 8th, 2016, from the Ministries of Mines and Energy, and Environment. The ordinance is in accordance with the environmentally friendly way of disposal of used oil as established in the aforementioned CONAMA’s resolution.
CONAMA’s resolution states that the finished lubricant blender and importer are directly responsible for the collection of used oil or should at least cover the cost of used oil collection by third parties. The volumes to be collected by the finished lubricant blender and importer are proportional to the volume of finished lubricants sold by them.
These proportions have been gradually increasing in the last few years. The current percentages were established in 2016 and predict different levels of collection by region, as a means to reflect the socio-economic differences in different parts of Brazil.
The last update on the required percentages was published in end of 2019 (PORTARIA INTERMINISTERIAL Nº 475, in Portuguese) and has settled the percentages of minimal collection of used oils to the period 2021-2023.

## Slide 66: Material Balance
Chart: USED OIL COLLECTION, 2020
| Collected | Not collected-a
Sales | 0.69 | 0.31
Chart: USED OIL GENERATION, 2020
| Used oil generated | Lubricant lost
Sales | 0.55 | 0.45
Total: 1,201.5 Kilotonnes
Chart: USED OIL DISPOSAL, 2020
| Used oil re-refining | All others-a
Sales | 397.5658 | 52.3248
Chart: USED OIL RE-REFINING, 2020
| Re-refined basestocks | All others-a
B/E | 251.5711 | 145.9947
Total: 657.8 Kilotonnes
Total: 452.5 Kilotonnes
Total: 400.4 Kilotonnes
Brazilian finished lubricants demand was around 1,201.5 kilotonnes in 2020. However, around 264 kilotonnes of 22% of total lubricant demand is exempt from recycling. Lubricants exempted from recycling include lubricants used for agriculture pulverization, chainsaw oils, process oils that do not generate residues, forming fluids, 2T engine oils, oils used in sealed systems, soluble oils, asphalt-based oils, and all finished lubricants exported.
  As a result, lubricants that account for 937.5 kilotonnes of lubricant demand is eligible for used oil industry in Brazil.
Total generation of used oil was around 657.8 kilotonnes in 2020. This is approximately 5% lower than used oil generated in 2019. The decline was mainly due to decline in lubricant demand in 2020.
The minimal percentage of collection was set at 42% of total eligible lubricant demand in 2020. However, the total used oil collection was around 48% of the total eligible lubricant demand in 2020. From the total used oil generated, around 69% or 452.5 kilotonnes was collected.
Around 31% of generated used oil is not collected. It is mainly because it is economically unviable to collect the used oil as the generation site is in a remote location or the used oil is actually collected but not recorded as it is disposed of in an illegal way such as used as a fuel.
  It is estimated that around 51.9 kilotonnes of used oil was illegally disposed as fuel in 2020.
In 2020, Brazilian re-refiners processed a total of around 400.4 kilotonnes of used oils yielding (in average) 252 kilotonnes of re-refined basestocks (including API Group I and Group II), and around 148.4 kilotonnes of byproducts and losses.
a – Mainly illegally disposed as fuel
a – Mainly asphaltic residue, fuels, water and other losses
a – Mainly illegally disposed as fuel

## Slide 67: Used Oil Industry Outlook
Chart: USED OIL COLLECTION, 2021
| Collected | Not collected-a
Sales | 0.7 | 0.3
Chart: USED OIL GENERATION, 2021
| Used oil generated | Lost
Sales | 0.55 | 0.45
Total: 1,222.7 Kilotonnes
Chart: USED OIL DISPOSAL, 2021
| Used oil re-refining | All other-a
Sales | 0.88 | 0.12
Chart: USED OIL RE-REFINING, 2021
| Re-refined basestocks | All other-a
B/E | 270.3493 | 156.8923
Total: 668.6 Kilotonnes
Total: 468.8 Kilotonnes
Total: 410.5 Kilotonnes
In 2021, Brazilian finished lubricants demand is expected to grow by approximately 1.8% to reach 1,222.7 kilotonnes. However, around 293 kilotonnes of 24% of total lubricant demand is exempt from recycling as explained on slide 9.
  As a result, lubricants that account for 929.7 kilotonnes of lubricant demand is eligible for used oil industry in Brazil.
Total generation of used oil was around 668.6 kilotonnes in 2020. This is around 1.6% more than used oil generated in 2020. This is in line with increase in lubricant volume, which increased by 1.8% in 2021.
The minimal percentage of collection was set at 44% of total eligible lubricant demand in 2021. Kline estimates the effective collection to be around 50.4% of the total eligible lubricant demand, which is much higher than 44% as mandated by law in 2021.
From the total used oil expected to be collected in the Brazilian market in 2021, around 88% or 410.5 kilotonnes of the total used oil is estimated to be collected for re-refining.
Around 31% of generated used oil is not collected. It is mainly because it is economically unviable to collect the used oil as the generation site is in a remote location or the used oil is actually collected but not recorded as it is disposed of in an illegal way such as used as a fuel.
  It is estimated that around 60.9 kilotonnes of used oil was illegally disposed as fuel in 2021.
In 2021, Brazilian re-refiners are expected to process a total of around 410.5 kilotonnes of used oil yielding (in average) 259 kilotonnes of re-refined basestocks (including API Group I and Group II) and around 151.5 kilotonnes of byproducts and losses.
a- Mainly illegal disposal as fuel
a– Mainly asphaltic residue, fuels, water and other losses.
a- Mainly illegal disposal as fuel

## Slide 68: Used Oil Generation
In the industrial segment for finished lubricants, the losses happen due to the usage of oil until extinction as well as leakages. It is estimated that around 65% of hydraulic fluids demand is generated as used oil.
Automotive lubricants generate most of the used oil in Brazil, accounting for approximately 72.7% of the total generated used oil. Industrial lubricants account for the balance. Hydraulic fluids are the highest generator of used oil among industrial lubricants.
Automotive used oil is generated during a lubricant change, which usually takes place in workshops, quick lubes, and fuel stations.
Workshops account for approximately 60% of total used oil generated. The corresponding figure for quick lubes and fuel stations is 20% each in the automotive market segment.
Used oils generated in the industrial applications of the Brazilian lubricants market come mainly from hydraulic fluids and other general industrial oils.
Brazilian Institute JOGUE LIMPO is an association of lubricants producers and importers, and it is the managing entity responsible for carrying out the reverse logistics of plastic packaging used in finished lubricants as well as used/contaminated lubricating oil.
Chart: USED OIL GENERATION RATES BY PRODUCT IN COUNTRY, 2020-a
| PCMO | HDMO | Hydraulic fluids | MCO | All other-a
Series 1 | 0.72 | 0.67 | 0.65 | 0.65 | 0.36
Used oil generation increased at a CAGR of 7.7% during 2016-2019 mainly due to increase in finished lubricants demand, which recovered as economy recovered from recession during 2014-2016.
In 2020, used oils generation dropped around 5% as lubricant demand declined due to COVID-19.
Currently, most of the volume loss in the HDMO, PCMO, MCO, and other automotive fluids occurs due to inadequate disposal of used oil, especially in less-developed areas of Brazil.
It is estimated that 67% of HDMO, 72% of PCMO, and 65% of MCO demand is generated as used oil. 45% of remaining automotive lubricants demand volume is generated as used oil.
USED OIL GENERATION BY PRODUCT IN BRAZIL, 2020 AND 2021 |  |  |  | 
LUBRICANT | KILOTONNES |  | % OF TOTAL USED OIL GENERATED | 
 | 2020 | 2021 | 2020 | 2021
HDMO | 226.6 | 229.3 | 34.4 | 34.3
PCMO | 122.3 | 124.1 | 18.6 | 18.6
Hydraulic Fluid | 69.9 | 71.6 | 10.6 | 10.7
MCO | 62.1 | 63.1 | 9.4 | 9.4
All other-a | 176.8 | 180.5 | 26.9 | 27.0
Total | 657.8-b | 668.6 | 100.0 | 100.0
a- Includes ATF, process oil, MWF, industrial engine oil, among others b- Does not add due to rounding |  |  |  | 
a- Generation rates are same in 2021.
b- Includes ATF, process oil, MWF, industrial engine oil, among others

## Slide 69: Used Oil Collection
Chart: USED OIL COLLECTION RATES BY PRODUCT IN COUNTRY, 2020-a
| PCMO | HDMO | MCO | Hydraulic fluids | All other-b
Series 1 | 0.75 | 0.65 | 0.68 | 0.7 | 0.69
Used oil generation increased at a CAGR of 4.3% during 2016-2019 mainly due to increase in finished lubricants demand leading to increase in used oil generation.
Further, increase in mandated used oil collection volume as set under regulation also led to increase in collection of used oil volume.
It is to be noted that illegal disposal of used oil has increased in 2016-2019. The reason is not clear for this increase.
Currently, most of the volume loss in the HDMO, PCMO, MCO, and other automotive fluids occurs due to inadequate disposal of used oil, especially in less-developed areas of Brazil.
In 2021, the used oil collection increased by around 8.9%. The growth in used oil collection is around 2% more than increase in used oil generation in 2021. This is due to increase in mandatory collection of used oil by 1%-3% in different provinces.
In 2020, used oils collection declined by around 4.4% as used oil generation declined. The decline in used oil collection volume is lower than decline in used oil generation volume as the mandatory collection increased by 1%-3% in different provinces of Brazil.
Automotive finished lubricant applications including PCMO/MCO, HDMO, and other automotive lubricants account for around 71.3% of the total collected used oil volumes.
USED OIL COLLECTION BY PRODUCT IN BRAZIL, 2020 AND 2021 |  |  |  | 
LUBRICANT | KILOTONNES |  | % OF TOTAL USED OIL COLLECTED | 
 | 2020 | 2021 | 2020 | 2021
HDMO | 147.3 | 155.9 | 32.6 | 33.3
PCMO | 91.7 | 94.3 | 20.3 | 20.1
Hydraulic Fluid | 49.0 | 50.1 | 10.8 | 10.7
MCO | 42.3 | 43.5 | 9.3 | 9.3
All other-a | 122.3 | 124.9 | 27.0 | 26.6
Total | 452.5-b | 468.8-b | 100.0 | 100.0
a- Includes ATF, process oil, MWF, industrial engine oil, among others b- Does not add due to rounding |  |  |  | 
a- Collection rates were 76% and 68% for PCMO and HDMO, respectively, in 2021.
b- Includes ATF, process oil, MWF, industrial engine oil, among others
Continued…

## Slide 70: Used Oil Collection
AUTOMOTIVE USED OIL COLLECTION BY SOURCES, 2020 |  | 
SOURCE | KILOTONNES | % OF USED OIL COLLECTED
Independent workshops | 60.0 | 18.5
Car dealers’ workshops | 48.0 | 14.9
Quick lube | 44.0 | 13.6
Fuel stations | 44.0 | 13.6
Vehicle fleets | 32.0 | 9.9
Motorcycle workshops | 20.0 | 6.2
All other-a | 74.7 | 23.3
Total | 322.7 | 100.0
a - Includes do-it-yourself, among others |  | 
Continued…

## Slide 71: Used Oil Collection
Most collection of used oil is done re-refiners. They accounted for more than 80% of total used oils collected in 2020.
Top 10 used oil collectors in the Brazilian market in 2020 (values in kilotonnes) are:
  Lwart 127 KT
  Petrolub 47 KT
  Fenix 36 KT
  Proluminas 36 KT
  Tasa 34 KT
  Lubrasil 22 KT
  Falub 19 KT
  IHS Ind. 18 KT
  IPS 17 KT
  Nortlub 12 KT
Finished lubricant blenders and importers are responsible for collecting, or financially enabling the collection of used oil in proportion to the volume of finished lubricants sold by them in Brazil.
The volume of used oil to be collected by each marketer is defined annually based on the company’s annual sales.
The proportion of finished lubricants sales to be collected as used oil is determined by the Ministry of Environment and the Ministry of Mines and Energy.
IBAMA, ANP, and environmental agencies in each state are responsible for verifying the collected volume of used oil.
The Ministry of Environment also defines the minimum percentage of the collection at the beginning of every year based on environmental and economic factors, among others.
Used oil collectors must have collection contracts with one or more producers or importers and sales contracts with one or more basestock re-refiners or any other party that can ensure that the used oil is only used for recycling.
Collection is the most critical activity in the re-refined base oils business since the input is physically pulverized throughout the country in hundreds of collection points, owned by operators of oil change stations and workshops, which are not held accountable for current collection regulations.
Collection is the most critical activity in the re-refined basestocks business since the input is physically pulverized throughout the country in hundreds of thousands of collection points, owned by operators of oil change stations and workshops, which are not held accountable for current collection regulations – that is, does not have a regulatory incentive to facilitate or cooperate with regular collection.
Furthermore, despite re-refining being only authorized destination for collected used oils, in fact a significant portion of the material ends up being incinerated e.g., in cement kilns or melting furnaces, replacing fuel oil, especially when prices favor it.
CONAMA (the Brazilian National Environment Council)’s resolution states that the finished lubricant blender and importer are directly responsible for the collection of used oil or should at least cover the cost of used oil collection by third parties.
Promoting re-refining of used oils is the responsibility of lubricant marketers. They do so by purchasing collection certificates issued by the collectors, which in many cases are re-refiners as well.
The money paid to buy collection certificates is merely a reimbursement of the logistics costs of collecting used oil, which is the lubricant marketer’s responsibility.
Lubricant marketers do not get any tax breaks for buying collection certificates. As a result, lubricant marketers either raise the prices of their lubricants to maintain margins or absorb the cost of collection certificates in their margins.
Collection certificates are priced in the range of BRL 0.35 to BRL 0.45/liter (7-9 US cents/liter). For many collectors, the core business that generates value is re-refining.
Many of these collectors re-refine used oil to produce basestocks and then sell re-refined basestocks to the same blenders, who had bought collection certificates from them.
It is quite normal that the blenders and collectors bundle purchase of collection certificates together with re-refined basestock and negotiate a larger deal.
For some blenders, it represents an opportunity; however, for others that might mean a challenge, as some companies have the policy of not using re-refined basestocks in their finished lubricant formulations.
INFRASTRUCTURE OF THE MAJOR BRAZILIAN RE-REFINERS VS. USED OIL COLLECTION, 2020 |  |  |  |  | 
COMPANY | OWN FLEET | OUTSOURCED FLEET | TOTAL FLEET | COLLECTION CENTERS | COLLECTION POINTS
Lwart | 320 | 23 | 343 | 17 | >150,000
Proluminas | >100 | 150 | >250 | 4 | >35,000
Petrolub | 157 | 29 | 186 | 4 | 12,000
Tasa | 139 | 46 | 185 | 1 | 12,000
Lubrasil | 77 | 50 | 127 | 7 | 35,000
Fenix | 63 | 12 | 75 | 1 | 11,000
IPS-a | 56 | 13 | 69 | 1 | 25,000
Falub | 9 | 4 | 13 | 0 | 12,000
All Other | n/a | n/a | n/a | n/a | >15,000
TOTAL | >921 | 327 | >1248 | 35 | >307,000
a - Indústria Petroquímica do Sul |  |  |  |  | 

## Slide 72: Used Oil Disposal
Chart: USED OIL DISPOSAL IN BRAZIL, 2020
| Re-refining | All other-a
Disposal | 397.5658 | 52.3248
Total: 400.4 Kilotonnes
The Brazilian legislation defines that all used oil collected must be recycled/re-refined, but it is known that some used oil is burned as industrial fuel in Brazil.
It is estimated about 10% of used oil not collected or 52 kilotonnes was illegally burned as industrial fuel in 2020 in the Brazilian market. The corresponding figure for 2021 is 60.9 kilotonnes.
As per ANP (the Brazilian National Agency of Petroleum, Natural Gas and Biofuels) database, the overall used oil collection declined by around 4.4% in 2020 mainly due to the impact of COVID-19 pandemic in Brazil.
In 2021, the used oil volume for re-refining increased by around 7.9% as used oil collection volume increased in 2021.
Disposing of used or contaminated oil in the environment is a federal crime, with penalties that vary from financial fines to prison terms.
Safely storing the used oil helps used oil generators to comply with regulations and allow them to sell it at virtually no extra cost.
The re-refiners are responsible for receiving all used oil exclusively from an authorized collector, which in many cases are the re-refiners themselves.
The re-refiners are also required to give a certificate of receipt after receiving the used oil from the collector and must also keep these documents updated and maintain a record for five years.
Further, re-refiners are required to submit information on used oil received from each collector and re-refined basestocks sold to each finished lubricant blender to regulatory bodies such as IBAMA and other state agencies on a periodic basis.
USED OIL DISPOSAL BY PRODUCT TYPE IN BRAZIL, 2020 AND 2021 |  |  |  | 
LUBRICANT TYPE | KILOTONNES |  |  | 
 | 2020 | All other-a | 2021 | 
 | RE-REFINING | ALL OTHER-a | RE-REFINING | ALL OTHER-a
HDMO | 129.6 | 17.7 | 135.6 | 20.3
PCMO | 82.6 | 9.1 | 84.0 | 10.4
Hydraulic fluids | 44.1 | 4.9 | 45.1 | 5.0
MCO | 35.5 | 6.8 | 34.8 | 8.7
All other-b | 108.6 | 13.8 | 111.0 | 14.2
Total | 400.4 | 52.3 | 410.5 | 58.6
a- Mainly illegal disposal as fuel b- Includes ATF, process oil, MWF, industrial engine oil, among others. |  |  |  | 
a- Mainly illegally
disposal as fuel

## Slide 73: Used Oil Re-Refining
MAJOR USED OIL RE-REFINERS IN BRAZIL, 2020 |  |  | 
 | KILOTONNES |  | 
COMPANY | USED OIL FEED CAPACITY | RE-REFINED BASESTOCK CAPACITY | RE-REFINED BASESTOCK PRODUCTION
Lwart-a | 186.0 | 135.0 | 115.0
Proluminas-b | 63.0 | 39.0 | 30.0
Petrolub-b | 65.0 | 39.0 | 29.0
Lubrasil-b | 43.0 | 27.0 | 20.0
All other-b | 171.0 | 93.0 | 57.0
Total | 528.0 | 334.0 | 252.0
a- Group II capacity b- Group I capacity |  |  | 
Brazilian used oil re-refiners in Brazil produced around 252 kilotonnes of re-refined basestock in 2020 or in terms of yield around 63% of the total used oil shipped to them.
The material balance, 37% of total processed used oils or 150 kilotonnes, is mainly asphaltic residues, fuel oil water and other wastes.
Total re-refined basestock capacity is about 334 kilotonnes. The average operating rate was around 77% mainly pushed by Lwart (about 85%) in 2020.
In spite of negative impact of COVID-19 on the Brazilian lubricants market the production of re-refined basestocks dropped just 1% in 2020 YoY.
Technologies for re-refined basestocks:
  Except Lwart that uses a hydrogenation technology to produce API Group II re-refined basestock in its plant located in Lençois Paulista, almost all other re-refiners use old technologies for production of Group I.
Technologies for re-refined basestocks (continued):
  The main technology used by Brazilian GI re-refiners is the improved Meiken (or acid/clay), which contemplates the neutralization of the acid sludge in the conventional process and requires lower investments and overall maintenance costs.
  On the other hand, this process has lower efficiency in basestocks production and yields lower-quality basestocks.
  Few re-refiners in Brazil have invested in advanced technologies such as Distillation/Thin Film Evaporation or Propane Extraction and Hydrogenation.
Pricing for re-refined basestocks:
  Group I: In general, its pricing follows Petrobras pricing for Group I basestocks produced at refineries Reduc (mainly) and Rlam less a discount of 5% to 10% but of course depending on specific supply-demand balance situation sometimes re-refined basestocks can include a price premium vs. Petrobras prices.
Pricing for re-refined basestocks (continued):
  Group II: Lwart basestocks have a high quality compared to virgin Group II basestocks and its pricing is based on international prices which as also followed by its main competitors (wholesale distributors) in Brazil.
Over 50% of total volume of re-refined basestocks are sold and negotiated between re-refiners and lubricant blenders on spot basis in the Brazilian market.
There is no plans to upgrade Group I re-refined basestocks plants to higher quality basestocks in Brazil for the future.

## Slide 74: Used Oil Re-Refiner Profiles
Lwart
Lwart is the leader in the Brazilian re-refining market, with 46% overall market share during 2018-H1 2021.
The company is also at the forefront in terms of collection and process efficiency. It is the only re-refiner in Brazil to produce re-refined hydrogenated Group II basestocks.
Lwart has two re-refineries, one in Lençóis Paulista, state of São Paulo, where its headquarters are located, and one in Feira de Santana, state of Bahia, which is currently inactive due to recent investments in the re-refinery at Lençóis Paulista. Investments were made at re-refinery at Lençóis Paulista to upgrade it to produce re-refined Group II basestocks. As a result, the re-refinery in Bahia has become obsolete due to the constraint in used-oil supply and the higher profitability of the Group II basestocks. The current used-oil processing capacity is 210 kilotonnes per year. The basestocks production capacity is about 150 kilotonnes per year.
The company has 14 collection centers strategically located throughout Brazil and a fleet of approximately 320 trucks, and another 20 trucks from third parties, which collects from over 80,000 used oil generators, such as fuel stations, car dealers, workshops, transportation fleets, and industrial plants, collecting nearly 130 kilotonnes of used oil in 2018. The company also purchases some small parcels of used oil from third-party collectors.
The company has more than 150,000 used oil generators registered in its database.
Petrolub
Petrolub is one of the fastest-growing re-refiners and used oil collectors in Brazil, having recently reached the second place in the Brazilian market, with a 15% share in re-refined basestock sales in Brazil in 2018-2021 H1.
Petrolub (continued)
Located in Sete Lagoas, state of Minas Gerais, Petrolub has four collection centers and a 186-truck fleet. Its re-refined Group I basestocks production capacity is estimated at 42 kilotonnes.
The company processed 62.7 kilotonnes of used oil in 2018 and produced 34 kilotonnes of Group I re-refined basestocks in 2018. The company uses acid-clay technology with process efficiency at 60% for processing used oil.
Lubrasil
Founded in 1977, Lubrasil is the third-largest re-refiner in Brazil, with a 12% share in re-refined basestocks overall sales in 2018-2021 H1 in Brazil.
The company, with headquarters in Piracicaba, state of São Paulo, operates a plant with acid-clay technology and a 62% average efficiency. It has seven collection centers and collects used oil in 20 different states (out of the 26 Brazilian states).
The company has a plant expansion project on hold due to the recent economic crisis, and the timeline to resume the expansion is not clear. It is a propane extraction plant, sized to process 126 kilotonnes of used oil per year.
Proluminas
Proluminas was founded in 1987 and holds 12% of the Brazilian market during 2018-2021 H1.
The plant uses Thin Film Evaporation technology and operates at 62% average efficiency. According to specialists, it is perceived to have one of the best quality re-refined basestocks available in Brazil.
The company headquarters are in Varginha, state of Minas Gerais, and its plant is supplied by collection centers located in Betim, state of Minas Gerais; Osasco, state of São Paulo; and Duque de Caxias, state of Rio de Janeiro.
Tasa
Tasa is located in Nova Iguaçu, state of Rio de Janeiro, and has approximately 9% share in re-refined basestock sales in Brazil during 2018-2021 H1.
Its plant operates with acid-clay technology, with process efficiency around 60%.
Tasa has set a tolling agreement with Lwart to outsource its re-refining operations so the re-refined Group I basestocks produced in Lwart’s plant is marketed by Tasa.
IPS (Indústria Petroquímica do Sul)
IPS was founded in 1961 and besides collecting and re-refining used oils, the company blends finished lubricants for automotive and industrial segments.
The company is located in Alvorada, state of Rio Grande do Sul (the southernmost state of Brazil), where it produces re-refined Group I basestocks through acid-clay technology.
The company has no plans for making any investments in the upcoming years.

## Slide 75: SWOT Analysis: LWART
STRENGTHS | WEAKNESSES
The sole producer of API Group II basestocks not only in Brazil but in the whole Latin American region. Modern used oils hydrogenation plant and facilities located in the city of Lençois Paulista, in the state of Sao Paulo, near to biggest lubricant blenders in the country. Lwart is the largest collector of used oils in the country, and it also has the largest nameplate production capacity for re-refined basestocks accounting for more than 40% of total re-refining installed capacity in Brazil. Compared to its main competitors, Lwart has, by far, the best infrastructure for the collection of used oils in the Brazilian market including the largest own fleet (over 300 small and mid-size specialized trucks) and total fleet (over 340 trucks including outsourced fleet) for used oil collection, the largest number of used oil collection centers (17) and used oil collection points (>150,000) in the country. | Kline has not identified any internal factor that could be classified as a relevant weakness for Lwart in the foreseeable future in the Brazilian re-refining industry.
OPPORTUNITIES | THREATS
In long-term, Brazilian finished lubricants market is expected to grow above global average particularly when compared to developed regions, e.g., North America and Europe. Among other factors, ongoing technological evolution, increasing quality and higher pressure from customers to reduce TCO (Total Cost of Ownership) of finished lubricants will continue favoring the use of GII basestocks replacing GI products in its main applications in the global and Brazilian market. Depending on Lwart production economics/re-refining margins vs. crude oil prices in the global market maybe it can be possible for Lwart, from times to times, to increase its overall API Group II production processing VGO (vacuum gasoil) as feedstock to compensate partially the lack of used oils in the Brazilian market. Brazil is huge net importer of high quality basestocks and Group II has the highest deficit among all basestock groups in the country and Lwart can capitalize this situation as the sole producer in Brazil. | Long-term fundamentals point out for a tight supply-demand balance for used oils market in Brazil which is expected to cap Lwart maximum production of re-refined basestocks at 80-85% of operating rate. Increasing import of GII basestocks from USA due to very favorable logistics, shorter transit time, huge overcapacity in the North American market and competitive production costs for basestocks GI and GII compared to other regions. During end of 2020, Petrobras announced in its Strategic Plan a new plant for production of GII basestock by 2025 (GasLub project formerly called Comperj).

## Slide 76: Re-Refined Lubricants
In 2020, the total quantity of local re-refined basestocks blended in the Brazilian finished lubricants market was estimated by Kline in about 252 kilotonnes.
Among main finished lubricant market categories HDMO, hydraulic fluids and PCMO/MCO together accounted for over 80% of total re-refined basestocks demand in 2020 in the country.
In the industrial market segment, the largest demand for re-refined basestock is hydraulic fluids (mainly for AW68) and greases also play an important role in the industrial applications for re-refined basestocks.
Hydraulic fluids represent 23.3% of re-refined basestocks demand. Another relevant consumer is conventional greases, which accounts for 6.9% of re-refined basestocks volume in 2018. Except Group II basestocks produced by Lwart in Brazil, re-refined basestocks are usually perceived as lower-quality products when compared to virgin basestocks.
Blenders claim that many re-refined basestocks cannot be used in their formulations as the lubricants produced will not meet the current minimum American Petroleum Institute (API) service category approved by ANP.
In Brazil, re-refined basestocks are mainly used by lubricant marketers such as Iconic (JV between Ipiranga and Chevron), Ultrax, Lubri-Motor’s, Petronas LI Ingrax, Promax, Incol-lub, and Energis 8.
Former Ipiranga Lubrificantes (lubricant production and marketer business included in Iconic joint venture) is still the biggest end user of re-refined basestocks in Brazil, despite reducing its consumption after a deal with Chevron to establish Iconic (JV between Ipiranga [controlled by Ultrapar] and Chevron).
The quantity of re-refined basestocks used by different lubricant marketers is not so clear, as the lubricant marketers do not disclose such information.
It is also not possible to understand consumers’ views about using lubricants made from re-refined basestocks as lubricant brands in Brazil do not disclose if a lubricant is made from virgin or re-refined basestock.
As a result, consumers do not know if they are using a lubricant made from virgin or re-refined basestocks.
  Basically, no customer knows if they are buying virgin lubricants or re-refined lubricants.
In general, few used oil re-refiners also sell branded re-refined lubricants in the Brazilian market.
CONSUMPTION OF RE-REFINED BASESTOCKS IN BRAZIL BY PRODUCT CATEGORY, 2020 |  | 
 | Kilotonnes | Share, %
HDMO | 97.0 | 38.5
Hydraulic fluid | 59.0 | 23.4
PCMO/MCO | 51.0 | 20.2
Grease-a | 17.0 | 6.7
Process oils | 11.0 | 4.4
General Industrial oils | 8.0 | 3.2
Metalworking fluids | 4.0 | 1.6
Other automotive-b | 3.0 | 1.2
Industrial engine oil | 2.0 | 0.8
Total | 252.0 | 100.0
a- Includes automotive and industrial greases |  | 
b- Includes ATF, HTF, and gear oil |  | 

## Slide 77: Finished Lubricant Market Outlook
Chart: PROJECTED FINISHED LUBRICANT MARKET IN BRAZIL, 2020-2030
| Industrial | Commercial | Consumer
2020 | 444.6 | 449.6 | 307.3
2021 | 456.3 | 454.5 | 311.9
2025 | 504.3 | 475.8 | 331.1
2030 | 565.9 | 505.1 | 353.2
Despite many future concerns about macroeconomics and political-economic issues, the mid- and long-term growth prospects for finished lubricant demand growth in Brazil remains positive.
Brazilian finished lubricant market is expected to grow at a CAGR of around 1.8% during 2020-2025 to reach 1,292 kilotonnes in 2025.
The lubricant demand growth rate is expected to fall marginally to 1.7% CAGR to reach around 1,407.2 kilotonnes in 2030.
In the consumer market segment, lower viscosity multigrade oils, especially 0W-20 and 5W-30 are expected to grow faster, while demand for higher viscosity grades, namely 15W-40 and 20W-50 API grades, will continue to decline as engine parts become more precise and thus, require lower viscosity lubricants.
The consumer segment is expected to decrease in percentage share in the total volume of lubricant demand by 0.8%, going from 25.9% to 25.1% during 2020-2030. Despite that, the total consumer segment lubricant demand will grow at a CAGR of 1.4% reaching 353.2 kilotonnes in 2030.
A similar trend can be foreseen for the commercial lubricants segment, as minimum API requirements will force the residual SAE 40 volumes (approximately 3% of the HDMO market) to migrate to 15W-40.
New heavy-duty vehicles in most cases are recommended to use 10W-40 or 5W-30, which will also increase their market share during the forecast period. However, 15W-40 will continue to be the main viscosity grade from 2020 to 2030.
The commercial lubricants segment is expected to lose 2.1% share in total volume of lubricants during 2020-2030. The total volume will grow at a CAGR of 1.2% reaching 505.1 kilotonnes in 2030.
In the industrial segment, process oils will lead the market, especially rubber process oils, which are aimed primarily at supplying the tire and automotive industries. Hydraulic fluids, which are mainly based on Group I basestocks and are primarily represented by AW68, will remain as the second-most-consumed industrial lubricant in Brazil during the forecast period.
The industrial lubricants segment is expected to increase its percentage share in the total volume of lubricant demand by 2.9%, going from 36.1% in 2020 to 39% in 2030. The total volume will grow at a CAGR of 2.5% reaching 548.9 kilotonnes in 2030.

## Slide 78: Used Oil Industry 2025
Chart: USED OIL COLLECTION, 2025
| Collected | Not collected-a
Sales | 0.7 | 0.3
Chart: USED OIL GENERATION, 2025
| Used oil generated | Lost
Sales | 0.56 | 0.44
Total: 1,311.2 Kilotonnes
Chart: USED OIL DISPOSAL, 2025
| Used oil re-refining | All other-a
Sales | 464.1269 | 43.6035
Chart: USED OIL RE-REFINING, 2025
| Re-refined basestocks | All other-a
B/E | 0.63 | 0.37
Total: 734.3 Kilotonnes
Total: 514 Kilotonnes
Total: 467.7 Kilotonnes
Brazilian finished lubricants demand is expected to be around 1,311.2 kilotonnes in 2025.
From total lubricant demand, about 350.1 kilotonnes of 26.7% of the total lubricant demand is expected to be exempted from recycling. As a result, the total eligible lubricant demand for the used oil industry is 961.1 kilotonnes for 2025.
Kline estimates used oil collection to be around 70% as the minimal percentage of collection is estimated at 47.5% of total eligible lubricant demand in 2025. Since this percentage was more than 50% in 2021, Kline does not estimate used oil collection to grow beyond 70% by 2025.
From the total used oil expected to collected in the Brazilian market, around 91% or 467.7 kilotonnes of this total is estimated to be supplied for re-refining.
It is estimated that around 8.6% of used oil not collected or 44 kilotonnes will be illegally disposed as fuel in 2025.
In 2025, Brazilian re-refiners are expected to process a total of around 464 kilotonnes of used oils yielding (in average) 294.7 kilotonnes of re-refined basestocks (including API Group I and Group II) and around 173 kilotonnes of byproducts and losses.
a- Mainly illegal disposal as fuel
a– Mainly asphaltic residue, fuels, water and other losses.
a- Mainly illegal disposal as fuel

## Slide 79: Used Oil Industry 2030
Chart: USED OIL COLLECTION, 2030
| Collected | Not collected-a
Sales | 0.7 | 0.3
Chart: USED OIL GENERATION, 2030
| Used oil generated | Lost
Sales | 0.57 | 0.43
Total: 1,424.2 Kilotonnes
Chart: USED OIL DISPOSAL, 2030
| Used oil re-refining | All other-a
Sales | 524.5102 | 36.7157
Chart: USED OIL RE-REFINING, 2030
| Re-refined basestocks | All other-a
B/E | 63 | 37
Total: 811.8 Kilotonnes
Total: 568.3 Kilotonnes
Total: 528.0 Kilotonnes
Brazilian finished lubricants demand is expected to be around 1,424.2 kilotonnes in 2030.
From total lubricant demand, about 414.4 kilotonnes of 29.1% of total is expected to be exempted from recycling, thus, total eligible lubricant demand for the used oil industry is estimated at 1,010 kilotonnes in 2030.
Kline estimates used oil collection to be around 70% as the minimal percentage of collection is estimated at 50% of total eligible lubricant demand in 2030. Since this percentage was more than 50% in 2021, Kline does not estimate used oil collection to grow beyond 70% by 2030.
It is estimated around 7% of used oil not collected or 37 kilotonnes will be illegally disposed as fuel in 2030.
In 2030, Brazilian re-refiners are expected to process a total of around 528 kilotonnes of used oils yielding (in average) 334 kilotonnes of re-refined basestocks (including API Group I and Group II) and around 194 kilotonnes of byproducts and losses.
a- Mainly illegal disposal as fuel
a– Mainly asphaltic residue, fuels, water and other losses.
a- Mainly illegal disposal as fuel

## Slide 80: Used Oil Re-Refined Basestocks Capacity Outlook
Total production capacity for re-refined basestocks in the Brazilian markets is estimated in around 300 kilotonnes per year including API Group I and API Group II basestocks.
Lwart is, by far, the largest re-refiner in Brazil, accounting for over 40% of total production capacity; it is the sole producer of API Group II basestocks not only in Brazil but in the whole Latin American region.
Lubrasil, Petrolub, and Proluminas are the largest re-refiners of API Group I basestocks in the country and together account for around 65% of total production capacity of these basestocks in the Brazilian market.
No significant changes in the overall Brazilian re-refining capacity impacting are expected in the foreseeable future.
MAJOR USED OIL RE-REFINERS IN BRAZIL, 2020-2030 |  |  |  | 
 | RE-REFINED BASESTOCKS CAPACITY (KILOTONNES) |  |  | 
COMPANY | 2020 | 2021 | 2025 | 2030
Lwart-a | 135.0 | 135.0 | 135.0 | 135.0
Lubrasil-b | 39.0 | 39.0 | 39.0 | 39.0
Petrolub-b | 39.0 | 39.0 | 39.0 | 39.0
Proluminas-b | 27.0 | 27.0 | 27.0 | 27.0
All other-b | 93.0 | 93.0 | 93.0 | 93.0
Total | 334.0 | 334.0 | 334.0 | 334.0
a- Group II re-refinery b- Group I re-refinery |  |  |  | 

## Slide 81: Market Evaluation
Opportunities
In long term, the Brazilian finished lubricants market is expected to grow above global average particularly when compared to developed regions such as North America and Europe.
This market growth is expected to create new opportunities in the used oil and the re-refining business in Brazil.
Those opportunities arise from the market scenario and are based on two main drivers:
  Brazilian market is a huge net importer of basestocks. It is expected that overall imports will increase in the long term.
  Group I basestocks demand will continue to remain significant mainly in the industrial segment despite a declining trend in its demand.
Basestocks imports account for almost 50% of the total basestocks demand in Brazil in 2020. Overall imports are expected to grow further as the demand for higher quality grades of basestocks is growing, mainly for Group II and Group III basestocks.
As Brazil is expected to remain a net importer of basestocks, this will provide business opportunities for used oil re-refiners to market re-refined basestocks in order to reduce Brazil’s dependence on imports.
In this sense, re-refining industry opportunities are two-fold; however, re-refiners need to be seen as a reliable supply alternative for finished lubricants blenders:
  Usage of used oil as fuel needs to be controlled to increase used oil’s availability for re-refining.
  Investments need to be made in used-oil processing technology to ensure a better quality of re-refined Group I basestocks.
Challenges
Used oil collection is a big challenge, fundamentally due to the lack of inspection to and fiscalization from Brazilian main regulators preventing used oil's usage as a fuel for burning in the country.
Overall data transparency is increasing in the country and mandated by the Government and main regulators. For example, ANP (the Brazilian National Agency of Petroleum, Natural Gas and Biofuels) is demanding more detailed information on collection, processing, production, and sales of used oil from collectors and re-refiners. However, industry players do not believe that inspection and imposition of penalties have grown.
Further, due to a difficult economic situation and poor infrastructure, it is not possible for authorities to check the used oil disposal in remote areas. As a result, there are still areas in Brazil where used oil is seldom collected.
Also, long-term fundamentals in the Brazilian market point out for a tight supply-demand balance for used oils market in the country which is expected to cap the maximum production of re-refined basestocks.
The growing imports of API Group I and Group II basestocks, mainly from the U.S., is also a big challenge for Brazilian re-refiners due to very favorable logistics, shorter transit time, huge overcapacity in the North American market, and competitive production costs for Group I and Group II basestocks compared to other regions.
Re-refiners should continue investing to upgrade their production technology to improve the quality of their Group I basestocks, which, in several cases, is still seen as an inferior product when compared to virgin Group I basestocks.
Re-refiners could look to produce Group II basestocks to better compete in a growing segment of the market. This would be the only way to meet the increasing performance requirements from OEMs (Original Equipment Manufacturers) and ANP’s continuous increase in the API service category levels.

## Slide 82
China

## Slide 83: China Market Synopsis
Chart: USED OIL MATERIAL BALANCE IN CHINA, 2021-2030 (MILLION TONS)
| Finished Lube Demand | Used Oil Generated | Used Oil Collected | Used Oil Re-refined | RRBO produced
2021 | 6967.4 | 3605.8 | 2993.8 | 1362.6 | 913
2025 | 6650.3 | 3657.7 | 3109 | 1710 | 1162.8
2030 | 6176.6 | 3520.7 | 3168.6 | 2344.8 | 1641.3
Used Oil Regulations
Used oil industry in China is regulated through administration policies and national standards. These include National Hazardous Waste Catalogue (2021 version), Technical Guides for Collection and Re-refining of Used Oil (GB/T17145-1997), among others.
Generators should entrust an entity with Hazardous Waste Operation Permit, issued by Ecology and Environment Bureau (EEB) at/above county level, to collect, dispose or recycle used oil.
Used oil collectors should have Waste Operation Permit for collecting used oil.
Re-refiners must be licensed with Hazardous Waste Comprehensive Operation Permit.
Used Oil Material Balance
Used oil generation increased by 7.3% in 2021, which is in line with 6.9% increase in lube demand in 2021.
83% of the total generated used oil is collected in 2021. remaining used oil is not collected because either the oil has a high concentration of impurities, or it is economically unfeasible to do so. The uncollected used oil is placed into landfilling or poured into water or sewer.
Collectors need to have Hazardous Waste Operating Permit in China. However, unlicensed collectors still play a role in China’s collection market. These collectors usually sell used oil to licensed collectors or re-refiners and processors.
46% of used oil collected is re-refined into basestocks, mainly Group I basestocks. Remaining used oil is used as fuel or incinerated.
Used Oil Re-refining
The yield of re-refineries in China is around 67%.
Re-refined basestocks are mainly produced by local private refineries with no API/OEM certifications. Thus, major blenders are not willing to inform their clients that they are using re-refined basestocks. Some basestocks re-refiners also produce and sell lubricants by themselves, or even sell basestocks as total-loss oils to low-end markets such as agriculture.
No significant changes in the re-refining capacity in China. A used oil project with an 80 KT production capacity of Group II basestocks is under construction; however, the commissioning date is not clear yet.
Opportunities
Collectors could collect high-quality used oil more easily from generators at a lower price if unlicensed collectors phase out in a well-regulated market.
Re-refiners would enjoy better chances to develop their basestocks businesses with the volume and quality of used oils trending higher. Some leading re-refiners are likely to forward-integrate to the lubricant blending business increasing their profitability.
Re-refiners can upgrade to produce Group II basestocks as re-refined Group II basestocks have a price edge over virgin Group II basestocks.
Challenges
Lubricant blenders hesitate to use re-refined basestocks as end users have concerns about the quality and performance.
MAJOR USED OIL RE-REFINERS IN CHINA, 2021-2030 | MAJOR USED OIL RE-REFINERS IN CHINA, 2020-2030 |  | 
 | RE-REFINED BASESTOCKS CAPACITY (KILOTONNES) |  | 
Company | 2021 | 2025 | 2030
Hebei Jingu Renewable Resources | 235.0 | 235.0 | 235.0
Dongying Guo’an Chemical | 135.0 | 135.0 | 135.0
Yantai Liheng Environmental Tech. | 70.0 | 70.0 | 70.0
Xinjiang Juli Environment Protection Tech.-a | 33.0 | 33.0 | 33.0
All other-b | 867.0 | 920.6 | 920.6
Total | 1,340.0 | 1,393.6 | 1,393.6
a- Group II re-refinery. b- Includes Shanxi Kejiada Energy, Zibo Zhongtai Environmental Technology, etc. |  |  | 

## Slide 84: Economic Background
In 2020, China’s gross domestic product (GDP) exceeded CNY 101.6 trillion (USD 14.72 trillion), up by 2.3% from 2019, which has been the slowest since 1990 due to the unprecedented disruption caused by the COVID-19 pandemic upon the overall economy. China’s GDP growth target is to be over 6% in 2021.
During Q1 2020, GDP registered a 6.8% contraction, while total imports and exports were down by 8.5% in USD terms as China completely stayed in lockdown. Total retail sales of consumer goods dropped substantially by 19% year-on-year, and total fixed-asset investment declined 16.1%. Since Q2, GDP rebound gradually, with a 3.2% like-for-like growth rate, because business activities recovered as the travel ban lifted and strong government incentives were released to boost the economical growth. In the second half of 2020, the GDP growth rate continued to rise, reaching 4.9% in Q3 and 7.0% in Q4, respectively. The economy in China was already back to normal performance by the end of 2020.
GDP growth was 18.3% in Q1 2021 and 7.9% in Q2 2021. However, in Q3 2021, GDP growth was only 4.9%. From Q1 to Q3, the GDP growth was 9.8%. IMF foresees that China’s overall GDP growth in 2021 will be 8.0%. In 2021, the impact of COVID-19 was quite limited thanks to the large portion of the population already vaccinated. However, the growing price of raw materials and power supply shortage in the second half of 2021 limited the GDP growth.
China and the United States have been engaged in a trade conflict through increasing tariffs and other measures since 2018. Affected by trade tensions, China’s GDP grew by 6.2% in Q2 2019, registering the slowest quarterly growth rate since 1992. By August 2021, China’s total imports from the United States had achieved only 62% of targets under the phase one trade agreement.
However, the Chinese government has been embracing globalization. In November 2018, customs tariffs were further cut for 1,585 items across industrial sectors, and a total of 94 commodities were subject to zero export tariffs as of January 1, 2019. By August 2021, China had signed 19 free trade agreements involving 26 countries and regions. Trade between China and these countries and regions thereby entered the age of zero tariffs. Moreover, China took the lead to develop The Regional Comprehensive Economic Partnership (RCEP), which is a free trade agreement with 15 Asia-Pacific countries.
SELECTED ECONOMIC CHARACTERISTICS OF COUNTRY, 2020 AND 2021 |  | 
KEY INDICATOR | 2020 | 2021-e
Population (Billion) | 1.41 | 1.41
GDP at current prices (USD Trillion) | 14.72 | 15.90
GDP per capita, current prices (USD) | 10,500.40 | NA
GDP growth rate, constant prices (Annual % change) | 1.9% | 8.0%
Inflation, average consumer prices (Annual % change) | 2.90% | 1.5% (October 2021)
Current account balance (% Of GDP) | 1.86% | NA
Share in Real GDP |  | Till Q3 2021
Services (%) | 54.5% | 54.8%
Industry (%) | 37.8% | 39.0%
Agriculture (%) | 7.7% | 6.2%
Source: National Statistics Bureau of China, IMF World Economic Outlook, The World Bank
Continued…

## Slide 85: Economic Background
According to the National Bureau of Statistics, the total value of China’s industrial sectors exceeded CNY 38.4 trillion (USD 5.6 trillion) in 2020, increasing 2.6% compared to 2019. However, the growth was lower than 2019, when the year-on-year growth was 5.7%. The 13th Five-Year Plan for National Economy and Social Development approved in March 2015 aims to bring in reforms on the supply side of industrial sectors to upgrade equipment and manufacturing technology while removing the surplus production capacity.
Privately owned companies and companies engaged in joint ventures with foreign companies are eligible to import crude oil directly, based on the application on the annual crude-oil import quota. According to the Ministry of Commerce (MOC), the approved crude oil import quota for privately owned companies totaled 184.55 million tonnes in 2020, 11.17% higher than 2019. The total import quota for 2021 approved by MOC reduced to 177.14 million tonnes, 4% lower than 2020.
China currently applies an import duty of 6% on the cost-insurance-freight value of imported basestocks and finished lubricants and 6.5% on the cost-insurance-freight value of imported lubricant additives. There is no import tariff on basestocks from South Korea as per the agreement reached in 2015. China also has FTA with ASEAN. Therefore, basestocks from Singapore, Thailand, Malaysia, and Indonesia do not need to pay custom duty. 6% custom duty is imposed on basestocks imported from for the most favored nations, i.e. Japan, the UAE, Qatar, and Taiwan. For other countries, the custom duty is 17% on imports of basestocks.
The consumption tax on finished lubricants has remained CNY 1.52 per liter in recent years. Meanwhile, value-added tax rates for basestocks, finished lubricants, and additives were cut twice, from 17% to 16% on May 1, 2018, and 16% to 13% on April 1, 2019. No further adjustment happened in 2020 and 2021.

## Slide 86: Vehicle Population
Though significantly impacted by COVID-19, the Chinese automotive industry (passenger and commercial) grew in 2020. Sales and production volume increased by 3.5% and 2.7%, respectively. In 2021, sales in the automotive industry grew by 7.7% and vehicle production by 8.4%.
In 2020, COVID-19 negatively impacted the sales and production of passenger vehicles and buses, with sales of passenger vehicles and buses declining 5.9% and 5.5%, respectively. The production of passenger vehicles and buses declined 6.4% and 4.0%, respectively.
In 2021, passenger car sales are expected to grow at 7% to reach 21.6 million units. The growth could be even higher if the supply shortage of chips can be solved in Q4 2021. From Q1 to Q3, sales of passenger cars increased 11% compared to 2020, but in Q3, sales of passenger cars decreased by 12% compared to Q3 2020.
In 2020, COVID-19 stimulated the sales of two-wheelers, which increased 10.3%. Growth was driven by people’s concern of coronavirus transmission in public transportation. The export of motorcycles also showed an upward tendency, as China controlled the pandemic much earlier than other countries. In 2021, motorcycle sales are expected to grow to 19.1 million units, with a growth rate of around 12%. From Q1 to Q3 2021, sales of motorcycles increased 17% compared to 2020. However, starting August, the growth pace slowed down. In September 2021, sales of motorcycles declined 8%. Since around 40% to 50% of sales are exported, the production recovery in export markets in Q3 2021 gradually reduced the dependence on motorcycles produced in China.
Chart: VEHICLE PRODUCTION BY VEHICLE TYPE IN CHINA, 2019-2021
| Passenger vehicles | Motorcycles | Trucks | Buses
2019 | 21.366 | 15.4302 | 3.888 | 0.472
2020 | 19.994 | 17.0235 | 4.778 | 0.453
2021 | 21.4 | 19.3 | 4.65 | 0.43
Chart: VEHICLE SALES BY VEHICLE TYPE IN CHINA, 2019-2021
| Passenger vehicles | Motorcycles | Trucks | Buses
2019 | 21.44 | 15.1938 | 3.85 | 0.474
2020 | 20.178 | 17.0667 | 4.685 | 0.448
2021 | 21.63 | 19.12 | 4.5 | 0.43
Million units
Million units
Continued…

## Slide 87: Vehicle Population
The sales and production of trucks increases 21.7% and 22.9%, respectively, in 2020. The sales of new trucks that comply with National IV emission standards grew 8.4% year-on-year (YOY) and reached 3.4 million units in 2020, despite a slight decline in 2019 and 2020. The positive change is driven by governments’ plan for phasing out National III standard trucks and enhanced regulations on overloading.
  Many heavy trucks compliant to the National III standard (referred to as type III trucks) were disposed of by the end of 2020 due to the government push. Major cities, including Shanghai and Beijing, banned National III trucks from operating. In some cities, even National IV trucks are banned in certain areas during select periods.
  Stricter regulations on overloading are pushing new truck sales. Starting 2020, overloaded trucks have been banned from entering expressways.
  National VI emissions standard, which was implemented after July 2020 for trucks in use in cities, led significant growth in new truck sales, especially heavy trucks in 2020.
  The change of highway toll fee is expected to drive the sales of medium and heavy trucks. Starting 2020, the highway toll is charged according to the number of axles of the vehicle instead of the overall weight of the vehicle and the load it carries. Light trucks no longer have the advantage of saving on tolls.
In 2021, sales of trucks are expected to decline around 4% compared to 2020. Sales of heavy and medium trucks are expected to decline around 7%. From Q1 to Q3 2021, sales of trucks already declined by around 1.6%. Truck dealers reduced the price of National V standard trucks significantly in the first half of 2021 before the implementation of National VI standards. The logistic demand is also weak due to high raw material prices, leading to lower demand for trucks.
In 2020, new energy vehicles (NEVs) kept growth momentum, despite the decline in conventional automobiles due to COVID-19. NEV sales increased 10.9% in 2020. Sales of NEVs led by battery electric vehicles (BEVs) have soared from 247,500 units in 2015 to 1.1 million units in 2020, registering a CAGR of 35.2%. Electric vehicles are expected to account for 7% and 18% of the total vehicle parc in China by 2023 and 2028, respectively. Government push is the key reason to drive the growth in sales of NEVs. Policies on government subsidies for the promotion and application of NEVs will be extended to the end of 2022, further declining successively 10%, 20%, and 30% in 2020, 2021, and 2022.
  Consumer vehicles take the lead in e-mobility penetration, accounting for 91% of the total NEV sales in 2020, up from 63% in 2015.
  In the commercial segment, e-mobility penetration is constrained by long-distance travel and heavy-load vehicle features. Therefore, electric commercial vehicles are developing faster in the light-duty logistics truck and bus segments. These vehicles typically travel shorter distances and are lightly loaded, so they are better-suited to electric power. However, the sales volume of electric trucks has been declining in recent years, due to the decrease in government subsidy for these vehicles. The newest policy in 2020 has reduced subsidies for major electric truck types by around 10%. In 2025, the penetration rate of electric trucks in the light trucks segment is estimated to reach 3%. New energy buses are undoubtedly a trend for the future, especially for city buses.
In 2021, sales growth of NEVs continue. From Q1 to Q3 2021, in the passenger car segment, NEV sales increased by 199% compared to 2020, with BEVs growing 215% and PHEVs growing 141%. From Q1 to Q3 2021, in commercial vehicles, NEVs also increased 55% compared to 2020.

## Slide 88: Finished Lubricant Market
Chart: OVERALL LUBRICANT DEMAND BY SEGMENT IN CHINA, 2020
| Industrial | Commercial | Consumer
Sales | 0.47 | 0.33 | 0.2
Total: 6,517.3 Kilotonnes
Finished lubricant demand in China was 6,517.3 KT in 2020, down significantly 12.9% from 2019, because of the outbreak of COVID-19 in 2020. In 2021, finished lubricant demand is estimated at 6,967.4 KT, an 6.9% increase compared to 2020.
Industrial lubricants remained the best performer among the three segments and was the largest segment for lubricant demand in 2020. In 2020, it accounted for 47% of the total lubricant demand, which is 8.4% lower than the 2019 demand. Its performance is closely related to industrial output and fixed investment. The average manufacturing purchasing manager’s index (PMI) was 49.9, compared to 45.9 in Q1 2020 and 49.7 in 2019. Driven by the government’s stimulus, the growth in infrastructure investment in 2020 was 0.9% compared to 2019. In 2021, industrial lubricants grew 5%.
Commercial automotive lubricants, the second leading segment, declined 17.9% in 2020, primarily due to the lockdown in Q1 2020. HDMO is the predominant product category, representing 71% of the total volume in 2020, mainly due to its large consumption in on-highway commercial vehicles. With continuous product upgrades, multigrade HDMO has been increasingly replacing monograde in recent years, reaching a leading 93% of the total HDMO supply in 2020. In 2021, commercial automotive lubricants grew 7.8%.
Demand for consumer automotive lubricants totaled 1,310.4 KT in 2020, down 13.9% from 2019 mainly because of the lockdown in Q1 2020 and the persistent concerns regarding traveling, which led to a decline of miles driven by passenger vehicles. In addition, most passenger vehicle owners using full synthetic PCMO tend to change oil based on time, at least once or twice a year, rather than on real mileage, which partially hedged this segment from a decline. Demand for MCO products, 2T/4T, continued its declining trend at around 18.3% in 2020. Rebounding sales of motorcycles, including growing electric motorcycle sales, did not balance the negative impact of the prolonged oil drain interval (ODI). In 2021, consumer automotive lubricants are estimated to grow 10.1% compared to 2020.
a: all other included automatic transmission fluid, grease, process oil, metalworking fluid, turbine and circulating oils, refrigeration oil, compressor fluid, slide way oil, chain oil, knitting machine oil, paper machine oil, spindle oil, bearing oil, and heat transfer fluid, among others
Chart: OVERALL LUBRICANT DEMAND BY PRODUCT TYPE IN CHINA, 2020 AND 2021
| HDMO | Process oils | PCMO | Hydraulic fluids | Industrial engine oils | All other-a
2020 | 1506.9 | 1448.6 | 1031.8 | 455.5 | 291.6 | 1782.9
2021 | 1627.3 | 1528 | 1127.1 | 471.7 | 293.9 | 1919.4
KT

## Slide 89: Lubricant Blenders
Lubricant blender market
The lubricant market landscape in China is fragmented, with around 900 blenders, including multinational blenders, state-owned local blenders, and private blenders.
Sinopec and PetroChina are the two largest blenders in the Chinese lubricant market, with market shares of 20% and 19% in 2020, respectively. They are state-owned and have several blending facilities across China. Both companies focus on the commercial and industrial segments of the lubricants market. They also have captive basestocks production, mainly producing Group I and Group II basestocks.
Shell, ExxonMobil, and BP are the three major multinational blenders, with market shares of 10%, 6%, and 5% in 2020, respectively. Total and Fuchs have a smaller presence in China, with market shares of 3% in 2020, each. Multinational blenders mainly focus on the consumer segment of the lubricants industry.
There are hundreds of local private blenders in China, but most of them have small production capacities. Leading private blenders include Tongyi, Yuangen, and Lopal. After being divested by Shell, Tongyi now is the largest local private blender, with around 4% market share in 2020. However, the other private blenders are very small, with each having less than 1% market share in 2020. In terms of products, local private blenders focus on commercial and industrial lubricants.
Usage of re-refined basestocks
Local private blenders such as Tongyi use re-refined Group I basestocks due to two possible reasons:
  These blenders generally use Group I basestocks as they focus on industrial lubricants. However, as many Group I refineries have closed or upgraded to produce Group II basestocks in recent years, there is a shortage in the supply of Group I basestocks. Re-refined basestocks can partially fill this demand-supply gap.
  These blenders are price-sensitive and favor low-priced re-refined Group I basestocks.
At present, most of the major blenders, including both multinationals and locals, do not claim in public to use re-refined basestocks, as many end users still hold a negative impression on the quality of lubricants produced using re-refined basestocks. Currently, major blenders use re-refined basestocks but in low quantities as they do not want their clients to know that.
Approval from OEMs are not required by lubricant blenders for re-refiners that produce re-refined basestocks, mainly because a majority of re-refined basestocks are still Group I.
Future Trends
In the past two years, some re-refiners such as Shandong Zibo Zhongtai Environmental Technology have started operating in a closed-loop business model. Reasons for this trend are that re-refiners intend to secure high-quality used oil from lubricant customers and can maximize their profit margins by expanding their business size.
Lubricant end users are expected to be more open to using lubricants made from re-refined basestocks as public awareness improves. As a result, lubricant blenders may tend to be more open to using re-refined basestocks in China. On June 17, 2019, Tongyi became the strategic shareholder of Dongying Guo’an (Guo’an), a used oil re-refiner. Tongyi is expected to use its network to collect used oil and supply it to Guo’an. In turn, Guo’an will provide re-refined basestocks to Tongyi to produce lubricants.
Note: Closed loop business refers to those re-refiners that collect used oil from their lubricant customers and produce re-refined basestocks, which are used to produce finished lubricants. The finished lubricants are then sold to the customers from whom the re-refiners have procured used oil.

## Slide 90: Summary of Used Oil Regulations
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | Yes
2. How is used oil classified i.e. hazardous waste, special waste etc.? | Hazardous waste
3. Are there any requirements on who can collect used oil? | Yes
4. Does the country have association(s) managing the collection and disposal of used oil? | Yes, China Recycling Oil Committee of China National Resources Recycling Association
5. Does a levy charged on sales of lubricants to support used oil collection associations? | No
6. Are there any requirements for how used oil generators manage used oil? | Yes
7. Are there requirements for oil manufacturers, marketers, or retailers to take back used oil? | No
8. Do any requirements/legislation exist around different types of used oil? | Yes, National standard for used engine oil, used gear oil, used hydraulic fluids etc. and required to be stored separately
9. Does the country have requirements or regulations regarding the export or import of used oil? | Yes, export of used oil is allowed but import is fully banned since 2020
10. Does the country have any legislation that requires used oil to be re-refined? | Encouraged but not mandatory, used oil can also be incinerated, placed in a landfill or processed as raw materials and fuel
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No, related regulations only exist for eligibility of tax benefits
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | No, used oil need to be processed/pre-treated before burning as fuel
Continued…

## Slide 91: Summary of Used Oil Regulations
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | No, they share the same set of air emissions requirements, but energy recovery equipment is encouraged by the government for burner to increase the total energy efficiency
14. Is used oil allowed to be placed in a landfill? |  | Yes, but pre-treatment is required to remove the ignitability and reactivity of used oil
15. Does the country have legislation that gives incentives, financial subsidies, or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | Yes, exemption of consumption tax and 50% VAT refund for qualified processors and re-refiners, and reduced income tax rate for collectors, processors, and re-refiners
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes (assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | No such regulations to prohibit
 | ii. Blending with crude oil at a refinery | 
 | iii. Dust suppressant | 
17. Are there companies/associations advocating in used oil category? |  | Yes

## Slide 92: List of National Regulations and Policy Overview
Key Used Oil Regulations
i. Administration Policies
National Hazardous Waste Catalogue (2021 version)
Solid Waste Pollution Prevention and Control Law of People’s Republic of China (2020 Amendment)
Announcement on Comprehensive Solid Waste Import Ban 2020
Management Measures on Hazardous Waste Export Approval 2008 (2019 Amendment)
Administrative Measures on Hazardous Waste Operating Permit 2004 (2016 Amendment)
Hazardous Waste Disposal Fee System 2003
Management Measures for Hazardous Waste Transfer Forms 1999
ii. National Standards
Technical Guides for Collection and Re-refining of Used Oil (GB/T17145-1997)
Technical Specifications for Pollution Control of Used Mineral Oil Recovery, Recycle and Reuse (HJ607-2011)
Standard for Pollution Control on Hazardous Wastes Storage (GB 18597-2001)
Standard of Pollution Control on the Hazardous Waste Landfill (GB 18598-2019)
Standard of Pollution Control on Hazardous Waste Incineration (GB 18484-2020)
iii. Tax Benefits
Announcement on Policy Issues Regarding Corporate Income Tax of Third-party Enterprises Conducting Pollution Prevention 2019
Catalogue of Value-Added Tax Benefits for Products and Services of Resources Comprehensive Utilization 2015
Notice of State Taxation Administration and Ministry of Finance on Exemption of Consumption Tax on Re-refining Products of Waste Mineral Oil 2013
i. Generation
Use oil generators should entrust an entity licensed with Hazardous Waste Operation Permit to collect and dispose of used oil. Generators are allowed to conduct re-refining or disposal themselves only if Comprehensive Operation Permit is granted.
ii. Classification (Hazardous waste)
Used oil is classified as hazardous waste
iii. Collection
Hazardous Waste Operation Permit is a must for used oil collection. Two types of Operation Permit are available: one is Collection Operation Permit, for use oil collection from automobile maintenance sector only, and the other one is Comprehensive Operation Permit, for collection, storage and disposal (re-refining) of used oil from all sources.
iv. Transportation and Storage
Hazardous Waste Transfer Form should be filled out and submitted to county/provincial-level Environment and Ecology Authority before transfer
Vehicles to be licensed with Road Transport Permit for Dangerous Goods and storage facility to be licensed with Hazardous Waste Operating Permit
v. Disposal – Re-refining
Re-refiners should obtain Hazardous Waste Comprehensive Operation Permit and meet requirements of re-refining capacity, facilities, and environmental protection
vi. Disposal – Fuel
Used oil is not legally allowed to be used as fuel for any industry; however, it is allowed to burn diesel and other types of oil processed from used oil
vii. Disposal – Other
Other major disposal ways are burning and landfill, which should be operated with Hazardous Waste Comprehensive Operating Permit

## Slide 93: Details of National Regulations
i. Generation
Generators should entrust an entity with Hazardous Waste Operation Permit, issued by Ecology and Environment Bureau (EEB) at/above county level, to collect, dispose of or recycle used oil. Generators are also allowed to conduct collection and disposal of used oil itself if it is having Hazardous Waste Operation Permit and equipped with related facilities.
Generators are required to categorize used oils into two levels, based on oil type, appearance, viscosity level, water content and flash level, degree of contamination, and store different levels of used oil in separate tanks.
Generators are required to set up a Used Oil Management Standing Book and submit Used Oil Management Plan and materials related to nature, quantity, flow, storage, and disposal of used oil to local EEB on a yearly basis. The provincial and city level EEB provides annual inspection on generators’ used oil management.
Generators are required to pay disposal fee to collectors based on guiding prices provided by local governments and negotiation between both parties.
ii. Classification (Hazardous waste)
According to the National Hazardous Waste Catalogue (2021 version), used mineral oil and waste containing mineral oil are classified as hazardous waste with toxicity and ignitability.
iii. Collection
Hazardous Waste Operation Permit is a must for collection activities of all kinds of hazardous waste, including used oil. Two types of permit, Collection Operation Permit and Comprehensive Operation Permit, are available for different businesses types.
  Collection Operation Permit allows companies to collect used mineral oil from automobile maintenance industry only. The permit is valid for three years.
  Comprehensive Operation Permit allows companies to collect and dispose of used oil from other industries in addition to automobile maintenance. The permit is valid for five years.
  Companies with Collection Operation Permit is allowed to receive disposal fee from used oil generators and transfer used oil to disposition companies with Comprehensive Operation Permit.
iv. Transportation and Storage
Used oil must be transported by special-designed vehicles with Road Transport Permit for Dangerous Goods issued by Municipal Road Transportation Administration.
Companies with facilities for storing over 5 tons of used oil every batch or storing used oil for over 90 working days should obtain Hazardous Waste Comprehensive Operation Permit issued by EEB at/above county level. The limit of storage period is one year.
Continued…

## Slide 94: Details of National Regulations
v. Disposal – Re-refining
Re-refiners must be licensed with Hazardous Waste Comprehensive Operation Permit and meet following requirements
A minimum annual feed capacity of 10 KT is required for single re-refining project established before 2016, and 30 KT for new or expanded projects established after 2016.
Maximum energy consumption of producing re-refined basestocks should not be more than 900 kWh/tonne.
Re-refiners should be equipped with re-refining, testing, and experiment facilities, and a tail gas treatment system in accordance with disposal capacity and environmental-protection requirements.
Sulfuric acid/Bentonite acid-leached method is banned for re-refining used oil.
Re-refiners can enjoy tax benefits if certain requirements are met
50% VAT refund and exemption of consumption tax for sales of re-refined end products (basestocks) if the products contain over 90% of used oil and the re-refining process meets a minimum yield of 65% (1.0 ton of used oil should produce 0.65 ton of re-refined basestocks)
Reduced corporate income tax to 15% (originally 20%)
Exemption of business tax for disposal fees paid by generators
vi. Disposal – Fuel
Used oil is not allowed to be directly used as fuel by any company without pre-treatment.
Oil products after processing of used oil, such as diesel, is allowed to be used as industrial fuel.
vii. Disposal – Others
Disposers that conduct burning and landfill of used oil are supposed to receive disposal fees from used oil generators.
Companies must obtain Hazardous Waste Comprehensive Operating Permit for burning or landfill of used oil.
Burning and landfill facilities must be equipped with pre-treatment and exhaust gas/liquid purification systems.
Co-processing of used oil in cement kiln has been officially allowed since 2014.

## Slide 95: Key Influencers and National Regulation Impacts
Key Influencers
i. Public Sector
Ministry of Ecology and Environment and local EEB
ii. Private Sector
China Recycling Oil Committee of China National Resources Recycling Association has four major responsibilities:
  Undertake researches on policies and regulations regarding used oil collection, processing, and recycling
  Organize evaluation and promotion of new technologies and products
  Provide services around training, information exchange, and consultation of integrated utilization of used oil
  Develop international communication and cooperation in the used oil industry
Eight leading re-refiners/disposal companies shortlisted as “demonstrative companies” by Ministry of Industry and Information Technology: Jilin Jialuxi Recycled Resources Utilization, Yantai Liheng Environmetal Technology, Hunan Hongwang Environmental Technology, Jiangsu Senmao Energy Development, Anhui Guofu Lubricant Industry, Dongying Guoan Chemical, Hubei Aiguo Chemical, and Xinjiang Juli Environmental Technology.
Regulation Impacts
i. Impact of Current Regulations
Low impact mainly due to outdated regulations, unclear responsibility bodies, and light punishment for misconduct
Many regulations and standards are not renewed in time to accommodate industry changes, and one-fit-for-all rules fail to consider different situations, leading to ineffective enforcement of regulations.
Responsibility body for every task is not clearly stated in some regulations, such as Measures for Management of Hazardous Waste Transfer Forms 1999, rendering it difficult to hold a specific party accountable for misconducts.
Existing penalties are either fines under CNY 100,000 or administrative warnings, far from enough to prevent illegal activities.
ii. Probable Future Regulations
Medium impact as pending regulations are more stringent and strictly enforced for operating permit, transfer, and disposal activities
Amended policies specify the accountability of key stakeholders.
More public sector agencies involved for establishing collaborative administration, such as Ministry of Transport and Ministry of Public Security.
Penalties are planned to increased from under CNY 100,000 to CNY 2 million at most.
More efficient administration and monitoring with digitalization tools such as National Solid Waste Management Information System.

## Slide 96: Probable Future Regulations
PROBABLE FUTURE REGULATIONS |  | CHANGES OF REGULATIONS
Collection | Administrative Measures on Hazardous Waste Environment Permit 2020 (draft) Amendment to Administrative Measures on Hazardous Waste Operating Permit 2004 (2016 Amendment) Currently undergoing public consultation Technical Guidance of Used Mineral Oil Recycling and Re-refining (20204991-T-469) Disposal Methods of Used Mineral Oil National standards under planning Currently at drafting stage | Hazardous Waste Environment Permit will replace Hazardous Waste Operation Permit as the new permit for all collection, storage, processing, and disposal (re-refining) businesses related to hazardous waste. New Collection Permit allows companies to conduct storage business in addition to the collection. Also, limitations over automobile maintenance shops have been lifted, allowing collection from all sources. New Comprehensive Permit allows companies to conduct processing business in addition to collection, storage, and disposal (re-refining). Regulation enforcement is enhanced through higher fines for any violation, increasing from CNY 10,000 to CNY 100,000 to CNY 0.1 to CNY 2 million, and higher administration level, switching from county-level to municipal-level department for permit issuance.
Disposal |  | 
Re-Refining |  | 
Transport | Management Measures for Hazardous Waste Transfer Environment 2020 (draft) Amendment to Management Measures for Hazardous Waste Transfer Forms 1999 Currently undergoing public consultation | Management Measures for Hazardous Waste specify the accountability of every stakeholder along the transfer process from sending to receiving. Cross-provincial transfer of hazardous waste is not encouraged except for national-planned, region-collaborative, and group-share hazardous waste disposal facilities. The transfer form and application process are digitalized through National Hazardous Waste Information Management System These measures simplify administration procedures by expanding the application of one transfer form from a single type of hazardous waste to different types within one form.
Key Influencers |  | Ministry of Transport and Ministry of Public Security will be jointly responsible for supervising the transfer of used oil

## Slide 97: Provincial Regulations of Cross-Province Used Oil Transfer
Transfer in of used oil from other provinces is banned in some provinces.
However, some provinces allow conditional transfer in.
Liaoning province: Disposal tasks are assigned by the national government.
Qinghai province: The disposal and comprehensive utilization of hazardous waste transferred from other provinces are not allowed when (a) hazardous waste is burned or placed in the landfill; (b) hazardous waste contains high-level heavy metals and cannot be reused; (c) the receiver used over 60% of storage capacity or used oil has been stored for over one year; (d) The receiver has accepted used oil from other provinces over 60% of its approved business scale, etc.
Transfer in and out of used oil is both banned in some provinces.
Shaanxi province: Storage and disposal of hazardous waste from other provinces is banned in the province. Transfer out of hazardous waste is not allowed except that disposal technologies and facilities within the province cannot perform disposal tasks. In this case, the generator shall only transfer hazardous waste after raising transfer application and being approved by EEB at county/municipal/province levels.
Transfer in and out of used oil is allowed in some provinces.
However, some provinces issue strict rules targeted at transfer in of used oil.
Jiangxi province: The entity that wants to transfer hazardous waste to Jiangxi shall submit an all-component analysis report provided by certified third-party testing institutions. The county-level Ecology and Environment Bureaus (EEB) at the receiving place shall conduct random sample testing. The receiver shall not dispose of hazardous waste before receiving sample testing results.
Anhui province: Transfer-in quota of hazardous waste shall be strictly carried out. Hazardous waste is not allowed to be burned, dried, reified, or placed in the landfill in the province.
Aligned with national regulations of hazardous waste, most provinces allow cross-province transfer of used oil with permission of all the concerning provincial departments of ecology and environment. However, some provincial governments have specifically forbidden hazardous waste to be transferred in/out of the province.
Transfer in and out of used oil is allowed in some provinces
Transfer in of used oil from other provinces is banned in some provinces
Transfer both in and out of used oil is banned in some provinces

## Slide 98: Provincial Regulations
Details of provincial regulations
i. Generators
Hazardous waste generators over certain production amount are required to be equipped with self-owned disposal and reusing facilities.
In Shandong province, enterprises that generate over 5,000 tons hazardous waste and chemical parks that generate over 10,000 tons hazardous waste shall be equipped with disposal and reusing facilities.
In Jiangsu province, enterprises that generate over 5,000 tons hazardous waste shall build self-owned disposal and reusing facilities.
ii. Collection
Regional collection centers are under development in some provinces for tackling collection barriers of small used oil generators.
Jilin province plans to develop charged collection and shipping services for small enterprises, research institutes, and schools that generate less than 3 tons hazardous waste and develop hazardous waste collection and storage pilot stations for industrial parks.
Hainan province plans to develop point-to-point collection and storage pilot projects for industrial parks.
Hunan, Henan, and Shanxi provinces are working on collection, storage, and shipping pilot projects for small enterprises.
iii. Disposal fee
According to national regulations, disposal fee can be negotiated between involving parties within the range of government guiding prices, which vary with different provinces based on local economical situations.
For example, Fujian province regulated that disposal charge standard of used mineral oil is CNY 2,000/tons, while Hubei province provided guiding prices between CNY 2,500 and 3,600 per ton for used oil disposal.
Few provinces specifically regulated disposal fee for used oil, which mostly are categorized into the disposal fee of hazardous waste categories. Guiding prices of two common disposal ways, burning and landfill, range from CNY 1,000 to 5,000 in different provinces.

## Slide 99: Summary of Regulation Enforcement
Regulatory Enforcement
i. Responsible Agencies
Ministry of Ecology and Environment is responsible for the supervision and administration of the used oil industry and the approval of Hazardous Waste Operation Permit.
EEBs at/above the county level are responsible for the issuance of Hazardous Waste Operation Permit, along with the regular supervision and inspection of business operations of local industry players.
Ministry of Finance and State Taxation Administration provides financial incentives and tax benefits for qualified operators.
Ministry of Industry and Information Technology provides guidance on key technologies and industry standards.
ii. Enforcement Mechanisms
Three major enforcement mechanisms in effect are as follows:
Hazardous Waste Operation Permit is required for all business operations related to used oil. EEBs at/above the county level carry out a random inspection on used oil collectors, re-refiners, and other disposers to ensure their feed capacity, facilities, and other qualifications align with the content shown on the permit.
Hazardous Waste Transfer Form is required to be filled out by used oil generators, transporters (collectors), and receivers (re-refiners and other disposers) to document the transfer process in detail and submitted to the local EEB before the transfer of used oil. The transfer form is kept by all parties and local EEBs for at least five years. Digital Transfer Form is allowed in provinces such as Beijing and Shanghai.
The National Solid Waste Management Information System was launched in 2020 to digitalize all administration processes related to used oil for better monitoring all procedures and higher data transparency and consistency across provinces.

## Slide 100: Material Balance
Total: 1,189.7 Kilotonnes
Chart: USED OIL GENERATION, 2020
| Used oil generated | Lubricant lost
Sales | 0.52 | 0.48
Total: 6,517.3 Kilotonnes
Chart: USED OIL COLLECTION, 2020
| Collected | Not collected
Sales | 0.82 | 0.18
Chart: USED OIL DISPOSAL, 2020
| Re-refined | Fuel | All other-a
Sales | 0.43 | 0.41 | 0.156
Chart: USED OIL RE-REFINING, 2020
| Basestock | All other
Sales | 0.67 | 0.33
Total: 3,361.2 Kilotonnes
Total: 2,740.6 Kilotonnes
Total estimated lubricant demand in China was 6,517.3 kilotonnes in 2020. Around 3,361.2 kilotonnes or 52% was generated as used oil. The remaining 48% was lost in consumption/handling or collected on-site and reused as lubricants. Losses can be due to technical losses such as evaporation, combustion, leakages, and handling losses. Some categories of lubricants such as white oils, selected metalworking fluids, and most grease are consumed totally during industrial processes.
Collected used oil accounted for 2,740.6 kilotonnes in 2020 or 82% of the total generated used oil. The rest was placed into landfilling or poured into water or sewer. About 18% of the generated used oil is not collected because either the oil has a high concentration of impurities, such as water, or the generators are located in remote areas and the generation amount is small. It is therefore not economically feasible to collect the used oil from them. Collectors are regulated to operate with the Hazardous Waste Operating Permit in China. However, unlicensed collectors still play a role in China’s collection market. These collectors usually sell used oil to licensed collectors that intend to save transportation and labor costs, as well as licensed or unlicensed re-refiners and processors.
41% of used oil collected is processed into fuel, and 43% is re-refined into basestocks. Most of the remaining 16% used oil is incinerated in furnaces. Furthermore, only licensed companies can incinerate the used oil after removing harmful impurities.
The current yield of re-refining is at 67% on average, meaning that 1,189.7 kilotonnes used oil could produce 797 kilotonnes of re-refined basestocks. Other products generated during the re-refining process include fuel, asphaltic oil, residuum, and wastewater.
a- Includes incineration, landfill, etc.

## Slide 101: Used Oil Industry 2021
Chart: USED OIL RE-REFINING, 2021
| Basestock | All other
Sales | 0.672 | 0.33
Chart: USED OIL GENERATION, 2021
| Used oil generated | Lubricant lost
Sales | 0.52 | 0.48
Total: 6,967.4 Kilotonnes
Chart: USED OIL COLLECTION, 2021
| Collected | Not collected
Sales | 0.83 | 0.17
Chart: USED OIL DISPOSAL, 2021
| Re-refined | Fuel | All other-a
Sales | 0.457 | 0.39 | 0.153
Total: 3,605.8 Kilotonnes
Total: 2,993.8 Kilotonnes
Total: 1,362.6 Kilotonnes
In 2021, total used oil generation showed a similar growing trend of finished lubricant demand in China, increasing 7.3% to 3,605.8 KT.
A slight rise of 1% is expected to see in the share of collected used oil as new regulations such as Administrative Measures on Hazardous Waste Environment Permit, Technical Guidance of Used Mineral Oil Recycling and Re-refining (20204991-T-469), and Disposal Methods of Used Mineral Oil roll out along with more stringent punishment measures.
Of all collected used oil, 39% is processed into fuel and 46% is re-refined into basestocks, mainly Group I. Other disposal ways, including incineration and landfilling, remain stable at around 15%.
The estimated yield rate of re-refining is 67% on average, i.e., 1,362.6 kilotonnes used oil produces 913 kilotonnes of re-refined basestocks.

## Slide 102: Used Oil Generation
USED OIL GENERATION BY PRODUCT IN CHINA, 2020 AND 2021 |  |  |  | 
LUBRICANT | KILOTONNES |  | % OF TOTAL USED OIL GENERATED | 
 | 2020 | 2021 | 2020 | 2021
HDMO | 1,009.6 | 1,090.3 | 30.0 | 30.2
PCMO | 794.5 | 867.9 | 23.6 | 24.1
Hydraulic Fluid | 318.9 | 330.2 | 9.5 | 9.2
Process Oil | 289.7 | 305.6 | 8.6 | 8.5
MWF | 176.0 | 184.1 | 5.2 | 5.1
Industrial Engine Oil | 131.2 | 132.3 | 3.1 | 3.1
MCO | 94.3 | 102.0 | 2.7 | 2.5
All other-a | 547.0 | 593.5 | 15.0 | 15.2
Total | 3,361.2 | 3,605.8-b | 100.0 | 100.0
a- Includes ATF, compressor oil, refrigeration oil, and turbine oil, among others b- Does not add due to rounding. |  |  |  | 
Chart: USED OIL GENERATION RATES BY PRODUCT IN CHINA, 2020 AND 2021-a
| HDMO | PCMO | Hydraulic Oil | MWF | Process Oil | Industrial Engine Oil | MCO | All other
% of generation | 0.67 | 0.77 | 0.7 | 0.5 | 0.2 | 0.45 | 0.6 | 0.43
Used oil generation remained nearly flat in 2019 and slipped in 2020 due to reduced lubricant demand through the pandemic year. In 2020, used oil generated declined 11.7% due to a 12.9% decline in lubricant demand in China.
In 2020, used oil generated from the automotive segment dropped to 2,345.1 kilotonnes, down significantly by 13.2% compared to 2019, mainly caused by reduced average miles driven by passenger and commercial vehicles during the lockdown. This in turn led to a decline in oil changing of automotive lubricants. Other reasons for the downward trend are stagnant new passenger vehicle sales, extended ODIs, increasing sales of EVs, and the penetration of synthetic lubricants in the automotive segment.
Among all categories, HDMO generated the most used oil, followed by PCMO. Automotive oils are mostly generated at OEM franchised workshops and independent workshops, while HDMO can also be generated at logistics companies.
Industrial used oil represents around 31% of total used oil generation, up over 5% compared to 2018, driven by the government’s investment in traditional and new infrastructure to increase demand for industrial lubricants. Hydraulic fluids generated the most industrial used oil at about 462.4 kilotonnes in 2020. Although the consumption of process oil is huge, the amount of used oil generated is rather small because rubber process oils and white oils do not generate used oil. Additionally, some factories use filtration systems to remove impurities and thus extend the life of industrial lubricants, which also adversely affects the volume of industrial used oil generated. Industrial oils are majorly generated at end users’ factories.
In 2021, used oil generation increased 7.3%. This is in line with an increase in lubricant demand, which has grown 6.9% in 2021.
a- Generation rates are same for 2020 and 2021. Therefore, only one bar chart is shown.

## Slide 103: Used Oil Collection
USED OIL COLLECTION BY PRODUCT IN CHINA, 2020 AND 2021 |  |  |  | 
LUBRICANT | KILOTONNES |  | % OF TOTAL USED OIL COLLECTED | 
 | 2020 | 2021 | 2020 | 2021
HDMO | 827.9 | 915.8 | 30.2 | 30.6
PCMO | 715.0 | 798.4 | 26.1 | 26.7
Hydraulic Oil | 248.7 | 264.2 | 9.1 | 8.8
Process Oil | 217.3 | 229.2 | 7.9 | 7.7
MWF | 132.0 | 138.0 | 4.8 | 4.6
Industrial Engine Oil | 101.0 | 101.8 | 3.7 | 3.4
MCO | 75.5 | 83.6 | 2.8 | 2.8
All other-a | 423.2 | 462.6 | 15.4 | 15.5
Total | 2,740.6 | 2,993.8 | 100.0 | 100.0
a- Includes ATF, compressor oil, refrigeration oil, and turbine oil, among others |  |  |  | 
Chart: USED OIL GENERATION RATES BY PRODUCT IN CHINA, 2020 AND 2021
| HDMO | PCMO | Hydraulic Fluid | MWF | Process Oil | Industrial Engine Oil | MCO | All other-a
2020 | 0.82 | 0.9 | 0.784 | 0.75 | 0.75 | 0.77 | 0.8 | 0.78
2021 | 0.84 | 0.92 | 0.8 | 0.75 | 0.75 | 0.77 | 0.82 | 0.78
In 2020, the total collection rate of used oil increased to 82%, up 7% compared to 2018, as governments tightened up regulations and enhanced enforcement mechanisms for hazardous waste collection. However, total collection volume slightly slipped by 3% as a result of the reduced lubricant demand due to COVID-19.
Automotive used oils remain at a higher-than-75% collection rate, mainly because used oil generated from the automotive segment contains less impurities and therefore has better quality than its industrial counterparts. PCMO has the highest collection rate among all used lubricants, followed by HDMO and MCO at 82% and 80%, respectively.
Industrial used oils have a relatively lower collection rate than that of automotive used oils due to the low quality of used oil. Hydraulic oil and gear oil are the two most collected industrial lubricants, which together account for 44% of total collected industrial used oils.
In 2021, used oil collection increased 9.2%, which is 2% higher than the 8.9% increase in used oil generation. The higher increase in used oil collection is due to the implementation of new regulations such as Administrative Measures on Hazardous Waste Environment Permit, Technical Guidance of Used Mineral Oil Recycling and Re-refining (20204991-T-469), and Disposal Methods of Used Mineral Oil, along with stricter punishment measures.
a- Includes ATF, compressor oil, refrigeration oil, and turbine oil, among others
Continued…

## Slide 104: Used Oil Collection
USED OIL COLLECTION BY SOURCE, 2020 |  | 
SOURCE | KILOTONNES | % OF USED OIL COLLECTED
Independent workshops | 1,068.8 | 39.0
OEM franchised workshops | 602.9 | 22.0
Factories | 767.4 | 28.0
Fleet | 301.5 | 11.0
Total | 2,740.6 | 100.0
The ratio of collected automotive used oils to industrial used oils is around 72:28. 2018 and 2020 witnessed an increasing collected volume of industrial used oils, mainly because of stricter administrations on hazardous waste produced by industry entities. In provinces with concentrated heavy-industry enterprises, such as Shandong province, the scaling-up of large industrial enterprises to replace small factories contributes to a growing collection rate of used industrial oils by curbing illegal disposal practices of small factories. Additionally, growing synthetics penetration reduced the generated amount of recyclable automotive oils, which in turn decreased the share of collected automotive oils.
OEM franchised workshops, where PCMO is mostly collected, represent an estimated 22% of total collected automotive used oils. HDMO can be collected at logistics companies with heavy-duty truck fleets. About 39% of automotive used oils is collected at independent workshops. Many independent workshops are small shops scattered around China.
Industrial used oils are primarily collected at steel groups, boat manufacturers, and other factories.
Continued…

## Slide 105: Used Oil Collection
Practice
Collector
There are three types of players engaged in used oil collection. The major one is independent collectors, which mainly collect small amounts of used oil generated from automotive workshops and small factories, particularly those located in remote areas. Another two types are processors and re-refiners, which purchase used oils from independent collectors or themselves collect industrial used oil from large factories and automotive used oil generated from workshops nearby. Currently, 60%–80% of used oil collection is done by independent collectors, while 20%–40% is directly collected by re-refiners or processors from generators.
As of 2020, there were about 800 to 1,000 used oil collectors (licensed collectors) that have Hazardous Waste Collection Operation Permit issued by governments in China. Shandong province has the highest number of licensed collectors, between 120 and 140, followed by Heilongjiang province, with around 60–70 licensed collectors. The rest of the collectors are mostly located in the northeast and middle regions of China.
Price
Collection practices consist of three steps:
Contract signing, auctioning, or spot trading: Contract is the most common way of used oil trading, normally renewed every year with the use oil supply amount set by both trading parties. Auction is usually adopted by large generators of industrial used oil, which happens once or twice a year. Spot trading is mainly for small amounts of used oil collection.
Sample testing: In most cases, independent collectors and re-refiners conduct sample testing to guarantee used oil quality and decide prices of every batch based on impurity content. Some re-refiners do not test used oil collected from large generators because of a guaranteed origin.
Delivery: Delivery fees are paid depending on a bilateral negotiation between the parties involved. Longer distances mean higher delivery fees. Used oil can be transported by independent collectors, processors/re-refiners, or third-party transportation fleets.
Although collectors are entitled to charge disposal fees from used oil generators, collectors actually pay used oil generators, ranging from CNY 2,000~4,000 or USD 308 to 616 per tonne (as of 2020), as China is under-supplied for high-quality used oil. Only when the batch of used oil contains excessive impurities or the generation amount is too small, generators are likely to pay a disposal fee of CNY 800~2,000 or USD 123 to 308 per tonne to collectors (as of 2020).
Collection price paid by collectors is determined primarily by impurity content and the volume of oil mixture.
If used oil does not meet the standards of the particular re-refiner, the collection price is deducted based on the excessive weight of impurities. Water content and impurities are the two most important parameters to decide the used oil price. However, the batch of used oil is turned down if the impurity content is above a certain level, which varies from one re-refiner to another.
Prices decline when collection volume is small, due to the high cost of transportation.

## Slide 106: Used Oil Disposal
Chart: USED OIL DISPOSAL IN CHINA, 2020
| Re-refined | Fuel | All other-a
Sales | 0.43 | 0.41 | 0.156
Total: 2,740.6 Kilotonnes
USED OIL DISPOSAL BY PRODUCT TYPE, 2020 |  |  |  | 
LUBRICANT TYPE | KILOTONNES |  |  | 
 | RE-REFINING | FUEL | ALL OTHER-a | TOTAL
HDMO | 455.3 | 339.4 | 33.2 | 827.9
PCMO | 393.3 | 264.6 | 57.1 | 715.0
Hydraulic Fluid | 101.4 | 110.0 | 37.3 | 248.7
Process Oil | 39.1 | 26.1 | 152.1 | 217.3
MWF | 21.1 | 11.9 | 99.0 | 132.0
Industrial Engine Oil | 35.4 | 58.7 | 6.9 | 101.0
MCO | 5.7 | 62.3 | 7.5 | 75.5
All other-b | 138.4 | 258.4 | 26.4 | 423.2
Total | 1,189.7 | 1,131.4 | 419.5 | 2,740.6
a - Includes incineration b – Includes ATF, compressor oil, refrigeration oil, and turbine oil, among others |  |  |  | 
Two predominant disposal ways for used oils are re-refining and processing into industrial fuel. Additionally, used oils can be incinerated or placed into landfilling after pre-treatment to remove ignitability and reactivity.
Compared to 2018, the overall disposal volume of used oil stayed flat in 2019 and dropped slightly due to a decline in used oil collection in 2020. Since 2018, the share of re-refining in the disposal of used oil has increased 7%. This is mainly due to a downfall in the processing of used oil into industrial fuel. The share of incineration and other disposal ways remained stable at around 16%.
Used oils generated from automotive and wind power industries are preferred for re-refining, thanks to less impurities and the guaranteed origin. Industrial used oils below the aforementioned collection baseline are preferred for use as fuels.
Continued…

## Slide 107: Used Oil Disposal
Chart: USED OIL DISPOSAL IN CHINA, 2021
| Re-refined | Fuel | All other-a
Sales | 0.46 | 0.39 | 0.15
Total: 2,993.8 Kilotonnes
USED OIL DISPOSAL BY PRODUCT TYPE, 2021 |  |  |  | 
LUBRICANT TYPE | KILOTONNES |  |  | 
 | RE-REFINING | FUEL | ALL OTHER-a | TOTAL
HDMO | 531.2 | 348.0 | 36.6 | 915.8
PCMO | 463.1 | 272.1 | 63.2 | 798.4
Hydraulic Fluid | 107.7 | 116.8 | 39.7 | 264.2
Process Oil | 41.3 | 27.5 | 160.4 | 229.2
MWF | 22.1 | 12.4 | 103.5 | 138.0
Industrial Engine Oil | 35.6 | 59.2 | 7.0 | 101.8
MCO | 6.8 | 68.5 | 8.3 | 83.6
All other-b | 154.8 | 264.7 | 43.1 | 462.6
Total | 1,362.6 | 1,169.2 | 319.4 | 2,993.8
a - Includes incineration b – Includes ATF, compressor oil, refrigeration oil, and turbine oil, among others |  |  |  | 
Re-refining of used oil increased in 2021, mainly driven by improved collection amid the growing demand for basestocks in China.
As a result, a decline in terms of share of fuel for the disposal of used oil is expected in 2021.

## Slide 108: Key Re-refining Technologies in China
DISTILLATION METHODS | DEFINITION
Atmospheric and Vacuum Distillation | A process in which the boiling point of the distillate is lowered by increasing the vacuum in the system and the material is vaporized and separated according to the boiling point difference under reduced pressure, so as to obtain different distillate products
Molecular Distillation | A process that uses the difference in the mean free path of the molecular motion of chemical substances to separate the light components mixed in the used mineral oil under different conditions, to make the lubricant molecules far below their boiling point and cracking temperature
Thin Film Distillation | A way of separating mixtures and substances by making use of low evaporation temperatures and low vacuum to tackle the chore. Its wipe film variant generates a thin film of liquid on the inner surface of the vertical evaporator using a wiper system
REFINING METHODS | DEFINITION
NMP Solvent | A process of refining the oil by selectively separating the non-ideal components based on different solubilities of the solvent to the components in the oil
Clay Refining | A refining process that uses clay as an adsorbent to improve the color and stability of oil products
Hydrogenation | The process of hydrogenation reaction of oil products under certain operating conditions through hydrogenation reactor filled with a catalyst; hydrogenation saturation of unsaturated hydrocarbons in oil products; ring-opening of fused aromatic hydrocarbons; and removal of sulfur, nitrogen, and other heteroatoms process
The mainstream re-refining process in China is mainly composed of distillation and refining. In the distillation process, used oil obtains the middle distillate of re-refined basestocks through three distillation methods. After distillation, the oil products are refined through NMP solvent or clay refining to produce re-refined Group I basestocks, and in some plants, through Hydrogenation to produce re-refined Group II basestocks.

## Slide 109: Used Oil Re-refining
MAJOR USED OIL RE-REFINERS IN CHINA, 2020 |  |  | 
 | KILOTONNES |  | 
COMPANY | USED OIL FEED CAPACITY | RE-REFINED BASESTOCKS CAPACITY | RE-REFINED BASESTOCKS PRODUCTION
Hebei Jingu Renewable Resources | 360 | 235 | 200
Dongying Guo’an Chemical | 200 | 135 | 80
Yantai Liheng Environmental Technology | 100 | 70 | 60
Zibo Zhongtai Environmental Technology | 100 | 70 | 60
Yantai Qisheng Petrochemical | 100 | 70 | 40
Shanxi Kejiada Energy | 100 | 65 | 48
Inner Mongolia Chengrun Energy Technology | 100 | 70 | 24
Xinjiang Juli Environment Protection Tech.-a | 50 | 33 | 7
All other-b | 890 | 592 | 278
Total | 2,000 | 1,340 | 797
a- Group II re-refinery. b- Includies Auhui Guofu Lubricant Industry, Chedi Chemical Industry, Jiean New Energy Tech, Changzhou Finas, Zhuhai Clean Oil Petrochemical, Dingshen Petrochemical, Shanxi Jiahe Environment Tech, Huayang Changqing, etc. |  |  | 
In 2020, 797 KT re-refined basestocks were produced in China, which is 18% higher than the total production amount in 2018, despite a decline in used oil collection volume due to pandemic. The growing trend indicates that re-refining has emerged as the main disposal method of used oil, mainly driven by the higher profitability of re-refined basestocks than industrial fuels.
In China, about 40–50 re-refiners were operating with an annual re-refining capacity at 1,340 kilotonnes as of 2020. Among them, two are large re-refiners with an annual feed capacity of over 200 kilotonnes. Around 10–15 are midsized re-refiners with a feed capacity between 50 and 100 kilotonnes. The rest 30~45 are small re-refiners with an annual feed capacity of smaller than 50 kilotonnes, mostly about 10 kilotonnes.
Regarding re-refining technologies, N-Methyl Pyrrolidinone (NMP) solvent after distillation is popular among all re-refiners, whereas distillation methods vary among different-sized re-refiners. Large and medium-sized re-refiners choose atmospheric vacuum distillation, some small ones use molecular distillation that operates at a lower distillation temperature. Kettle-type distillation has gradually been phased out of the market due to low-quality end products.
Continued…

## Slide 110: Used Oil Re-refining
Re-refiners primarily produce Group I basestocks. The key barrier to producing Group II basestocks is the high fixed investment and operation cost of hydrogenation facilities. However, some re-refiners, such as Changzhou Finas, Zibo Zhongtai, and Xinjiang Juli, have plans for upgrading to Group II basestocks production considering higher selling prices of Group II basestocks, around CNY 1,000 (USD 154) per tonne more than re-refined Group I basestocks, as well as less hazardous waste emitted during production process. For instance, Xinjiang Juli Environmental Protection Technology currently has an annual production capacity of 33 kilotonnes Group II re-refined basestocks at a yield rate of 65%.
Re-refined Group I basestocks are mainly sold to local small and medium-sized lubricant blenders via contracts. The price of re-refined basestocks fluctuates with the price of crude oil but is about CNY 200-500 (USD 31 to 77) per tonne cheaper than virgin basestocks.
A majority of re-refiners operate open-loop re-refining businesses by selling re-refined basestocks only. Recently, the closed-loop business model has become an emerging trend. In this business model, re-refiners collect used oil from lubricant customers and produce re-refined basestocks, which are used to produce finished lubricants and then sold to the customers from whom they purchase used oil. To maximize profit margins, some leading re-refiners have moved or attempted to move downstream into selling finished lubricants to the same customer from where they purchase used oil, which completes a closed-loop re-refining business. Currently, in Shandong province, Zibo Zhongtai and Yantai Liheng both operate closed-loop re-refining businesses, representing nearly 20% of overall businesses each.
A CLOSED LOOP USED OIL RE-REFINING BUSINESS MODEL, 2020

## Slide 111: Hebei Jingu Recycling Resources Development
Company Overview
Ownership: Private. 90% owned by Huichuan Zhao, 10% owned by Long Zhao.
CEO: Huichuan Zhao
Location: Xinji, Hebei
Employee number: ~600
Business model: open loop, covering used oil re-refining and lubricant blending
Key technologies: Atmospheric and vacuum distillation; molecular distillation; NMP solvent after distillation
Main products: Group I basestocks; lubricant, fatty acid methyl ester (biodiesel); asphalt plant (by-product)
Activities: Hebei Jingu, founded in 1987, owns two subsidiaries, Hebei Jingu New Energy and Hebei Jingu Plasticizer. The company registers a total annual production capacity of 150,000 tonnes re-refined basestocks and 250,000 tonnes biodiesel under the current Hazardous Waste Operation License. In 2011, Jingu started the lubricant blending business with an annual capacity of 50,000 tonnes, mainly producing gear oil, hydraulic oil, HDMO, and PCMO, etc. By-products of re-refining processes in the asphalt plant are mainly sold to fuel oil manufacturers.
KEY RE-REFINERY ASSETS, 2020 |  | Key Re-refinery Assets |  |  | 
 | KILOTONNES | Kilotonnes |  |  | 
MAIN PRODUCTS | UO FEED CAPACITY | UO COLLECTION | RRBO CAPACITY | RRBO PRODUCTION | YIELD
Gp.I basestocks | 360 | 308 | 235 | 200 | 65%
USED OIL VALUE CHAIN POSITIONING
Collection
Disposition
(Incineration/landfilling etc.)
Blending
Re-refining
(Base Oils)
Processing
(VGO/MDO etc.)
Continued…
Notes: This slide provide a profile used oil re-refiners in a country. Information will be provided on:
Background
Short description of used oil re-refining process
Information on re-refined basestocks sold by the company.
  What type of re-refined basestocks is sold by the company? Group I vs. Group II vs. Group III?
  How does the company operate? Closed loop vs. open loop re-refining?
Plans to upgrade to produce higher quality of basestocks？

## Slide 112: Hebei Jingu Recycling Resources Development
Hebei Jingu
  The company has a large feed capacity at 360 KT/year, collecting used oil mainly from North China provinces.
  It obtained technology certificates published by the Hebei government.
  It is forward-integrated for lubricant production, including gasoline engine oil, diesel engine oil, gear oil, hydraulic oil, etc. It also operates a toll-blending business.
Strength
Weakness
Opportunity
Threat
  The Hebei government encourages the local recycling industry via tax exemption.
  Downstream lubricant integration could increase the margin if volume grows evidently, as well as operation certificates for a larger business size are obtained.
  Currently, the yield rate is comparatively low at 65% mainly due to the low-quality used oil sourced from collectors to ensure capacity utilization.
  The company pays a high feed cost as it is mainly reliant on collectors.
  Currently, nearly 60% margin comes from tax reduction, which has a high level of uncertainty.

## Slide 113: Dongying Guo’an Chemical
Company Overview
Ownership: Private. 98.9% owned by Hui Chen, 1% owned by Chongyang Zhang
CEO: Chongyang Zhang
Location: Dongying, Shandong
Employee number: 150
Business model: open loop, covering used oil collection, processing, re-refining; production, transportation, trade of petroleum
Key technologies: atmospheric and vacuum distillation; molecular distillation; NMP solvent after distillation
Main products: Group I basestock (150SN/250SN/350SN); Asphalt; Diesel; Naphtha
Activities: Established in April 2007, Dongying Guo’an Chemical is a high-tech new-energy industrial enterprise with a total investment amount of CNY 2 billion. Between 2011 and 2015, the company invested nearly CNY 1 billion in a used oil re-refining project with the molecular distillation method, whose annual capacity is 200,000 tonnes. This project has increased the yield rate of base oil to 88%. After years of upgrading, the total utilization rate of used oil has reached 98%. However, Guo’an has gradually switched the core business from basestocks to re-refined fuels in recent years, due to misconducts in environment-protection terms. In August 2021, Guo’an invested CNY 10 million in the environmental renovation of the 200,000 tonnes/year re-refining project.
KEY RE-REFINERY ASSETS, 2020 |  | Key Re-refinery Assets |  |  | 
 | KILOTONNES | Kilotonnes |  |  | 
MAIN PRODUCTS | UO FEED CAPACITY | UO COLLECTION | RRBO CAPACITY | RRBO PRODUCTION | YIELD
Gp.I basestocks (150SN/250SN/350SN) | 200 | 91 | 135 | 80 | 60%
USED OIL VALUE CHAIN POSITIONING
Collection
Disposition
(Incineration/landfilling etc.)
Blending
Re-refining
(Base Oils)
Processing
(VGO/MDO etc.)
Continued…
Notes: This slide provide a profile used oil re-refiners in a country. Information will be provided on:
Background
Short description of used oil re-refining process
Information on re-refined basestocks sold by the company.
  What type of re-refined basestocks is sold by the company? Group I vs. Group II vs. Group III?
  How does the company operate? Closed loop vs. open loop re-refining?
Plans to upgrade to produce higher quality of basestocks？

## Slide 114: Dongying Guo’an Chemical
Guo’an Chemical
Strength
Weakness
Opportunities
Threats
  The company is the largest re-refiner in Shandong province with annual feed capacity of 200 KT.
  It is renowned in the re-refining basestock market, with a long history and a good reputation.
  The company has a low utilization rate of a large feed capacity due to the undersupplied local market of used oil and strong competition in other cities of Shandong.
  The difficulty of collecting high-quality used oils leads to a decline of producing high-quality RRBO.
  Enhanced environmental enforcement in Shandong province raises fixed costs of waste treatment facilities.
  One of its largest RRBO customer, Tongyi, terminated its partnership with Guo’an and selected Hebei Jingu as its primary supplier of RRBO in 2020.
  The Shandong government supports large re-refiners in terms of land usage, provides a simplified administration procedure for cross-city transportation of used oil, etc.

## Slide 115: Zibo Zhongtai Environmental Technology
Company Overview
Ownership: Private. 90.5% owned by Feng Gao, 9.5% owned by Zhen Wang
CEO: Feng Gao
Location: Zibo, Shandong
Employee number: <50
Business model: closed loop, covering used oil collection and re-refining; re-refined lubricant blending
Key technologies: atmospheric and vacuum distillation; NMP solvent after distillation
Main products: Group I basestocks (100/150/250/350); Group II basestocks; Lubricants (HDMO, gear oil, and hydraulic oil)
Activities: Zibo Zhongtai, founded in April 2000, collected around 86 KT used oil and produced 60 KT re-refined basestocks in 2020 with a high utilization rate of 86%. About 90% of the total basestocks production is Group I base oils, and the rest 10% falls into the Group II category. The company also operates a lubricant blending business with an annual capacity of 150 KT. The main re-refined lubricants are HDMO, gear oil, and hydraulic oil. However, the company primarily works as a toll blender for other lubricant blenders and does not own a lubricant brand.
KEY RE-REFINERY ASSETS, 2020 |  | Key Re-refinery Assets |  |  | 
 | KILOTONNES | Kilotonnes |  |  | 
MAIN PRODUCTS | UO FEED CAPACITY | UO COLLECTION | RRBO CAPACITY | RRBO PRODUCTION | YIELD RATE
Gp.I basestocks (100/150/250/350) | 100 | 86 | 70 | 60 | 70%
USED OIL VALUE CHAIN POSITIONING
Collection
Disposition
(Incineration/landfilling etc.)
Blending
Re-refining
(Base Oils)
Processing
(VGO/MDO etc.)
Notes: This slide provide a profile used oil re-refiners in a country. Information will be provided on:
Background
Short description of used oil re-refining process
Information on re-refined basestocks sold by the company.
  What type of re-refined basestocks is sold by the company? Group I vs. Group II vs. Group III?
  How does the company operate? Closed loop vs. open loop re-refining?
Plans to upgrade to produce higher quality of basestocks？

## Slide 116: Guofu Technology
Company Overview
Ownership: Private. 46.17% owned by Shulong Li, 13.9% owned by Anqing Guorui Enterprise Management Consulting, the rest share owned by financial institutes and individuals.
CEO: Shulong Li
Location: Anqing, Anhui
Employee number: ~80
Business model: open loop, used oil re-refining only
Key technologies: atmospheric and vacuum distillation; NMP solvent after distillation
Main products: Group I basestocks; Substandard diesel (by-product of base oil production process)
Activities: Established in 2008, Guofu Technology is a high-tech enterprise specialized in the production and sales of re-refined base oils, with a total company capital of CNY 90.45 million. Guofu owned four fully owned subsidiaries, two of which operate re-refined-based oil businesses. Currently, Guofu has one used oil utilization project in operation, with an annual feed capacity of 50,000 tonnes. Another used oil project with an 80,000 tonnes/year production capacity of Group II basestocks is under construction; however, the commissioning date is not clear yet.
KEY RE-REFINERY ASSETS, 2020 |  | Key Re-refinery Assets |  |  | 
 | KILOTONNES | Kilotonnes |  |  | 
MAIN PRODUCTS | UO FEED CAPACITY | UO COLLECTION | RRBO CAPACITY | RRBO PRODUCTION | YIELD
Gp.I basestocks | 50 | 28 | 35 | 23 | 70%
USED OIL VALUE CHAIN POSITIONING
Collection
Disposition
(Incineration/landfilling etc.)
Blending
Re-refining
(Base Oils)
Processing
(VGO/MDO etc.)
Notes: This slide provide a profile used oil re-refiners in a country. Information will be provided on:
Background
Short description of used oil re-refining process
Information on re-refined basestocks sold by the company.
  What type of re-refined basestocks is sold by the company? Group I vs. Group II vs. Group III?
  How does the company operate? Closed loop vs. open loop re-refining?
Plans to upgrade to produce higher quality of basestocks？

## Slide 117: Xinjiang Juli Environment Protection Technology
Company Overview
Ownership: Private. 80% owned by Demin Cai, 10% owned by Desheng Cai, 7% owned by Xiaoxia Li, 3% owned by Jianqiang Luan.
CEO: Demin Cai
Location: Urumqi, Xinjiang
Employee number: 67
Business model: open loop, covering used oil collection and re-refining.
Key technologies: atmospheric and vacuum distillation; hydrogenation process
Main products: Group II basestocks, diesel (byproduct of base oil production process)
Activities: Juli Environmental Protection Technology has invested CNY 136 million in two sets of production facilities for re-refined Group II basestocks — an atmospheric and vacuum distillation facility and a hydrogenation facility — with a designed capacity of 50,000 tonnes per year. According to the CEO, the company completed the upgradation of the production facility in May 2021. The anticipated annual production of Group II basestocks is around 10,000 tonnes by the end of 2021. To secure used oil supply and lubricant clients, Juli plans to operate a closed-loop business by collecting used oil from lubricant clients in the future.
KEY RE-REFINERY ASSETS, 2020 |  | Key Re-refinery Assets |  |  | 
 | KILOTONNES | Kilotonnes |  |  | 
MAIN PRODUCTS | UO FEED CAPACITY | UO COLLECTION | RRBO CAPACITY | RRBO PRODUCTION | YIELD RATE
Gp.II basestocks | 50 | 11 | 33 | 7 | 66%
USED OIL VALUE CHAIN POSITIONING
Collection
Disposition
(Incineration/landfilling etc.)
Blending
Re-refining
(Base Oils)
Processing
(VGO/MDO etc.)
Notes: This slide provide a profile used oil re-refiners in a country. Information will be provided on:
Background
Short description of used oil re-refining process
Information on re-refined basestocks sold by the company.
  What type of re-refined basestocks is sold by the company? Group I vs. Group II vs. Group III?
  How does the company operate? Closed loop vs. open loop re-refining?
Plans to upgrade to produce higher quality of basestocks？

## Slide 118: Attitudes Toward Re-refined Lubricants
RRBO BUYER TYPES | KEY PLAYERS | RATIONALE FOR BUYING RE-REFINED BASE OILS
Supermajors | Shell, Sinopec, PetroChina | Low cost
Multinational Blenders | Total, Quaker | Low cost
Base Oil Re-refiners | Hebei Jingu, Yantai Liheng, Zibo Zhongtai | Forward integration
Large Private Local Blender | Tongyi | To produce the sub-brand of Chuncui, which claims to use RRBO in formulation To build circular economy To reduce production cost
Midsized and small local blenders | Lopal, Yuangen, Amer | Low cost
KEY BUYERS OF CHINA RE-REFINED BASESTOCKS
Although China has a large capacity of re-refined basestocks, these are mainly produced by local private refineries with no API/OEM certifications. Thus, major blenders are not willing to inform their clients that they are using re-refined basestocks. Some basestocks re-refiners also produce and sell lubricants by themselves, or even sell basestocks as total-loss oils to low-end markets such as agriculture.
Re-refining technologies are improving, and standards for re-refined basestocks have been set up. Consequently, more and more lubricant blenders are purchasing re-refined basestocks from credible re-refiners. For instance, Tongyi currently procures re-refined basestocks from Hebei Jingu.
The key driver of re-refined basestocks purchase is lower prices, as using re-refined basestocks is 15% to 20% less expensive than virgin basestocks. Leading re-refined basestocks buyers are therefore small and medium-sized private local blenders, because they are the most cost-sensitive players in the lubricant market.
State-owned companies such as Sinopec and PetroChina have shown interest in investing in the re-refined basestocks business in the future, but nothing has been finalized yet:
  Sinopec plans to invest 40 billion RMB in “Green Enterprise Action” in the next three years. This action may include investing in the basestock re-refining business through acquisition or building up a new plant in one of its subsidiaries.
  PetroChina aims to collaborate with private companies to invest in one re-refining basestock plant in the next three to five years.

## Slide 119: Finished Lubricant Market Outlook
Chart: PROJECTED FINISHED LUBRICANT MARKET IN CHINA, 2020-2030
| Industrial | Commercial | Consumer
2020 | 3090 | 2116.9 | 1310.4
2021 | 3243.6 | 2281.6 | 1442.2
2025 | 3353.6 | 1944.6 | 1352.1
2030 | 3386.9 | 1664.1 | 1125.6
Overall market demand for finished lubricant is expected to see significant growth of 6.9% to an estimated 6,967.4 KT in 2021 because of the sharp decline in lubricant demand in 2020. The next decade is anticipated to witness low growth of 0.4% per year between 2020 and 2025, and then a decline to 6,176.6 KT in 2030, representing an average annual decline of 1.5% from 2025 to 2030.
Industrial lubricants are anticipated to be the largest and best-performing segment throughout the forecast period. Besides recovering from the pandemic, the rising trend between 2020 and 2025 will mainly be driven by the first 10-year strategy plan, Made in China 2025, issued by the Chinese government for smart manufacturing development targeting high-value industrial sectors. The growing penetration of equipment digitalization will also drive demand for premium lubricants given real-time monitoring and total fluid analysis that can better illustrate the benefits of these lubricants.
  This is expected to lead to a decline in lubricant demand in the industrial segment due to an increase in ODIs.
Demand for commercial lubricants is anticipated to remain flat in the first five years and decline 3.1% per year from 2025 to 2030. The reduced demand will be led by the adoption of long ODI vehicles and extended oil change intervals. In the off-highway sector, the upsizing trend of agriculture machinery encouraged by government subsidies and new emission standards, National Standard VI, also leads to less lubricant consumption in terms of volume and a shift in lubricant product portfolios.
The consumer segment is projected to experience stable annual growth of 1.1% from 2020 to 2025 but is expected to decline at an annual average rate of 3.6% from 2025 to 2030. After bouncing back from 2020, the overall demand is adversely impacted by multiple trends: the slowdown of new passenger vehicle sales as a result of diversified transportation choices, prolonged ODIs, the increasing penetration of synthetics (full and semi) in PCMO from currently 71% to 97%, and the slump of PCMO demand driven by the growing e-mobility penetration.

## Slide 120: Used Oil Industry Outlook
Chart: USED OIL GENERATION, 2025
| Used oil generated | Lubricant lost
Sales | 0.55 | 0.45
Total: 6,650.3 Kilotonnes
Chart: USED OIL COLLECTION, 2025
| Collected | Not collected
Sales | 0.85 | 0.15
Chart: USED OIL DISPOSAL, 2025
| Fuel | Re-refined | All other
Sales | 0.305 | 0.545 | 0.149
Chart: USED OIL RE-REFINING, 2025
| Basestock | All other
Sales | 0.68 | 0.32
Total: 3,657.7 Kilotonnes
Total: 3,109 Kilotonnes
Total: 1,710 Kilotonnes
In 2025, total used oil generation is expected to maintain stable annual growth of 1.7% to 3,657.7 KT as lubricant demand rises.
An estimated collection rate of 85% is expected in total used oil generation, representing 3,109 KT, due to stricter enforcement of regulations on used oil disposal.
Around 55% of all collected used oils is anticipated to be re-refined into basestocks, while another 31% is to be processed into industrial fuels. The continuously growing re-refining rate is driven by the improved quality of used oil and relatively higher profit margins of re-refined basestocks than those of industrial fuels. There will be no changes in the share of incineration, landfilling, and other disposal ways.
The average yield rate of re-refining is expected to reach 68% as re-refining technology improves.
Continued…

## Slide 121: Used Oil Industry Outlook
Chart: USED OIL GENERATION, 2030
| Used oil generated | Lubricant lost
Sales | 0.57 | 0.43
Chart: USED OIL COLLECTION, 2030
| Collected | Not collected
Sales | 0.9 | 0.1
Chart: USED OIL DISPOSAL, 2030
| Fuel | Re-refined | All other
Sales | 0.127 | 0.739 | 0.134
Chart: USED OIL RE-REFINING, 2030
| Basestock | All other
Sales | 0.7 | 0.3
Total: 6,176.6 Kilotonnes
Total: 3,520.7 Kilotonnes
Total: 3,168.6 Kilotonnes
Total: 2,344.8 Kilotonnes
In 2030, the supply of used oil is estimated to decrease at an annual rate of 1.3% to 3,520.7 KT as the total consumption of lubricants declines. However, the generation rate of used oil has risen from 53% to 57%, mainly led by a declining lubricant loss in the consumption/handling process, better-designed vehicles and machinery, and the adoption of better-quality lubricants.
Of all generated used oil, an estimated 90% will be collected, equivalent to 3,168.6 KT, if a well-regulated used oil market is in place by 2030. This is expected based on the implementation of regulations.
The re-refining rate of used oil is expected to show a continuous upward trend, growing from 55% in 2025 to 74% in 2030. The growth is driven by the improved quality of used oil as a result of the growing usage of better-quality lubricants. Accordingly, the share of processing into industrial fuels is expected to decline to 13% during the same period, while the share of other disposal ways will slightly decline to 13%. This is because the proportion of used oil that cannot be re-refined or processed into fuel is expected to remain stable between 2020 and 2030.
The volume of re-refined basestocks is expected to be nearly doubled during 2020–2030, reaching 2,344.8 KT, thanks to the technological improvement of midsized and small re-refiners. Additionally, governments incentives to encourage a circular economy also exert a positive impact on the used oil industry in China.

## Slide 122: Re-refined Basestock Capacity Outlook
Currently, Guofu has one used oil utilization project in operation with an annual feed capacity of 50,000 tonnes.
Another used oil project with an 80,000 tonnes/year production capacity of Group II basestocks is under construction; however, the commissioning date is not clear yet.
MAJOR USED OIL RE-REFINERS IN CHINA, 2020-2030 |  |  |  | 
 | RE-REFINED BASESTOCKS CAPACITY (KILOTONNES) |  |  | 
Company | 2020 | 2021 | 2025 | 2030
Hebei Jingu Renewable Resources | 235.0 | 235.0 | 235.0 | 235.0
Dongying Guo’an Chemical | 135.0 | 135.0 | 135.0 | 135.0
Yantai Liheng Environmental Technology | 70.0 | 70.0 | 70.0 | 70.0
Zibo Zhongtai Environmental Technology | 70.0 | 70.0 | 70.0 | 70.0
Yantai Qisheng Petrochemical | 70.0 | 70.0 | 70.0 | 70.0
Shanxi Kejiada Energy | 65.0 | 65.0 | 65.0 | 65.0
Inner Mongolia Chengrun Energy Technology | 70.0 | 70.0 | 70.0 | 70.0
Xinjiang Juli Environment Protection Tech.-a | 33.0 | 33.0 | 33.0 | 33.0
All other-b | 592.0 | 592.0 | 645.6 | 645.6
Total | 1,340.0 | 1,340.0 | 1,393.6 | 1,393.6
a- Group II re-refinery. b- Includies Auhui Guofu Lubricant Industry, Chedi Chemical Industry, Jiean New Energy Tech, Changzhou Finas, Zhuhai Clean Oil Petrochemical, Dingshen Petrochemical, Shanxi Jiahe Environment Tech, Huayang Changqing, etc. |  |  |  | 

## Slide 123: Market Evaluation
Opportunities
The use oil industry is expected to demonstrate growth opportunities for different stakeholders as stricter regulations roll out and a higher level of enforcement gets in place.
Generators would be regulated to reduce selling prices of used oils or pay disposal fees to collectors and re-refiners for used oil generated. Better-quality used oil can be collected if generators are enforced to store different types of used oil separately.
Collectors could collect high-quality used oil more easily from generators at a lower price if unlicensed collectors phase out in a well-regulated market.
Re-refiners would enjoy better chances to develop their basestocks businesses with the volume and quality of used oils trending higher. Some leading re-refiners are likely to forward-integrate to the lubricant blending business. This closed-loop business model expands profit margins of re-refiners by increasing the utilization rate of the basestocks production capacity and securing a part of raw material supply, because re-refiners can directly collect used oils from their lubricant end users. In addition, some re-refiners would choose to upgrade their re-refining technologies to produce Group II basestocks with enough capital in place and higher end-user acceptance of re-refined basestocks, given that re-refined Group II basestocks have a price edge over virgin Group II basestocks.
Large lubricant blenders could reduce the production cost of lubricants if they adopted re-refined basestocks in their formulations when the quality of re-refined basestocks can be paralleled to virgin basestocks. Some established lubricant blenders are possible to engage in the re-refining business via acquisitions or backward integration to build a closed lubricant recycling business loop, when lubricant end users adopt a relatively positive attitude toward re-refined lubricants. For instance, Tongyi plans to invest in a re-refinery in Xi’an, Shanxi, to supply re-refine basestocks for its own lubricant production by collecting used oil from its end customers or distributors.
Continued…

## Slide 124: Market Evaluation
Challenges
Several persisting challenges still hinder the development of the used oil industry, including the low end-user acceptance of re-refined lubricants, difficulties in collecting high-quality used oil, lagging re-refining technologies, and high reliance on tax benefits.
Low end users’ acceptance of re-refined lubricants based on used oils is the top barrier to industry development. Leading lubricant blenders hesitate to adopt or claim the usage of re-refined basestocks in their formulations, mainly because end users have concerns about the quality and performance. Such concerns further put a ceiling over the production of these basestocks.
Difficulties in collecting high-quality used oil are mainly caused by low policy enforcements for generators and collectors to date. Almost no generators and collectors store different types of used lubricant separately as regulated, which lowers the average volume of high-quality used oil. Additionally, some generators sell used oils to unlicensed collectors because they offer higher collection prices than the licensed ones, or because generators themselves deliberately hide parts of used oil generation to avoid being shortlisted as key monitoring entities by local governments.
Lagging re-refining technologies lead to low quality and a stagnant yield rate of re-refined basestocks, which is similar to the 2018 levels, remaining at 67% on average. This is because most small and midsized re-refineries that adopt molecular and kettle-type distillation methods have an under-average yield rate of 65%. The yield rate is topped at 70% at the current stage and shows minimal improvement space with current technologies. Apart from that, high fixed investment required by the Group II basestocks production stops a vast majority of re-refiners from upgrading their re-refining technologies.
The profit margin of re-refiners and processors highly relies on tax benefits. The proportion of tax refund in overall profit margins increases from 38% to 46% as the quality of used oil decreases for basestocks production. Regarding processors, the share of tax refund further increases to about 62% for fuel production. The high reliance on tax benefits indicates that re-refiners and processors would be adversely impacted by uncertainties of tax benefits in the future.

## Slide 125
India

## Slide 126: India Market Synopsis
Chart: USED OIL MATERIAL BALANCE IN INDIA, 2021-2030 (MILLION TONS)
| Finished Lube Demand | Used Oil Generated | Used Oil Collected | Used Oil Re-refined | RRBO produced
2021 | 2594.3 | 1216.6 | 776.6 | 100.9 | 63.6
2025 | 2926.3 | 1404.6 | 927 | 148.3 | 93.4
2030 | 3133.5 | 1535.4 | 1044.1 | 185.7 | 117
Used Oil Regulations
The key used oil regulation in India is Hazardous Waste Management Handling & Transboundary Movement Rules, 2016.
Generators generating used oil upwards of 10 tonnes annually must sell or auction the oil to a registered re-refiner or recycler/re-processor possessing a valid certificate of registration.
The state pollution control boards authorized re-refiners are responsible for the collection of used oil from the point of generation to shipping it to their facilities.
A re-refiner and recycler shall use only environmentally sound technologies while recycling used oil.
Used Oil Material Balance
Used oil generation is low in India due to high consumption of process oils such as rubber process oils and limited development in the automotive segment, particularly related to engine efficiency, since large number of vehicles in use in the country still have BS-IV engine in which lubricant losses are higher.
In 2021, no significant change in used oil generation and collection rates as the implementation of regulations remains unchanged .
By 2025, the used oil market is expected to witness growth as companies such as IOCL are looking to use re-refined basestocks (based on the e-tender issued in April 2021). Further, with transition toward BS-VI engines and shift toward lighter viscosity grade, losses in automotive lubricants will reduce leading to increase in the used oil generation rate to 45%.
Used Oil Re-refining
The yield of re-refineries in India is around 63%. Only Group I basestocks is produced by re-refiners in India.
Only 13% of the collected used oil is re-refined in India. The remaining used oil is either used as fuel or regenerated or disposed in other ways such as land filling. Some used oil is also disposed by blending it with solvents such as Superior Kerosene Oil (SKO) and is sold as a replacement for Light Diesel Oil (LDO).
The Indian government has passed a mandate for OMCs to use 25% of re-refined basestocks for the producing lubricants by 2023. In case, these targets are met then re-refining could experience huge growth in the next one to two years.
No change in re-refined basestocks capacity is anticipated as large portion of this capacity remains unutilized in India.
Opportunities
Public sector oil marketing companies such as IOCL, HPCL, and BPCL are focusing on circular economy in the used oil market and are trying to increase usage of re-refined basestocks to produce lubricants.
Challenges
The proper enforcement of regulations and awareness of proper disposal of used oil are among the major challenges in the market.
The unorganized and fragmented nature of the market, leading to misuse of used oil in the form of industrial fuel. This results in low availability of the used oil to re-refiners.
MAJOR USED OIL RE-REFINERS IN INDIA, 2021-2030 |  |  | 
 | RE-REFINED BASESTOCKS CAPACITY (KILOTONNES) |  | 
COMPANY | 2021 | 2025 | 2030
Tanu Petrochemical-a | 21.2 | 21.2 | 21.2
Lucky Oil Company | 15.1 | 15.1 | 15.1
Mangalam Lubricants (P) Ltd | 14.2 | 14.2 | 14.2
Jawrawala Petroleum | 9.9 | 9.9 | 9.9
APJ Refinery Pvt. Ltd. | 9.5 | 9.5 | 9.5
Universal Hydrolubes | 9.4 | 9.4 | 9.4
Continental Petroleum Ltd. | 7.5 | 7.5 | 7.5
Mazda Industrol | 6.5 | 6.5 | 6.5
Bharat Oil Company | 3.9 | 3.9 | 3.9
Century Refineries-a | 5.9 | 5.9 | 5.9
Southern Refineries-a | 4.7 | 4.7 | 4.7
Cee Jee Lubricants | 4.7 | 4.7 | 4.7
IFP Petro Products (P) Ltd. | 3.9 | 3.9 | 3.9
Trimurti Enterprises | 0.7 | 0.7 | 0.7
Total | 117.1-b | 117.1-b | 117.1-b
a- Not operating currently, however, may resume in the future. b- The table shows used oil feed capacity of few selected re-refiners in India. |  |  | 

## Slide 127: Economic Background
The economy of the country is characterized as a middle-income developing market economy. In 2020, India slipped to sixth largest economy from fifth position in 2019, largely due to the impact of COVID-19 on the economy in 2020.
  The country's GDP growth has been amongst the highest in the world in the last decade by achieving a CAGR of 7.1% during 2009 to 2019. India was among the fastest-growing major economies in the world in 2019; however, the GDP declined due to COVID-19 pandemic in 2020.
According to International Monetary Fund (IMF), the country’s GDP contracted by 7.3% in 2020. The first half of 2020 witnessed sharp decline due to lockdown to prevent the spread of COVID-19 leading to adverse impact on business activities. The economy recovered in the second half of 2020 due to easing of lockdown and increased sales due to pent-up demand.
  Import and exports activities which were down during the first half of 2020 witnessed gradual recovery with economic activity rebounding in the country in the second half of 2020. However, at an overall level, agriculture was the only sector which grew in 2020. The manufacturing and the services sectors witnessed decline in the same year. Being under essential services, agriculture activities such as rabi harvesting and kharif sowing remained unaffected amid the COVID-19-induced restrictions and lockdowns.
The Indian economy bounced back in the first quarter of 2021. According to the Ministry of Statistics & Programme Implementation, GDP at constant prices registered growth of 24.8% in Q1 2021 as compared to GDP in Q1 2020.
  However, the situation again changed in the second quarter due to the second COVID-19 wave that the country experienced in 2021. The second COVID-19 wave impacted all the sectors of economy including the agriculture sector as rural areas were also affected this time.
  The second COVID-19 wave receded by July 2021 and the restrictions were eased. As a result, the economic activity resumed. Continued normalization in economic activity along with strong rebound in domestic consumer demand as well as export activities in second half of 2021 is leading to economic recovery in 2021.
According to the IMF’s World Economic Outlook October 2021 estimates, real GDP growth is expected to be around 9.5% for India in 2021. Strong rebound in manufacturing activities, push to infrastructure investments, and recovery in consumer demand and exports are some of the factors that will drive the growth in the Indian economy over the next few years.
SELECTED ECONOMIC CHARACTERISTICS OF INDIA, 2020 AND 2021 |  | 
KEY INDICATOR | 2020 | 2021
Population (million) | 1,378.6 | 1,389.4 (October 2021 estimate)
GDP at current prices (USD trillion) | 2.66 | 2.95 (October 2021 estimate)
GDP per capita, current prices (USD Thousand) | 1.93 | 2.12 (October 2021 estimate)
GDP growth rate, constant prices (annual % change) | (7.3) | 9.5 (October 2021 estimate)
Inflation, average consumer prices (annual % change) | 6.2 | 4.9 (October 2021 estimate)
Share in Real GDP (%) |  | 
Services (%) | 55.3 | 55.3
Industry (%) | 25.9 | 25.9
Agriculture (%) | 20.1 | 20.1
Source: The World Bank Group,, International Monetary Fund’s (IMF’s) World Economic Outlook (WEO), October 2021, Ministry of Statistics and Programme Implementation (MOSPI) |  | 

## Slide 128: Vehicle Population
India’s automotive industry became the fourth largest vehicle market in the world surpassing Germany in 2019. It is further anticipated to surpass the Japanese automotive market to become the third largest by 2021.
In 2020, there was a de-growth in sales of all segments compared to the previous years.
  Passenger vehicles declined by 14.9% in 2020. Similar trend was seen in the sales of commercial, three-wheeler, and two-wheeler segments. The commercial vehicle sales register a fall of 40.8% in 2020 whereas three wheelers and two-wheeler sales declined by 62.1% and 23.2%, respectively, in 2020. A structural slowdown in the industry even before the pandemic, combined with the impact of COVID-19 in 2020, led to huge decline in vehicles sales in 2020.
In addition, shift from BS-IV to BS-VI effective April 1, 2020, had a strong impact on the sales volume during 2020. Surge in vehicle price due to this transition was also an important factor which impacted the sales of automotive vehicles in the country in 2020.
In Q1 2021, automotive industry rebounded strongly registering nearly 42% increase sales in passenger vehicle segment, with more than 934,000 units sold as compared to sale of 657,244 units in the corresponding period in 2020. This surge in sales is attributed to economic recovery in 2021.
However, in Q2 2021, due to the second wave of COVID-19 hindered the economic recovery and consequently recovery in the automotive industry in India. Many manufacturers shut down their manufacturing plants to make oxygen available for medical purposes, supporting health care facilities and helping local communities.
  Due to lockdown, many dealers could not operate, leading to subdued sales in Q2 2021. As a result, in Q2 2021, overall vehicle sales declined by 43% as compared to Q1 2021. Later, as restrictions were eased and economic activity resumed, vehicle sales went up in Q3 2021. It is expected that vehicle sales will grow in Q4 2021 supported by festival demand season in the country.
Chart: VEHICLE SALES BY VEHICLE TYPE IN INDIA, 2019-2021
| Passenger Vehicles | Commercial Vehicles | Three Wheelers | Two Wheelers
2019 | 2.9605 | 0.85466 | 0.68745 | 18.5668
2020 | 2.5198 | 0.50555 | 0.26034 | 14.2682
2021 | 3.1267 | 1.1073 | 0.363 | 15.4715
Million units
Source: Society of India Automotive Manufacturers (SIAM)
Note:
- In 2021, the data for vehicle sales data in first three quarters is taken from SIAM and the fourth quarter vehicle sales are estimated.
-BMW, Mercedes, and Volvo Auto sales data is not available for passenger vehicle segment for 2021 estimates.
-Daimler, JBM Auto, & Scania sales data are not available for commercial segment for 2021 estimates.
Continued…

## Slide 129: Vehicle Population
With all the technological advancement in various sectors, India automotive industry is also shifting toward the adoption of more innovative and ecofriendly technologies for generating more revenues. Several technology and automotive companies have expressed interest and made investments into the Indian EV space.
  During the initial stage of EV development, the auto industry also faced a tight situation wherein industry and the policymakers could not decide on the timeline to convert some vehicle categories to electric from the present internal combustion engine (ICE) technology. However, previous initiatives and plans of the government have actively helped in pushing the EVs adoption in recent years.
  According to India Brand Equity Foundation (IBEF), the EV market, excluding E-rickshaws, in the country has seen a growth of 20.0% in FY 2020, driven by growing demand for two wheelers. Premium motorbike sales registered seven-fold hike in domestic sales, reaching 13,982 units during April-September 2019. According to IBEF, the luxury car segment is anticipated to register sales of 28,000-33,000 units in 2021, up from 20,000-21,000 units sold in 2020.
Economic slowdown coupled with drop in private sector investments and banking crisis were the major factors which led to low domestic consumer demand in 2019 which resulted in lower automotive production in 2019. This was further adversely affected by the unprecedented outbreak of COVID-19 pandemic in the country. Several lockdown measures, movement restrictions, and supply chain disruptions resulted in further decline in the production for automotive vehicles in the country in 2020.
All categories witnessed production declines in 2020. Three-wheelers registered sharp decline due to steep drop in demand for these vehicles post lifting of lockdown. The sales of three vehicle declined by 44.4% in 2020 as compared to previous years, whereas sales of passenger cars, commercial vehicles, and two-wheelers declined by 21.3%, 30.1%, and 22.6% in 2020.
In Q1 2021, automotive production recovered with surge in the demand. However, in Q2 2021, the vehicle production was adversely impacted by lockdown measures implemented to contain the second COVID-19 wave. Shortage of semi-conductor chips, increasing price of steel, and lack of inventory have compelled automotive manufacturers to reduce production. In Q3 2021, as restrictions were eased, automotive manufacturers carefully resumed operations in a phased manner.
Speedy recovery in the overall economic activity of the country as per the IMF projections and coming festival season supported the growth in sales as well as production of vehicles in Q4 2021. However, the shortage of semi-conductor chips continue to be an obstacle in smooth functioning of the industry.
Chart: VEHICLE PRODUCTION BY VEHICLE TYPE IN INDIA, 2019-2021
| Passenger vehicles | Commercial Vehicles | Three Wheelers | Two Wheelers
2019 | 3.6057 | 0.84434 | 1.1792 | 22.0935
2020 | 2.8365 | 0.59038 | 0.65558 | 17.099
2021 | 3.2776 | 0.66889 | 0.65415 | 19.6404
Million units
Source: SIAM
Note:
- In 2021, the data for vehicle production data for Q1-Q3 2021 is taken from SIAM. The sales data for Q4 2021is estimated.
-BMW, Mercedes, and Volvo Auto data is not available for passenger segment for 2021 estimates.
-Daimler, JBM Auto & Scania data are not available for commercial segment for 2021 estimates.

## Slide 130: Finished Lubricant Market
The Indian finished lubricants market is the third-largest lubricants market in the world after United States and China. It accounts for 6%-7% of total global lubricant demand.
  In 2020, the COVID-19 pandemic had brought economic activities to a standstill, not only in India but in most parts of the world. This resulted in partial to full closure of several sectors for a period ranging from a fortnight to almost three months.
  During this period, the industrial sector was hit hardly because of the slump in consumer demand, both in domestic and export markets. The automotive sector was also greatly hit due to movement restrictions. This has impacted the demand for automotive and industrial lubricants in the country. However, in second half of 2020 demand recovered as the economic and industrial activities resumed.
The overall finished lubricant demand accounted for 2,516.7 KT in 2020, contracted by 10.1% from 2019.
  Industrial lubricants segment dominated the total finished lubricant market. Within this segment, the demand is led by process oils followed by general industrial oils (GIOs), industrial engine oils, metalworking fluids (MWFs), and greases.
  Commercial automotive lubricants segment accounted for the second position in 2020. Significant demand from on-road commercial vehicles and equipment such as trucks, buses, and three-wheelers as well as off-highway vehicles used in agriculture, construction and mining supported the demand for lubricant demand in the commercial segment. However, the demand of commercial automotive lubricant decline by 11.1% in 2020 from previous year.
  The consumer automotive lubricants demand declined by 9.3% in 2020 as compared to previous year. Limited demand from two-wheelers, and passenger vehicles owing to the declining sale of consumer vehicle caused by outbreak of COVID-19 attributed to lowering the demand of consumer automotive lubricant.
Chart: OVERALL LUBRICANT DEMAND BY SEGMENT IN INDIA, 2020
| Industrial | Commercial | Consumer
Sales | 0.552 | 0.29 | 0.161
Total: 2,516.7 Kilotonnes
Continued…

## Slide 131: Finished Lubricant Market
In 2021, total lube demand is estimated to reach at 2,594.3 kilotonnes, witnessing 3.1% growth overall.
In 2021, process oil estimated to account the highest share of 31.5% of the total finished lubricants consumed in India in 2021. With in-process oil, electric oil constitute a larger share owing to their high demand in the power sector.
  Electrical transformer oil finds application in transformers, cables, and switchgear. The demand for electrical oil arises only when a new transformer is installed, and electrical oil is very rarely changed in old transformers.
  In 2021, process oil segment is expected to reach 817.1 KT as compared to 795.5 KT in 2020, witnessing a growth of 2.5%. Increasing investment in transmission and distribution network projects and rise in number of nuclear and solar power projects supported the increased deployment of transformers in the country. The Government of India has released its roadmap to achieve 227 GW capacity in renewable energy (including 114 GW of solar power and 67 GW of wind power) by 2022. Rise in transformer installation projects is expected to support the demand for electrical oil in 2021.
  White oils are also acquired significant share as they are widely used in pharmaceuticals, food, plastics, polymers, cosmetics, and paper industries.
In 2021, heavy duty motor oil (HDMO) accounts for 15.7% of total demand for total finished lubricants consumed in India. Shift toward better quality lubricants to address stricter fuel economy norms, environmental pollution concerns, and growing emission standards are some of the factors supporting growth of multigrades.
  In addition, shift toward BS-VI emission norms and introduction of scrappage policy in 2020 would promote scrappage of older vehicles and addition of new vehicles to the existing parc in compliance to latest emissions standards and with superior technology. This will certainly drive the demand for better quality lubricants oils especially lighter viscosity multigrades such as 10Ws and 5Ws in the coming years.
Chart: OVERALL LUBRICANT DEMAND BY PRODUCT TYPE IN INDIA, 2020 AND 2021
| Process Oils | HDMO | MCO | Industrial Engine Oils | Hydraulic Fluids | PCMO | MWF | All other-a
2020 | 795.5 | 394.9 | 240.5 | 148.8 | 132.5 | 123.6 | 114 | 566.9
2021 | 817.1 | 407.5 | 250.5 | 152.6 | 136 | 128.1 | 117.1 | 585.4
a- Includes automotive and industrial gear oils, grease, ATF, compression fluid, refrigeration oils, turbine & circulating oil, and other industrial oils.

## Slide 132: Finished Lubricant Market
KEY TRENDS IN THE LUBRICANT DEMAND IN INDIA | 
 | DESCRIPTION
Commercial automotive lubricants | With the advent of BS-VI compliant vehicles in the market, engine oil meeting the API CK-4 service category are expected to gain popularity in the coming years. In addition, introduction of scrappage policy in 2020 promoting scrappage of older vehicles, and addition of new vehicles to the existing parc in compliance to latest emissions standards and with superior technology will certainly drive the demand for better quality lubricants oils especially lighter viscosity multigrades such as 10Ws and 5Ws through 2030. OEMs are increasingly pushing lighter viscosity grades such as 10W-40 and 10W-30 in the market by recommending them for use in newer vehicles for service and factory fill applications. As a result, they are expected to witness the fastest growth through 2030. Rising penetration of electric vehicle, especially three-wheeler and buses, in the commercial automotive segment is expected to slow the growth of engine oil in the coming years. In 2020, monthly sales of e-rickshaw peaked at around 10,000 units but due to COVID-19, the sales for the year 2020 were around 80,000 units. Increasing trend toward the use of genuine oils and co-branded oils is witnessed in the commercial automotive segment in the country. Various OEMs have recently launched their genuine and co-branded oils in the last two to three years. For instance, in 2018, Tata Motors launched its genuine oil for all commercial vehicles. The trend continued in 2019 when Gulf Oil, which is one of the fastest-growing lubricant suppliers in India, partnered with Piaggio for marketing genuine and co-branded oils for commercial vehicles including BS-VI compliant models starting January 2020.
Consumer automotive lubricants | With the advent of better technology engines, more passenger car OEMs are recommending lighter viscosity grades, such as 5W-30, 5W-40, 0W-30, and 0W-20. Introduction of BS-VI emission standard coupled with shift toward better quality products to address the increasing fuel economy and environmental pollution concerns are driving demand for lower viscosity oils. Shifting of preference of consumers toward semi-synthetics and fully-synthetics due to increased service life lubricants, and less price difference between them. Moreover, dealers and distributors get high margins on synthetic products, and thus they are promoting synthetics more.
Industrial lubricants | Increasing mining projects, power plants, cement manufacturing plants, and steel plants in the country will support increase in output of these industries, thus supporting the demand for industrial lubricants over the forecast period.

## Slide 133: Lubricant Blenders
The lubricants blending market is highly fragmented and extremely competitive due to the presence of large number of blenders.
Public oil companies such as IOCL, HPCL, and BPCL together are the leaders followed by international and national private suppliers such as BP, Tide Water Oil, Gulf Oil International, among others.
  In India, public companies enjoy a strong position compared to other participants due to various factors such as: lower product pricing, vast distribution network, strong hold in the government projects in the mining, and construction segments.
Blender used Group I/II/III basestocks to produce lubricants. However, basestocks demand is experiencing a shift from Group I to Group II/III basestocks not only in the automotive but also in the industrial segment. Several oil marketing companies (OMCs) are preferring Group II/III basestocks to achieve optimal solution for top quality lubricants which Group I basetocks are not able to provide.
In India, only Group I basestocks are being produced by the re-refining of used oil due to technological constrain in the market. Blenders mix re-refined basestocks with the pool of virgin basestocks to get better result and sell it under their brand name. However, they may not reveal that they are using re-refined basestocks to produce lubricants.
  In recent years, the OMCs have shifted their focus toward circular economy to gain organic growth in the market. The repercussions of COVID-19 and volatility in the crude oil price as well as growing supply and demand gap in the virgin basestocks have compelled lubricant blenders to shift focus toward re-refined basestocks for production of lubricants. It is not clear the extent to which the OMCs are using re-refined basestocks.
  Earlier, blenders were not in the favor of using re-refined basestocks due to cheaper, abundant availability of virgin basestocks, and inferior quality but now they are compelled to procure re-refined basestocks due to increase in prices of virgin basestocks. Several oil marketing companies are now focusing on usage of re-refined basestocks and planning to launch new products made of re-refined basestocks.

## Slide 134: Regulations
SUMMARY OF REGULATIONS IN INDIA | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | Yes. used oil is covered under Hazardous Waste Management Handling & Transboundary Movement Rules, 2016.
2. How is used oil classified i.e., hazardous waste, special waste etc.? | Hazardous waste
3. Are there any requirements on who can collect used oil? | Yes, used oil collectors should be authorized from the Central Pollution Control Board( CPCB) and State Pollution Control Board (SPCB).
4. Does the country have an association(s) managing the collection and disposal of used oil? | No
5. Is a levy charged on sales of lubricants to support Used Oil collection associations? | No
6. Are there any requirements for how used oil generators manage used oil? | Yes, proposed operating practices have been developed to help generators of used oil to manage their wastes in environmentally safe manner, as per the Hazardous Waste Management Handling & Transboundary Movement Rules, 2016.
7. Are there requirements for oil manufacturers, marketers or retailers to take back Used Oil? | No
8. Do any requirements/legislation exist around different types of Used Oil? | No
9. Does the country have requirements or regulations regarding the export or import of Used Oil? | Yes. As per Rule 12 of Hazardous Waste Management Handling & Transboundary Movement Rules, 2016, import of hazardous waste is not allowed for disposal. However, it is permitted to be re-refined or regenerated as per Rule 13 as specified in Part A & Part B of Schedule III.
10. Does the country have any legislation that requires Used Oil to be re-refined? | No
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | Yes, Indian government has passed mandate of utilizing 25% re-refined basestocks for lubricants by 2023.
Continued…

## Slide 135: Regulations
SUMMARY OF REGULATIONS IN INDIA |  | 
QUESTION |  | ANSWER
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? |  | Nothing has been given regarding usage of used oil as a fuel. However, oil that is categorized as a waste oil such as tank bottom slugged of crude oil, or mixtures containing synthetic oil can be burned as fuel as per specification laid down in Schedule V Part B of Hazardous Waste Management Handling & Transboundary Movement Rules, 2016
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | Yes, As per HW rule 2016, waste oil burner shall comply with prescribed standards for particulate matter, HCl, SO2, CO, HF, NOx (NO and NO2 expressed as NO2), Hydrocarbons, Dioxins/Furans, Cd +Th (and its compounds), Hg (and its compounds), Sb + As + Pb + Cr + Co + Cu + Mn + Ni + V (and their compounds).
14. Is used oil allowed to be placed in a landfill? |  | Yes, only authorized Treatment Storage Disposal Facility (TSDF) are allowed to place used oil in a landfill after meeting specification laid down in Schedule - I, II (Part A, B and C of the Hazardous Waste Management Handling & Transboundary Movement Rules, 2016
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | No
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | No information has been given
 | ii. Blending with crude oil at a refinery | No information has been given
 | iii. Dust suppressant | No information has been given
17. Are there companies / associations advocating in used oil category? |  | Yes, public sector OMCs such as IOCL, HPCL and BPCL

## Slide 136: Used Oil Regulations
USED OIL REGULATIONS FOR DIFFERENT STAKEHOLDERS |  | 
 |  | DESCRIPTION
Generation | Sell or auction | Generators generating used oil upwards of 10 tonnes annually must sell or auction the oil to a registered re-refiner or recycler/re-processor possessing a valid certificate of registration as per the notification in HW (M, H & TM) Rules 2016. However, there has been no mention of generators generating less than 10 tonnes of used oil on an annual basis even in the amended 2017, 2018, 2019 HW (M, H & TM) Rules. Any waste oil which does not meet the specifications laid down in Schedule 6 of HW (M, H & TM) Rules 2016 shall not be auctioned or sold; however, it shall be disposed of in hazardous wastes incinerator installed with air pollution control devices and meeting emission standards.
Disposal | Disposal | To dispose used oil landfill/incineration, as per specification laid down in the HW rules 2016, only Treatment Storage Disposal Facility (CHW TSDF) are approved by SPCB and duly authorized for disposal of used oil.
Recycling of used oil | Recycling of used oil | For recycling of used oil, the generator must get the sample tested from MoeF approved laboratory and comply with the Hazardous Waste for reprocessing as the case may be, as per specification laid down in Schedule-V of the HW 2016 Rules.
Handling | Handling | Generators shall securely seal used oil in a container made up of mild-steel or HDPE or in gunny bag whereby no leachate/liquid leaks and label the waste as per Form-8 of the rules.
Storage | Storage | The used oil generators may store the hazardous wastes for a period not exceeding 90 days and shall maintain a record of sale, transfer, storage, recycling, and reprocessing of such wastes and make these records available for inspection by the CPCB and/or the SPCBs. The SPCBs may extend this period of 90 days in the following cases: Small used oil generators generating up to 10 tonnes of used oil per annum Used oil generators that do not have access to any treatment, storage, disposal facility in the concerned state The waste needs to be specifically stored for development of a process for its recycling and reuse.
Continued…

## Slide 137: Used Oil Regulations
USED OIL REGULATIONS | 
 | DESCRIPTION
Classification | Used oil is classified as a hazardous waste by the Ministry of Environment and Forest, Government of India under the Hazardous Waste Management Handling & Transboundary Movement Rules, 2016 According to the schedule I of Hazardous Waste Management Handling & Transboundary Movement Rules, 2016, 1989, any type of petroleum refining or reprocessing of used oil or recycling of waste oil generates oil sludge or emulsion, spent catalyst, slop oil, organic residue from processes, spent clay containing oil shall fall under as hazardous waste
Collection | The SPCBs authorized re-refiners are responsible for the collection of used oil from the point of generation to shipping it to their facilities. The re-refiner must be registered with the SPCB of the state, where the re-refinery is located and must obtain a “no objection certificate” (NOC) from the state from which it obtains used oil.
Transportation | The used oil generators shall provide the transporter with the relevant information in Form 9, regarding the hazardous nature of the used oil and measures to be taken in case of an emergency and shall label the containers as per Form 8. Transporter need to obtain permission from the SPCB for transport of hazardous waste [in addition to any other permissions that may be required under the Motor Vehicles (Amendment) Act of 1988]. In case of transportation of used oil for final disposal to a facility existing in a State other than the State where the waste is generated, the sender shall obtain 'No Objection Certificate' from the SPCB of both the States. In case of transportation for recycling, the sender shall intimate both the SPCBs before handing over the waste to the transporter. Transporter shall not accept hazardous wastes from generator unless six-copy (with color codes) of the manifest in Form 9 is provided by the generator Copy 1 (white) to be forwarded by the generator to the State Pollution Control Board or Committee Copy 2 (yellow) to be retained by the generator after taking signature on it from the transporter and rest of the four copies to be carried by the transporter Copy 3 (pink) to be retained by the operator of the facility after signature Copy 4 (orange) to be returned to the transporter by the operator of facility after accepting waste Copy 5 (green) to be returned by the operator of the facility to State Pollution Control Board/Committee after treatment and disposal of wastes Copy 6 (blue) to be returned by the operator of the facility to the occupier after treatment and disposal of wastes Used oils shall be transported in the closed drums/containers.
Continued…

## Slide 138: Used Oil Regulations
USED OIL REGULATIONS | 
 | DESCRIPTION
Storage | Generator may store the hazardous and other wastes for a period not exceeding 90 days and shall maintain a record of sale, transfer, storage, recycling, recovery, pre-processing, co-processing, and utilization of such wastes and make these records available for inspection. The SPCB may extend the period of 90 days for storing used oil if :- Small generators generating used oil below or up to 10 tonnes per annum can store used oil up to 180 days. Actual users and disposal facility operators can store used oil up to 180 days based on their annual capacity Occupiers who do not have access to any treatment, storage, disposal facility in the concerned state; or The waste which needs to be specifically stored for development of a process for its recycling, recovery, pre-processing, co-processing or utilization; In any other case, on justifiable grounds up to 180 days.
Disposal – Re-refining | Per Hazardous Waste Management Handling & Transboundary Movement Rules, 2016 under Environment Protection Act, 1989, a re-refiner and recycler shall use only environmentally sound technologies while recycling used oil. Re-refiner shall follow environmentally sound technologies such as Vacuum distillation with clay treatment; Vacuum distillation with hydrotreating; Film evaporation process, or any other technology approved by the Ministry of Environment and Forests Refiner registered with the Ministry of Environment and Forests or the CPCB shall file a compliance report of having adopted one of the technologies within six months from the date of commencement of the Hazardous Wastes (Management and Handling) Amendment Rules, 2003.
Continued…

## Slide 139: Used Oil Regulations
Disposal – Fuel
As per Hazardous Waste Management Handling & Transboundary Movement Rules, 2016, used oil shall only be recycled/re-refined by the authorized recycler if it meets the specification laid down in Part A of Schedule V. However, waste oil such as tank bottom slugged of crude oil or mixtures containing synthetic oil can be used as a fuel in industry applications as per specification laid down in Schedule V Part B of Hazardous Waste Management Handling & Transboundary Movement Rules, 2016.
Disposal – Other
Used oil that does not meet specifications laid under Hazardous Waste Management Handling & Transboundary Movement Rules, 2016 for recycling/refining shall be dispose at SPCB approved Treatment Storage Disposal Facility (TSDF).
SPECIFICATION OF FUEL DERIVED FROM WASTE OIL (SCHEDULE V PART B) | 
PARAMETER | MAXIMUM PERMISSIBLE LIMITS
Sediment | 0.25%
Lead | 100 ppm
.Arsenic | 5 ppm
Cadmium+Chromium+Nickel | 500 ppm
Polyaromatic hydrocarbons (PAH) | 6%
Total halogens | 4000 ppm
Polychlorinated biphenyls (PCBs) | . <2 ppm
Sulfur | 4.5%
Water Content | 1%
SPECIFICATION OF SPECIFICATIONS OF USED OIL SUITABLE FOR RECYCLING (SCHEDULE V PART A) | 
PARAMETER | MAXIMUM PERMISSIBLE LIMITS
Polychlorinated biphenyls (PCBs) | < 2ppm
Lead | 100 ppm
Arsenic | 5 ppm
Cadmium+Chromium+Nickel | 500 ppm
Polyaromatic hydrocarbons (PAH) | 6%

## Slide 140: Regulatory Enforcement
Responsible Agencies
SPCBs and Pollution Control Committees (PCCs) have been entrusted with duty to ensure compliance of the various provisions stipulated under the Hazardous Waste Management Handling & Transboundary Movement Rules, 2016, through monitoring and take actions against defaulters as per Rule 21 of the Hazardous Waste Management Handling & Transboundary Movement Rules, 2016.
There are several other regulatory agencies such as Ministry of Environment, Forests, and Climate Change, monitoring handling, generation, collection, storage, packaging, transportation, use, treatment, processing, recycling, recovery, pre-processing, co-processing, utilization, offering for sale, transfer or disposal of the hazardous waste in the India.
LIST OF AGENCIES AND CORRESPONDING DUTIES | 
AGENCIES | CORRESPONDING DUTIES
Ministry of Environment, Forests and Climate Change under the Environment (Protection)Act, 1986 | Identification of hazardous and other wastes Permission to exporters of hazardous and other wastes Permission to importer of hazardous and other wastes Permission for transit of hazardous and other wastes through India. Promote environmentally sound management of hazardous and other waste. Sponsoring of training and awareness programs on Hazardous and Other Waste Management related activities.
Central Pollution Control Board constituted under the Water (Prevention and Control of Pollution) Act, 1974 | Co-ordination of activities of SPCBs Conduct training courses for authorities dealing with management of hazardous and other wastes Recommend standards and specifications for treatment and disposal of wastes and leachates, recommend procedures for characterization of hazardous wastes. Inspection of facilities handling hazardous waste as and when necessary. Sector specific documentation to identify waste for inclusion in these rules. Prepare and update guidelines to prevent or minimize the generation and handling of hazardous and other wastes. Prepare and update guidelines/ Standard Operating Procedures (SoPs) for recycling, utilization, pre-processing, co-processing of hazardous and other wastes. To prepare annual review report on management of hazardous waste. Any other function assigned by the Ministry of Environment, Forest and Climate Change, from time to time.
Continued…

## Slide 141: Regulatory Enforcement
LIST OF AGENCIES AND CORRESPONDING DUTIES | 
AGENCIES | CORRESPONDING DUTIES
State Government/Union Territory Government/Administration | Identification of site (s) for common Hazardous and Other Waste Treatment Storage and Disposal Facility (TSDF) Assess Environment Impact Assessment (EIA) reports and convey the decision of approval of site or otherwise Acquire the site or inform operator of facility or occupier or association of occupiers to acquire the site Notification of sites. Publish periodically an inventory of all potential or existing disposal sites in the State or Union Territory
State Pollution Control Boards or Pollution Control Committees constituted under the Water (Prevention and Control of Pollution) Act, 1974 | Inventorization of hazardous and other wastes Grant and renewal of authorization Monitoring of compliance of various provisions and conditions of permission including conditions of permission for issued by Ministry of Environment, Forest and Climate Change for exports and imports Examining the applications for imports submitted by the importers and forwarding the same to Ministry of Environment, Forest and Climate Change Implementation of program to prevent or reduce or minimize the generation of hazardous and other wastes Action against violations of these rules Any other function under these Rules assigned by Ministry of Environment, Forest and Climate Change from time to time
Port authority under Indian Ports Act, 1908 (15 of 1908) and Customs Authority under the Customs Act, 1962 (52 of 1962) | Verify the documents Inform the Ministry of Environment, Forests and Climate Change of any illegal traffic Analyze wastes permitted for imports and exports, wherever required Train officials on the provisions of these rules and in the analysis of hazardous and other wastes Take action against exporter or importer for violations under the Indian Ports Act, 1908 or Customs Act, 1962
Continued…

## Slide 142: Regulatory Enforcement
Enforcement Mechanisms
A set framework laid down by the CPCB for enforcement of Hazardous Wastes including enforcement tools, monitoring, and tracking of noncompliance, categorization of non-compliances and approach for application of the said enforcement tools in cases of non-compliances of the Hazardous Waste Management Handling & Transboundary Movement Rules, 2016.
Enforcement tool
  Under the enforcement tool, the CPCB has issued the guidelines for the imposition of liability for damages caused to the environment or third party including financial penalty for violation of provisions under Hazardous Waste Management Handling & Transboundary Movement Rules, 2016.
  A set of guidelines issued by the CPCB for the imposition of environmental compensation directed by the National Green Tribunal, Principal Bench. The National Green Tribunal, Principal Bench, New Delhi directed the regulatory authorities (CPCB/SPCBs/PCCs) to assess and recover the environmental compensation for the damages caused to the environment in order to make polluting activities unprofitable.
  Prosecution for imprisonment with fine in case of failure to comply with or contravenes any of the provisions of the Act, or the rules made, or orders or directions issued under Section 19 of the Environment (Protection) Act, 1986.
  Prohibition against establishment of industries in restricted area.
Monitoring/Tracking of non-compliances
  Through technology interventions
  Through field investigation
Categorization of violations
For imposing financial penalty and environmental compensation, the CPCB has broadly classified various violations of Hazardous Waste Management Handling & Transboundary Movement Rules, 2016, into the following two categories:
  Category A: Procedural violations of Hazardous Waste Management Handling & Transboundary Movement Rules, 2016, which has not caused damage to environment or third party
  Category B: Violations causing environmental damage including procedural violations
Based on each category assessment, financial penalty would be applicable as outlined under section 7 of Hazardous Waste Management Handling & Transboundary Movement Rules, 2016.
Continued…

## Slide 143: Regulatory Enforcement
Effectiveness of Regulations Enforcement
There have been several enforcement procedures followed by the regulatory authorities for the effective implementation of the hazardous waste rules and regulations imposed by Indian government on the used oil market. However, the used oil market is highly fragmented and unorganized, regulatory authorities face several challenges in the enforcement of regulations resulting in major chunk of generated used oil end up going in the black market or used as fuel in the industry applications.
Some of the major issues that are affecting the effectiveness of regulations enforcement by regulatory authorities (SPCBs and PCCs) in used oil market are:
  Lack of Standardized Protocols: There are no standard inspection and sampling procedures prescribed in the Water Act, Air Act or Environmental Protection Act. The CPCB and the SPCBs have also not issued uniform guidelines for inspections procedures. As a result, the quality of inspection depends on the interpretation of the officer conducting the inspection.
  Lack of Legal Authority: The SPCBs have no deterrent mechanisms such as fines or penalties that could be imposed on non-complying industries. As per chapter 3 of Hazardous Waste Management Handling & Transboundary Movement Rules, 2016, the SPCBs are allowed to impose civil fines on generators and operators if they violate provisions of the Hazardous Wastes Rules. However, the SPCB must get approval from the CPCB before it imposes the fine. This approval process are difficult and time consuming, hence, few SPCBs use this provision.
Other issues are such as lack of financial budgets, lack of resources, and less reliance on technology with SPCBs and PCCs are further posing a big challenge and reducing the effectiveness of regulation enforcement in the Indian used oil market.
To overcome these challenges so as to make the enforcement system more effective, both the union and the state governments are continuously engaged in developing new strategies. For instance, recently Gujarat PCB (GPCB) has automated many of its enforcement duties through the use of Extended Green Node (XGN) software. This software is used by industries to submit documents online, including applications for grants of authorization and grants of renewal, annual reports, and monitoring data.
Key Influencer
Public Sector
  Indian Oil Corporation Limited (IOCL)
  Bharat Petroleum Corporation Limited (BPCL)
  Hindustan Petroleum Corporation Limited (HPCL)
Private Sector
  IFP Petro Products
  Other private players operating in the industry

## Slide 144: Impact of Current Regulations
There has been a moderate impact of hazardous waste regulations in the Indian used oil market as it is highly fragmented and unorganized, with presence of more than 550 authorized re-refiners/recyclers and large number of generators.
Impact of the regulations is more prevalent in the industrial segment, as compared to automotive segment, as operations in the industries are organized and generators have proper used oil generation and disposal record maintained.
  In the industrial segment, the inadequate disposal of used lubricants is less common than in the automotive segment as regulatory bodies have tighter control over industries. Further, industries will need to pay heavy penalties if they dump the used oil and contaminate the environment or not comply with the set standards. As a result, refiners are switching to the Environmentally Sound Technologies (EST) for re-refining/recycling of used oil/waste oil in an environmentally sound manner which was earlier done by acid clay process or other non eco friendly process.
  Companies are designing a framework to store the used oil and sell or auction it to authorized re-refiners.
The impact of regulation in automotive segment is less as it becomes difficult to monitor how each car/two-wheeler workshop collects and discards automotive used oils given the huge number of such workshops in the country.
  Mechanics know that the used oil drained from vehicles possesses value and, hence, they do not dispose of it. They either sell used oil to re-refiners or as lubricants in the black market.
Monitoring of these unauthorized practices is a big challenge for regulatory authorities due to lack of standardized protocols, shortage of staff, a lack of legal authority and limited tracking technologies, leading to lower impact of regulations
In small industries, unauthorized garages and Independent workshops, impact of regulations is very low. At present, there is no accountability for the collection of used oil in this segment, which leads to fervent malpractices such as blending with solvents to be ultimately expended as fuel or refilling old lubricant bottles or in new packaging similar to the original lubricant brand only to be sold as counterfeit lubricant on the black market. It allows them to earn a high margin but also reduces the used oil available for re-refining. As a result, the operating efficiencies of many re-refiners are quite low in India.
Functions of regulatory agencies
To ensure safe handling , generation, processing, treatment, package, storage, transportation, collection, reprocessing, and disposal of used oil
Monitoring of units engaged in used oil collection/ recycling/ utilization/ pre-processing/ co-processing/ disposal and import of used oil
Monitoring compliance with contractual obligations to the government and users, and other legal and regulatory requirements.
Establishing technical, safety and quality standards
Design and enforce framework for effective implementation of hazardous waste regulations

## Slide 145: Material Balance 2020
Chart: USED OIL GENERATION, 2020
| Used oil generated | Lubricant lost
Sales | 0.47 | 0.53
Total: 2,516.7 Kilotonnes
Chart: USED OIL COLLECTION, 2020
| Collected | Not collected
Sales | 0.64 | 0.36
Chart: USED OIL DISPOSAL, 2020
| Fuel | Re-refined | All other-a
Sales | 0.67 | 0.14 | 0.19
Chart: USED OIL RE-REFINING, 2020
| Basestock | All other
Sales | 0.63 | 0.37
Total: 1,179.5 Kilotonnes
Total: 752.8 Kilotonnes
Total: 105.6 Kilotonnes
The total demand for finished lubricants in India was estimated to be 2,516.7 kilotonnes in 2020. Of this total, 58% is lost due to lubricant consumption in usage in vehicle and machineries, improper handling, and leakage
The generation rate of used oil in India stands at 47% of the total lubricant demand, witnessed slight increase since 2018 due to increasing penetration of synthetic and better grade lubricants in automotive segment.
However, it is lower in comparison to other markets such as the United States, Western Europe, Brazil, etc., where the generation rate is between 55%-60%.
  The major reason for lower used oil generation rate in India is the high consumption of process oils such as rubber process oils and white oils that account for around 17% of total lubricant demand in India.
  Secondly, limited development in the automotive segment, particularly related to engine efficiency, since large number of vehicles in use in the country still have BS-IV engine in which lubricant losses are higher. However, Indian government have passed mandate to use BS-VI engines in all vehicles effective from April 2020, which is expected to reduce lubricant loss and increase generation rate of used oil in India in the future.
a- Includes regeneration of used oil to lubricant by removing some impurities, land filling and other disposal methods.
Continued…

## Slide 146: Material Balance 2020
The used oil collection rate in India is about 64% or 752.8 kilotonnes used oil collection in 2020.
  In 2020, the collection rate is similar to 2019, however, the collection volume declined by around 6%-7% due to decline in lubricant demand, which led to decline in used oil generation, due to COVID-19.
  In 2020, collection rate is largely impacted by the closures of garages, workshop and authorized center due to lockdown imposed to limit the spread of COVID-19 in India. In addition, delay and cancellation of used oil auctioning in industrial segment as several industrial operations were shut down due to pandemic also significantly impacted the used oil collection volume in 2020.
Ideally, the used oil collected should be re-refined to produce the basestocks.
  However, it is observed that only 14% of the collected used oil is re-refined in India. The remaining used oil is either used as fuel or regenerated or disposed in other ways such as land filling.
  Some used oil is also disposed by blending it with solvents such as Superior Kerosene Oil (SKO) and is sold as a replacement for Light Diesel Oil (LDO).
  The average yield for a used oil re-refinery was around 63%, which translates to re-refined basestocks production of about 60 kilotonnes.in 2020. The remaining 37% primarily includes residues such as light oil, ethylene glycol, water, etc.

## Slide 147: Material Balance 2021
Chart: USED OIL GENERATION, 2021
| Used oil generated | Lubricant lost
Sales | 0.42 | 0.58
Total: 2,594.3 Kilotonnes
Chart: USED OIL COLLECTION, 2021
| Collected | Not collected
Sales | 0.64 | 0.36
Chart: USED OIL DISPOSAL, 2021
| Fuel | Re-refined | All other-a
Sales | 0.66 | 0.13 | 0.21
Chart: USED OIL RE-REFINING, 2021
| Basestock | All other-b
Sales | 0.63 | 0.37
Total: 1,216.6 Kilotonnes
Total: 776.6 Kilotonnes
Total: 100.9 Kilotonnes
In 2021, no significant change has happened for the used oil industry as there is no announcement on the policy front as well as the fact that the implementation of regulations remains unchanged.
  The generation rate and collection rate share are expected to remain same as in 2020. However, growing focus of government and several manufacturing companies on the circular economy is expected to increase the share of used oil collection in the market in the coming years.
  As compared to 2020, regeneration of used oil is expected to increase slightly, supported by the increase in demand after re-opening of industrial sector in the country in 2021. Several small-scale manufacturing companies use regenerated lubricants in place of virgin lubricants as regenerated lubricants prices are lower than virgin lubricants. Due to lockdown and movement restriction in 2020 most of manufacturing industries were shut down or operating at low-capacity rate which has negatively impacted the demand for regenerated lubricants. However, reopening of industrial sector in the second half of 2020 increased the demand for regenerated lubricants.
  The volume of used oil supplied for re-refining declined slightly as demand for regenerated lubricants increased in 2021.
a- Includes regeneration of used oil to lubricant by removing some impurities, land filling and other disposal methods. CC

## Slide 148: Used Oil Generation
Out of 2,516.7 kilotonnes of finished lubricant in India, only 47% or 1,179.5 KT is generated as used oil. The remainder is accounted for by technical losses inherent to different applications such as evaporation, combustion, etc. Leakages and mishandling also contribute to losses incurred.
  For example, process oils such as white oils or rubber process oils are either consumed completely in the process or are part of the final product. Therefore, they do not contribute to the used oil generation.
  The automotive segment, which mainly includes HDMO, PCMO, 4T MCO oils, gear oils, and HTF is responsible for the generation of about 53.7% of the total used oil generated in the country. Automotive oils such as PCMO and HDMO have the highest used oil generation rate of 80% and 70%, respectively. The used oil generation rate could vary from 60%-80%, depending upon the type of vehicle.
  Automotive used oil is generated during lubricant change, which usually takes place at authorized workshops, garages, and local unauthorized workshops. The used oil generated at these venues is usually mixed and stored in barrels or tanks. However, there are instances when the used oil generators store used HDMO and PCMO, and other types of used oil separately.
Chart: USED OIL GENERATION RATES BY PRDOUCT IN INDIA, 2020 AND 2021-a
| PCMO | HDMO | Hydraulic Fluid | MCO | MWF | Industrial Engine Oil | Process Oils | All Other-b
Series 1 | 0.8 | 0.7 | 0.7 | 0.6 | 0.3 | 0.3 | 0.4 | 0.3
USED OIL GENERATION BY PRODUCT IN INDIA, 2020 AND 2021 |  |  |  | 
LUBRICANT | KILOTONNES |  | % OF TOTAL USED OIL GENERATED | 
 | 2020 | 2021 | 2020 | 2021
Process oil | 318.2 | 326.8 | 27.0 | 26.9
HDMO | 276.4 | 285.3 | 23.4 | 23.5
MCO | 144.3 | 150.3 | 12.2 | 12.4
PCMO | 98.9 | 102.5 | 8.4 | 8.4
Hydraulic fluid | 92.8 | 95.2 | 7.9 | 7.8
Industrial engine oil | 44.6 | 45.8 | 3.8 | 3.8
MWF | 34.2 | 35.1 | 2.9 | 2.9
All other-a | 170.1 | 175.6 | 14.4 | 14.45
Total | 1,179.5 | 1,216.6 | 100.0 | 100.0
a- Includes ATF, compressor oil, refrigeration oil, and turbine oil, among others. |  |  |  | 
a- Generation rates are same for 2020 and 2021. Therefore, only one bar chart is shown.
b- Includes ATF, compressor oil, refrigeration oil, turbine oil, among others.
Continued…

## Slide 149: Used Oil Generation
In 2020, the domestic sales of automotive lubricants declined by around 10%.
  In 2020, automotive sales volume was significantly impacted by the outbreak of the COVID-19 coupled with increased pricing of vehicle due to the transition from Bharat Stage IV (BS-IV) to BS-VI emissions norms in the automotive industry. This has resulted in the decline in the demand for lubricants in the automotive industry and consequently, negatively impacted used oil generation from the new vehicles. Moreover, delay in the servicing and maintenance work of vehicle due to closure of service centers and limited use of vehicle by consumers as most of them are working from home has impacted the used oil generation volume in 2020.
The used oil generation rate is more than 75.0% in the automotive segment. HDMO accounted for 23.4% of total used oil generation in the country in 2020.
  Despite the decline in sales of commercial vehicles in 2020 due to the COVID-19 pandemic, used oil generation from the commercial segment remained stable, supported by a boom in the logistic sector due to growth in e-commerce.
  In 2020, the large number of trucks and commercial vehicles (except those used in public transport) were operating during the pandemic for transportation of goods, medical equipment, and food supply.
  However, used oil generation volume remained low during lockdown as workshops and garages were closed but used oil generation for the rest of the year remained normal.
  The commercial segment also witnessed growth in THF demand due to strong growth in tractor production in the country in 2020. Moreover, strong agriculture produce supporting more tractor usage and subsequently more service and oil change activities in the tractor segment significantly contributed to growth in the THF demand. It should be noted that agriculture activities were considered essential and were exempted from lockdown.
During the lockdown period in 2020, most of the non-essential manufacturing industries were shut down and others were operating at very low output. This led to the reduced demand for industrial lubricants in 2020 and consequently, the generation of used oil also declined in 2020.
However, the recovery was fast post lockdown in the second half of 2020, which helped the industry in achieving pre-COVID product manufacturing index for 2020.
In the industrial sector, used oil is generated through factories.
  Hydraulic fluids, turbine and circulating oils, industrial engine oils, and other industrial oils are the major used oil sources as they are consumed by manufacturing sector.
Industrial oils have a used oil generation rate lower than automotive lubricants as companies try to reclaim as much lubricant as possible.
  In industries, losses are observed due to the usage of oil until extinction and leakages.
  General industrial fluids such as hydraulic fluids have an estimated used oil generation rate of 70%.
  Industrial fluids like metalworking fluids and greases generate small volume of used oil as they are usually used until extinction.

## Slide 150: Used Oil Collection
Used oil is one of the major hazardous wastes generated from automobile and industrial segment that have contribute immensely toward the degradation of the environment and the problem of this has been traced to the poor handling of used oil and the ignorance of the major disposers of this used oil.
Thus, lately, the government authorities such as SPCB and CPCB have been actively focusing on the proper collection of used oil from the different sources of generations.
According to a CPCB report for 2019-20, 556 authorized facilities were approved for collection and recycling/re-refining of used/waste oil in the country.
The companies are licensed by the SPCBs and the CPCB for a period after which it must be renewed. The licensing period for each state is decided by the respective SPCB of the state and varies from state to state.
  In 2020, used oil collection in India estimated at 685.6 kilotonnes. India had an average used oil collection rate of 64% of the total used oil generated.
  Automotive segment accounted for largest contributor in used oil collection. In 2020, 50.6% of used oil collected was from automotive segment.
  Industrial segment is responsible for the collection of remaining used oil in India.
Chart: USED OIL COLLECTION RATES BY PRODUCT IN INDIA, 2020 AND 2021-a
| PCMO | HDMO | Hydraulic Fluid | Metalworking Fluids | Industrial Engine Oil | Process Oil | All Other-b
Series 1 | 0.64 | 0.7 | 0.7 | 0.48 | 0.48 | 0.65 | 0.55
USED OIL COLLECTION BY PRODUCT IN INDIA, 2020 AND 2021 |  |  |  | 
LUBRICANT | KILOTONNES |  | % OF TOTAL USED OIL COLLECTED | 
 | 2020 | 2021 | 2020 | 2021
Process Oil | 206.8 | 212.4 | 27.5 | 27.3
HDMO | 193.5 | 199.7 | 25.7 | 25.7
MCO | 92.4 | 96.2 | 12.3 | 12.4
Hydraulic Fluid | 64.9 | 66.6 | 8.6 | 8.6
PCMO | 63.3 | 65.6 | 8.4 | 8.4
Industrial Engine Oil | 21.4 | 22.0 | 2.8 | 2.8
MWF | 16.4 | 16.9 | 2.2 | 2.2
All other-a | 94.1 | 97.2 | 12.5 | 12.5
Total-b | 752.8 | 776.6 | 100.0 | 100.0
a- Includes ATF, compressor oil, refrigeration oil, turbine oil, among others. |  |  |  | 
a- Collection rates are same for 2020 and 2021. Therefore, only one bar chart is shown.
b- Includes ATF, compressor oil, refrigeration oil, turbine oil, among others.
Continued…

## Slide 151: Used Oil Collection
Automotive segment accounted for 416.4 kilotonnes used oil collected in 2020.
The collection of used oil is done through multiple sources depending on the generation point.
  In automotive segment, it is collected at garages, authorized workshops (AWS), independent workshop (IWS), franchised workshops, in-house workshop, and fuel stations (service bays).
  Garages and authorized workshop are among the major sources of used oil collection in the country and accounted for 82% of total used oil collected from automotive segment in 2020.
  Large garages and AWS generally have tie up with the collectors, to whom they sell used oil to earn revenues. Therefore, they store used oil properly to avoid spillage and misuse in the workshops or in garages, leading higher collection rate.
IWS and small garages do not have tie-ups with the collectors and generally use used oil either for personal usage such as burning and lubricate automotive components or sell it to independent collectors for higher profit margin. Therefore, the collection of used oil from IWS and garages is lower than AWS.
  In 2020, the outbreak of COVID-19 has significantly impacted the operations of small garages and independent workshop. Most of them were shut down during lockdown. Also, after lifting of lockdown in the second half of 2020, only few IWS and garages resumed their operation due to lesser number of vehicles coming for servicing and workforce constraints.
In industrial segment, used oil is collected at factories through e-auctions and tenders which are conducted by MSTC Limited for public companies and by individual factories in private sector.
AUTOMOTIVE USED OIL COLLECTION BY SOURCES IN INDIA, 2020 |  | 
SOURCE | KILOTONNES | % OF USED OIL COLLECTED
Authorized workshops (AWS ) | 237.3 | 57.0
Garages | 104.1 | 25.0
Independent workshop (IWS) | 50.0 | 12.0
All other-a | 20.8 | 5.0
Total | 416.4 | 100.0
a- Includes in-house workshop/maintenance team and fuel stations |  | 
Continued…

## Slide 152: Used Oil Collection
The SPCBs authorized re-refiners are responsible for the collection of used oil from the point of generation to shipping it to their facilities.
  The re-refining facilities are mostly located near industrial hubs in proximity to the source of used oil.
  Some re-refiners are also known to collect used oil from different states depending on the availability of used oil. However, the re-refiner must be registered with the SPCB corresponding to the re-refinery’s location and must obtain a “no objection certificate” (NOC) from the state from which it obtains used oil.
The collection is done through two segments – small generators mostly in automotive segments such as dealers, workshops, garages, and large generators from industrial segment.
  In automotive segment, re-refiner generally deals with authorized dealerships, and workshops because they have proper process for used oil collection and storage, that small garages and workshops do not have. Also, authorized dealerships, and workshops file Good and Service Tax (GST) returns, which help re-refiners in gauging authenticity of the generator to maintain continuous supply of used oil.
  Authorized workshops, dealerships, and garages usually have a long-term contract with a used oil collector/traders with whom they directly negotiate on an individual basis.
  Used oil is generally collected from these facilities when the storage capacity is almost full. Therefore, each facility has a varying collection window dependent on the number of vehicles being catered to. Industries also follow the same trend and contact the trader/collector once their storage capacity for used oil is almost full.
  There are independent collectors who collects used oil from small generators and sell it to industries or local vehicle owners for alternative usages such as burning. Some of these used oils are also sold as a counterfeit lubricant.
  Small industries often procure used oil from independent collectors for application as a fuel in burners and furnaces. And in some cases, commercial truck divers or large truck owners procure used oil for counterfeiting in their vehicles to save money. However, these practices are banned in India as per the Hazardous Waste Material rule 2016.
Large re-refiners generally have a fleet of trucks for the collection and transportation of the used oil to their facilities. Re-refiners also use the transport companies specializing in handling of hazardous waste for transporting used oil from the site to the facility intended for re-refining. Small re-refiners usually transport the used oil in large drums or barrels.

## Slide 153: Used Oil Disposal
It becomes difficult to monitor how each car/two-wheeler workshop collects and discards automotive used oils, as the number of such workshops present in the country is huge.
  Mechanics know that the used oil drained from vehicles possesses value and, hence, they do not dispose of it. They resort to either selling the used oil to re-refiners or selling the used oils as lubricants in the black market.
  Authorized service workshops of original equipment manufacturers (OEMs) such as Maruti Suzuki store the used oil and arrange an auction for sale to a re-refiner/trader. In small towns or cities, OEM workshops generally sell used oil to local vendors or scrap dealers who further sell used oil to industries for application as fuel.
  Large workshops organize the auction based on the instruction given by the OEMs. The auction is open to all the re-refiners and traders authorized by the SPCBs and happens several times in a year when sufficient quantity of used oil is available.
  OEMs either direct the workshop to organize an auction or sell the used oil to either a re-refiner or a trader depending upon its policy. Most OEM workshops usually have a long-term contract with a re-refiner or a trader.
In the industrial segment, the inadequate disposal of used lubricants is less common than in the automotive segment, as regulatory bodies have tighter control over industries. Further, industries will have to pay heavy penalties if they dump the used oil and contaminate the environment.
  The CPCB and the SPCBs have authorized used oil collectors and re-refiners to collect and refine used oil. Hence, when the companies change their lubricants, they store the used oil in large barrels/drums and auction it to re-refiners.
The industrial segment in India is divided between state-owned companies and private sector companies. There are similarities and differences in the way used oil is handled by these two types of companies, as explained below.
In the government sector, e-auctions are conducted by MSTC Limited, which is a Mini Ratna Category I Public Sector Undertaking (PSU) under the administrative control of Ministry of Steel, Government of India.
  The company is one of the leading PSU entities engaged in the provision of services such as e-auction/e-sale and e-procurement services. It organizes e-auctions for commodities such as used/waste oil, scrap plastic, aluminum, brass, cables, electrical/electronic items, and engine assemblies. The company partners with various government agencies and ministries in conducting the e-auctions.
Chart: USED OIL DISPOSAL IN COUNTRY, 2020
| Fuel | Re-refined | All other-a
Sales | 0.67 | 0.14 | 0.19
Total: 752.8 Kilotonnes
a- Includes regeneration of used oil to lubricant by removing some impurities, land filling and other disposal methods.

## Slide 154: Used Oil Re-Refining
According to CPCB, in 2019, there are 556 authorized facilities handling used/waste oil in India.
  The re-refiners bear the responsibility of collection and transportation of the used oil, which is subsequently processed and eventually sold in the domestic market.
  The re-refining quality varies with each re-refiner and depends upon the type of process used by the facility to re-refine the used oil. Modern re-refiners usually produce a high volume of basestocks, while the old and smaller re-refiners have lower yields.
  Small scale re-refiners often treat the used oil through simple processes such as filtration to remove impurities as well as water and sell the filtrate used oil as their product. Some of these re-refiners sell the filtrate product as fuel, while some supply it to the local market where it is sold as a lubricant.
Re-refiners believe that the used oil market in India shall benefit from the introduction of Extended Producer Responsibility (EPR), wherein the producer upholds the responsibility of ensuring that the used oil is re-refined and not utilized for any malpractices.
  Countries such as Spain have the Spanish Used Oil Management Act (Royal Decree 679/2006, of June 2) in place; it mandates EPR in used oil management. Spain also has an integrated management system, SIGAUS, in place for waste oil collection and subsequent treatment of used oil generated from industrial and automotive sources. This enforces industrial manufacturers to guarantee and finance the amount of used oil in proportion to the volume of new oil brought into the market, which ensures correct management of used oils by the lubricant manufacturers.
Currently, India has EPR in place only for plastic waste and e-waste management. If EPR is enforced upon the OMCs, the re-refiners can play the role of a producer responsibility organization (PRO). The role of a PRO in the case of used oil would include but not limited to organizing collection mechanisms for used oil, arrangement of logistics, ensuring that the used oil is treated using EST, etc.
At present, there is no accountability for the collection of used oil in the Indian market, which leads to fervent malpractices such as blending with solvents to be ultimately expended as fuel or refilling old lubricant bottles or in new packaging similar to the original lubricant brand only to be sold as counterfeit lubricant on the black market. This has led to a small amount of used oil reaching to re-refiners.
  Also, in states such as Mizoram, Meghalaya, and union territories such as Lakshadweep, there are no industrial areas. Used oil is generated from the workshops and diesel generators, which is collected by local business owners such as furniture workshops for use as lubricants in their machines and not reaching re-refiners. Therefore, implementation of EPR and enforcement of regulations for proper disposal of used oil will help in increasing the supply of used oil reaching re-refiners.
  Re-refiners express concern about the cheap re-refined basestocks being imported to India from foreign countries, especially from the Gulf region as it is free to import and is not restricted by the government. The lower price of imported re-refined basestocks makes it difficult for Indian re-refiners to compete in the market, leading to the shutting down of small re-refineries.
Continued…

## Slide 155: Used Oil Re-Refining
According to CPCB, India has 176 registered waste oil and 370 used oil re-refiner/reprocessors with installed used oil feed capacity of 1,674.9 kilotonnes in 2019. However, nearly 205 kilotonnes of used oil re-refined/reprocessed/regenerated by re-refiners in 2019, representing only 12% of their total capacity.
In 2020, it is estimated that 95.4 kilotonnes of used oil was re-refined to produce around 60 kilotonnes of re-refined basestocks.
  The volume of used oil re-refining into basestocks declined in 2020 as compared to 2018 due to closure of re-refineries in 2019 and 2020. For instance, refineries such as Southern Refineries and Tanu Petrochemical Products have not been producing basestocks since 2019. Also, in 2020, Century Refineries stopped their production of basestocks due to low used oil feedstock supply. It is not clear if the closure is temporary or permanent.
  The large share of used oil is used as fuel. A significant portion is either regenerated or mixed with SKO to be used in place of LDO.
Major lubricant blenders in India do not prefer to use re-refined basestocks for lubricant production, as they consider re-refined basestocks to be of inferior quality as opposed to virgin basestocks. No regulation in India forces the lubricant blending companies to use re-refined basestocks. This translates to low demand for re-refined basestocks among the major lubricant blenders in India.
  The demand for re-refined basestocks can only increase, provided the government enforces the companies to use the re-refined basestocks to manufacture lubricants. Such a move by the government shall help increase the production of re-refined basestocks in the country. In this context, Indian government mandates the use of 25% of re-refined basestocks for public sector OMCs by 2023.
  In 2018, HPCL invited expression of interest (EoI) on behalf of the public sector OMCs. The three companies including IOCL, BPCL, and HPCL decided on recruiting consultants to set up used oil collection centers across India.
  For instance, in April 2021, IOCL launched e-tender for procurement of re-refined Group I SN500 basestock for producing lubricants. The finalization of tender is in process as of now.
MAJOR USED OIL RE-REFINERS IN INDIA, KILOTONS, 2020 |  |  | 
COMPANY | LOCATION | USED OIL/WASTE OIL FEED CAPACITY | BASE STOCK CAPACITY- a
Tanu Petrochemical Products-b | A. Pradesh | 32.5 | 21.2
Lucky Oil Company | Andhra Pradesh | 23.3 | 15.1
Mangalam Lubricants (P) Ltd | Jharkhand | 21.8 | 14.2
Jawrawala Petroleum | Gujrat | 15.2 | 9.9
APJ Refinery Pvt. Ltd. | Kerala | 14.6 | 9.5
Universal Hydrolubes | Haryana | 14.4 | 9.4
Continental Petroleum Limited | Rajasthan | 11.5 | 7.5
Mazda Industrol | Uttar Pradesh | 10.0 | 6.5
Bharat Oil Company | Uttar Pradesh | 10.0 | 3.9
Century Refineries-b | Karnataka | 9.0 | 5.9
Southern Refineries-b | Kerala | 7.3 | 4.7
Cee Jee Lubricants | Kerala | 7.2 | 4.7
IFP Petro Products (P) Ltd. | Gujrat | 6.0 | 3.9
Trimurti Enterprises | Maharashtra | 1.0 | 0.7
Total |  | 183.8- c | 117.1-c
a- Re-refined basestocks capacity has been estimated after assuming a 63% yield rate for all the re-refineries. b- Not operating currently. c- The table shows used oil feed capacity of few selected re-refiners and not all re-refiners in India. In addition to these, there are 357 used oil re-refiners/reprocessor authorized facilities in the country with the total used oil feed capacity of 1491.0 kilotonnes. However, there basestocks capacity is unknow as they are also engaged in re-reprocessing of used oil. Note: The used oil feedstock capacity of re-refiners is taken from CPCB report on national inventory on Generation and Management of Hazardous and Other Wastes, 2019-20. It is considered that there is no change in the used oil feedstock capacity of re-refiners/reprocessors in 2020. |  |  | 
Continued…

## Slide 156: Used Oil Re-Refining
Re-refiners in developed countries such as the United States and the European Union produce both Group I and Group II basestocks, while Indian re-refiners only produce re-refined Group I basestocks. Re-refined Group II basestocks are produced using the hydrotreating process, while Group I basestocks are made with the aid of solvent refining. Hydrotreating is a sophisticated process compared to solvent refining and therefore requires higher initial capital investment.
  Most of the re-refiners in India are small- to medium-sized businesses and cannot make the investment needed to employ the hydrotreating process for re-refining and producing re-refined Group II basestocks. As a result, only re-refined Group I basestocks are produced in India.
  The outbreak of COVID 19 has severely impacted businesses of small and medium scale refiners; however, large refiners managed to sustain during this period. Limited supply of used oil due to halt in the manufacturing industries and low generation from automotive segment pushed small and medium scale refiner to operate in reduce production rate and low marginal profits. This has led to closures of several refining facility across the country.
Re-refined basestocks are either supplied to blenders, who use it to blend lubricants and sell them to industries, or to re-refiners that manufacture lubricants under their own brand name and sell those in the open market. Mangalam Lubricants is one such re-refiner that produce re-refined basestocks and use it to manufacture its own lubricant brand, Mangol, catering to both automotive and industrial end users.
  The company is also trying to supply re-refined basestocks to OMCs for producing lubricants. In June 2021, Mangalam Lubricants, bid for e-tender release by IOC for supply of re-refined Group I SN500 Basestocks. The finalization of tender is in process as of now.
In certain instances, the re-refiner procures used oil from an industrial facility, re-refines it into basestocks, and then blends the re-refined basestocks into lubricant. This lubricant is then supplied to the same facility from where used oil was sourced. The re-refiners often claim that lubricants made from re-refined basestocks are equivalent to those manufactured from virgin basestocks.
Currently, in India, re-refiners use CPCB approved environmentally sound technologies such as Vacuum distillation with clay treatment, Vacuum distillation with hydrotreating, and film evaporation process for the production basestock or re-refined lubricants.
The pricing of re-refine basestock is majorly based on landed cost of used oil, processing cost, and recovery rate or recovery loses during the production and taxes on final product.
Large re-refiners sell their re-refined basestocks through tenders. Once allocation of tender is completed purchase order is placed by the blender mentioning the quantity of basestocks needed. After that, call off order is placed by the blender for final approval of purchase.
Small re-refiners engaged in the regeneration re-refined lubricants generally follow the close loop for selling their product and sell it those industries from where they procure used oil on contract basis.

## Slide 157: IFP Petro Products
IFP Petro Products (P) Ltd.
IFP was founded in 1977 in a technical collaboration with Indian Institute of Petroleum (IIP), Dehradun and is located in Ghaziabad, Uttar Pradesh.
The company engaged in used oil collection and re-refining process. Used oil collection is done from both industrial and automotive segment.
It has the laurel of being the first used oil re-refining unit in northern India. Its re-refining unit is also approved by the Ministry of Petroleum and Ministry of Environment.
The company has a registered re-refining capacity of 6,000 metric tonnes per annum for used/waste oil approved by the Uttar Pradesh State Pollution Control Board (UPSPCB).
The company produces re-refined Group I basestocks by employing the process of three-stage vacuum distillation with solvent extraction.
It follows open loop refining process and sell their basestocks to blenders for producing lubricants. The company also produces re-refined lubricants for industry.
PRODUCT PORTFOLIO | 
PRODUCT/BRAND | APPLICATION
Re-refined base oil | Used as raw material in production of re-refined lubricants
Re-refined industrial and automotive lubricants | Used for industrial and automotive application
STRENGTHS | OPPORTUNITIES
Strong presence in the market for more than four decades with 150 plus lubricant retail outlet in the country Tie-up with large oil marketing companies to provide re-refined basestocks and re-refined lubricants Diverse product portfolio include contract packaging, basestocks, and lubricants such as hydraulic fluids, gear oil, and transformer oil. Technical collaboration with Indian Institute of Petroleum (IIP), Dehradun for providing professional, technical and QC services to its customers. | Rising inclination of OMCs toward the usages of re-refined basestocks for reducing their carbon footprints will offer an opportunity to the company to build their relations with major OMCs as a supplier of re-refined basestocks and helps in gaining organic growth in the coming future.
WEAKNESSES | THREATS
No proper used oil collection centers Limited collection of used oil for re-refining. Technological constraint for production of re-refined Group II and III basestocks. | Stringency of green house emissions regulations coupled with continuously growing demand for higher grade basestocks is becoming a major threat for the company as growth in demand of Group I basestocks slowdown.

## Slide 158: Mangalam Lubricants
Mangalam Lubricants
Mangalam Lubricants is one of the largest re-refiners in India and was established in 1978. The company is in Ranchi, Jharkhand and bears the ISO 9001:2008 certification.
The company is authorized by the Jharkhand State Pollution Control Board (JSPCB) to recycle 16,000 kiloliters per annum of used oil.
The unit makes use of Wiped Film Evaporation Technology. The company sells its own lubricants under the brand name Mangol, some of which is made from re-refined basestocks. It sells automotive lubricants, gear oils, coolants, industrial lubricants, and lubricants for agricultural purposes under the Mangol brand.
The company also offers consultancy for green field used oil re-refining projects
The company might upgrade to an API Group II basestocks plant in the future, as it is exploring options for upgrading.
PRODUCT PORTFOLIO | 
PRODUCT/BRAND | APPLICATION
Regenerated Transformer Oils | Used for industrial applications
Regenerated Gear Oils | Used for both industrial and automotive application
Regenerated Engine Oils | Used for both industrial and automotive application
STRENGTHS | WEAKNESSES
One of the leading re-refiners and blenders in the eastern India with more than 16000 Kiloliter re-refining capacity of used oil. Strong client base across the country. | Due to the low collection rate operation is major concentrated in the Jharkhand region, limiting the growth of the company.
OPPORTUNITIES | THREATS
Government compelling OMC’s for using re-refined baseoil for production lubricants is expected to increase the demand for refined basetock and offer growth opportunity to the company. Limited large-scale re-refiner in the region is expected to offer opportunity to acquire large market share in the coming years. | Stringency of green house emissions regulations coupled with continuously growing demand for higher grade basestock is becoming a major threat for the company as demand of Group I base oil is continuously shrinking.

## Slide 159: Bharat Oil Company
Bharat Oil Company
Bharat Oil was established in 1965 and is located in Ghaziabad, Uttar Pradesh. The company is engaged in offering complete solutions in waste testing, tracking and management. The company provides waste management solutions for hazardous wastes, electrical & electronic waste management service, recycling/re-refining used lube oil, laboratory testing, waste management & tracking enterprise software and technology Solutions.
The company provided re-refined lubricant for both industrial and automotive segment
The company has approved licensed for used oil re-refining from Ministry of Petroleum & Natural Gas, the CPCB, and the Uttar Pradesh Pollution Control Board (UPSPCB).
The company also has license for secured landfill, hazardous waste incinerator, and for operating laboratory / TSDF from the UPSPCB and Ministry of Environment, Forest and Climate Change.
The UPSPCB has authorized the company to handle 10 kiloliters of used/waste oil per annum. The facility makes use of thin-film vacuum technology for refining the used oil. It is also known to have a storage capacity of 2 million liters or 1.8 kilotonnes.
PRODUCT PORTFOLIO | 
PRODUCT/BRAND | DESCRIPTION/APPLICATION
Re-refined automotive lubricants | It offers re-refined gear oil, engine oil, grease and coolants for automotive applications
Re-refined industrial lubricants | It offers re-refined cutting oil, hydraulic oil transformer oil, compression oil for industrial applications
STRENGTHS | WEAKNESSES
Broad range of service offerings including safe Hazardous waste management service, electrical & electronic waste management service, recycling/re-refining used lube oil, laboratory testing, Complete Technology (Software, Hardware, Cloud or SaaS) Solutions for Waste Management and Tracking. | Limited reach to outside the UP state due to less operational capacity. Only re-refined Group I basestocks is produced by the company due to technological constraint.
OPPORTUNITIES | THREATS
Regulation authorities are continuously engaged in improving the enforcement of regulations in the market and are also proposing EPRs for used oil generators for proper disposal of used oil and for OMCs for usage of re-refined baseoil for production of lubricants. This will lead to proper used oil collection and rise in the demand for re-refine baseoil in the country. | Growing adulteration of used oil, waste oil or hazardous waste by generators to capture more revenue particularly in the outer NCR region and rural area of the state due to low enforcement of regulations is reducing the collection rate of used oil for refining purpose.

## Slide 160: Re-Refined Lubricants
Re-refined lubricants amount to a negligible share in the overall lubricant market in India.
  End users possess no awareness with respect to the uses and advantages of lubricants manufactured from re-refined basestocks.
  Consumers perceive lubricants manufactured from re-refined basestocks to be of inferior quality.
  Many customers in India are driven by the brand of the lubricant, which further hurts the re-refined lubricants market prospects.
Indian OMCs do not prefer to utilize re-refined basestocks in the lubricants they manufacture, as they believe re-refined basestocks to be inferior in quality to the virgin basestocks. However, due to the growing awareness of circular economy and to decrease dependency from the import of used oil, OMCs are now shifting toward application of re-refined basestocks in the production of lubricants.
  Similarly, other oil marketing companies with their presence in India such as IOCL, BPCL and HPCL are also seeking to explore the opportunity to gain organic growth and reduce their carbon footprint by using re-refined basestock in the production of their lubricants. For instance, in April 2021, IOCL launched e-tender for procurement of re-refined Group I SN500 basestock for producing lubricants.
Generally, large oil marketing companies adopt way to approach to sell the re-refined lubricants to the end users. They either sell their re-refined lubricant to the factories from where used oil was procured on the contract basis or mixed limited proportional of re-refine basestock in larger virgin basestock pool for production of lubricants and then sell re-refined lubricants under their brand name. Whereas small refiner sell their re-refined lubricant under local brand or often unbranded directly to end users of factories or automotive workshops.

## Slide 161: Finished Lubricant Market Outlook
Kline & Company forecasts that the total demand for finished lubricants (including process oils) in India will augment from 2,516.7 kilotonnes in 2020 to 3,133.5 kilotonnes in 2030.
Consumer automotive lubricants segment is anticipated to witness the highest growth among all the three segments propelled by a demand for consumer automotive vehicles during the forecast period, 2020 to 2030.
The consumer vehicles sales declined in 2020 due to lockdown and mobility restrictions introduced to control the spread of COVID-19. In addition, consumer preference has shifted toward using personal vehicles instead of public transportation for commute. This would certainly support the growth of passenger vehicles and two-wheelers in the overall parc over the forecast period.
Commercial lubricant demand is projected to grow at a CAGR of 3.1% during 2020-2025 supported by growing demand for off-highway vehicles in mining and construction including infrastructure projects in the country.
Strong growth in logistic sector coupled with increasing output of agriculture industry will also support increased demand for lubricants in the commercial segment in the coming years.
Introduction of BS-VI norms and scrappage policy is expected to support growth of new vehicles in the country. This will result in increased demand for lower viscosity grades in the consumer and commercial segments over the forecast period.
Industrial expected to be the largest segment in the lubricant market over the forecast period supported by growing demand for Refrigeration oils, MWFs, GIOs from steel and aluminum manufacturing plants, and automotive manufacturing facilities.
Chart: PROJECTED FINISHED LUBRICANT MARKET IN INDIA, 2020-2030
| Industrial | Commercial | Consumer
2020 | 1383.9 | 724.2 | 408.6
2021 | 1420.6 | 748.8 | 424.9
2025 | 1574.9 | 854.2 | 497.2
2030 | 1678.4 | 913.2 | 541.9

## Slide 162: Used Oil Industry Outlook 2025
In the next five years, the used oil market is expected to witness moderate growth.
  No stringent steps has been announced by the CPCB as well as the SPCBs to enforce collection of used oil and using it for re-refining instead of its use as an industrial fuel. Therefore, it is expected that there would be no major changes in the handling of used oil, especially in the retail market, and will remain informal and unstructured. As a result, majority of used oil is expected to continue to be used as fuel or is used to make adulterated fuels and lubes.
  However, with OMCs such as IOCL looking to use re-refined basestocks (based on the e-tender issued in April 2021), it can be expected that the re-refining of used oil will grow in the future.
  With transition toward BS-VI engines and shift toward lighter viscosity grade of automotive lubricants will reduce the lubricant losses and is expected to increase the generation rate of used oil to 48%, which would amount to 1,404.6 kilotonnes by 2025.
The collection rate is expected about to grow to 66%, which translates to 927 kilotonnes by 2025. This is because re-refiners are planning to set up used lubricating oil centers across the country to not only increase used oil collection but also ensure quality of used oil collected. This is expected to increase the collection rate in the future.
Used oil re-refining is expected to grow moderately as more public sector OMCs such as HPCL and BPCL are expected to follow IOCL to use re-refined basestocks.
The Indian government has passed a mandate for OMCs to use 25% of re-refined basestocks for the producing lubricants by 2023. In case, these targets are met then re-refining could experience huge growth in the next one to two years (faster than anticipated currently).
The public sector OMCs and few re-refiners are continuously working under the circular economy.
  There is a technical committee constituted by NITI Aayog, on behalf of the Ministry of Petroleum and Natural Gas, where the major OMCs and members of technical committee are working together to organize the used oil management.
  The Committee plans to bring generators of used oil under the purview of extended producer responsibility rules to ensure that higher volume of used oil reaches re-refiners. However, this process may take few years, so no significant change is expected in the market till 2025.
Chart: USED OIL GENERATION, 2025
| Used oil generated | Lubricant lost
Sales | 0.48 | 0.52
Total: 2,926.3 Kilotonnes
Chart: USED OIL COLLECTION, 2025
| Collected | Not collected
Sales | 0.66 | 0.34
Chart: USED OIL DISPOSAL, 2025
| Fuel | Re-refined | All other-a
Sales | 0.65 | 0.16 | 0.19
Chart: USED OIL RE-REFINING, 2025
| Basestock | All other
Sales | 0.63 | 0.37
Total: 1,404.6 Kilotonnes
Total: 927 Kilotonnes
Total: 148.3 Kilotonnes
a- Includes regeneration of used oil to lubricant by removing some impurities, land filling and other disposal methods.

## Slide 163: Used Oil Industry Outlook 2030
Total: 3,133.5 Kilotonnes
Total: 1,535.4 Kilotonnes
Total: 1,044.1 Kilotonnes
Total: 185.7 Kilotonnes
Chart: USED OIL GENERATION, 2030
| Used oil generated | Lubricant lost
Sales | 0.49 | 0.51
Chart: USED OIL COLLECTION, 2030
| Collected | Not collected
Sales | 0.68 | 0.32
Chart: USED OIL DISPOSAL, 2030
| Fuel | Re-refined | All other-a
Sales | 0.66 | 0.18 | 0.16
Chart: USED OIL RE-REFINING, 2030
| Basestock | All other
Sales | 0.63 | 0.37
By 2030, used oil generation rate is expected to reached at 49%, with advent of better engines technology and increasing penetration of synthetic lubricant oil in the automotive segment.
Collection rate is expected to grow to 68% of total used oil generated. Thus, used oil collection is expected to grow to 1,044.1 kilotonnes by 2030.
Re-refining of used oil to produce re-refined basestocks is expected to grow as more OMCs use re-refined basestocks and EPR scheme is implemented. However, this depends upon the experience of OMCs with re-refined basestocks and implementation of EPR scheme.
Further, the Indian government has passed a mandate for OMCs to use 25% of re-refined basestocks for the producing lubricants by 2023. In case, these targets are met then re-refining could experience huge growth by 2030 (faster than anticipated currently).
However, in case, the experience of OMCs is poor and the EPR scheme is not implemented effectively, the re-refining is expected to remain low.
a- Includes regeneration of used oil to lubricant by removing some impurities, land filling and other disposal methods.

## Slide 164: Re-Refined Basestock Capacity Outlook
In 2020, several small- and large-scale re-refiners such as Century Refineries Pvt. Ltd., Southern Refineries Ltd. and Tanu Petrochem Products Pvt. Ltd shut down their facility due to the limited supply of used oil in 2019 and 2020.
  In 2021, the used oil feed capacity and re-refined basestock capacity of re-refiners is expected to remain same as 2020. There is no information regarding the resumption of re-refined basestocks production by Century Refineries Pvt. Ltd., Southern Refineries Ltd. and Tanu Petrochem Products Pvt. Ltd in 2021. However, they may resume in the future.
  Currently, no plans have been announced by re-refiners to expand the existing re-refining capacity. This is because re-refiners continue to operate at low-capacity rate as due to low supply of used oil. As a result, it is expected that there will be no capacity expansion of existing re-refining capacity or addition of new re-refining capacity in the next five to 10 years.
In India, only Group I basestocks is produced by re-refiners in 2020.
  As demand for Group II and III basestocks grow, re-refiners are expected to upgrade themselves to produce Group II re-refined basestocks, However, due to technological constraints, currently, there is no plan for upgradation.
RE-REFINED BASESTOCK CAPACITY, KILOTONS, 2020, 2021, 2025, AND 2030-a |  |  |  | 
COMPANY | 2020 | 2021 | 2025 | 2030
Tanu Petrochemical Products-b | 21.2 | 21.2 | 21.2 | 21.2
Lucky Oil Company | 15.1 | 15.1 | 15.1 | 15.1
Mangalam Lubricants (P) Ltd | 14.2 | 14.2 | 14.2 | 14.2
Jawrawala Petroleum | 9.9 | 9.9 | 9.9 | 9.9
APJ Refinery Pvt. Ltd. | 9.5 | 9.5 | 9.5 | 9.5
Universal Hydrolubes | 9.4 | 9.4 | 9.4 | 9.4
Continental Petroleum Limited | 7.5 | 7.5 | 7.5 | 7.5
Mazda Industrol | 6.5 | 6.5 | 6.5 | 6.5
Bharat Oil Company | 3.9 | 3.9 | 3.9 | 3.9
Century Refineries-b | 5.9 | 5.9 | 5.9 | 5.9
Southern Refineries-b | 4.7 | 4.7 | 4.7 | 4.7
Cee Jee Lubricants | 4.7 | 4.7 | 4.7 | 4.7
IFP Petro Products (P) Ltd. | 3.9 | 3.9 | 3.9 | 3.9
Trimurti Enterprises | 0.7 | 0.7 | 0.7 | 0.7
Total | 117.1-c | 117.1-c | 117.1-c | 117.1-c
a- Re-refined basestocks capacity has been estimated after assuming a 63% yield rate for all the re-refineries. b- Not operating currently, however, may resume in the future. c- The table shows used oil feed capacity of few selected re-refiners and not all re-refiners in India. In addition to these, there are 357 used oil re-refiners/reprocessor authorized facilities in the country with the total used oil feed capacity of 1491.0 kilotonnes. However, there basestocks capacity is unknow as they are also engaged in reprocessing of used oil. Note: The used oil feedstock capacity of re-refiners is taken from CPCB report on national inventory on Generation and Management of Hazardous and Other Wastes, 2019-20. It is considered that there is no change in the used oil feedstock capacity of re-refiners/reprocessors. |  |  |  | 

## Slide 165: Market Evaluation
Opportunities
Presently, the market is highly unorganized and informal due to presence of large number of small players in the market. However, large refiners and government authorities are focusing on making it more organized by implementing EPR scheme for used oil generators as well as re-refiners that will help in the growth of re-refining in India in the future.
Public sector OMCs such as IOCL, HPCL, and BPCL are focusing on circular economy in the used oil market and are trying to increase usage of re-refined basestocks to produce lubricants.
  The Indian government has passed a mandate for OMCs to use 25% of re-refined basestocks for the producing lubricants by 2023.
  Also, used oil technology solutions committee, set up by NITI Aayog on behalf of Ministry of Petroleum and Natural Gas, to set EPR scheme for using certain amount of re-refined lubricants and proper disposal of used oil.
  This will provide an opportunity to re-refiners to attend better economy of scale by maintain proper collection, sufficient supply and higher demand of their final product.
Challenges
The proper enforcement of regulations and awareness of proper disposal of used oil are among the major challenges in the market.
  The government has been mulling over making better used oil collection system, however, it has not taken any concrete steps. People still denounce used oil, and it is commonly termed “kaala tel,” which translates to “black oil.”
The unorganized and fragmented nature of the market, leading to misuse of used oil in the form of industrial fuel. This results in low availability of the oil to re-refiners which are struggling to break even.
Further, re-refiners in India are facing a huge supply deficit of used oil due to mishandling of used oil by generators and intermediators such as kabadi walas (waste collectors), traders which generally dump collected used oil in black market. This has resulted in the lower re-refined basestock capacity utilization by re-refiners.
Other challenges include lubricant blenders who usually do not prefer to use re-refined basestocks for lubricant production, as they consider re-refined basestocks to be of inferior quality as opposed to virgin basestocks. This has led to low demand for re-refined basestocks in the country. However, if EPR scheme is rolled out, it is expected that demand for re-refined basestocks will increase.

## Slide 166
Mexico

## Slide 167: Mexico Market Synopsis
Chart: USED OIL MATERIAL BALANCE IN MEXICO, 2021-2030 (MILLION TONS)
| Finished Lube Demand | Used Oil Generated | Used Oil Collected | Used Oil Re-refined | RRBO produced
2021 | 689.2 | 383.8 | 237.6 | 2.5 | 1.5
2025 | 928.3 | 557 | 356.5 | 7.1 | 4.3
2030 | 1024.3 | 614.6 | 393.3 | 7.9 | 4.7
Used Oil Regulations
The key used oil regulation in Mexico are General Law on Ecological Equilibrium and Environmental Protection 1988 (LGEEPA) and General Law on the Prevention and Comprehensive Management of Waste (Ley General para la Prevencion y Gestion Integral de los Residuos, LGPGIR).
Environmental regulations are issued at the federal, the state, and the municipal levels. The regulations by the state and the municipalities are based on the federal regulations.
In Mexico, under the LGPGIR, are the Mexican Official Norms (NOMs) and the Mexican Norms (NMX). It is important to note that the NOMs must be complied with while the NMX are voluntary in nature.
Used Oil Material Balance
In 2021, used oil generation increased by around 7.7%, which is similar to increase in lubricant demand in 2021.
COVID-19 did not have any impact on used oil collection volume in Mexico. The used oil volume collected has increased by around 2%-3% in the last two years. This is due to the increase in the interest of used oil market, especially its usage as fuel by various industries.
Used oil is mainly disposed as fuel (85%) in Mexico. Remaining 15% is mostly disposed as additive on asphalt formulations for road construction or burn material in cement industries with very small volume for re-refining.
Used oil disposal is not expected to change during the forecast period. Disposal as fuel will remain the main method.
Used Oil Re-refining
Mexico has very small base for re-refining. EYL and Bravo Energy has some re-refining capacity but the exact capacity is not clear.
Mexico only produces Group I re-refined basestocks.
The re-refining capacity is not expected to grow during the forecast period due to low demand for re-refined basestocks in the country.
Further, fuel is a more profitable way of disposing used oil in Mexico. This is another reason for low re-refining capacity in the country.
Opportunities
Mexican used oil market is gaining momentum, mainly due to the valorization of subproducts like diesel for industries and MGO.
Demand of used lubricants on the northern countries for processing is a window of opportunity for generators and collectors. There are some collectors already present that export hazardous residues.
Challenges
Even though used oils are regulated from generation to processing, stricter implementation is needed to tackle black marketing or ensure traceability of used oil.
Re-refining for basestock manufacturing is not prevalent in Mexico. Only one company in Mexico, EyL, re-refines used oil. EYL does it at small scale as the market is very small for re-refined basestocks in Mexico. Earlier, Bravo Energy re-refined basestocks, however, due to COVID-19, they have stopped re-refining used oil as it was not profitable.

## Slide 168: Economic Background
SELECTED ECONOMIC CHARACTERISTICS OF MEXICO, 2020 AND 2021 |  | 
KEY INDICATOR | 2020 | 2021
Population (Million) | 127.8 | 129.0
GDP at current prices (USD billion) | 1073.9 | 1285.5
GDP per capita, current prices (USD) | 8,403.60 | 9967.4
GDP growth rate, constant prices (annual % change) | -8.3 | 6.2
Inflation, average consumer prices (annual % change) | 3.4 | 5.4
Current account balance (% of GDP) | 2.5 | 0.03
Share in Real GDP-a |  | 
Services (%) | 66.5 | 66.5
Industry (%) | 29.6 | 29.6
Agriculture (%) | 3.4 | 3.4
Source: CIA World Factbook, International Monetary Fund World Economic Outlook 2021 a- Kline estimations based on 2017 data |  | 
Mexico had a population of 127.8 million in 2020. The country is the 15th largest economy in the world and the second largest economy in Latin America. The Mexican economy is highly dependent on exports to its northern neighbor United States (U.S.), its largest trading partner.
The International Monetary Fund (IMF) estimated a GDP contraction of 8.2% in 2020 due to the outbreak of COVID-19. The economic recovery is expected from 2021 onwards. The International Monetary Fund (IMF) predicted a GDP growth of 5% in 2021.
Continued…

## Slide 169: Economic Background
The Mexican society is characterized by a big wealth gap in its population. Despite the challenges it faces as a developing country, Mexico is one of the main economies and political forces in Latin America. The country has a dynamic industrial and services sector along with vast mineral resources.
In 2018, a new government was elected, which is headed by President Andres Manuel López Obrador (AMLO). The current government is strong on anti-corruption measures, and wants to implement nationalistic economic policies, starting with the reversal of the previous government’s education and energy reforms.
The Mexican economy is currently recovering from its steepest recession in decades. The key challenges for the country are raising productivity and tackling poverty.
The key public-private investments in infrastructure and technology have the potential to boost economic growth in the country. Digitalization across a variety of industries, notably energy and banking, should help Mexico to address structural vulnerabilities and procure benefits of global economic trends. At the same time, targeting the unbanked segment of the population and taking advantage of fresh demand for lithium and other minerals will generate further growth opportunities.
Currently, Mexico has 23 preferential trade agreements with different countries/blocks in force. Foreign direct investment is permitted in most of the sectors, but certain key sectors such as mining for metals like lithium are still reserved for the state.
As the pandemic hit the country, the Mexican administration acted differently from many countries in Latin America. Mexico did not implement stringent measures as number of cases rose. However, lockdown was implemented eventually with March to May 2020 being the strictest months. It is believed that the absence of an early comprehensive response to COVID-19 led to Mexico recording the fourth-highest death toll as of mid-June 2021 in the world.
Mexico implemented fiscally restrained adjustments in response to the pandemic. The country focused on monetary policy and the redistribution of federal budgets, avoiding new loans from multilateral institutions such as the IMF. In April 2020, the federal government announced fiscal austerity reforms, under which up to 75% of the available general budget would not be spent.
The country has maintained an open border policy to sustain the economic benefits of tourism, manufacturing, and trade. The open border policy allowed Mexico to become the third-most visited country in the world in 2020. Service industry is the largest sector that accounts for more than 60% of the national GDP.
By the end of 2021, manufacturing and exports are expected to reach above pre-pandemic levels. Services are re-opening, and unemployment is declining. However, the pandemic has taken a severe toll on the country as poverty has increased even further. The strong US growth will help the economy to rebound faster and presents an opportunity to implement policies to achieve fast economic growth.
According to the World Economic Forum, Mexico’s GDP is not expected to return to pre-pandemic levels until 2023, largely due to the absence of substantial fiscal stimulus.

## Slide 170: Vehicle Population
Chart: VEHICLE SALES BY VEHICLE TYPE IN MEXICO, 2019-2021
| Passenger vehicles | Light trucks | Buses and Trucks | Tractor and construction vehicles
2019 | 2.9927 | 0.81833 | 0.082697 | 0.11945
2020 | 2.261 | 0.77915 | 0.059964 | 0.077109
2021 | 1.7478 | 0.77264 | 0.050979 | 0.083402
Million units
Chart: VEHICLE REGISTRED IN MEXICO, 2018-2020
| Passenger vehicles | Commercial vehicles-a | Two-wheelers
2018 | 32.2901 | 11.4137 | 4.0802
2019 | 33.6036 | 11.4765 | 4.7896
2020 | 33.988 | 11.0986 | 5.261
Million units
In 2019, the total vehicle population, or total number of registered vehicles, increased by 4.4% to reach 49.8 million vehicles in Mexico. However, in 2020, due to the COVID-19 pandemic, the number of vehicles registered only increased by 1% in Mexico.
  Passenger vehicles is the largest segment in the automotive industry in Mexico. The total number of registered vehicles increased by 4.1% and 1.1% in 2019 and 2020, respectively.
  Commercial vehicles that include autobuses and commercial fleets, represent 22% of the vehicles registered in 2020. The total number of registered commercial vehicles declined by 3.3% in 2020.
  Two-wheelers is the fastest growing vehicle type in Mexico. It accounts for 10% of total number of vehicles registered in Mexico. The number of motorcycles registered increased by 9.8% in 2020.
In Mexico, the average age of a car is 12 years. The country has approximately 3,000 dealerships.
In Mexico, overall vehicle sales decreased by 28.5% in 2020. The segment that decreased the most was tractors and construction vehicles, followed by buses and trucks.
From 2016 to 2020, 86,639 electric vehicles (EV) are registered in the country, with around 2% being fully electric. At least 1,000 EV charging stations are in the country. In 2020, 24,405 EVs were sold in the country.
The number of EV registered is quickly increasing, at a CAGR of 80% from 2016 to 2020. And it is expected to that EV would be 15% of the total car population by 2030.
Continued…

## Slide 171: Vehicle Population
Mexico is the sixth-largest global vehicle manufacturer, producing approximately 3.2 million units in 2020. 89% of vehicles produced in Mexico are exported. The US, accounting for 80% of total vehicles produced in Mexico, is the biggest export market for the Mexican automotive industry.
Audi, Baic Group, BMW, Stellantis (made up of FCA and PSA Group), Ford, General Motors, Honda, Kia, Mazda, Nissan, Toyota, and Volkswagen are the key automotive companies established in Mexico.
Largest producers of heavy-duty vehicles include Cummins, Detroit Diesel Allison, Freightliner–Daimler, Kenworth Mexicana, Mack Trucks de México, International-Navistar, Dina Camiones, Scania, Volvo Group VW, Man Truck & Bus, Mercedes-Benz, Hino Motors, and Isuzu Motors in Mexico.
Automotive manufacturers are concentrated in the northern region of the country, in states like Baja California, Sonora, Chihuahua, Coahuila, Nuevo León, and San Luis Potosí. The industry also has strong base in the central region including areas like Guanajuato, Aguascalientes, Jalisco, Estado de Mexico, Hidalgo, Morelos, Puebla, and Veracruz.
The vehicles production decreased by 20.8% in 2020 due to COVID-19 pandemic. And it is expected to shrink by 7.2% in 2021 due to chip's shortages.
Chart: VEHICLE PRODUCTION BY VEHICLE TYPE IN MEXICO, 2019-2021
| Passenger vehicles | Light trucks | Buses and Trucks | Tractor and construction vehicles
2019 | 1124.395 | 193.536 | 46.239 | 35.797
2020 | 794.652 | 155.411 | 29.673 | 21.824
2021 | 700.511 | 133.975 | 30.639 | 20.454
Thousand units
Electric vehicles are also expected to be produced in the near future in Mexico. Electric vehicles manufacturers are attracted to Mexico due to low wages, existing infrastructure, dense supply network, strategic location, educational system allowing supply of qualified technical workers. General Motors has already announced the investment of USD 1 billion for a plant expected to be commissioned by 2023.
However, there will be a need of strong investment to modernize the infrastructure. Additionally, the final decision will also be influenced by politics regarding battery mineral compounds such as lithium.

## Slide 172: Finished Lubricant Market
Chart: OVERALL LUBRICANT DEMAND BY SEGMENT IN MEXICO, 2020
| Consumer | Commercial | Industrial
Sales | 241.2 | 201.5 | 197.2
Total: 640.0 Kilotonnes
Chart: OVERALL LUBRICANT DEMAND BY PRODUCT TYPE IN MEXICO, 2020 AND 2021
| PCMO | HDMO | Process Oils | Metalworking fluids | Hydraulic fluids | All other-a
2020 | 176 | 97.4 | 51.7 | 44.9 | 40.7 | 229.3
2021 | 189.6 | 104.2 | 55.4 | 48.7 | 44.2 | 247.1
KT
In 2020, the overall lubricant demand in Mexico was estimated at 640.0 kilotonnes. The lubricant demand declined by around 24% in 2020. In 2019, the finished lubricants demand increased by 2.3%.
In 2020, the decline in finished lubricants demand was due to COVID-19 pandemic. The lubricant demand declined in all the three segments – commercial, consumer, and industrial – by around 24% in each segment.
The consumer segment was affected the most, due to low mobility and social distancing restrictions. In the largest cities, the work from home policy was applied for most of 2020 and continued in the first half of 2021. This reduced the traffic up to 60% in some cities leading to sharp decline in lubricant demand in the consumer segment.
Industrial activity was restricted to essential activities, during April and May 2020, leading to decline in the lubricant demand in the industrial segment. As the COVID-19 situation improved, the economy was opened; however, the recovery was slow due to which the lubricant demand could not recover fully.
Another aftermath of the COVID-19 crisis was the global chain supply disruptions that adversely impacted the lubricant demand in the commercial segment.

## Slide 173: Finished Lubricant Market and Lubricant Blenders
In Mexico, lubricants that are used are not of the latest specifications. Monogrades still have a significant share in the overall lubricant demand in the country. Furthermore, the newest PCMO and HDMO specifications are not widely used in the country, as a considerable part of the vehicle parc consists of old vehicles with average age of 12 years. As sales of new vehicle has slow growth in Mexico, demand of new engine oil standards progresses at moderate pace on the country.
Finished lubricants market is led by two international suppliers, ExxonMobil and Shell. Nevertheless, the Mexican firms: MexLub, Roshfrans, Raloy, Bardahl, and Lubral, together, also have 32% share in the lubricant market in Mexico. ExxonMobil is the largest seller, with a total estimated market share of 20%. It is strongest in the industrial segment and has 26% market share in this segment. On the other hand, Shell, that has 16% share in the lubricants market in Mexico, is strongest in the consumer segment and has 20% share in the segment.

## Slide 174: Regulations
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | No. However, the General Law for Prevention and Management of Waste (LGPGIR) defines hazardous waste, that includes used oils.
2. How is used oil classified i.e., hazardous waste, special waste etc.? | Hazardous waste
3. Are there any requirements on who can collect used oil? | Yes
4. Does country have an association(s) managing the collection and disposal of used oil? | No
5. Is a levy charged on sales of lubricants to support used oil collection associations? | No
6. Are there any requirements for how used oil generators manage used oil? | Yes
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | No
8. Do any requirements/legislation exist around different types of used oil? | No
9. Does the country have requirements or regulations regarding the export or import of used oil? | No
10. Does the country have any legislation that requires used oil to be re-refined? | No
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | Yes
Continued…

## Slide 175: Regulations
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | There is not extra regulations on the type of fuel burner emission.
14. Is used oil allowed to be placed in a landfill? |  | No
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | No
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | Yes
 | ii. Blending with crude oil at a refinery | Yes
 | iii. Dust suppressant | Yes
17. Are there companies/associations advocating in used oil category? |  | No
Continued…

## Slide 176: Regulations
Key Used Oil Regulations
In Mexico, the primary environmental law that frames all general legal national legislation on the subject is the General Law on Ecological Equilibrium and Environmental Protection 1988 (LGEEPA). This law, together with the General Law on the Prevention and Comprehensive Management of Waste (Ley General para la Prevencion y Gestion Integral de los Residuos, LGPGIR) are the main legal codes that frame the regulations for used oil management.
Environmental regulations are issued at the federal, the state, and the municipal levels. The regulations by the state and the municipalities are based on the federal regulations, and include guidelines on hazardous waste, water, environmental audits, air emissions, natural protected areas, and ecological ordinance.
In Mexico, under the LGPGIR, are the Mexican Official Norms (NOMs) and the Mexican Norms (NMX). It is important to note that the NOMs must be complied with while the NMX are voluntary in nature.
  NOM-052-SEMARNAT-2005, establishes the characteristics, the identification procedure, the classification, and the list of hazardous wastes.
  NOM-053-SEMARNAT-1993, establishes the procedure to carry out the extraction test to determine its contents to determine its toxicity, based on which a waste is classified as hazardous or non-hazardous.
i. Classification
Hazardous wastes in the Mexican environmental legislation are identified and classified under Article 16 and Article 19 of LGPGIR, and the guidelines on the NOM-052-SEMARNAT-2005 and the NOM-053-SEMARNAT-1993.
Once the waste is classified as hazardous, the responsibility of the disposal lies with the generating company. The generators only need to prove that the waste was handled by an authorized collecting company. Industry participants that seek registration to handle, store, transport, and/or re-use hazardous wastes must comply with Article 50 of LGPGIR.
Used oils are classified as hazardous waste due to its environmental toxicity and flammability according to the definitions.
ii. Generation
Generators of used oils must be registered in SEMARNAT and need to have an authorized management program. At the National Agency for Industrial Safety and Environmental Protection of the Hydrocarbons Sector (ASEA). Under this program, the generators need to maintain records for generation, transport and final disposal, and submitting their annual operation card (cédula de operación annual) to the authorities.
However, the obligations vary depending on the volume of hazardous waste generated yearly.
Used oil generators based on volume used oil generation volume are classified as:
  Large generators: Those generating more than or equal to 10 tonnes of used oil annually.
  Small generators: Those generating more than 400 kilograms but less than 10 tonnes of used oil annually.
  Micro generators: Those generating less than 400 kilograms of used oil annually.
A generator has the obligation of:
  Self assessment of hazardous waste
  Maintain records of used oil generation, collection, etc.
  Have a specific area for waste management and carry management and storage of used oil. The guidelines for waste management vary based on the type of generator.
  Small and micro generators are allowed to carry hazardous waste on private vehicles if the volume is smaller than 200 kg per trip.
iii. Collection
All professional services rendered in relation to the recollection, storage, transport, and final disposal of hazardous waste must have the prior authorization of SEMARNAT.
iv. Transportation and Storage
Industry participants that seek registration to handle, store, transport, and/or re-use hazardous wastes must comply with Article 50 of LGPGIR.
Continued…

## Slide 177: Regulations
Regulatory Enforcement
i. Responsible Agencies
The Federal Prosecutor for Environmental Protection in Spanish Procuraduría Federal de Protección al Ambiente (PROFEPA): PROFEPA is the enforcement arm of SEMARNAT, and it has the authority, under the internal regulations of SEMARNAT, to:
  Carry out inspection visits
  Prosecute environmental non-compliance
  Apply sanctions
  Generally, enforce environmental laws and regulations
  Perform inspections and sanction the entities and individuals subject to air emissions reports under the recently published General Law on Climate Change and its regulations
  PROFEPA also oversees the federal voluntarily environmental audit program.
ii. Enforcement Mechanisms
Administrative law is strictly enforced. Enforcement is driven by the constitutional principle of legality and due process.
Environmental statutes and regulations are generally clear about the consequences and penalties for non-compliance with them, and on the procedures to enforce and apply them.
iii. Effectiveness of Regulations Enforcement
In the last few years, Mexico has improved in enforcement practices. However, reduction on budgets and change on governmental politics have impacted the law enforcement in general, resulting in an overall weak application.
  Current administration is less focused on environmental matters.
  Limited budgetary and human resources leading to lax enforcement of regulations.
  Relatively limited involvement from the judiciary on environmental matters. Historically, environmental issues have been kept away from the courts in Mexico.
  Consequently, there are a relatively small number of decisions by the courts on environmental laws and regulations that can guide the regulatory authorities.
The National Environmental Audit Program (PNAA) is an accreditation scheme by PROFEPA.
  Important to point out the PNAA has a voluntary character.
  The program gives benefits of certifications on the product or process.
  For marketing proposes many companies pursue this accreditation.
  Companies and business that work on this program ensure better management of hazardous waste like used oils.
Key Influencers
i. Public Sector
Secretaría de Medio Ambiente y Recursos Naturales -SEMARNAT (Ministry of the Environment and Natural Resources)
Procuraduría Federal de Protección al Ambiente - PROFEPA (Federal Prosecutor for Environmental Protection)
Agencia de Seguridad, Energía y Ambiente – ASEA (Security, Energy and Environment Agency)
ii. Private Sector
Asociación Nacional de la Industria Quimica A.C. – ANIQ (National Association of the Chemical Industry A.C.)
Asociación Mexicana de la Industria Automotriz A.C. – AMDA (Mexican Association of the Automotive Industry A.C.)
Impact of Current Regulations
Low to medium. On the industry, companies are not obliged to treat the oil, and many companies prefer to sell it for fuel manufacturing or burning.
Probable Future Regulations
For the moment, there is no change in regulations that could directly affect the used oil market.

## Slide 178: Material Balance 2020
Chart: USED OIL GENERATION, 2020
| Used oil generated | Lubricant lost
Sales | 0.56 | 0.44
Total: 640.0 Kilotonnes
Chart: USED OIL COLLECTION, 2020
| Collected | Not collected
Sales | 0.62 | 0.38
Chart: USED OIL DISPOSAL, 2020
| Fuel | Re-refined | All other-a
Sales | 0.86 | 0.01 | 0.13
Chart: USED OIL RE-REFINING, 2020
| Basestock | All other
Sales | 0.6 | 0.4
Total: 356.4 Kilotonnes
Total: 220.6 Kilotonnes
Total: 2.3 Kilotonnes
In 2020, the volume of total finished lubricants consumption in Mexico was estimated at 640.0 kilotonnes.
  It is estimated 56% of the lubricant demand was generated as used oil. The rest was lost through evaporation, consumed in use or due to poor handling of used oil. The generation rate has been improving in the last few years, increasing from almost 50% in 2018, to 56% in 2020.
  Out of the 356.4 kilotonnes of used oil generated, around 62% is collected. However, there is still room for improvement for improving efficiency of collection.
  Approximately 85% of the collected used oil is used to produce fuel such as diesel or marine gas oil. It is mainly used as fuel in cement companies.
  Re-refining for basestock manufacturing is not prevalent in Mexico. Only one company in Mexico, EyL, re-refines used oil. EYL does it at small scale as the market is very small for re-refined basestocks in Mexico. Earlier, Bravo Energy re-refined basestocks, however, due to COVID-19, they have stopped re-refining used oil as it was not profitable.
a- Burn material, asphalt mixture, exports, regeneration, etc.

## Slide 179: Material Balance 2021
Chart: USED OIL GENERATION, 2021
| Used oil generated | Lubricant lost
Sales | 0.56 | 0.44
Total: 689.2 Kilotonnes
Chart: USED OIL COLLECTION, 2021
| Collected | Not collected
Sales | 0.62 | 0.38
Chart: USED OIL DISPOSAL, 2021
| Fuel | Re-refined | All other-a
Sales | 0.86 | 0.01 | 0.13
Chart: USED OIL RE-REFINING, 2021
| Basestock | All other
Sales | 0.6 | 0.4
Total: 383.8 Kilotonnes
Total: 237.6 Kilotonnes
Total: 2.5 Kilotonnes
In 2021, the lubricant consumption is expected to reach 689.2 kilotonnes.
  It is expected to generate around 55% or 383.8 kilotonnes of used oil. The growth in used oil generation volume is due to growth in lubricant demand in 2020.
The collection of used oils is also expected to improve due to the growing interest in used oil in Mexico. This is mainly due to growth in demand of used oil for fuel production.
The disposal of used oil is not expected to change in Mexico in 2021. Fuel production, diesel for heating machinery, and marine gas oil are the main products demanded in the market.
a- Burn material, asphalt mixture, exports, regeneration, etc.

## Slide 180: Used Oil Generation
In 2020, used oil generated was estimated to be 356.4 kilotonnes in Mexico. The volume of used oils generated in Mexico decreased in 2020 compared to 2018, as the lubricants demand also decreased. However, the generation rate increased by around 6% during 2018 to 2020.
  This increase in generation rate is due to the improvement in recovery practices of automotive lubricants, mainly for PCMO and HDMO, that together accounted for 56.1% of used oil generation volume in 2020.
  Volume of used oil from industry has also improved as maintenance practices have improved leading to higher generation of used oil. However, industrial lubricants such as white oils, water-miscible metalworking fluids, rubber process oils, greases, etc., do not generate any used oil.
In 2021, the lubricant demand has grown by around 7.7%, which has led to increase in used oil generation volume by 7.7%. The growth is lower in used oil generation volume probably due to decline in law enforcement. The Mexican government has reduced internal budget for different ministries, including SEMARNAT. As a result, the number of audits have reduced while the time needed for permit authorization or renewal authorizations has increased.
Chart: USED OIL GENERATION RATES BY PRDOUCT IN MEXICO, 2020
| PCMO | HDMO | Hydraulic fluid | All other-a
Series 1 | 0.75 | 0.7 | 0.7 | 0.4
USED OIL GENERATION BY PRODUCT IN MEXICO, 2020 AND 2021 |  |  |  | 
LUBRICANT | KILOTONNES |  | % OF TOTAL USED OIL GENERATED | 
 | 2020 | 2021 | 2020 | 2021
PCMO | 132.0 | 142.2 | 37.0 | 37.1
HDMO | 68.2 | 72.9 | 19.1 | 19.0
Hydraulic fluid | 28.5 | 30.9 | 8.0 | 8.1
All other-a | 127.7 | 137.7 | 35.9 | 35.9
Total | 356.4 | 383.8 | 100.0 | 100.0
a- Includes other automotive and industrial lubricants |  |  |  | 
a- Includes other automotive and industrial lubricants

## Slide 181: Used Oil Collection
In 2020, used oil collected volume was estimated at 220.6 kilotonnes in Mexico. This volume represents 62% of generated used oil in the country.
  The main collection points of used oil include vehicle service stations, garages, commercial transport workshops, and industries. Collectors need to be registered and authorized by SEMARNAT. However, it is also possible that some collection is done by non-authorized collectors.
  Despite the drop of volume demand for finished lubricants and generated used oils, the used oil volume collected has increased by around 2%-3% in the last two years. This is due to the increase in the interest of used oil market, especially its usage as fuel by various industries.
In 2021, the used oil collected volume has increased by 10.4%, which is in line with the growth in the used oil generation volume. Due to the decrease in funding of various government bodies, the registering process of used oil collectors is taking long. Further, some collectors have not renewed their authorizations on time due to COVID-19.
Chart: USED OIL COLLECTION RATES BY PRDOUCT IN MEXICO, 2020
| PCMO | HDMO | Hydraulic fluid | All other-a
Series 2 | 0.6 | 0.7 | 0.85 | 0.54
USED OIL COLLECTION BY PRODUCT IN MEXICO, 2020 AND 2021 |  |  |  | 
LUBRICANT | KILOTONNES |  | % OF TOTAL USED OIL COLLECTED | 
 | 2020 | 2021 | 2020 | 2021
PCMO | 79.2 | 85.3 | 35.9 | 35.9
HDMO | 47.7 | 51.1 | 21.6 | 21.5
Hydraulic fluid | 24.2 | 26.3 | 11.0 | 11.1
All other-a | 69.4 | 74.9 | 31.5 | 31.5
Total | 220.6 | 237.6 | 100.0 | 100.0
a- Includes other automotive and industrial lubricants |  |  |  | 
a- Includes other automotive and industrial lubricants
Continued…

## Slide 182: Used Oil Collection
AUTOMOTIVE USED OIL COLLECTION BY SOURCES, 2020 |  | 
SOURCE | KILOTONNES | % OF USED OIL COLLECTED
Workshops for consumer and commercial vehicles and other installed segment facilities (dealerships, fuel stations, quick lubes) | 105.6 | 65.0
Commercial vehicles reparation or services centers | 56.8 | 35.0
Total | 162.4 | 100.0
It is estimated that around 65% of used oil generated is collected from workshops while remaining 35% is collected from repair centers or services centers for commercial vehicles.
  The main collection points of used oil include vehicle service stations, garages, commercial transport workshops and industries. Service facilities and collectors need to be registered and authorized by SEMARNAT in order to operate.
  It is rare that a collector would obtain used oil from individuals providing maintenance services such as change of oil or DIY customers. However, it is possible that a person could dispose the used oil to familiar or known workshop. In largest cities, where environmental awareness is increasing, this is a practice that could increase in the future.
Industrial used oils are collected directly at the facilities by collectors, in most of the cases. By law, any generator must keep a record of volume of used oil generated and the disposal, or company taking care of disposal (collector).
  However, rumors of bad practices exists, where companies dispose their hazardous residues to water bodies, especially when the companies are small.
In Mexico, most of the used oil is collected by private collecting companies. Only two companies, Bravo Energy and Lubyrec integrate collection and disposal services.
  Therefore, it is estimated around 60% of used oil is collected and sold by independent registered collectors. Around 30% is collected by processors like Bravo Energy, and the rest 10% is collected either by illegal collectors or by non-registered end users.
  When it comes to preference for collecting a particular type of used oil, there is no known difference except for transformer used oil. The transformer oil needs to be collected separately as not all companies are able to process it as it contains polychlorinated biphenyl (PBs).
Continued…

## Slide 183: Used Oil Collection
In order to be able to provide the collection services, it is necessary for a company to get authorization from SEMARNAT, and audits done by PROFEPA.
  Leading collecting companies are Bravo energy, Lubyrec, ProAmbiente (CEMEX), Enermex (PEMEX), and Gen Industrial in Mexico.
  Collection of used oils is concentrated in the central and northern part of the country.
  Two state-owned companies, PEMEX and CFE, work together with many small collectors fragmenting the markets even more.
  Other companies with large collection capacity diversified their portfolio with different type of wastes and residues. On SEMARNAT records, there are many companies registered, however, not all of them provide these services. This is because a company registers for different types of hazardous wastes at one go even though they may not want to provide collection services for it. This is a loophole in the regulation that causes issues in enforcing regulations.
Used oils collection in Mexico works under three different schemes.
  When the collectors buy used oil from generators and transport it to recyclers to resell it.
  When collectors pick up the used oil and charge for the disposal service.
  When collectors only provide the transport service since the generators already have a contract with the recycling company.
  In the last few years, the most common scheme is the first one, when the collectors buy or pay for the used oil collected. This is because the demand of used oil is growing in Mexico.
Depending on the size of the companies, the type of agreement varies. For example, larger generators tend to get contract with established pick-up dates and volumes. On the other hand, smaller generators would dispose their used oil in smaller volumes as the contract collection system does not work for them.
Price of collection of used oil can vary depending on the volume, recipient, and the contract or agreement between the generator and the collector. Normally, collectors do not differentiate between type of lubricants.
  On average, automotive lubricants such as PCMO and HDMO cost between MXN 2.0 to MXN 3.5 (USD 0.09 to USD 0.17) per liter, depending on the volume to be collected and the frequency.
  Demand of used oil is higher in the central and the north of Mexico. In these regions, the price could be higher.

## Slide 184
Chart: USED OIL DISPOSAL IN MEXICO, 2020
| Fuel | Re-refining | All other-a
Sales | 0.86 | 0.01 | 0.13
Total: 220.6 KT
In Mexico, by law, lubricant oils once finished their life cycle or utility, must not be disposed to water bodies or to open landfills. Traceability starts when the company that will generate used oil register it, in case of automotive oil. In case of industrial lubricants, it is according to process.
  In the last few years, as the environmental awareness has increased, together with the increase in demand of used oils, therefore the disposal as per law has improved.
  In 2020, due to COVID-19 crisis, demand of finished lubricants decreased, which in turn led to lower generation of used oil. However, demand for used oils still increased, especially for its usage as fuel as a cheaper alternative for industry in 2020.
  The main application of used oils is the production of fuel, like diesel and marine gas oil (MGO). Fuels account for almost 85% of used oil disposal.
  Other 15% of used oil collected is used for different purposes.
  As additive on asphalt formulations for road construction
  In the cement and other industries, used oil is utilized for burning.
  Regeneration and recycling
  Exports
  In Mexico, there is very little re-refining of used oils. However, it has been reported some experimental re-refining by Ecologia y Lubricants (EyL) company together with research centers.
USED OIL DISPOSAL BY PRODUCT TYPE, 2020 |  |  |  | 
LUBRICANT TYPE | KILOTONNES |  |  | 
 | RE-REFINING | FUEL | ALL OTHER-a | TOTAL
PCMO | 1.2 | 78.0 | - | 79.2
HDMO | 0.7 | 47.0 | - | 47.7
Hydraulic fluid | 0.4 | 4.5 | 19.4 | 24.2
All other-b | - | 59.7 | 9.8 | 69.4
Total-c | 2.3 | 189.2 | 29.2 | 220.6
a- Includes usage in construction, regeneration, etc. b- Includes other automotive and industrial lubricants. c- Totals may not add due to rounding. |  |  |  | 
Used Oil Disposal 2020

## Slide 185
Chart: USED OIL DISPOSAL IN MEXICO, 2021
| Fuel | Re-refining | All other-a
Sales | 0.86 | 0.01 | 0.13
Total: 237.6 KT
In 2021, no change in the disposal of used oil is expected. The disposal is expected to remain same as 2020.
Overall disposal volume increased by 7.7%, due to growth in the lubricant demand in Mexico in 2021.
Around 15.4% of volume of used oil destinated to fuel manufacturing is coming from industrial oils. Companies that are subsidiaries of PEMEX and CEMEX participate actively in this cycle.
USED OIL DISPOSAL BY PRODUCT TYPE, 2021 |  |  |  | 
LUBRICANT TYPE | KILOTONNES |  |  | 
 | RE-REFINING | FUEL | ALL OTHER-a | TOTAL
PCMO | 1.3 | 84.0 | - | 85.3
HDMO | 0.8 | 50.3 | - | 51.1
Hydraulic fluid | 0.4 | 4.9 | 21.0 | 26.3
All other-b | - | 64.3 | 10.2 | 74.9
Total-c | 2.5 | 203.5 | 31.6-c | 237.6
a- Includes usage in construction, regeneration, etc. b- Includes other automotive and industrial lubricants. c- Totals may not add due to rounding. |  |  |  | 
Used Oil Disposal 2021

## Slide 186: Used Oil Processors
MAJOR USED OIL PROCESSORS IN MEXICO, 2020 |  |  | 
 | KILOTONNES |  | 
COMPANY | USED OIL FEED CAPACITY | FUEL CAPACITY | FUEL PRODUCTION
Bravo Energy | 146.0 | 109.5 | 48
EyL | 1.4 | 1.1 | 0.6
Lubyrec | 1.1 | 0.8 | 0.4
Total | 148.5 | 111.4 | 49.0
Note: This table only gives details of major used oil processors in Mexico. |  |  | 
There is very little re-refining of used oil in Mexico.
For lubricant blenders, it is not profitable to buy basestocks in the country, when the offer for imported basestocks from the US and Canada is cheaper.
  Before COVID-19, Bravo Energy was the largest company re-refining used oil in Mexico. However, they stopped operation in 2020, without plans to continue.
  Currently, EyL is re-refining at a small scale in Mexico.
However, companies like Bravo Energy and EyL have installed the capacity for used oil re-refining and can resume re-refining.
Most processors of used oils produce fuel from used oil or recycle or regenerate lubricants from used oils. Regeneration is a process under which impurities from used oil are removed, which is then used as lubricant.
COVID-19 crisis also influenced used oil processors.
  For example, some companies closed businesses since there was not enough volume demanded nor volume collected, as it was the case of Inlubsa S.A. de C.V.
  Other companies started focusing on management of other wastes like water treatments or metal recovery, rather than used oil.
  On the other hand, companies with larger volume capacity to process, like Bravo Energy and EyL, gained market demand of fuel produced based on used oils.
In Mexico, used oil processors could be:
  Fuel producers, diesel for industry and MGOs. Together with subproducts as drilling fluids, demolding agents, asphalt additives.
  Regeneration and recycling. Although this process takes place using mostly the used oil of the industry, there is a postprocessing outside at the used oil processors facilitates.
  Subsidiary companies that work for state owned companies like PEMEX and CFE.

## Slide 187: Used Oil Processors: Bravo Energy Profile
Bravo Energy is the largest used oil processor in Mexico, and present in the country since 2007, with a processing capacity of 146 kilotons per year.
The headquarters of Bravo Energy are in California, United States. The company is also present in Chile and Argentina.
Bravo Energy has authorization from Mexican authorities for collection, recycling, and transforming of used oils, as it is registered in SEMARNAT records.
Their main product is marine gas oil. The MGO Bravo Energy produces is under the specs of the International Marine Organization (IMO) 2020.
  The IMO 2020 are specifications that put limit on the sulfur content in the fuel oil used on board ships, aiming to improve air quality, preserve the environment, and protect human health.
  As Bravo Energy MGOs fulfilled these specifications, their product is competitive in the international market. Ships with international cargos demand their products at the Mexican ports.
  In Mexico, there is no other company that specialized on MGO.
In smaller volumes, it also produces fuel for other industries like mining, cement, manufacturing, and construction. In this area, the company has other competitors in the market.
Geographically, Bravo Energy covers center and north of Mexico, with some presence on eastern states like Veracruz, due to the maritime ports. With one collection center in Tamaulipas, and in Queretaro with a collection center plus production plant.
During 2020, due to COVID-19 crisis, the offer on used oil decreased, while the demand of MGO increased.
  Many industries, like automotive industries, decreased production and as a consequence, also led to decrease in used oils generation, same as workshops or service centers.
  Other companies, especially the small companies, closed business.
Another aftermath of COVID-19, the company stopped production of re-refined basestocks. This decision was due to low demand of re-refined basestocks in Mexico due to better offer for virgin basestocks from the US.

## Slide 188: SWOT Analysis: Bravo Energy
STRENGTHS | WEAKNESSES
Largest re-refining installed in the country Well-defined market of MGO, and product on agreement with IMO 2020 specifications Diverse portfolio of suppliers of used oils Have a large collection network in the industrial area of the country | Largely focus on MGO and small diversification on their portfolio Prices of MGO set internationally, leading to a currency exchange vulnerability
OPPORTUNITIES | THREATS
Growing demand of MGO Increasing environmental awareness in the industry | Large competition on collection of used oil for fuel production Weak regulations and poor control on the used oil production chain, making black market a constant threat

## Slide 189: Finished Lubricant Market Outlook
Chart: PROJECTED FINISHED LUBRICANT MARKET IN MEXICO, 2020-2030
| Consumer | Commercial | Industrial
2020 | 241.3 | 201.5 | 197.2
2021 | 260.4 | 215.6 | 213.2
2025 | 352.5 | 282.4 | 293.4
2030 | 379.9 | 303.4 | 341
The finished lubricants demand is expected to grow by 7.7% in 2021. During 2020-2025, lubricant demand is expected tog row at a CAGR of 7.7%, before slowing down to 2.0% during 2025-2030. Main drivers for growth in the coming years are:
  Economy bouncing back after COVID-19 crisis in 2020, increasing mobility.
  Mexico’s infrastructure projects and manufacturing industry, like the new airport and south train construction.
  However, industries like automotive, food processing, chemicals, plastics, metals, and machinery industries are expected to slow down or recover at lower speed.
In the industrial segment, lubricant suppliers will find sources of growth in the infrastructure and manufacturing sectors of the automotive industries, food and beverages, plastic, rubber, basic metal industries, as well as machinery and equipment. Metalworking fluids will benefit from the increased specialization of the Mexican automotive and aerospace manufacturers in the country and expected new investment for electric car manufacturing plants.
The commercial lubricant market is expected to show a growth driven by the expansion of the commercial vehicle parc and the movement of manufacturing goods, considering that an estimate of 63% of cargo exports are made by truck. The segment will benefit from growth in hydraulic and transmission fluids demand. In HDMOs, SAE 15W-40 and 25W-50 grades are expected to continue to be in the highest demand over the next 10 years, since mechanics, fleet operators, and drivers are long habituated to using these viscosity grades. The imports of used vehicles will also continue expanding demand for 25W-50.
Demand in the consumer automotive sector is expected to grow in 2021 as mobility increases following ease in restrictions due to COVID-19. During 2020-2030, the growth in demand is expected to be driven by the growth in the vehicle parc, especially motorcycle parc, that is still estimated to grow between 10% and 20% annually during the next 10 years.

## Slide 190: Used Oil Industry Outlook 2025
Chart: USED OIL GENERATION, 2025
| Used oil generated | Lubricant lost
Sales | 0.6 | 0.4
Total: 928.3 Kilotonnes
Chart: USED OIL COLLECTION, 2025
| Collected | Not collected
Sales | 0.64 | 0.36
Chart: USED OIL DISPOSAL, 2025
| Fuel | Re-refined | All other
Sales | 0.86 | 0.02 | 0.12
Chart: USED OIL RE-REFINING, 2025
| Basestock | All other
Sales | 0.6 | 0.4
Total: 557 Kilotonnes
Total: 356.5 Kilotonnes
Total: 7.1 Kilotonnes
Used oil generated is expected to increase to 557 kilotonnes in 2025. The collected volume is also expected to grow to 356.5 KT in 2025.
Mexico, through SEMARNAT and the Transports and Communications Minister, proposed a new norm (NORM-44) that originally obliged all new commercial transport acquired after 2022 must use ultra-low-sulfur diesel (ULSD). However, PEMEX is not suppling enough ULSD to Mexican market. And in the last two years, diesel supply by private companies has increased. Therefore, the new norm was delayed from 2022 to 2025. Under this scenario:
  Demand of diesel from the industry will continue. While diesel from used oils is mostly used in industries, as the fuel demand from the automotive segment increases, it may lead to increase in price of diesel produced from the used oil in Mexico.
a- Burn material, asphalt mixture, exports, regeneration, etc.

## Slide 191: Used Oil Industry Outlook 2030
Chart: USED OIL GENERATION, 2030
| Used oil generated | Lubricant lost
Sales | 0.6 | 0.4
Total: 1,024.3 Kilotonnes
Chart: USED OIL COLLECTION, 2030
| Collected | Not collected
Sales | 0.64 | 0.36
Chart: USED OIL DISPOSAL, 2030
| Fuel | Re-refined | All other
Sales | 0.87 | 0.02 | 0.11
Chart: USED OIL RE-REFINING, 2030
| Basestock | All other
Sales | 0.6 | 0.4
Total: 614.6 Kilotonnes
Total: 393.3 Kilotonnes
Total: 7.9 Kilotonnes
Lubricant demand is expected to increase to 1,024.3 kilotonnes at a CAGR of 2% during 2025-2030 in Mexico. This will drive the growth in generation and collection of used oil in the country.
During 2020-2030, one of the main growth drivers of demand of used oils will be the growing demand of clean fuels such as diesel. As a result, the interest in using used oil to produce diesel is growing in Mexico. Companies are expected to increase investment in research to develop cleaner technologies in the country.
  Renovation on transport infrastructure, railways and roads, and the increase on maritime traffic will also promote the demand for alternative fuels.
On the global climate change fight, Mexico has announced compromises that are aimed to help the reduction of emissions. However, the significant actions to reduce emissions are expected to come from the industry in Mexico. This is also expected to drive the environmentally friendly way of disposal of used oil in the country.
Re-refining of used oil is not expected to change much during 2020-2030. This is because no new capacity expansion or building a new re-refining capacity has been announced in Mexico.
a- Burn material, asphalt mixture, exports, regeneration, etc.

## Slide 192: Market Evaluation
Opportunities
Mexican used oil market is gaining momentum, mainly due to the valorization of subproducts like diesel for industries and MGO.
PEMEX is decreasing supply on diesel, being the private companies suppling it. With the new norm entering in 2025, the demand for diesel will increase.
Increasing environmental awareness by companies, gaining interest on voluntary certifications like “clean industry” or the national environmental audit program. As market is increasing demand on sustainable and socially responsible companies, this is a driving motivation.
National and multinational companies, before COVID, were investing on technology development and research. These initiatives are expected to continue in coming years. Main interest is on regeneration of used oils for industries and the distillation of environmentally friendly fuels for automotive, maritime and railway transport.
  As with maritime and railway, diesel is the main energy source, thus, with the expansion of railway network in Mexico and the maritime traffic increasing in Mexico, it is expected to have a continual growing demand.
Demand of used lubricants on the northern countries for processing is a window of opportunity for generators and collectors. There are some collectors already present that export hazardous residues.
Challenges
Even though used oils are regulated from generation to processing, stricter rules are necessary in terms of controls and monitoring, in order to combat different threats on the industry:
  Black market happening during collection and in small to medium generators
  Shared responsibility on the traceability of the used oil chain. Avoiding loss of used oil that affect the market and the environment
After COVID crisis, the automotive industry has been affected severely, mainly due to a global lack of raw materials. Automotive industry is an important economic driver in the country and different industries are linked to it.
Main business partners for Mexico, USA, Canada and European Union, are moving toward cleaner energy, while Mexico has not made progress on the matter. This will have an impact on the automotive demand and lubricant offer.
  As the export demand for engine gas cars will decrease, Mexico will need to update their production in order to stay competitive.
  As demand growth of supply of lubricants will decrease in the mentioned countries, the offer for Mexico and the new lubricants will increase, potentially increasing generation of used oils. However, storing and processing capacity of small and medium companies could represent a challenge on the infrastructure.

## Slide 193
Russia

## Slide 194: Russia Market Synopsis
Chart: USED OIL MATERIAL BALANCE IN RUSSIA, 2021-2030 (MILLION TONS)
| Finished Lube Demand | Used Oil Generated | Used Oil Collected | Used Oil Re-refined | RRBO produced
2021 | 1506.7 | 835.2 | 419.2 | 64.1 | 44.9
2025 | 1633.8 | 947.6 | 502.2 | 65.3 | 45.7
2030 | 1766.5 | 1077.6 | 603.4 | 72.4 | 50.7
Used Oil Regulations
The key used oil regulations in Russia are The Federal Law: 458-FZ, Basel Convention on the Control of Transboundary Movements of Hazardous Wastes and Their Disposal, ratified by 458-FZ, National standard “Waste treatment. Elimination of used petroleum products”, GOST 2146 “Used Petroleum products”, and Technical regulation of the Customs Union 030/2012 “Requirements for lubricants, oils and special liquids“.
According to GOST 2146, used oil must be collected and re-refined by used oil generators, or outsource these operations to other licensed companies.
Collectors must have license to operate in Russia.
Used Oil Material Balance
It is estimated that half of the used oil generated in the country is not collected properly and is absorbed by the grey/black markets. This is disposed either as fuel without removing the hazardous materials or dumped into soil or water.
The Russian industrial sector’s modernization and the implementation of energy-saving technologies in various industries, would drive used oil generation during the forecast period.
Used oil collection rate is expected to grow by 2025 as the number of Waste Recycling Association’s members grow. This will allow Rosprirodnadzor to have a broader register of the used oil generators and will also help to control illegal collectors.
MAJOR USED OIL RE-REFINERS IN RUSSIA, 2021-2030 |  |  | 
 | RE-REFINED BASESTOCKS CAPACITY (KILOTONNES) |  | 
COMPANY | 2021 | 2025 | 2030
Rosa-1 | 42.0 | 58.0 | 58.0
Perm Oil Factory | 7.0 | 7.0 | 7.0
Tekh-engineering | 3.5 | 3.5 | 3.5
Vtornefteprodukt | 3.4 | 3.6 | 3.6
Roskhim | 2.8 | 2.8 | 2.8
Shaumyan's Oil Plant | 1.8 | 1.8 | 1.8
Rikos | 1.4 | 1.6 | 1.6
Orgsintezkhim | 1.9 | 1.9 | 1.9
Total | 63.8 | 80.2 | 80.2
Used Oil Re-refining
The yield of re-refineries in Russia is around 70%.
There is only one big re-refinery in Russia: Rosa-1. It is followed by the Perm Oil Factory and many other small re-refiners.
The number of small re-refiners has slightly increased over the past three years as prices of Group I basestocks increased making re-refining profitable.
Re-refined lubricants represent a negligible share in the Russian lubricants market. End users are not aware of the benefits of lubricants made from re-refined basestocks.
The Russian lubricants market is driven by the brand. Russian consumers tend to prefer foreign brands, such as Shell, Mobil, and Castrol. Without the support from lubricant majors, the prospect for the re-refined lubricants are poor in the country.
Opportunities
Waste Recycling Association currently is the main driver heading toward making unorganized and uncontrolled market of used oil in Russia more organized and formal.
Russian majors keep investing in new production capacities, upgrading existing Group I basestock refineries to produce Group II and III basestocks. This is expected to have a positive impact on used oil re-refining in Russia.
Challenges
Currently, overcapacity for Group I basestocks is adversely impacting the growth of re-refined basestocks in Russia.
Due to the large distances, in Russia, used oil collectors are usually operating in a radius of 500 – 1,000 km around the industrial hubs, many garages in the rural area may remain uncovered by the collectors’ services.

## Slide 195: Economic Background
SELECTED ECONOMIC CHARACTERISTICS OF RUSSIA, 2020 AND 2021 |  | 
KEY INDICATOR | 2020 | 2021
Population (Million) | 146.3 | 145.4
GDP at current prices (USD billion) | 1,473.6 | 1,710.7
GDP per capita, current prices (USD) | 10,126.7 | 11,000.0
GDP growth rate, constant prices (Annual % change) | -2.7 | 3.4
Inflation, average consumer prices (Annual % change) | 4.9 | 4.5
Current account balance (% of GDP) | 2.3 | 3.8
Share in Real GDP |  | 
Services (%) | 63.1 | 62.3
Industry (%) | 33.1 | 32.4
Agriculture (%) | 3.8 | 4.7
Russia is the largest country in the world, and has large reserves for crude oil, natural gas, coal, etc. This places Russia in a crucial place among industrialized countries. During the current administration of the country, Russian economy has been witnessing growing dependency on hydrocarbons. The share of oil and gas production in the Russian economy increased from 34% to 39% over the past decade. There are large deposits of crude oil, natural gas, coal, and uranium in Russia. Although mineral deposits are abundant, many are in remote areas, with extreme climatic conditions due to which it is expensive to extract them.
Russia may hold as much as one-half of the world’s potential coal reserves and may hold larger reserves of crude oil than any other country in the world. Following the United States, Russia remains the second largest producer of natural gas and the third largest producer of crude oil globally.
In 2020, Russia experienced its largest population decline since 2005, largely due to the COVID-19 pandemic. According to Federal State Statistics Service (Rosstat), the excess mortality rate in the country increased by about 18%, compared to 2019. Additionally, an increase in the level of immigration from Russia over the past two years has been witnessed due to worsening of internal political situation. It is estimated that during 2018-2021, the population in Russia has decreased by about 1.4 million.
The coronavirus pandemic has reduced business activity, leading to a decline in demand and prices for hydrocarbons. In addition, the OPEC+ agreement influenced a significant decrease in crude oil extraction in 2020. Participating countries agreed in April 2020 to cut oil production gradually by 9.7 million barrels per day (mbpd) in May-June 2020, then by 7.7 mbpd in the second half of 2020. Following production decline by 5.8 mbpd is agreed to be provided until the end of April 2022. As a result, in 2020, the crude oil production in the country declined to its lowest level over the past 10 years. Production volume (including gas condensate) decreased by 8.6% to 512.68 million tonnes in 2020.
Gazprom, a Russian natural gas supplier, plans to increase exports to Europe by means of the Nord Stream 2 pipeline, which has a projected annual capacity of 55 million cubic meters. The Nord Stream 2 pipeline was initially slated for completion in early 2020, with a view to being operational in mid-2020. However, the launch of the pipeline has been postponed due to the prolonged construction process due to the U.S. sanctions.
In response to the poisoning and imprisonment of Aleksey Navalny, a Russian opposition leader and Kremlin critic, sanctions against Nord Stream 2, which included companies providing insurance and certification services required to complete the construction, were expanded in the beginning of 2021. As a result, at least 18 European companies left the project. However, regardless of other European Union states, Germany still supports the construction of the Nord Stream 2 gas pipeline.
In 2020, the Ministry of Energy of Russia continued work on the implementation of the import substitution policy in the fuel and energy sector. The share of domestically produced catalysts for oil refining in Russia rose to 66% in 2020, compared to 32% in 2014. Since 2014, the import substitution policy has significantly reduced the demand for imported lubricants: from 21% in 2014 to 14% in 2020.

## Slide 196: Vehicle Population
Chart: VEHICLE SALES BY VEHICLE TYPE IN RUSSIA, 2019-2021
| Passenger vehicles | Trucks | Buses | Off-highway vehicles and equipment | Motorcycles | Agricultural vehicles
2019 | 1593.1 | 112.1 | 13.9 | 13.3 | 13 | 11.2
2020 | 1447.5 | 104.3 | 13.2 | 13.3 | 16.4 | 16.4
2021 - a | 1557.5 | 113.6 | 13.6 | 13.5 | 14.5 | 14.8
Thousand units
Chart: VEHICLE PRODUCTION BY VEHICLE TYPE IN RUSSIA, 2019-2021
| Passenger vehicles | Trucks | Buses | Agricultural vehicles | Off-highway vehicles and equipment | Motorcycles
2019 | 1523.6 | 155.3 | 41.2 | 6.8 | 3.1 | 1.9
2020 | 1257 | 141.8 | 37.2 | 7.1 | 3.3 | 1.5
2021 - a | 1506.5 | 156.8 | 37.5 | 7.3 | 3.2 | 1.6
Thousand units
The passenger vehicle segment is the leader in the total vehicle fleet in Russia. In 2020, it reached approximately 50 million units, which was 84% of the overall vehicle parc. The passenger vehicle parc in Russia is rather old, with the average age of about 14 years, and about 60% of it is more than 10 years old. Over 40% of the passenger car parc in the country is under 10 years old.
  Global trends such as vehicle electrification and natural gas-fueled vehicles are influencing the development of the passenger vehicle market, worldwide. However, over the past five years, Russia’s automotive market did not witness a significant sales and production of these new technology vehicles. This situation is also unlikely to markedly change over the next five to 10 years.
Due to COVID-19, overall Russian automotive production contracted by 16% in 2020, and domestic sales by 9%; however, the overall vehicle parc is steadily growing. It is expected that it will exceed an estimated parc of 59 million units by 2025.
The Government of the Russian Federation is currently developing measures to improve the state of the automotive industry, which should have an impact on road transport and its infrastructure. Both the volume of goods transported, and the turnover of goods are expected to increase significantly. The logistical costs and services are gradually increasing due to the growing shortage of transport. Many cargo companies have been continuously investing in fleet modernization. KAMAZ, the Russian truck market leader, benefits from the sharply increased demand for premium trucks in construction, oil and gas production, housing, and utilities.
a – Estimated values
a – Estimated values

## Slide 197: Finished Lubricant Market
Chart: OVERALL LUBRICANT DEMAND BY SEGMENT IN RUSSIA, 2020
| Industrial | Commercial | Consumer
Sales | 0.5 | 0.31 | 0.19
Total: 1,477.3 Kilotonnes
Chart: OVERALL LUBRICANT DEMAND BY PRODUCT TYPE IN RUSSIA, 2020 AND 2021
| HDMO | PCMO | Industrial engine oils | Hydraulic fluids | Process oils | All other-a
2020 | 334.9 | 238.7 | 136.9 | 113.2 | 96 | 557.6
2021-b | 341 | 245.6 | 139.4 | 115.7 | 96.9 | 568.1
KT
Demand for finished lubricants is experiencing a slight increase in the consumer automotive segment due to growth in the total passenger vehicle parc in Russia. Over the past five years, the passenger vehicle parc has increased by 11%: from 44.3 million units in 2015, to 49.7 million units in 2020. The share of foreign vehicles accounts for about 65% of the total passenger vehicle parc. Before the COVID-19 crisis, the overall Russian passenger vehicle parc has been growing at a CAGR of 2.2% on average; however, the growth in sales of foreign vehicles was more substantive at a CAGR of 6%.
The lockdown in response to the COVID-19 pandemic led to a sharp reduction in passenger traffic in Russia in 2020. PCMO demand for service fill declined by more than 10%, due to reduced use of passenger vehicles. There was a reduction in factory fill lubricant consumption due to a decline in production and sales of new passenger vehicles.
The commercial automotive industry has not been as badly impacted by COVID-19 as the consumer segment. Distribution and urban logistics operated at almost full capacity. However, private fleets and taxi fleets had much lower utilization rates. This led to a reduction in the annual consumption of commercial automotive lubricants by about 4.6% in 2020.
However, the Russian economy proved to be more resilient than many other emerging economies worldwide that experienced a much steeper decline. This resilience can be attributed to a relatively small service sector, a large share of protected public employment, and COVID-19 related restriction policies that excluded much of the industrial sector. As a result, industrial production in Russia only declined by 3.5% in 2020.
In 2020, lubricants demand witnessed a decline of about 6% due to recession in the global economy associated with the pandemic. However, the relatively stable new vehicles market in Russia, low penetration of electric vehicles in Russia, and recovery in the industry and national economy over the last few months of 2020 are expected to lead to lubricant demand growth in the future in the country.
a – Includes transmission fluids, greases, compressor, turbine and circulating oils, among others.
b – Estimated values

## Slide 198: Lubricant Blenders
The Russian lubricants blending market is highly fragmented and extremely competitive due to the presence of large number of blenders.
Most Russian passenger vehicle owners still prefer foreign motor oil brands over those from domestic suppliers. Strong demand for foreign lubricant brands is based on vehicle parc model. Owners of foreign vehicles tend to trust foreign lubricant brands, and the belief is supported by the OEMs’ recommendations. The foreign OEMs are recommending synthetic grades that is driving the usage of synthetics in Russia. Domestic suppliers such as LUKOIL and Gazpromneft-Lubricants, are gradually gaining OEM approvals in addition to the growing availability of API Group III basestocks among domestic lubricant suppliers.
Russian lubricant majors such as LUKOIL, Rosneft, and Gazpromneft-Lubricants enjoy a strong position compared to other participants in commercial and industrial sectors due to lower product pricing, strong distribution network, and strong hold in the government projects in the manufacturing, power generation, oil and gas, and construction segments.
Russia has a domestic basestock production capacity of about 2.6 million tonnes with an estimated operating utilization rate of around 75% in 2020. The entire capacity is for paraffinic basestocks, as the country does not have the capacity to produce naphthenic basestocks.
Historically, Russian basestock production was focused on API Group I basestocks, which accounts for 87% of overall basestock capacity in the country. However, Group I basestocks consumption has been declining both outside of Russia and in the domestic market. This resulted in a surplus production of Group I basestocks in Russia. Capacity of Group II/II+ and Group III basestocks account for shares of 7% and 6%, respectively, in the total basestocks capacity in Russia. Currently, there is no Group III+ capacity in Russia.
LUKOIL is the largest basestock producer in Russia, accounting for 40% of the total basestock capacity. It has an estimated annual production capacity of more than 1,000 kilotonnes for basestocks. The company produces Group I (SN-150, SN-350, SN-500, SN-650, SN- 900) and Group III (VHVI-4) basestocks.
Rosneft enjoys the second place in basestocks production in Russia. However, most of the Rosneft facilities are outdated and require modernization.
Rosneft as well as Gazpromneft-Lubricants, and LUKOIL are investing in new basestocks units in order to increase exports and improve the quality of domestic lubricants. Rosneft plans to increase the capacity of its Novokuibyshevsk plant to produce Group II by 250 kilotonnes. By 2022, Gazpromneft-Lubricants Omsk refinery will add 220 kilotonnes of capacity of Group II and III basestocks. Meanwhile, LUKOIL plans to add to its Volgograd refinery, additional capacity of 250 kilotonnes of Group II and III basestocks by 2022.

## Slide 199: Regulations
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | No, used oil is categorized as a hazardous waste under National standard “Waste treatment. Elimination of used petroleum products.”
2. How is used oil classified i.e., hazardous waste, special waste etc.? | According to Russian environmental legislation, oil waste is subject to mandatory disposal and processing and is classified as III-IV hazard class.
3. Are there any requirements on who can collect used oil? | Yes. Operators licensed by The Ministry of Natural Resources and Environment (Rosprirodnadzor)
4. Does country have an association(s) managing the collection and disposal of used oil? | Waste Recycling Association
5. Is a levy charged on sales of lubricants to support used oil collection associations? | No
6. Are there any requirements for how used oil generators manage used oil? | Yes, (GOST 2146-a) regulates standards under which used oil generators manage the waste in environmentally safe manner.
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | No
8. Do any requirements/legislation exist around different types of used oil? | No
9. Does the country have requirements or regulations regarding the export or import of used oil? | No
10. Does the country have any legislation that requires used oil to be re-refined? | Yes. Technical regulation of the Customs Union 030/2012 “Requirements for lubricants, oils and special liquids"
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | Burning of used oils is carried out only in cases that are allowed by the National standard “Waste treatment. Elimination of used petroleum products.” Legal burning of used oils implies that the contaminants need to be removed from used oil before burning it.
a- Russian Technical Regulations Certificate (GOST) Standards were developed in Soviet Union, however, still in use in Russia.
Continued…

## Slide 200: Regulations
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | Yes, waste oil burner should comply with the National Standard: Resources saving. Best available techniques. Used oils must not be burned unless hazardous substances are removed from it, according to the standard.
14. Is used oil allowed to be placed in a landfill? |  | No. According to the restrictions on waste disposal as per the Industry Development Strategy for the processing, utilization, and disposal of production and consumption of waste it is illegal to dispose of the used oil in the landfill.
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | No
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | Yes, Russian legislation does not contain a direct prohibition on burning of used oil as fuel. However, used oil is allowed to be burned only in specially equipped installations approved by Rosprirodnadzor.
 | ii. Blending with crude oil at a refinery | No
 | iii. Dust suppressant | No
17. Are there companies/associations advocating in used oil category? |  | Yes. Waste Recycling Association is the main public organization for the re-refining industry in Russia advocating for the recycling of used oil.
Continued…

## Slide 201: Regulations
Key Used Oil Regulations
The Federal Law: 458-FZ “On Production and Consumption Wastes”
Basel Convention on the Control of Transboundary Movements of Hazardous Wastes and Their Disposal, ratified by 458-FZ
National standard “Waste treatment. Elimination of used petroleum products”
GOST 2146 “Used Petroleum products”
Technical regulation of the Customs Union 030/2012 “Requirements for lubricants, oils and special liquids"
i. Generation
According to GOST 2146, used oil must be collected and re-refined by used oil generators, or they must outsource these operations to other licensed companies.
ii. Classification
Used oil is classified as both petroleum-based products and hazardous waste in Russia (III-IV hazard class).
iii. Collection
As per the National standard “Waste treatment: Elimination of used petroleum products” collectors must have a license for the waste collection operation.
“Waste Management Instructions for III, IV Hazard Classes containing petroleum products” set the rules for collectors, such as different oil categories should not be mixed during collection. While transporting the used oil, the tank should be filled at a maximum level of 95% of its volume.
According to GOST 2146, when collecting used oil, it is necessary to exclude the ingress of greases, organic solvents, fats, varnishes, paints, emulsions, chemicals and contaminants into them. Crude oil, gasoline, kerosene, diesel fuel mixing should be avoided as well.
According to 458-FZ, in accordance with the “Extended Producer and Importer Responsibility (EPR)”, lubricant manufacturers, importers and suppliers are responsible for used oil collection.
In December 2020, a new Concept of the “EPR” was adopted determining the level of waste utilization for different waste groups including used oils.
The Concept provides for the setting of recycling ratios as a percentage of the total volume of products made in Russia or imported from third countries. Previously, the law provided for the establishment of targets as a percentage of the volume of products released for consumption in Russia.
iv. Transportation and Storage
Used oil is usually stored by generators in small containers in a special area. Once the used oil is accumulated at the volume of about 3-4 tonnes, the generators contact the collector to collect the used oil.
Canisters and tanks are used which are not liable to oxidation and are not damaged.
v. Disposal – Re-refining
Re-refiners are required to obtain a license from Rosprirodnadzor as per the Federal Law On Environmental Protection.
Each re-refiner develops its internal regulations of the used oil re-refining technology based on GOST 26378 which specifies physio-chemical parameters of the treated used oil sample such as viscosity, flash point, water amount and particle counting among the others. Settling at elevated temperatures, coagulant treatment, and mineral absorbent filtration as well as distillation process is as per GOST 55096.
vi. Disposal – Fuel
GOST 26432 sets the requirements for fuels allowed for use in the equipment operating in Russia, such as allowed sulfur content (max 1%).
vii. Disposal – Other
Small amounts of used automotive oil maybe dumped or burned by the DYI garages unofficially, this is not allowed as per the law.
458-FZ, sets the responsibilities of the lubricant manufacturers, importers and suppliers for used oil disposal as well, in accordance with the EPR.
Regulatory Enforcement
i. Responsible Agencies
The current used oil market in Russia is controlled by two governmental bodies: The Ministry of Energy and the Ministry of Natural Resources and Environment (Rosprirodnadzor).
Continued…

## Slide 202: Regulations
ii. Enforcement Mechanisms
As per 458-FZ, the responsibility for used oil collection and disposal lies with the lubricant manufacturers and importers in accordance with the “Extended Producer and Importer Responsibility (EPR)”. If they cannot meet their obligations, including hiring a specialized organization, they will have to pay an environmental fee to fund the collection, storage, and disposal of used oil.
The environmental fee depends on the type of product and volume. This fee is not considered to be a tax. Currently, non-payment of the fee just leads to fine.
iii. Effectiveness of Regulations Enforcement
Current enforcement is moderate. The Ministry of Finance has submitted for consideration a draft law on the introduction of an environmental tax instead of an environmental fee. Tax evasion in this case should carry a harsher sentence than non-payment of fee.
The changes to environmental tax should had taken effect on January 1, 2020. However, the implementation date was postponed to January 2022, to provide organizations with a transitional period to prepare for the new legislative requirements.
Key Influencers
i. Public Sector
Rosprirodnadzor.
The Ministry of Energy
ii. Private Sector
Waste Recycling Association.
Impact of Current Regulations
Russian used oil market is highly fragmented and unorganized. Regulatory authorities face several challenges in the used oil accounting, as the lion share of used oil generated in the country ends up in the black or grey market. Stronger emphasis placed on the enforcement of regulations will allow better control of the used oil generation, collection, and disposal.
Probable Future Regulations
The new law on the environmental tax is expected to provide an incentive for the development of independent execution of the EPR by the used oil market participants.
Furthermore, it will drive the increase of legal used oil collection and disposal shares in overall generated volume in the country.

## Slide 203: Material Balance 2020
Chart: USED OIL GENERATION, 2020
| Used oil generated | Lubricant lost
Sales | 0.55238 | 0.44762
Total: 1477.3 Kilotonnes
Chart: USED OIL COLLECTION, 2020
| Collected | Not collected
Sales | 0.50189 | 0.49811
Chart: USED OIL DISPOSAL, 2020
| Fuel | Regenerated | Re-refined | All other -a
Sales | 0.55 | 0.19 | 0.15 | 0.11
Chart: USED OIL RE-REFINING AND REGENERATION, 2020
| Basestocks | All other
Sales | 0.7 | 0.3
Total: 817.6 Kilotonnes
Total: 410.1 Kilotonnes
Total: 62.6 Kilotonnes
It is estimated that of the total lubricant consumption of 1,477.3 kilotonnes in 2020, around 817.6 kilotonnes or 55% is generated as used oil in Russia. The balance is accounted for technical losses such as evaporation, combustion, leakages, and handling losses. There are some categories of lubricants, such as white oils, selected metalworking fluids, and greases that do not generate used oil. These lubricants are either reclaimed on‐site through various filtration methods or are used to extinction.
There is no firm statistics on the used oils’ market in Russia. Several waste-collecting enterprises do not keep records of waste including used oil and understate the volumes they collect. It is estimated that half of the used oil generated in the country is not collected properly. This waste is absorbed by the grey/black markets and is disposed by either using it as fuel without removing the hazardous materials as required by law or dumped into soil or water. Black market can be described as an illegal economic activity wherein, for example, counterfeit lubricants and fuels are sold. On the other hand, the grey market includes used oil or lubricants’ trade through supply chains that are legal in nature but not authorized or provided for by the original manufacturer. Grey market participants usually avoid paying taxes.
Out of the 410.1 kilotonnes of collected used oil, 226.1 kilotonnes is used as a fuel mostly by individuals. The remaining 139.4 kilotonnes of used oil are re-refined into basestocks or regenerated into lubricants, while 44.6 KT of sludge must be handled as per the norms for handling hazardous waste. The sludge, such as tar, asphalt, is utilized in the oxidized and compounded bitumen production used in the construction of roads, buildings and structures.
Regeneration is essentially a process, where impurities are removed, and the obtained product is reused as lubricant. Depending on the amount and nature of contamination and aging products in the used oil, its regeneration could be provided by several methods: physical (gravitational settling, separation, filtration, fuel distillation, rinsing with water), physiochemical (coagulation, adsorption), and chemical (sulfuric acid treatment, alkaline treatment).
a- sludge (tar, asphalt)

## Slide 204: Material Balance 2021
Taking into account, the absence of any progress in environmental legislation, as well as the fact that the implementation of existing regulations remains sluggish, no significant changes are expected in the market in 2021.
The generation and collection share are expected to remain the same as in 2020. However, EPR mechanisms which have been strengthened in 2021 are expected to increase the share of used oil collection in the market in the coming years.
Yet, the fuel application of the collected used oil is expected to remain the biggest share in 2021, accounting for 55%. Used oil regeneration share is expected to witness an increase due to growing offer of equipment applied for the used oil treatment, mainly used oil regeneration units. The modular regeneration units may be mounted on used oil generators’ site.
Chart: USED OIL GENERATION, 2021
Total: 1,506.7 Kilotonnes
Chart: USED OIL COLLECTION, 2021
Total: 835.2 Kilotonnes
Total: 419.2 Kilotonnes
Total: 64.1 Kilotonnes
Chart: USED OIL GENERATION, 2021
| Used oil generated | Lubricant lost
Sales | 0.55238 | 0.44762
Chart: USED OIL COLLECTION, 2021
| Collected | Not collected
Sales | 0.5 | 0.5
Chart: USED OIL DISPOSAL, 2021
| Fuel | Regenerated | Re-refined | All other-a
Sales | 0.55 | 0.2 | 0.15 | 0.1
Chart: USED OIL RE-REFINING AND REGENERATION, 2021
| Basestocks | All other
Sales | 0.7 | 0.3
a- sludge (tar, asphalt)

## Slide 205: Used Oil Generation
COVID-19 pandemic, imposed sanctions, and the OPEC+ agreement reduced business activities in 2020 in Russia, leading to a decrease in lubricants’ consumption. This resulted in a reduced volume of generated used oil in the country by about 10% as compared to 2018. The main reduction was witnessed in the automotive segment. However, commercial automotive industry has not been as badly impacted by COVID-19 as the consumer segment. Even during the lockdown, freight traffic was not interrupted.
Automotive used oil is usually generated in authorized service centers, workshops, and quick-lube centers as well as in garages. It is usually stored on site in a special area in drums or tanks to supply it then to collectors and re-refiners. Once the used oil is accumulated at the volume of about 3-4 tonnes, the generators contact the collector to collect the used oil.
Chart: USED OIL GENERATION RATES BY PRDOUCT IN RUSSIA, 2020
| PCMO | HDMO | Hydraulic Fluid | MCO | Industrial Engine Oil | Process Oil | All other-a
Series 1 | 0.85 | 0.75 | 0.75 | 0.6 | 0.54 | 0.12 | 0.45
Instead of visiting a workshop, most vehicle owners in Russia still prefer to change PCMO at the garages (non-authorized service centers). It is still common that the used oil generated at garages is used for heating purposes or dumped in soil or drains. Significant share of HDMO generated in independent garages is believed to be burned as fuel, mainly in agricultural sector.
The used oil generation rate varies depending on lubricant category. PCMO, transformer oil, and HDMO have the highest used oil generation rate of 85%, 80%, and 75%, respectively.
Quite often, used motor oils can be stored together in one tank, due to similar formulations of HDMO and PCMO. Hence, mixing used motor oils does not impact the quality of re-refining. However, industrial used oils should not be combined with used motor oils, as their formulations are quite different. Further, industrial oils such as turbine oils, hydraulic fluids, and transformer oils are considered to be of higher quality, and if they are mixed with other types of lubricants, it will not be possible to regenerate them.
USED OIL GENERATION BY PRODUCT IN RUSSIA, 2020 AND 2021 |  |  |  | 
LUBRICANT | KILOTONNES |  | % OF TOTAL USED OIL GENERATED | 
 | 2020 | 2021 | 2020 | 2021
HDMO | 251.2 | 255.8 | 30.7 | 30.6
PCMO | 202.9 | 208.8 | 24.8 | 25.0
Hydraulic fluid | 84.9 | 86.8 | 10.4 | 10.4
Industrial engine oil | 73.9 | 75.3 | 9.0 | 9.0
Process oil | 11.5 | 11.6 | 1.4 | 1.4
MCO | 2.2 | 2.2 | 0.3 | 0.3
All other-a | 191.0 | 194.9 | 23.4 | 23.3
Total | 817.6 | 835.2 | 100.0 | 100.0
a- Includes ATF, compressor oil, refrigeration oil, turbine oil, among others. |  |  |  | 

## Slide 206: Used Oil Collection
According to GOST 2146, used oil must be collected for further disposal in accordance with technical documentation for different lubricant types and grades. Normally, Russian used oil generators either procure services of certified used oil collectors or collecting enterprise approach generators to buy used oil. The latter scheme is widely adopted in the country by the collectors without a license in the grey used oil market, whose size cannot be assessed.
The biggest challenge in the Russian market is logistics. Due to the long distances, collectors tend to transport only large volumes of used oil to make profit. In case when collectors have to drive long distances for collecting small volumes of used oils, the costs can be covered by the generator. Price varies depending on the used oil type, its quality and volume, and distance. Some collectors have a strategy to accumulate used oils from different industrial plants as well as from automotive workshops for some time and only then transport it to regenerators or re-refiners.
Chart: USED OIL COLLECTION RATES BY PRDOUCT IN COUNTRY, 2020
| Hydraulic Fluid | Process Oil | PCMO | HDMO | Industrial Engine Oil | All other-a
Series 1 | 0.75 | 0.75 | 0.6 | 0.5 | 0.36 | 0.33
In 2020, used oil collection in Russia was estimated at 411.5 kilotonnes. Due to reduced volume of generated used oil in the country during the COVID-19 pandemic, the used oil collection declined by about 16% compared to 2019.
Overall, there are about 80 licensed collectors of used oil in Russia. Most collectors operate in the European part of Russia. A quarter of the total number of Russian collectors operate in Moscow region. Over the past two years, the official number of small collectors in the country increased by 4%. Usually, their used oil collection capacity varies depending on the size of the fleet. On average, they may collect small volumes up to 1000 liters of used oil per month.
An average used oil collection rate in Russia is 50%.
Automotive segment accounted for largest contributor in used oil collection. In 2020, automotive aftermarket constituted 65% of overall used oil collected in Russia.
Despite the fact that industrial segment accounted for lower share of used oil collection in 2020, the volume of one-time used oil collection in the industrial segment is greater than the used oil collected in the automotive segment.
USED OIL COLLECTION BY PRODUCT IN RUSSIA, 2020 AND 2021 |  |  |  | 
LUBRICANT | KILOTONNES |  | % OF TOTAL USED OIL COLLECTED | 
 | 2020 | 2021 | 2020 | 2021
HDMO | 125.6 | 127.9 | 30.6 | 30.5
PCMO | 121.7 | 125.3 | 29.7 | 29.9
Hydraulic fluid | 63.7 | 65.1 | 15.5 | 15.5
Industrial engine oil | 26.6 | 27.1 | 6.5 | 6.5
Process oil | 8.6 | 8.7 | 2.1 | 2.1
All other-a | 63.9 | 65.2 | 15.6 | 15.6
Total | 410.1 | 419.2 | 100.0 | 100.0
a- Includes ATF, compressor oil, refrigeration oil, turbine oil, among others. |  |  |  | 
Continued…

## Slide 207: Used Oil Collection
AUTOMOTIVE USED OIL COLLECTION BY SOURCES, 2020 |  | 
SOURCE | KILOTONNES | % OF USED OIL COLLECTED
Franchised Workshops (FWS) | 109.8 | 41.0
Independent Workshops (IWS) | 91.0 | 34.0
Quick Lubes | 32.1 | 12.0
Auto Parts Stores | 8.0 | 3.0
All other | 26.8 | 10.0
Total | 267.7 | 100.0
Waste oil is classified as a hazardous cargo of IV- class. It is subject to mandatory disposal and further processing in accordance with the Technical Regulations of the Customs Union 030/2012. These regulations were developed by the Russian Ministry of Energy along with Belneftehim (Belarus) and the Ministry of Oil and Gaz in Kazakhstan.
As per GOST 2146, used oil must be collected and utilized/re-refined by used oil generators, or used oil generators must outsource it to other companies to utilize and regenerate/re-refine used oil. Used oil generators usually procure the services of specialized organizations such as the Recycling Association to collect and transport the used oil to re-refiners or regenerators. Only organizations licensed by Rosprirodnadzor have the right to perform these works. The transportation procedure is established in regulatory documents. For example, during used oil transportation regulations allow for a maximum 95% fill of the tank.
Independent and authorized workshop remain the major source of used oil collection in Russia. Together, they accounted for 75% of overall automotive used oil collected in 2020.
Independent workshops lead in the used oil collection volume in consumer segment, while the franchised workshops leads the collection for HDMO. Further, due to larger volume of used HDMO collected through franchised workshops, franchised workshops is the leading channel for used oil collection in the automotive segment in Russia. FWS accounted for the 41% of the overall volume collected in the automotive segment in 2020 in Russia.
The major share of the consumer automotive lubricants market in Russia is taken by DIY segment. Instead of visiting a workshop, most car owners in Russia still prefer to change oil themselves, buying the lubricants in auto parts stores. However, even though auto parts stores remain the biggest channel of PCMO distribution in the country’s market, the rate of used oil collection in DIY segment is quite low due to uncontrolled disposal by the end users. Some auto parts stores with an available storage capacity may accept used PCMO from their customers with an increased level of environmental awareness. Such storage volume is relatively small, not greater than 5-4 drums (about one tonne).
Generally, used oil collectors do not work with small amounts of used oil generated in DIYers’ garages. In Russia, garages are usually united in “cooperatives” which may have a person responsible for managing, controlling, organizing, and solving any problems faced by customers and garage owners. This person is also responsible for the collection of used oil generated by DIYers. If such a person exists, he/she usually collects used oil and ships it to the used oil collectors. However, the used oil is rarely shipped and, in most cases, is used for heating on site.
Commercial vehicles that are still under warranty are maintained in authorized/franchised workshops (FWS). Fleet owners and operators follow OEMs' recommendations in terms of lubricants’ specifications to be applied. When the warranty period expires, the oil drain interval (ODI) tends to be reduced compared to ODI recommended by OEMs. Fleet owners often partner with used oil collectors.
Continued…

## Slide 208: Used Oil Collection
Large amount of wastewater containing emulsions, cleaning solutions, and even neat oils is produced daily by metallurgical industries in Russia. Many companies like Magnitogorsk Iron and Steel Works (MMK), Mechel, and NovoLipetsk Steel (NLMK), Severstal, among others, have a special unit within the companies that is responsible for waste disposal of metalworking fluids. Metalworking fluid contamination with mechanical impurities needs to undergo an assessment in order to determine a metalworking fluid’s correct application. The maximum permissible impurity content is regulated by the corresponding national standard GOST 21046-2015.
Small and medium size industrial enterprises in the private sector may establish a long-term contract with used oil collectors under which, the collectors collect the used oil for further processing. In some cases, collectors are buying industrial used oil from generators. The price of the collected used oil depends on its chemical composition, its volume, finished product demand, and the distance of the used oil generator’s site from the collector’s storage or re-refinery location.
Re-refiners may also participate in the used oil collection to control the quality and ensure steady supply of used oil. Usually, possessing a license, re-refiners carry out the transportation of used oil either by their own vehicles or by railway, in compliance with all technological and environmental requirements. Re-refineries are usually located in industrial areas not far from the used oil generators or potential consumers of re-refined basestocks.
However, a significant part of used oil collection takes place in the shadow sector of the economy, releasing large quantities of hazardous waste into the environment. Burning used oils as a cheap fuel which has not been processed to remove impurities, makes up a major share of the shadow market. In winter, the price of used oil can reach over RUB 150,000 (USD 2,077). Another uncontrolled way of used oil application – producing counterfeit lubricants. Scammers may buy the used oil from service stations or garages and then after basic regeneration may sell it as a new motor oil of popular brand. The size of the grey market of Russian used oil is difficult to define, however, the estimated volume of it was about 100-300 kilotonnes in 2020.
Post-warranty commercial vehicles are usually serviced either in independent workshops or on site. Although keeping a mechanic on site is prevalent for most of the fleet owners, this trend is slowly changing, particularly for small and mid-sized fleet owners. Attracted by the lower total cost of ownership, they tend to prefer an external specialist (a third-party service provider) who takes care of all mechanical issues including the arrangement of used oil collection.
Usually, before collection, used oil quality is checked to ensure that it does not contain antifreeze, coolants, etc. The price of the used oil of poor quality would be low. According to the market participants, used oil collection in Russia is challenging because almost no used oil generator gives used oil without water, and very few collectors collect and store different types of used oil separately. If the used oil generators sell used oil without water, they will get a better price for it.
Industrial used oil generated in state-owned companies is usually collected through auctions and tenders. Collectors who bid the highest price wins the auction to buy used oil. For example, used transformer oil may cost up to RUB 31,000 (USD 429.3) per tonne, used turbine oil might cost up to RUB 25,000 (USD 346.2) per tonne, used hydraulic oil about RUB 19,000 (USD 263.1) per tonne, and used motor oil may cost up to RUB 16,000 (USD 221.6) per tonne.
It is common for big industrial factories to collect and regenerate the used oil on site. In this case, a factory must have a special equipment and a license that allows to operate with used oil as per the requirements of Russian legislation. Used oil regeneration equipment use physical processes to remove solid pollution, water, and easy-boiling fractions from the oil in the initial stages of regeneration of used oils, followed by physicochemical processes (mainly coagulation and adsorption) and, where necessary, chemical regeneration techniques may be applied more frequently on industrial site. Regeneration equipment allows to achieve the restoration of the operational properties of the used oil to the maximum possible level i.e., lubricant with as much similar properties as the original lubricant. This regenerated lubricant is then used again in the system where it had been flushed from.

## Slide 209: Used Oil Disposal
The market is dictating the price, and it varies from one case to another. The factors affecting the used oil prices are the type of used oil, quality, volume, and the distance between the generator and the collector. The biggest challenge in Russia is logistics. Due to the large territory, used oil market in Russia is highly segmented and distributed across eleven time zones. The main markets of Moscow, St. Petersburg, Yekaterinburg, and Novosibirsk are well served by a growing number of licensed enterprises operating with used oil. However, official markets in smaller cities and rural area especially are not as developed. As a result, uncontrolled burning of used oil can be seen more often in smaller cities and rural areas.
The high energy potential of the used oil makes it a good fuel, utilized either separately or in combination with other fuels: one liter of used oil processed for fuel contains about 3,900 kJ of energy. Facilities where their own waste oil is incinerated on-site shall comply with the requirements of the Ministry of Natural Resources and Environment. They remove contaminants from used oil before burning it. However, in most cases, in garages, small auto service centers, and industrial installations like cement kilns, it is not done properly. Some of the DIYers are burning it as it is, although they are aware of the environmental damage, caused by this action.
Used oils are also utilized as a fuel in power plants, however, it is worth noting that, the inadequate disposal of used oil in industrial segment is less common than in the automotive, as regulatory bodies have tighter control over industries. In 2009, The Waste Recycling Association was established in Russia to bring together stakeholders in the used oil industry to reduce environmental risks.
Re-refining and regeneration together account for 34% of overall used oil market in Russia. As a result of regeneration, acids, various deposits, sediments, mechanical impurities, gases, water condensate and other substances that reduce operational characteristics and violate the physicochemical composition are removed from used oil. After the impurities including PCBs as well as metal and particulate matter removed from the used oil it may be then reused or sold as a regenerated lubricant. For example, after cleaning, these oils can be reused in turbines, pumps, gearboxes, circulation systems from which they were drained. Regenerated lubricants must comply with the established quality standards (acid number, oxidation stability, and flash point among the others).
USED OIL DISPOSAL BY PRODUCT TYPE, 2020 |  |  | 
LUBRICANT TYPE | KILOTONNES |  | 
 | FUEL | RE-REFINING | ALL OTHER-a
HDMO | 75.4 | 25.1 | 121.6
PCMO | 73.0 | 24.3 | 
Hydraulic Fluid | 25.5 | 6.4 | 
Other Industrial and Automotive Lubricants | 52.2 | 6.8 | 
Total | 226.1 | 62.6 | 
a – Includes regeneration, sludge (tar, asphalt), etc. |  |  | 
Chart: USED OIL DISPOSAL IN RUSSIA, 2020
| Fuel | Regenerated | Re-refined | All other-a
Sales | 0.55 | 0.19 | 0.15 | 0.11
Total: 410.1 Kilotonnes
a- sludge (tar, asphalt)
Continued…

## Slide 210: Used Oil Disposal
In 2021, the used oil disposal is similar to 2020.
USED OIL DISPOSAL BY PRODUCT TYPE, 2021 |  |  | 
LUBRICANT TYPE | KILOTONNES |  | 
 | FUEL | RE-REFINING | ALL OTHER-a
HDMO | 76.7 | 25.6 | 124.0
PCMO | 75.2 | 25.1 | 
Hydraulic Fluid | 26.0 | 6.5 | 
Other Industrial and Automotive Lubricants | 53.2 | 6.9 | 
Total | 231.1 | 64.1 | 
a – Includes regeneration, sludge (tar, asphalt), etc. |  |  | 
Chart: USED OIL DISPOSAL IN RUSSIA, 2021
| Fuel | Regenerated | Re-refined | All other-a
Sales | 0.55 | 0.22 | 0.15 | 0.08
Total: 419.2 Kilotonnes
a- sludge (tar, asphalt)

## Slide 211: Used Oil Re-Refining
MAJOR USED OIL RE-REFINERS IN RUSSIA, 2020 |  |  | 
COMPANY | KILOTONNES |  | 
Company | USED OIL FEED CAPACITY | RE-REFINED BASESTOCK CAPACITY | RE-REFINED BASESTOCK PRODUCTION
Rosa-1 | 60.0 | 42.0 | 29.0
Perm Oil Factory | 10.0 | 7.0 | 5.0
Tekh-engineering | 5.0 | 3.5 | 2.0
Vtornefteprodukt | 4.8 | 3.4 | 2.5
Roskhim | 4.0 | 2.8 | 1.9
Shaumyan's Oil Plant | 3.0 | 1.8 | 1.3
Rikos | 2.0 | 1.4 | 1.2
Orgsintezkhim | 2.5 | 1.9 | 1.0
Total | 91.3 | 63.8 | 43.9
Depending on the technology and equipment used by the re-refiners in Russia, two or three fractions of basestocks are obtained. The recovered basestocks are used in blending of hydraulic, transmission fluids, motor oils, cutting fluids, and greases that comply with GOST standards. The lubricants are customized as per the customer’s requirements. However, re-refineries also use virgin basestocks in case they do not have enough re-refined basestocks to produce lubricants. They will mix the two types of basestocks and blend lubricants to sell it to the customers.
Technologies used for used oil re-refining include following steps: settling at elevated temperatures, coagulant treatment, and mineral absorbent filtration. Then distillation process follows in the rectification columns: in the atmospheric pressure and in vacuum. The vacuum distillation system makes it possible to reduce the operating temperatures of the process and to improve the quality of the basestocks produced. As a result of re-refining, three fractions of basestocks are obtained: 150SN, 250SN, and 350SN, oil residues (asphaltene and colloid) and some amount of diesel fuel are also emitted.
Currently, there is only one big re-refinery in Russia: Rosa-1 based in Moscow region with an annual used oil feed capacity of around 60 kilotonnes. It is followed by the Perm Oil Factory engaged in the production and sale of lubricants.
The other re-refining players in the market such as Tekh-engineering, Vtornefteprodukt and Roschim, are relatively small. However, the number of small players in the country has slightly increased over the past three years due to growing environmental awareness. Additionally, due to the API Group I basestocks price increase due to COVID-19 crisis, the used oil re-refining was more profitable in 2020. The re-refined basestock production increased to about 43.9 kilotonnes, which is about 2% more than re-refined basestocks production in 2018.
Currently, Russian re-refiners can produce only re-refined Group I basestocks, which is not very attractive in the country and is mainly used for the domestic production of low-tier lubricants, which are also known as GOST-oils or I-oils (unbranded lubricants produced in Russia using Group I basestocks with minimum degree of additives or even no additives). Additionally, Russian market is oversupplied with Group I basestocks and the domestic basestocks producers including lubricant blenders are gradually upgrading their facilities to produce Group II basestocks. This makes re-refined Group I basestocks unattractive for lubricant blenders in the Russian market.
Low demand for re-refined basestocks among the major lubricant manufacturing companies in Russia could be also explained by the lack of awareness about the quality of such basestocks. Many lubricant blenders do not use re-refined basestocks for lubricant production, considering them to be of inferior quality as opposed to virgin basestocks.
The price of re-refined basestocks is determined based on the purchase price of the used oil, refining costs, and taxes on the final product. Large re-refiners sell their basestocks through tenders, while small re-refiners usually sell them on a contractual basis to those enterprises from which the used oil was purchased. For example, companies like Rikos and Shaumyan's Oil Plant operate in a closed loop model in the country.

## Slide 212: Used Oil Re-Refiner Profiles
Rosa-1
Rosa-1 is the largest re-refiner in Russia, situated in Ryazan in European part of Russia. It was established in 1992 to liquidate the spilled petroleum products from an oil refinery in Novokuibyshevsk.
The estimated volume of used oil collected by Rosa-1in 2020 accounted for almost 80 kilotons. It has increased by a CAGR of 7% compared to the figures of 2018. The company has a used oil re-refining capacity (used oil feed capacity) of around 60 kilotonnes per year. However, 15-20 kilotonnes of used oil is usually stored in inventory.
Used oils treatment is provided in two stages: at first, water and mechanical impurities are removed at elevated temperatures in a facility which includes 36 reservoirs with a volume of 60 to 120 cubic meters. The second stage runs in vacuum rectification column. Deep vacuum allows to perform a clear separation of fractions and obtain highly refined basestocks.
Synthetic materials deduced during treatment processes are gathered and utilized by Rosa-1. The contact treatment uses a natural mineral absorbent, which is an ecologically clean product according to Rosa-1.
Sludge and distillation residue obtained after rectification is later used for low-quality heating oil production, and bleaching clay is used by the expanded clay plant after coagulation process.
The company produces Group I basestocks. Rosa-1 yet does not plan to upgrade its re-refining capacity to the higher-tier basestocks.
Using refined basestocks Rosa-1 produces finished lubricants for both industrial and automotive segments. The company’s lubricants storage capacity accounted for about 200 kilotonnes in 2020.
Rosa-1 collaborates with around 30 collectors across Russia. All collected used oil must be checked by Rosa-1 technicians for GOST 21046 compliance. The company also collects the used oil by its own means. It owns 32 specialized trucks, the capacity of which varies from 2 to 33 cubic meters.
The collecting services are provided on the expenses of Rosa-1 if the volume of used oil is between 500-1,000 liters. If the volume of used oil is below 500 liters, generators must pay for its transportation. In case the volume exceeds 1,000 liters, Rosa-1 usually buys it, depending on the agreement with the used oil generator. The price is determined based on several factors such as used oil quality, volume, human resource costs, the complexity of used oil collection, and its transportation.
After collection and re-refining, Rosa-1 produces different lubricants and coolants for the domestic market.
  Transmission fluids;
  Differential fluids such as GL-5 SAE 85w-90 and Nigrol
  Hydraulic fluids
  Industrial Gost-Oils (MK-20, MK-40, I-20 and I-30 among the others)
  Coolants

## Slide 213: SWOT Analysis
STRENGTHS | WEAKNESSES
Rosa-1 is the largest re-refiner in Russia. Companies working with ROSA-1 receive the full range of services: development and maintenance of environmental documentation; provision of special packaging for separate accumulation of hazardous waste; used oil collection by means of trained specialists and specialized transport. Rosa-1 collaborates with Waste Recycling Association in providing professional, technical and QC services to the customers and used oil generators. Except for the basestocks production, Rosa-1 also sells finished lubricants. | Logistical issues. Limited collection of used oil Only re-refined Group I basestocks could be produced by the company Despite the active assistance of all market participants, as well as regulatory and supervisory authorities, the market for the processing of used oils and lubricants is only at the beginning of its development. The absence of serious State regulation does not facilitate the collection, storage, transport and processing of used oils.
OPPORTUNITIES | THREATS
Rosa-1 is planning the construction of another re-refinery for the processing of used oil and for thermal destruction of hazardous waste in the Ural-Siberian part of Russia. At present, research is being carried out on the marketing of the hazardous waste situation in these regions. | Russian market is oversupplied with Group I basestocks, which creates poor business prospects for the re-refiners in the country. High cost of collection, storage, and transportation to the point of processing of used oils reduces the profitability of the operation.

## Slide 214: Used Oil Re-Refiner Profiles
Perm oil factory
Perm Oil Plant (Пермский завод масел) was established in 1992. The factory is engaged in the production and sale of petroleum products, oils, and technical fluids. The average production volume is about 25 kilotonnes per year. The product range includes heating oil, engine oils, gear oils, industrial oils, and hydraulic fluids, among others.
The average annual collection of used oils is estimated at around 10 kilotonnes, with the maximum possible collection volume of 12 kilotonnes per year. The company has a storage capacity of 2 kilotonnes. It normally collects used oils from the generators once the used oil volume reaches 3-4 tonnes. It operates in a radius of 1,000 km around the city of Perm. It filters used oils, removes water, uses vacuum distillation for re-refining to produce basestocks, and then adds additives to produce lubricants. Perm oil factory re-refines around 70% of collected used oils, while 20% is sold as fuel. The remaining 10% is waste and is disposed off as per the law.
In addition to automobile oils and hydraulic fluids, the plant is engaged in processing used metalworking fluids as well. Those fluids are divided into fractions. Each fraction is used for its intended purpose in production. The purified aqueous fraction is sent for re-preparation of cutting fluids or other technical needs.
STRENGTHS | WEAKNESSES
Perm oil factory is a mature market participant. Except for the basestocks production, perm oil factory also produces finished lubricants. As part of the EPR, perm oil factory regularly informs the consumer of the need to hand over used oils to licensed organizations for disposal with the indication of collection points. | Logistical issues. Limited collection of used oil Only Group I basestocks could be produced at the facility Despite all the existing environmental risks, most of the used oil is incinerated and most of it is discharged into water bodies, sewage systems or soil.
OPPORTUNITIES | THREATS
The introduction of mini-complexes for the regeneration of used oils to meet the needs of small areas (regions or cities with a population of 1-1.5 million people) will reduce transportation costs. The production of high-quality end products such as motor oils and industrial lubricants, makes such mini-complexes economically attractive as they are closer to the production of these products from virgin basestocks. | In view of the low profitability of the used oil recovery process, it is necessary to grant tax concessions or additional tariffs from the State in accordance with current European practice.

## Slide 215: Re-Refined Lubricants
Re-refined lubricants represent a negligible share in the Russian lubricants market. End users are not aware of the benefits of lubricants made from re-refined basestocks. Consumers still continue to consider lubricants made from re-refined basestocks as a product of poor quality.
The Russian lubricants market is driven by the brand. Russian car owners, for example, tend to prefer foreign brands, such as Shell, Mobil, and Castrol. Without the support of the lubricant majors (international and local ones), the prospects for the market of re-refined lubricants are poor in the country. There is no indication that the companies such as Shell or ExxonMobil use re-refined basestocks while blending lubricants. The Russian companies like LUKOIL, Rosneft, and Gazpromneft-Lubricants also do not use re-refined basestocks in its products as they have sufficient in-house supply of virgin basestocks.
Currently, industrial facilities controlled by the Russian government must comply with the import substitution policy declared by the government and must select local suppliers to award the procurement contracts to help shore up the Russian economy. Import substitution seems to have a limited impact on growth so far. The partial cyclical recovery on the back of rising crude oil prices is unlikely to go hand in hand with a reallocation to higher value-added non crude oil related activities.
However, local lubricant suppliers have been increasing sales of their premium products over the past three to four years. Low-tier lubricants, GOST-oils have been witnessing growing demand as well. Large industrial factories and mines in the country are supplied with locally-made low-cost industrial lubricants (usually GOST-type or I-oils type), as most of their industrial machinery is outdated. It is assumed that the independent lubricant blenders in Russia such as Delfin Group, Obninskorgsintez, and Devon, among the others use re-refined basestocks to produce lubricants.
Valvoline, on the other hand, decided to build its own marketing campaign on green circular economy. In 2011, the company introduced the NextGen blend, 50% of which is re-refined basestocks. Valvoline especially likes to mention that even the cars of the NASCAR racing series are filled with NextGen.
Despite the fact that Valvoline brand oils have been sold in Russia, the NextGen mixture is not included in the present product portfolio of Valvoline in the country.
Generally, there is no demand of re-refined lubricants in Russia.

## Slide 216: Finished Lubricant Market Outlook
Chart: PROJECTED FINISHED LUBRICANT MARKET IN RUSSIA, 2020-2030
| Industrial | Commercial | Consumer
2020 | 730.4 | 460.5 | 286.4
2021 | 743.4 | 468.3 | 295
2025 | 799.9 | 501.2 | 332.7
2030 | 840.2 | 536.5 | 389.8
It is estimated that the total demand for finished lubricants in Russia will increase from 1,477.3 kilotonnes in 2020 to 1,766.5 kilotonnes in 2030.
Affected by the COVID-19 pandemic, industrial lubricants demand is expected to grow at a CAGR of 2% between 2020 and 2025, followed by a growth at a CAGR of 1.6% between 2025 and 2030. Local/Domestic lubricants suppliers are actively working on improving the quality and range of their products, aiming to manufacture premium and high-quality lubricants while increasingly obtaining foreign OEMs’ approvals for their lubricants to gain market share.
The leading trend in the Russian lubricants market is a gradual decline of imports in accordance with the import substitution policy. In order to compete with the continuing development of their blending capacity by domestic majors, foreign suppliers such as Shell and TotalEnergies have started local production of lubricants in Russia.
Traditionally, the industrial sector is the least developed in terms of synthetic lubricants penetration (based on API Group III, Group IV); however, the demand for these high-performance lubricants is expected to increase over the forecast period driven by the modernization of the machinery and increasingly abundant local supply.
The renewal of the old fleet of vehicles is expected to remain the key driver of market development during the forecast period. The truck segment is expected to show the strongest growth among all commercial vehicles based on governmental support programs. The revival of vehicle production activities is also expected to have an impact on lubricant demand. Heavy-duty vehicles are now commonly being factory-filled with synthetic and semi-synthetic products for fill-for-life/longer ODI.
Considering the low level of passenger vehicle ownership in Russia (about 310 units per 1,000 people, which is more than 40% lower than the average in Western Europe), further growth of the vehicle parc is expected in the forecast period, leading to positive consumer lubricants demand.
Going forward, the demand for synthetic and semi-synthetic PCMO will see some growth due to the modernization of the fleet. The overall demand for full synthetic products in the consumer segment is expected to grow at a strong pace of a CAGR of more than 5%. By 2025, SAE 0W-20, 0W-30, 5W-20, and 5W-30 PCMO viscosity grades will experience the fastest growth rate in the market and will most likely grow in sales at a CAGR of 6.6% on average.

## Slide 217: Used Oil Industry Outlook 2025
Chart: USED OIL DISPOSAL, 2025
| Fuel | Regenerated | Re-refined | All other-a
Sales | 0.55 | 0.25 | 0.13 | 0.07
Chart: USED OIL COLLECTION, 2025
| Collected | Not collected
Sales | 0.53 | 0.47
Chart: USED OIL RE-REFINING AND REGENERATION, 2025
| Basestocks | All other
Sales | 0.7 | 0.3
Chart: USED OIL GENERATION, 2025
| Used oil generated | Lubricant lost
Sales | 0.58 | 0.42
Total: 1,633.8 Kilotonnes
Total: 947.6 Kilotonnes
Total: 502.2 Kilotonnes
Total: 65.3 Kilotonnes
The Russian industrial sector is characterized by a high degree of equipment wear. Its modernization and the implementation of energy-saving technologies, especially in automotive assembly, metallurgical, and oil and gas industries, would become key priorities. This is expected to give the impetus for the increase of used oil generation in the forecast period.
Used oil collection rate is expected to grow as well by 2025 in accordance with the growing number of Waste Recycling Association’s members (lubricant manufacturers, used oil generators, and re-refineries). This will allow Rosprirodnadzor to have a broader register of the used oil generators in Russia, the «grey» and illegal collectors’ activities are expected to witness tighter control.
Used oil regeneration share is expected to witness an increase due to growing capacities of the used oil treatment. An independent lubricant blender Pushkinskiy Zavod plans to build the used oils’ regeneration facility in Moscow region with a tank farm for storing products. At the facility with an area of ​​almost 20,000 square meters, purification, filtration, and dehydration systems will be installed. The estimated volume of investments account for RUB 1 billion. The commissioning of the facility is scheduled for the spring of 2022.
Chart: USED OIL COLLECTION, 2021
a- sludge (tar, asphalt)

## Slide 218: Used Oil Industry Outlook 2030
Chart: USED OIL DISPOSAL, 2030
| Fuel | Regenerated | Re-refined | All other
Sales | 0.54 | 0.29 | 0.12 | 0.05
Chart: USED OIL RE-REFINING AND REGENERATION, 2030
| Basestocks | All other
Sales | 70 | 30
Chart: USED OIL GENERATION, 2030
| Used oil generated | Lubricant lost
Sales | 0.61 | 0.39
Total: 1,766.5 Kilotonnes
Chart: USED OIL COLLECTION, 2030
| Collected | Not collected
Sales | 0.56 | 0.4
Total: 1,077.6 Kilotonnes
Total: 603.4 Kilotonnes
Total: 72.4 Kilotonnes
By 2030, used oil generation rate is expected to reach 61%, considering ongoing implementation of energy-saving technologies. It is expected that the automotive sector will witness an increased demand in the car’s aftermarket. The share of foreign vehicles in the overall Russian passenger vehicle parc is expected to increase significantly due to the growing number of foreign cars’ imports after the ICE ban in Europe.
Strict enforcement of regulations followed by audits from Rosprirodnadzor are expected to ensure the increased rate of the legal collection of used oil in the country. Following the global trends, the level of environmental awareness and concerns among Russian used oil generators is expected to increase, and the fuel application of the used oil will be eliminated, or it may be banned by the law.
Some growth of the re-refineries’ capacity is expected by 2025, due to ongoing process of modernization and the upgrade of the existing re-refinery capacities. Rosa-1 is expected to launch another used oil re-refinery in the Ural-Siberian region by 2025. The new facility is expected to produce re-refined basestocks of API Group I with a projected re-refined basestock capacity of 16 kilotonnes a year. The re-refined basestocks are expected to be used for producing industrial oils such as hydraulic fluids, heat-transfer fluids or plasticizing oils, as well as emulsifiers and metalworking fluids.
a- sludge (tar, asphalt)

## Slide 219: Re-Refined Basestock Capacity Outlook
RE-REFINED BASESTOCK CAPACITY, 2020, 2021, 2025, AND 2030 |  |  |  | 
 | KILOTONNES |  |  | 
COMPANY | 2020 | 2021 | 2025 | 2030
Rosa-1 | 42.0 | 42.0 | 58.0 | 58.0
Perm Oil Factory | 7.0 | 7.0 | 7.0 | 7.0
Tekh-engineering | 3.5 | 3.5 | 3.5 | 3.5
Vtornefteprodukt | 3.4 | 3.4 | 3.6 | 3.6
Roskhim | 2.8 | 2.8 | 2.8 | 2.8
Shaumyan's Oil Plant | 1.8 | 1.8 | 1.8 | 1.8
Rikos | 1.4 | 1.4 | 1.6 | 1.6
Orgsintezkhim | 1.9 | 1.9 | 1.9 | 1.9
Total | 63.8 | 63.8 | 80.2 | 80.2
Russian re-refiners produce only API Group I basestock in 2020. The basestock demand in the lubes market in the country is shifting from API Group I to Group II and Group III. Due to this trend, re-refined Group I basestocks remain unattractive for lubricant blenders. As of now, there is no announcement of any upgradation in the country.
The growth of the re-refineries’ capacity is expected by 2025, due to ongoing process of modernization and the upgrade of the existing re-refinery capacities. Rosa-1 is expected to launch another used oil re-refinery in the Ural-Siberian region by 2025 with a projected annual re-refined basestock capacity of 16 kilotonnes.
Small re-refiners such as Rikos, Orgsintezkhim, and Shaumyan's Oil Plant will keep operating in a closed loop model in the country over the forecast period, selling the re-refined basestocks on a contractual basis to those enterprises from which the used oil was purchased.

## Slide 220: Market Evaluation
Opportunities
Waste Recycling Association currently is the main driver heading toward making unorganized and uncontrolled market of used oil in Russia more organized and formal.
Russian majors keep investing in new production capacities, upgrading existing Group I basestock refineries to produce Group II and III basestocks. This is expected to have a positive impact on used oil re-refining in Russia. However, demand for Group I basestocks is also expected to reduce in Russia, partly negating the impact of the reduction in Group I basestocks supply in the country. As a result, re-refining is expected to remain stable at around 10%-11% in the forecast period of 2020-2030, however, the focus is expected to be on the used oil regeneration.
Plans of basestocks’ manufacturers to increasingly produce Group II and III basestocks as well as plans for lubricant blenders to increasingly adopt Group II basestocks is expected to boost used oil regeneration in Russia. It is expected to grow at a CAGR of 3.9% by 2025 and at a CAGR of 6.9% by 2030.
Challenges
Challenges in the used oil industry will be mentioned.
Currently, overcapacity for Group I basestocks is adversely impacting the growth of re-refined basestock in Russia.
Due to the large distances, in Russia, used oil collectors are usually operating in a radius of 500 – 1,000 km around the industrial hubs, many garages in the rural area may remain uncovered by the collectors’ services.
The absence of serious State regulation makes it difficult to collect, store, transport and process the used oils in the country.
The unorganized and fragmented market of the used oil in Russia, results in misuse of used oil in the form of industrial fuel.
The re-refining of basestocks is not likely to grow during 2020-2025, even though the used oil collection is expected to grow. However, due to plans to build new re-refineries or expand the capacities of existing re-refineries, after 2025, the used oil market is expected to witness gradual development of the re-refining volume.

## Slide 221
United States and Canada

## Slide 222: USA and Canada Market Synopsis
Chart: USED OIL MATERIAL BALANCE IN USA AND CANADA, 2021-2030 (MILLION TONS)
| Finished Lube Demand | Used Oil Generated | Used Oil Collected | Used Oil Re-refined | RRBO produced
2021 | 8147.5 | 4685.7 | 3435.8 | 1167.2 | 758.7
2025 | 8465.7 | 4994.8 | 3696.1 | 1352.8 | 879.3
2030 | 8214.5 | 4928.7 | 3696.5 | 1352.9 | 879.4
Used Oil Regulations
In the US, Regulation 40 CFR part 279 established by the Environmental Protection Agency (EPA) is the primary federal regulation for the management of used oils.
In the US, every activity from generation to collection to its disposal including its usage as fuel or re-refining is covered under regulations .
In Canada, the focus of regulation is mainly on the crankcase oils, as they generate most of the used oil in Canada.
In Canada, the reprocessing of used oil into lubricant or re-refining used oil into basestocks is allowed. However, in provinces such as British Columbia, permits are required to re-refine used oil.
Used Oil Material Balance
In the United States and Canada, some re-refiners also perform used oil collection as it reduces collection cost and ensures the quality of the used oil collected.
The used oil generated by industrial generators is either used onsite in space heaters and furnaces as fuel or collected by collectors. The usage of used oil for burning as fuel is higher in the industrial segment than in the automotive segment.
Out of the used oil collected in North America, approximately 60% is re-refined. This includes re-refining to basestocks, VGO/MDO, and regeneration of transformer oils. Approximately two-thirds of the re-refined used oil is re-refined to basestocks.
Re-refining is expected to grow as new re-refineries are commissioned in the region during the forecast period.
MAJOR USED OIL RE-REFINERS IN USA AND CANADA, 2021-2030 |  |  | 
 | RE-REFINED BASESTOCKS CAPACITY (KILOTONNES) |  | 
COMPANY | 2021 | 2025 | 2030
Safety-Kleen (Clean Harbors) | 255.0 | 255.0 | 255.0
Safety-Kleen (Clean Harbors) | 190.0 | 190.0 | 190.0
Heritage-Crystal Clean | 160.0 | 160.0 | 160.0
Universal Environmental Services | 133.0 | 133.0 | 133.0
Bango Refining (Clean Harbors) | 70.0 | 70.0 | 70.0
Heartland Petroleum (Clean Harbors) | 62.0 | 62.0 | 62.0
Universal Lubricants (Clean Harbors) | 40.0 | 40.0 | 40.0
Olein Recovery | 23.0 | 23.0 | 23.0
Terrapure (GFL) | 20.0 | 20.0 | 20.0
Ecolube Recovery | 18.0 | 18.0 | 18.0
Rational Resource | 13.0 | 29.0 | 29.0
Regen III-a | - | 192.0 | 192.0
Puraglobe-a | - | 49.0 | 49.0
Mesa Oil Recycling-a | - | 11.0 | 11.0
All other | 38.0 | 38.0 | 38.0
Total | 1,022.0 | 1,290.0 | 1,290.0
a– These projects are in financing or construction stage and will open in the near future. Their basestock capacity is calculated with the 65% yield rate for the re-refineries. |  |  | 
Used Oil Re-refining
As the demand for virgin Group I basestocks is declining and shifting toward Group II and Group III basestocks, the re-refining basestocks market is also following the same trend. Most of the re-refiners currently operating in the United States and Canada are producing Group II/II+ basestocks. The re-refined basestock capacity is expected to grow 26% during 2020 to 2025 as new players enter re-refining in the United States and Canada to cater to the growing demand for re-refined basestocks.
At present, no re-refiner has announced to close its re-refining facility in the countries in the near future. It is expected that Evergreen Oil, operating its re-refining facility in Irvine, CA, will close its plant in 2021. However, there has been no official announcement. Currently, Evergreen Oil is producing Group II/II+ basestocks in the United States.
Opportunities
Re-refiners, who can produce re-refined Group III basestocks have an opportunity to grow as demand for Group III basestocks, especially in the consumer segments, grows in the region.
Challenges
However, the re-refining scenario in the United States and Canada may not witness any drastic changes in the forecast period because lubricant demand is expected to decline slightly, due to increasing use of synthetic and semi-synthetic oils and a flat automotive market. Also, no major change in used oil generation, collection, and re-refining is expected to happen in these two countries. However, the existing situation does provide an opportunity for consolidation as well as forward or backward integration to companies in the industry.

## Slide 223: Economic Background
The United States is the largest economy in North America. The country has 50 states.
  According to the International Monetary Fund (IMF), its gross domestic product (GDP) at current prices was USD 20.9 trillion as of 2020 and is expected to increase to USD 22.9 trillion in 2021, supported by a sharp rise in consumer spending due to government financial support.
  In 2020, Canada’s GDP at current prices is about USD 1.6 trillion, which is around one-tenth of the U.S. GDP.
As of 2020, the total population of the United States was 329.8 million, while Canada’s total population was 38.0 million. Both the United States and Canada have a modern economic system, which is dominated by the service industry. Canada has an economy resembling the United States in terms of market-oriented policies, production base, and high living standards.
In 2020, the real GDP decline 3.4% and 5.3% in the United States and Canada, respectively, mainly due to a decline in the output of major industries such as agriculture, energy, technology, service, and manufacturing caused by COVID-19.
According to the IMF, in 2020, the United States and Canada had GDP per capita of USD 63,360.0 and USD 43,290.0, which increased to USD 69,380.0 and USD 52,790.0, respectively, in October 2021.
The opening of the economic activity post-COVID-19 pandemic coupled with the legislative response to support the economy with laws such as the Coronavirus Aid, Relief, and Economic Security Act (CARES Act); the Consolidated Appropriations Act; and the American Rescue Plan Act in 2020 and 2021 have boosted economic output in 2021.
  Moreover, with the ongoing effects of fiscal support, pent-up demand from consumers for face-to-face services, and the strength in labor markets and asset prices, economic growth is poised to be strong for the remainder of 2021.
SELECTED ECONOMIC CHARACTERISTICS OF COUNTRY, 2020 |  |  |  | 
KEY INDICATOR | UNITED STATE | UNITED STATE | CANADA | 
 | 2020 | 2021 (TILL OCTOBER) | 2021 | 2021 (TILL OCTOBER)
Population (Million) | 329.8 | 330.6 | 38.0 | 38.2
GDP at current prices (USD Billion) | 20,890.0 | 22940.0 | 1,640.0 | 2020.0
GDP per capita, current prices (USD) | 63,360.0 | 69,380.0 | 43,290.0 | 52,790.0
Real GDP Growth | (3.4) | 6.0 | (5.3) | 5.7
Inflation, average consumer prices (Annual % change) | 1.2 | 4.3 | 0.7 | 3.2
Current account balance (% Of GDP) | (2.9) | (3.5) | (1.8) | 0.5
Source: International Monetary Fund |  |  |  | 
Continued…

## Slide 224: Economic Background
With about a quarter of the world’s overall economic output, the United States was the world’s largest economy in 2020.
  The country has a strong manufacturing base and service sector. Industrial output in the country is the second-largest in the world.
According to the IMF, the country’s real GDP growth rate (annual change) decreased from 2.9% in 2018 to 2.3% in 2019 to -3.4% in 2020.
The consecutive decline in the country’s GPD growth is due to trade tensions between the United States and China. Moreover, the COVID-19 outbreak has further impacted global trade activities.
  The trade war between the United States and China aims at imposing huge tariffs and trade barriers resulted in a trade deficit in 2019, leading to a slight decline in the country’s GDP. However, in January 2020, the two countries signed the phase 1 of the trade deal in which China agreed to buy at least USD 200 billion more of U.S. goods and services over two years.
  In Q1 2020, the U.S. real GDP declined 5.0%, reflecting the response to the spread of COVID-19. In Q2 2020, the real GDP further declined 31.4% due to a decline in consumer spending, exports, private inventory investment, and state and local government spending. In Q3 2020, GDP rebounded strongly by 33.4% as restrictions were eased due to which business activities recovered. This coupled with government support boosted economic growth. In Q4 2020, the GDP grew 4.3%.
  In Q1 and Q2 2021, the GDP grew 6.3% and 6.7%, respectively, mainly due to government assistance payments in the form of loans to businesses and grants to state and local governments. However, in Q3 2021, the GDP declined due to the resurgence of COVID-19 resulting in new restrictions in some parts of the country.
Canada’s consumption patterns, living standards, and market-oriented economic system are very similar to those of the United States.
  Canada is a member of the Group of 7 (G7) nations of the world’s advanced economies and, in recent years, has led the G7 countries in economic growth.
  The country ranked 23rd in the world for ease of doing business, as well as per capita GDP by The World Bank. The country’s ease of doing business score is 79.6; the highest score in the world is 86.8.
  The World Economic Forum’s global competitiveness index places Canada at the 14th place.
  Economic activity in 2019 slowed toward the end of the year, with softening labor market conditions leading to a weak transition into 2020. The COVID-19 pandemic further hampered economic activity as public health guidelines significantly limited business and household activities in 2020. This led to labor force reductions and high unemployment.
  The country’s real GDP growth rate (annual change) declined from 2.4% in 2018 to 1.9% in 2019 to -5.3% in 2020.
As per IMF world economic outlook, October 2021, the country’s real GDP growth is recovered to 5.7% in 2021.
  In Q2 2021, the real GDP declined 0.3% in Canada, following 1.4% growth in Q1 2021. The decline in Q2 2021 was due to a decline in export volumes and in-home resale activities. In Q3 2021, the real GDP growth was 1.3%, driven by increased household spending and exports.

## Slide 225: Vehicle Population
Per the OICA, in 2020, the production of consumer and commercial vehicles contracted by over 20% in North America. However, the sales of vehicles in the region declined only 16%.
  The COVID-19 pandemic adversely impacted the automotive industry in the short term. The first half of 2020 saw large-scale curtailing of industrial activity and automotive mobility (commercial and personal), in order to contain the spread of COVID-19.
While the automotive sector witnessed a steep decline, it still contributed 3% of the country’s GDP in 2020. The sector has been one of the biggest employers in the United States. As per the U.S. Bureau of Labor Statistics, the sector employed 4.3 million in 2019.
In the United States, total vehicle sales were around 14.5 million units in 2020. The corresponding figure for Canada is 1.5 million units.
  Out of the total vehicles sales in the United States, commercial vehicles account for about 11.0 million vehicles or 76.5% of the total vehicle sales in the country. Passenger vehicles, including cars and motorcycles, accounted for the remaining 3.4 million vehicles in the country.
  In Canada, passenger vehicle sales account for about 0.3 million units or 20.9% of the total vehicle sales in the country in 2020. Commercial vehicles such as trucks, tractors, and buses account for the remaining 1.2 million units in Canada.
Million units
Chart: VEHICLE SALES BY VEHICLE TYPE IN UNITED STATE, 2019-2020
| Passenger vehicles | Commercial Vehicles
2019 | 4.7 | 12.3
2020 | 3.4 | 11.1
SOURCE: International Organization of Motor Vehicle Manufacturers (OICA).
Chart: VEHICLE SALES BY VEHICLE TYPE IN CANADA, 2019-2020
| Passenger vehicles | Commercial Vehicles
2019 | 0.5 | 1.4
2020 | 0.3 | 1.2
Million units
SOURCE: International Organization of Motor Vehicle Manufacturers (OICA).
Continued…

## Slide 226: Vehicle Population
in 2020, vehicle production declined 28.2% to reach 1.4 million units in Canada.
  Passenger vehicle production declined from 2.0 million units in 2018 to 1.9 million units in 2019, due to volatile fuel prices and increasing borrowing rates leading to high financing costs. In 2020, due to the pandemic impact, new motor vehicle production plunged by 29.7% to reach 1.3 million units.
  Most dealership showrooms across Canada were required to close for at least six weeks due to the pandemic.
  Passenger car sales declined 35.8% in 2020. Canadians continued to prefer pick-up trucks or light trucks, which is reflected in vehicles sales of 2020.
Vehicle production in the United States witnessed a decline of 3.6% from 11.3 million units in 2018 to 10.9 million units in 2019.
  This decline resulted due to decrease in the production of passenger vehicles, which declined at a rate of 9.8 % in 2019. Also, automotive manufacturers are encouraging the production of commercial vehicles, including heavy trucks, pickup trucks, and SUVs, as they are more profitable compared to passenger vehicles. The production of heavy trucks increased 5.2% in 2019 compared to 2018, supported by higher demand for the transportation of cargo and goods. The American Trucking Association (ATA) findings reveal that over 71% of the freight tonnage across the United States is transported using trucks.
  In 2020, the country witnessed decline in every segment including light-duty trucks, passenger cars, and heavy trucks. Among them, the production of heavy trucks witnessed the largest decline of 37.9%, followed by the production of passenger vehicles by 29% in 2020. Closure of production facilities in Q2 2020 and lower production rate for the rest of the year due to reduced demand for passenger cars and heavy trucks were among the major reasons for decline in the overall production.
The country witnessed recovery in production in Q1 and Q2 2021. According to OICA, the automotive production increased 35.8% in the first half of 2021 compared to the first half of 2020. However, the production was still lower than 2019. The U.S. automotive industry is facing shortage of semiconductor microchips and resins used in auto parts manufacturing due to the ongoing trade tension between the United States and China. This is disrupting the automotive production in the United States.
Canada is an important producer of motor vehicles, and the country is also the second-largest automotive market in North America in terms of sales.
  Vehicle production in Canada was already in a phase of decline even before the pandemic. This was because auto manufacturers have been optimizing production costs by making investments in the United States and Mexico, resulting in lower levels of production in Canada.
  In 2020, the automotive production in Canada declined 28.2% majorly due to the pandemic. Later, in Q1 and Q2 2021, the automotive production recovered slightly with recovery in demand; however, due to the lack of inventory and shortage of semiconductor chips, the recovery in automotive production was lower than expected.
AUTOMOTIVE PRODUCTION TREND IN UNITED STATES AND CANADA, 2019 AND 2020 |  |  |  |  |  | 
 | UNITS PRODUCED | UNITS PRODUCED |  |  |  | 
 | CANADA | CANADA |  | UNITED STATES | UNITED STATES | 
VEHICLE TYPE | 2018 | 2019 | 2020 | 2018 | 2019 | 2020
Light-duty trucks | 1,348,932 | 1,431,904 | 1,034,223 | 8,184,822 | 8,036,106 | 6,660,593
Passenger vehicles | 655,896 | 461,370 | 327,681 | 2,785,164 | 2,511,711 | 1,926,795
Heavy Trucks | 20,966 | 23,311 | 14,719 | 327,925 | 345,067 | 235,011
Total-a | 2,025,794 | 1,916,585 | 1,376,623 | 11,297,911 | 10,892,884 | 8,822,399
SOURCE: International Organization of Motor Vehicle Manufacturers. a-Includes only light-duty trucks, heavy trucks and passenger vehicles. |  |  |  |  |  | 

## Slide 227: Finished Lubricant Market
Lubricants demand in the United States and Canada declined 10.2% to reach 8,071.3 kilotonnes in 2020.
  This decrease is mainly due to a decline in demand in all the three segments of the lubricant industry in the United States and Canada due to the COVID-19 outbreak. In 2020, lubricant demand in the consumer segment declined 14.6%, which is the highest decline among all three segments.
  The spread of the pandemic led to movement restrictions as people worked from home, leading to lower demand for lubricants in the consumer segment.
  Moreover, a shift toward lower-viscosity synthetic oils also led to lower demand for lubricants in the two countries. The drain intervals have risen from 5,000 km to 8,000-10,000 km in the commercial segment and from 5,000 km to 12,000 km-15,000 km in the consumer segment, leading to a decline in the lubricant demand.
The United States with 7,373.3 kilotonnes or 91.4% of the total lubricant consumption in the two countries, leads the lubricant demand.
In 2020, the industrial segment accounted for 4,233.3 kilotonnes or 52.4% of total lubricant demand in both countries, leading the lubricant demand. It is followed by the consumer segment, accounting for 1998.0 kilotonnes or 24.8% demand. The commercial segment accounts for the remaining 1,840.0 kilotonnes or 22.8% of the total lubricant demand in both countries.
Chart: OVERALL LUBRICANT CONSUMPTION IN THE UNITED STATES AND CANADA BY MARKET SEGMENT, 2020
| Industrial | Consumer | Commercial
Sales | 0.524 | 0.248 | 0.228
Total: 8,071.3 Kilotonnes

## Slide 228: Finished Lubricant Market in the United States
In 2020, the total U.S. lubricant demand for lubricants decreased by 10.4% to reach 7,373.3 kilotonnes.
  In 2020, the lubricant demand in the consumer segment experienced the highest decline of 14.8%, while demand in the commercial and industrial segments declined 11.0% and 7.8%, respectively.
  This was mainly due to temporary shutdowns of factories as well as movement restrictions due to the COVID-19 pandemic.
The industrial segment accounts for 51.7% or 3,919.9 kilotonnes of the total lubricant demand in the United States.
  Process oils lead consumption among industrial lubricants with 1,733.5 kilotonnes demand in the United States.
The U.S. industrial lubricant demand reduced significantly in 2020.
  The economic slowdown due to the outbreak of COVID-19 severely impacted business activities of the U.S. manufacturers. Clampdowns and social distancing induced to prevent the spread of the virus affected operating efficiency and supply chains for raw materials and finished products in manufacturing industries.
  Nearly all automotive manufacturers halted production for several weeks and operated at much lower operating rates for a few months to adhere to social distancing measures.
In the consumer segment, PCMO leads consumption among consumer lubricants with 1,615.3 kilotonnes in the United States.
  The U.S. passenger vehicle parc is characterized as a mature, slow-growing sector. Passenger vehicles sales were already declining in the country, and the COVID-19 pandemic further hit the segment hard in 2020, leading to a decline in lubricant demand.
The commercial segment accounts for 22.2% or 1,622.4 kilotonnes of the total lubricants demand.
  Sales and production of commercial vehicles were significantly affected in 2020 due to the economic fallout from the COVID-19 pandemic. However, sales started to improve after August 2020.
Chart: OVERALL LUBRICANT DEMAND BY PRODUCT TYPE IN UNITED STATES, 2020 AND 2021
| Process Oils | PCMO | HDMO | Hydraulic Fluids | Industrial Engine Oils | MWF | All other-a
2020 | 1733.5 | 1615.3 | 1164 | 591.2 | 566.1 | 500.8 | 1202.4
2021 | 1750 | 1631.5 | 1186.6 | 594.5 | 567 | 503.8 | 1217.3
a – including grease, ATF, HTF, compression fluid, refrigeration oils, turbine & circulating oil, and other industrial oils

## Slide 229: Finished Lubricant Market in Canada
Total lubricant demand in Canada was 698 kilotonnes in 2020. The industrial segment in Canada accounted for 45.7% or 313.4 kilotonnes of the total demand.
  Process oils lead the consumption among industrial lubricants and account for about 84.9 kilotonnes in Canada. It is followed by industrial engine oils and metalworking fluids with demands of 67 kilotonnes and 59.0 kilotonnes, respectively.
  The industrial segment plunged by 10% due to lower industrial activities in the first half of 2020. While the industrial output was impacted, it rebounded quickly in most sectors, except oil and gas, in the second half of 2020. However, per Statistics Canada, the primary metal, manufacturing, and plastics and rubber industries witnessed the steepest decline in GDP contribution.
Industrial is followed by the commercial segment, which accounted for 31.2% or 217.6 kilotonnes of the total demand.
  HDMO led the commercial segment with 99.6 kilotonnes demand in Canada.
  HDMO demand declined 2.9% in 2020. Commercial vehicle fleets witnessed a significant decline in activity. However, the impact was less severe in this segment compared to the consumer and industrial segments.
The consumer segment followed at 167.0 kilotonnes or 23.9% of the total lubricants demand in the country. PCMO led the consumption among consumer lubricants with 139.8 kilotonnes demand in Canada.
  The consumer automotive lubricant segment was the most severely impacted by the lockdown and social distancing measures. This segment’s demand declined 12.9% in 2020.
  The growing penetration of electric cars will further limit the demand for PCMO over the long term.
  The Canadian government is encouraging the use of electric vehicles (EVs) by offering various incentives.
  Canada is a member of a campaign called EV30@30. The government's target for 2040 is to have 100% EVs in the overall passenger vehicle sales. This will adversely impact the demand for PCMO in the future. However, the impact is expected to be limited till 2025.
A – including grease, ATF, HTF, compression fluid, refrigeration oils, turbine & circulating oil and other industrial oils
B-Including automotive and industrial hydraulic fluids
Chart: OVERALL LUBRICANT DEMAND BY PRODUCT TYPE IN CANADA, 2020 AND 2021
| PCMO | HDMO | Process oil | Industrial Engine oils | MWF | Hydraulic fluids | All Other-a
2020 | 139.8 | 99.6 | 84.9 | 67 | 59 | 41.2 | 206.5
2021 | 137.3 | 99.4 | 85.8 | 66.8 | 59.5 | 41.8 | 206.2

## Slide 230: Finished Lubricant Market
KEY TRENDS IN THE LUBRICANT DEMAND | 
SEGMENTS | TRENDS
Commercial Automotive Lubricants | SAE 15W-40 has been the leading viscosity grade of HDMO. However, there had been a slow shift toward lower-viscosity oils in this product category. Though lubricant suppliers have started offering 15W-40 in full-synthetic and semi-synthetic types, their high prices restrict the shift. In Canada, demand for low-viscosity HDMOs, including 0Ws, 5Ws, and 10Ws, accounted for almost 40% of the overall HDMO demand. This is primarily because of the use of these viscosity grades during the extreme winter months. Penetration of synthetic lubricants in the commercial automotive segment has been small in the region. However, fleet owners are increasingly becoming conscious of fuel efficiency savings. In the long term, they would be more receptive to full- and semi-synthetic lubricants.
Consumer Automotive Lubricants | Japanese OEMs have been recommending 0W oils for passenger cars over the past years. While American OEMs have started recommending 0Ws for their new vehicles, 5Ws are also recommended for various models including those for diesel variants. With growing recommendations for lower-viscosity grades of PCMO, demand for synthetic lubricants has been growing. These lubricants are primarily blended using Group III/III+; select high-performance full-synthetic PCMO are blended using polyalphaolefins (PAOs). Fuel economy improvements and emissions regulations have been driving a rapid shift to full-synthetic lubricants at an expense of semi-synthetic and conventional products in the consumer automotive segment.
Industrial lubricants | Increased investments have been helping the industrial sector revive and register growth, however small. Except for 2020, most industrial segments are growing, which has helped maintain industrial lubricant demand in the region. In the industrial segment, synthetic lubricants have greater acceptance in select applications, such as mining, metalworking, textiles, and food. Refrigeration oil, compressor fluid, forming fluid, protecting fluid, hydraulic fluid (mainly fire-resistant), and turbine fluids are the industrial product categories that have a greater demand for synthetic oils.

## Slide 231: Lubricant Blenders
The North America lubricant blending market is highly fragmented with the presence of more than 300 suppliers of automotive and industrial products.
  Suppliers range from major oil companies, such as Shell, ExxonMobil, Chevron, Valvoline, and BP, to smaller independent lubricants manufacturers, which are represented by the Independent Lubricant Manufacturers Association (ILMA).
  Members comprise a mix of international companies, such as Quaker Houghton; regional companies, such as the American Refining Group; and CHS, an agribusiness cooperative that supplies lubricants, along with various other companies.
The major oil companies typically market the most well-known and established product brands and focus on the consumer, commercial, and industrial segments.
The ILMA companies tend to focus more on the specialty, niche, regional, or non-commodity segments and products/customers that the major companies do not serve.
In North America, the United States accounts for 91% of the lubricant demand due to which most of the lubricant blenders are based in the United States.
  Shell, ExxonMobil, Chevron, Valvoline, BP, and HollyFrontier are the major players in the lubricant blending market in the region.
In North America, blender mainly use Group II/II+ and Group III/III+ basestocks for producing lubricants.
  Basestocks demand in North America plummeted to 143.8 KBD in 2020 due to the COVID-19 pandemic. However, the demand recovered to 152.8 KBD in 2021 supported by recovery in the demand for lubricants from the automotive and industrial sectors in the region.
Chart: ESTIMATED LUBRICANT SALES SHARE BY SUPPLIER IN UNITED STATES, 2020
| Shell | ExxonMobil | Chevron | Ergon | Calumet | Holly Frontier | Valvoline | BP | All other-a
Sales | 0.125 | 0.079 | 0.068 | 0.061 | 0.058 | 0.054 | 0.05 | 0.037 | 0.468
Total: 7,373.3 Kilotonnes
a- Includes Phillips 66, CITGO, Quaker Houghton, Cross Oil, etc.
Continued…

## Slide 232: Lubricant Blenders
The region is witnessing a gradual shift for sustainability that will drive demand for better-quality lubricants that offer wider oil drain intervals and better fuel efficiency. This shift will be witnessed in not only the automotive segment but also the industrial segment.
  There will be a gradual but steady demand shift toward Group III and synthetic basestocks in the region. The shift will be more rampant in consumer automotive lubricants.
  Demand share for Group I basestocks will remain largely unchanged in automotive applications in the region. This is because almost all the automotive lubricants have already moved away from Group I basestocks to the extent possible.
  Group I basestocks are expected to witness a decline in the industrial segment as some industrial applications such as hydraulic fluids, gear oils, turbine oils, process oils, and railroad engine oils, which earlier used low-viscosity Group I basestocks, are now shifting to low-viscosity Group II basestocks, mainly because of supply push and low prices of Group II basestocks.
At present, re-refined Group II/II+ basestocks are the major re-refined basestocks produced in the United States and Canada. Other re-refined basestocks types such as Group I and Group III/III+ are produced in small quantity in the region.
  As the demand for Group I basestocks is declining and shifting toward Group II and Group III basestocks, the re-refining basestocks market is also following the same trend. Most of the re-refiners currently operating in the United States and Canada are producing Group II/II+ basestocks.
Major vehicle and engine manufacturers such as Ford, General Motors, Chrysler, and Detroit Diesel have issued warranty statements that allow the use of re-refined basestocks as long as it meets API standards. Many government and private fleets are also using re-refined lubricants in their vehicles.
  Ford recommends using engine oil meeting Ford Specification ESE-M2C 153-E and licensed as certified for gasoline engines by the American Petroleum Institute (API Certification). Both virgin and re-refined engine oils can meet these requirements by qualifying against a series of rigorous tests designed to ensure their suitability for modern gasoline engines.
  General Motors recommends for use in its vehicles engine oils, which meet the performance requirements specified in the latest International Lubricant Standardization and Approval Committee (ILSAC) Minimum Performance Standard and which are certified by the API for use in gasoline engines. The company encourages the use of properly qualified re-refined products, which consistently satisfy recommended performance requirements.

## Slide 233: United States Regulations Summary
SUMMARY OF REGULATION FOR UNITED STATES | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | Yes
2. How is used oil classified i.e., hazardous waste, special waste etc.? | Special Waste, not Hazardous Waste
3. Are there any requirements on who can collect used oil? | Yes
4. Does country have an association(s) managing the collection and disposal of used oil? | NORA represents the industry but does not manage collection or use
5. Is a levy charged on sales of lubricants to support used oil collection associations? | Not at the Federal level
6. Are there any requirements for how used oil generators manage used oil? | Yes
7. Are there requirements for oil manufacturers, marketers, or retailers to take back used oil? | No
8. Do any requirements/legislation exist around different types of used oil? | Yes
9. Does the country have requirements or regulations regarding the export or import of used oil? | Not specific to UO
10. Does the country have any legislation that requires used oil to be re-refined? | No
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | Yes
Continued…

## Slide 234: United States Regulations Summary
SUMMARY OF REGULATION FOR UNITED STATES |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | Not at the federal level
14. Is used oil allowed to be placed in a landfill? |  | No
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular Used Oil disposition – e.g., re-refining, fuel for burning, landfill etc. |  | Not at the federal level
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes, assuming that used oil is not being mixed first with a hazardous waste: | i. Burning in space heaters | Allowed
 | ii. Blending with crude oil at a refinery | Allowed
 | iii. Dust suppressant | Prohibited
17. Are there companies/associations advocating in used oil category? |  | Yes
Continued…

## Slide 235: United States Regulations Summary
i. Generation
Generators are responsible for environmental release cleanup.
Information or testing is required to ensure that the contaminants are under an acceptable limit.
Classification (Special Waste)
Used oil is classified into on-specification and off-specification used oil for using it as a fuel. On-specification used oil has an arsenic concentration of up to 5 parts per million (ppm), cadmium up to 2 ppm, chromium up to 10 ppm, lead up to 100 ppm, total halogens up to 4,000 ppm, and a minimum flash point of 100°F. Used oil is classified as off-specification if it does not meet the criteria mentioned above.
However, if the total halogen concentration goes beyond 1,000 ppm, used oil is classified as a hazardous waste. In case of hazardous waste, used oil must be disposed of per criteria laid out under 40 CFR 260 through 266, 268, 270, and 124. In case of non-hazardous solid waste, it must comply with regulations included under 40 CFR 239 through 259.
Used oil contaminated with PCBs
  Used oil with PCB concentrations ≥ 50 ppm is regulated for disposal under the Toxic Substances Control Act (TSCA).
  Used oil with lower PCB concentrations (≥ 2 ppm and < 50 ppm) may be burned as a fuel, subject to restrictions listed in 40 CFR §761.20(e), 40 CFR part 279, and any applicable state and local laws.
  Used oil with < 2 ppm may be managed as used oil.
  TSCA requirements may not be avoided through dilution.
  Contaminated oil must be disposed of in accordance with PCB regulations 40 CFR §761.79.
ii. a Prohibitions
Used oil as a dust suppressant (effectively)
  The regulations allow a state to petition the EPA for an exception; however, no states have been granted this permission.
Surface impoundments
Off-specification used oil fuel may only be burned for energy recovery in particular units
iii. Collection
Information or testing required to rebut the hazardous waste mixing presumption
Responsible for environmental release cleanup
Must be registered/licensed/permitted/recognized by a state/county/municipal government to manage used oil
When feasible, collection centers should obtain a sample of used oil from each batch received, known as a retain sample
iv. Transportation and Storage
Minimum storage tank and container requirements:
  Must be in good condition
  Must be labeled “Used Oil”
Continued…

## Slide 236: United States Regulations Summary
Generators, transporters, processors/re-refiners, and burners are also subject to Spill Prevention, Control, and Countermeasures (40 CFR part 112).
Storage in underground tanks is regulated under RCRA Subtitle I, 40 CFR 280.
Transportation & Transfer Facilities:
  Anyone transporting used oil, except under the self-transport provisions of 279.24(a), must also comply with 40 CFR Subpart E.
  Secondary containment required (not for transporters)
  Responsible for environmental release cleanup
  EPA Identification Number and notification required
Acceptance and delivery records (three years) must be kept.
Information or testing is needed to rebut the hazardous waste mixing presumption (keep records for three years).
Persons transporting used oil that meets the definition of hazardous material in 49 CFR 171.8 must comply with all applicable USDOT regulations in 49 CFR parts 171 through 180.
v. Disposal – Re-refining
Secondary containment required
Responsible for environmental release cleanup
Required EPA Identification Number and notification
Required to keep acceptance and delivery records (three years)
Required to create and follow an analysis plan that details how the hazardous waste mixing presumption will be rebutted
Information or testing needed to rebut the hazardous waste mixing presumption (keep records for three years)
A contingency plan and emergency procedures (same as Parts 264 & 265 subpart D)
Written report on biennial basis
vi. Disposal – Fuel
Secondary containment required
Responsible for environmental release cleanup
Required EPA Identification Number and notification
Must keep acceptance records (three years)
Information or testing needed to rebut the hazardous waste mixing presumption (keep records for three years)
Off-specification used oil fuel may be burned for energy recovery in only the following devices:
Industrial furnaces identified in §260.10
Boilers as defined in §260.10 and identified in §279.12
Hazardous waste incinerators subject to regulation under the Subpart O of parts 264 or 265
vii. Regulations on Imports or Exports of Used Oil
Transporters who import or export used oil are subject to the requirements of 40 CFR Subpart E from the time the used oil enters until the time it exits the United States.
Anyone transporting used oil, except under the self-transport provisions of 279.24(a), must also comply with 40 CFR Subpart E.
Continued…

## Slide 237: United States Regulations Summary
Regulatory Enforcement
i. Responsible Agencies
EPA
State, county, and/or municipal governments
ii. Enforcement Mechanisms
Federally required record-keeping
EPA notifications and identification numbers
State required reporting, registration, and/or notification
Federal EPA identification numbers
iii. Effectiveness of Regulations Enforcement
Moderate
The federal regulations and standards dictate the minimum standards of used oil management programs in the individual states
Individual states’ oversight is far more effective and differs widely between states
Key Influencers
i. Public Sector
EPA
DOE
State, county, and municipal governments
Executive Orders
ii. Private Sector
ExxonMobil
Chevron
Shell
Valvoline
ConocoPhillips
BP
Safety-Kleen
Impact of Current Regulations
Moderate
Federal used oil regulations and standards provide a general framework for used oil handlers to manage used oil operations and minimize the potential for environmental impact. However, the system largely relies on self-regulation and enforcement at the state and local levels. The implementation and oversight of a used oil management program is largely left to individual states, provided the state regulations are at least as strict as the federal used oil standards. Compliance and enforcement varies widely, with California (through CalRecycle) leading the way with state initiatives, which go well beyond Federal guidelines.

## Slide 238: Canada Regulations Summary
SUMMARY OF REGULATION FOR CANADA | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | Yes
2. How is used oil classified, i.e., hazardous waste, special waste etc.? | Hazardous Waste
3. Are there any requirements on who can collect used oil? | Yes
4. Does country have an association(s) managing the collection and disposal of used oil? | Yes
5. Is a levy charged on sales of lubricants to support used oil collection associations? | Yes
6. Are there any requirements for how used oil generators manage used oil? | Yes
7. Are there requirements for oil manufacturers, marketers, or retailers to take back used oil? | Extended producer responsibility principle applied​
8. Do any requirements/legislation exist around different types of used oil? | No
9. Does the country have requirements or regulations regarding the export or import of used oil? | Yes
10. Does the country have any legislation that requires used oil to be re-refined? | Yes
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | Yes, but only if used oil is pre-treated and its contaminants are reduced below certain levels
Continued…

## Slide 239: Canada Regulations Summary
SUMMARY OF REGULATION FOR CANADA |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | Yes​
14. Is used oil allowed to be placed in a landfill? |  | No
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular Used Oil disposition – e.g., re-refining, fuel for burning, landfill etc. |  | Yes
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes, assuming that used oil is not being mixed first with a hazardous waste: | i. Burning in space heaters | No
 | ii. Blending with crude oil at a refinery | No
 | iii. Dust suppressant | No, all the provinces and territories except Alberta have banned the usage of used oil as dust suppressant
17. Are there companies/associations advocating in Used Oil category? |  | Yes
Continued…

## Slide 240: Canada Regulations Summary
Key Used Oil Regulations
In Canada, the focus of regulation is mainly on the crankcase oils (lubricating oils used in internal combustions engines), as they generate most of the used oil in Canada. Used crankcase oil is defined as any used lubricating oil that is obtained from the crankcase of internal combustion engines. Such oils are a mixture of basestocks and additives. These oils also include various chemicals such as arsenic, cadmium, acidic, sulfidic and soluble inorganic nickel, trichloroethylene, 1, 1, 1-trichloroethane, PCBs, benzene, chromium and its compounds, polycyclic aromatic hydrocarbons, tetrachloroethylene, and lead.
Other lubricants such as hydraulic fluids and gear oils are also covered under the regulations for used oil. Furthermore, used oil filters and containers (containers used for holding lubricants) are also covered under these regulations as they might contain some residual oil, and disposing of them in the environment will lead to disposing of used oil in the environment.
In Canada, the reprocessing of used oil into lubricant or re-refining used oil into basestocks is allowed. However, in provinces such as British Columbia, permits are required to re-refine used oil. The capacity for regeneration and re-refining of used oils in Canada varies from one province to another. There are re-refineries present in all the provinces of Canada excluding Newfoundland and Labrador, Quebec, and Prince Edward Island.
REGULATIONS APPLICABLE IN CANADA FOR OF USED OIL, 2020 | 
PROVINCE/TERRITORY | REGULATION APPLICABLE
Newfoundland and Labrador | Used Oil and Used Glycol Control Regulation, 2018, Waste Management Regulation, 2003
Nova Scotia | Activities Designation Regulation
New Brunswick | Used Oil Regulation, Air Quality Regulation
Prince Edward Island | Used Oil Handling Regulation
Quebec | Article 70.9 paragraphe 2 de la Loi sur la qualité de l’environnement
Ontario | Regulation 347 (General - Waste Management)
Manitoba | Waste Reduction and Prevention Act
Saskatchewan | Environmental Management and Protection Act, Clean Air Act
Alberta | Activities Designation Regulation
British Columbia | Local Air Regulations
Yukon | Special Waste Regulations
Northwest Territories | Used Oil and Waste Fuel Regulations
SOURCE: Government of Canada. | 
Continued…

## Slide 241: Canada Regulations Summary
i. Generation
Used oil producers must register themselves under the regulations for managing and handling used oil in the provinces.
The used oil producers and owners must guarantee the delivery of used oils to an authorized collection center for their valorization or regeneration.
Producers that generate less than 200 liters per year or are generating used oil or waste fuel in the normal use of a residence are exempt from certain sections of the regulations. These users are still required to manage materials as directed in the Environmental Protection Act.
Except for an industrial vendor, all other generators of used oil shall have a proper storage system in accordance with section 21 and a written agreement, to accept used oil, with the owner of an approved storage facility for used oil. Industrial vendors or generators shall submit the specified life cycle management portion of their contract to the minister for approval.
Classification (Hazardous Waste)
Used oil is classified as hazardous waste that must be registered and disposed of at a licensed facility according to the Hazardous Waste Regulation in the country.
CLASSIFICATION OF USED OIL BY DIFFERENT CLASSES IN CANADA | 
CLASS | CONCENTRATION OF CONTAMINANTS
Class 1 | Polychlorinated Biphenyls (PCBs) <= 5 ppm Total Organic Halogens (as Chlorine) <= 1,000 ppm Cadmium <=2 ppm Chromium <= 10 ppm Lead <= 10 ppm
Class 2 | Polychlorinated Biphenyls (PCBs) <= 5 ppm Total Organic Halogens (as Chlorine) <= 1,000 ppm Cadmium <=2 ppm Chromium <= 10 ppm Lead (10 ppm < concentration <= 100 ppm)
Class 3 | Polychlorinated Biphenyls (PCBs) (5 ppm < concentration <= 50 ppm) Total Organic Halogens (as Chlorine) (1,000 ppm < concentration <= 3,000 ppm) Cadmium <=2 ppm Chromium <= 10 ppm Lead <= 10 ppm
Class 4 | If any one of the five contaminants is above the maximum defined limit in Class 1-3
Continued…

## Slide 242: Canada Regulations Summary
A Return Incentive (RI) is paid to private sector collectors and processors to pick up and deliver to government-approved recycling facilities where the materials are processed into new products.
iv. Transportation and Storage
In Canada, the transportation of used oil is subjected to the Transportation Of Dangerous Good (TDG) Act. Therefore, collectors transporting the used oil need to follow the standard procedure laid under the TDG regulation.
For the transportation of used oil from the storage facility, the storage facility owner must have approval from either the Environmental Protection Act or the regulation authority of provinces.
For storage purposes, users and collectors that store used oil need to ensure that class 1, class 2, class 3, and class 4 used oils are stored separately in approved storage tanks. A storage tank used to store used oil bears a label or other suitable identification that indicates the class of used oil contained in that tank.
There must be proper labeling of the used oil container to identify its contents – either “Used Oil” or “Waste Fuel”. If used oil and waste fuel are being stored in an institutional, commercial, or industrial location, the containers must also be labeled in accordance with the Workplace Hazardous Materials Information System (WHMIS).
In the case of an underground storage tank, the label or other identification is located on the fill pipe for the storage tank, and it needs not include the name and address of the storage facility.
iii. Collection
Programs to collect used oil are well-established in most provinces but not in the territories. A legislated Extended Producer Responsibility (EPR) approach is used in BC, Saskatchewan, Manitoba, Ontario (containers and filters only), Québec, and New Brunswick. With respect to the used oil collection gap for Ontario, the province encourages used oil collection and prohibits used oil disposal in the landfill, open burning, or other non-authorized uses via legislation.
Nova Scotia, Alberta, and Newfoundland and Labrador use a product stewardship model for used oil collection, in which associations have defined the framework for generators and collectors for minimizing the product’s environmental impact throughout all stages of the product’s life cycle.
In Yukon, under the Special Waste Regulations, a permit is required for the generation, collection, and handling of used oil.
Prince Edward Island (PEI) does have used oil regulations in place to require the collection and proper disposal as hazardous waste. This approach targets the commercial retail sector, rather than residential and does not involve stewards since the province does not have a significant steward base located in PEI.
In accordance with the provisions for collection of used oil, an operator of a used oil collection facility must register as a hazardous waste generator by submitting a completed registration form to regulatory authority in the provinces to obtain a Hazardous Waste Generator Registration Number (also referred to as a Provincial Registration I.D. or MBG Number) assigned by the Department.
Continued…

## Slide 243: Canada Regulations Summary
REGULATIONS APPLICABLE IN CANADA FOR THE RE‐REFINING AND RE‐PROCESSING OF USED OILS |  |  | 
PROVINCE/TERRITORY | USED OIL RECOVERY | REGULATION APPLICABLE | REGULATION APPLICABLE
Newfoundland and Labrador | Mandatory | Used Oil Control Regulation, 2002 | Lubricant sellers are required to accept used oil or suggest alternative return facility if they cannot accept the used oil.
Nova Scotia | Mandatory | Used Oil Regulations | Lubricant sellers are required to accept used oil or suggest alternative return facility if they cannot accept the used oil.
New Brunswick | Mandatory | Used Oil Regulations | Lubricant sellers are required to accept used oil or suggest alternative return facility if they cannot accept the used oil.
Prince Edward Island | Mandatory | Used Oil Handling Regulations | Lubricant sellers are required to accept used oil or suggest alternative return facility if they cannot accept the used oil.
Quebec | Mandatory | Regulation respecting the recovery and reclamation of used oils, oil or fluid containers and used filters | Managed by the Société de gestion des huiles usagées (SOGHU)
Ontario | Encouraged | - | No program in place
Manitoba | Mandatory | Used Oil, Oil Filters and Containers Stewardship Regulation | Managed by Manitoba Association for Resource Recovery Corporation
Saskatchewan | Mandatory | Used Oil Collection Regulations | Managed by Saskatchewan Association for Resource Recovery Corporation
Alberta | Mandatory | Lubricating Oil Material Recycling and Management Regulation | Managed by the Alberta Used Oil Management Association
British Columbia | Mandatory | Recycling Regulation | Managed by the British Columbia Used Oil Management Association
Yukon | Allowed | Yukon Environment Act | Pilot program completed Per this program, a person needs special permit to generate, dispose of, collect, transport, or handle special waste. The state government has mentioned specific quantities of various types of special waste that require special permits. Used oil is also included under the special waste category. A person will require this special permit for storing used oil on site.
Northwest Territories | Encouraged | - | No program in place
Nunavut | Allowed | - | Community programs for collection and storage
Continued…

## Slide 244: Canada Regulations Summary
v. Disposal – Re-refining
In Canada, reprocessing of used oil into original lubricant or re-refining used oil into basestocks is allowed. However, in some provinces, permits are required to re-refine used oil. The capacity for reprocessing and re-refining of used oils in Canada varies from one province to another. There are re-refineries present in all the provinces of Canada excluding Newfoundland and Labrador, Quebec, and Prince Edward Island.
All the Re-refiner shall follow environmentally sound technologies such as
  Vacuum distillation with clay treatment;
  Vacuum distillation with hydrotreating;
  Chemical dementalization/distillation/hydrotreating
REGULATIONS APPLICABLE IN CANADA FOR THE RE‐REFINING AND RE‐PROCESSING OF USED OILS |  | 
PROVINCE/TERRITORY | RE‐REFINING & RE‐PROCESSING | REGULATION APPLICABLE
Newfoundland and Labrador | Controlled | Used Oil Control Regulation 2002
Nova Scotia | Controlled | Activities Designation Regulation
New Brunswick | Controlled | Used Oil Regulation, Air Quality Regulation
Prince Edward Island | Controlled | Used Oil Handling Regulation
Québec | No controls | Article 70.9 paragraphe 2 de la Loi sur la qualité de l’environnement
Ontario | Controlled | Regulation 347 (General – Waste Management)
Manitoba | Controlled | Waste Reduction and Prevention Act
Saskatchewan | Controlled | Environmental Management and Protection Act, Clean Air Act
Alberta | Controlled | Activities Designation Regulation
British Columbia | Controlled | Local Air Regulations
Yukon | Controlled | Special Waste Regulations
Northwest Territories | Controlled | Used Oil and Waste Fuel Regulations
SOURCE: Government of Canada. |  | 
Continued…

## Slide 245: Canada Regulations Summary
vi. Disposal – Fuel
Burning of used oil as a fuel is allowed in the country; however, only if it complies with the provincial regulations.
vii. Disposal – Other
Incineration of used oil, waste fuel, and waste-derived fuel, such as in a used oil furnace, is permitted. However, it is not permissible to do so in residential areas. This restriction is intended to protect public health. Burning is allowed either through permitting or through Certificates of Approval; allowable limits for contaminants are also listed in most regulations. Space heaters are a problem due to the concern that burner units will not be maintained, and contaminants will be released to the environment and cause localized air degradation for humans.
The disposal of used oil as dust suppression is banned in eight provinces and three territories, except Alberta. In Alberta, interim guidelines for the application of Used or Waste Refined Oil to Road Surfaces for Dust Control recommend contaminant limits; continued use of used or waste oil on roads was reviewed and guidelines were revised in April 1999.
REGULATIONS APPLICABLE IN CANADA ON BURNING USED OIL AS A FUEL, 2020 |  |  | 
PROVINCE/TERRITORY | OPEN BURNING | BURNING AS A FUEL WITH RESTRICTIONS | REGULATION APPLICABLE
Newfoundland and Labrador | Prohibited | Allowed | Air Pollution Control Regulation, 2004
Nova Scotia | Prohibited | Allowed | Used Oil Regulation, Air Quality Regulation
New Brunswick | Prohibited | Allowed | Used Oil Regulation, Air Quality Regulation
Prince Edward Island | Prohibited | Allowed | Air Quality Regulation
Quebec | Prohibited | Allowed | Regulation respecting hazardous materials
Ontario | Prohibited | Allowed | Regulation 347 (General - Waste Management)
Manitoba | Prohibited | Allowed | Gas and Oil Burner Act
Saskatchewan | Prohibited | Allowed | Clean Air Regulation
Alberta | Prohibited | Allowed | Draft Code of Practice for Energy Recovery
British Columbia | Prohibited | Allowed | Hazardous Waste Regulation
Yukon | Prohibited | Allowed | Special Waste Regulation
Northwest Territories | Prohibited | Allowed | Used Oil and Waste Fuel Regulation
Nunavut | Prohibited | Allowed | Environmental Protection Act
SOURCE: Government of Canada. |  |  | 
REGULATIONS APPLICABLE IN CANADA ON DISPOSAL OF USED OIL, 2020 |  | 
PROVINCE/TERRITORY | DISPOSAL TO LAND, LANDFILL AND SEWER | REGULATION APPLICABLE
Newfoundland and Labrador | Prohibited | Air Pollution Control Regulation, 2004
Nova Scotia | Prohibited | Used Oil Regulation
New Brunswick | Prohibited | Used Oil Regulation
Prince Edward Island | Prohibited | Used Oil Handling Regulation
Quebec | Prohibited | Regulation respecting hazardous materials
Ontario | Prohibited | Regulation 347 (General - Waste Management)
Manitoba | Prohibited | Waste Disposal Grounds Regulation
Saskatchewan | Prohibited | Used Oil Collection Regulation, Municipal Refuse Management Regulation
Alberta | Prohibited | Waste Control Regulation
British Columbia | Prohibited | Hazardous Waste Regulation
Yukon | Prohibited | Special Waste Regulation
Northwest Territories | Prohibited | Used Oil and Waste Fuel Regulation
Nunavut | Prohibited | Environmental Protection Act
SOURCE: Government of Canada. |  | 
Continued…

## Slide 246: Canada Regulations Summary
Regulatory Enforcement
i. Responsible Agencies
In Canada, provincial used oil associations are responsible for enforcing regulations in their respective provinces.
  British Columbia Used Oil Management Association (BCUOMA)
  Alberta Recycling Management Authority (Alberta Recycling)
  Saskatchewan Association for Resource Recovery Corp. (SARRC)
  Manitoba Association for Resource Recovery Corp. (MARRC)
  Société de gestion des huiles usagées (SOGHU)
  UOMA Atlantic – New Brunswick (UOMA NB)
  UOMA Atlantic – Prince Edward Island (UOMA PE)
  UOMA Atlantic – Newfoundland and Labrador (UOMA NL)
  UOMA Atlantic – Nova Scotia (UOMA NS)
ii. Enforcement Mechanisms
The regulation of appropriate used oil management is the responsibility of the provincial and territorial governments in Canada. At instances where provincial regulations do not exist for adequate management of used oil, (i.e., storage, disposal, treatment, or transportation), federal regulations are applied. Provincially, however, the extent of the regulations and the degree to which these regulations are enforced vary.
At the federal level, 24 departments have a responsibility under about 30 statutes over different aspects of controlling toxic substances; added to these are provincial and municipal regulations. The federal government’s approach to waste management is an integrated one based on the 4Rs: Reduce, reuse, recycle, and recovery.
Compliances reviews and audits are conducted on three-to-four-year rotation with all members of the Used Oil Associations across Canada. It includes sample testing on Environmental Handling Charge (EHC) applicable sales. Based on this sample testing, assessing whether the EHC is being remitted on the applicable quantities sold, at the applicable provincial rate, and remitted to the appropriate provincial association.
ENVIRONMENTAL HANDLING CHARGES IN CANADA, 2020 | 
PROVINCE | CHARGES ON LUBRICANTS (USD/L)
Newfoundland and Labrador | 0.07
Nova Scotia | 0.04
New Brunswick | 0.03
Prince Edward Island | 0.03
Quebec | 0.05
Manitoba | 0.05
Saskatchewan | 0.05
Alberta | 0.05
British Columbia | 0.06 per liter effective July 1, 2021
SOURCE: Used Oil Management Associations. | 
Key Influencers
i. Public Sector
Provincial Associations
State, county, and municipal governments
ii. Private Sector
Safety Kleen
Terrapure (GFL)
iii. Effectiveness of Regulations Enforcement
Provinces have dedicated used oil management associations setup to dictate the standards for the collection, transportation, re-refining, disposal of, and regeneration of used oil.
A legislated EPR approach is also used in BC, Saskatchewan, Manitoba, Ontario (containers and filters only), Québec, and New Brunswick for used oil generation and collection.

## Slide 247: Material Balance 2020
Total lubricants consumption in the region accounted for 8,071.3 kilotonnes in 2020. Out of that, 57% of lubricant consumption is generated as used oil.
  The used oil collection in the region is estimated at 73% of total used oil generated. An estimated 51% of collected used oil is re-refined into basestocks or VGO/MDO or regenerated into transformer oil in 2020.
  In 2020, used oil collection declined nearly 11% compared to 2018 due to a decline in lubricant consumption as well as the closure of collection and service centers.
38% of collected used oil burned as a fuel in industrial furnaces in both the countries.
  Canada and parts of the United States face extreme cold conditions, and the used oil is used as a fuel for space heaters in industrial facilities in these countries. Used oil is either burnt directly or filtered before burning, depending on the amounts of impurities present in it.
Chart: USED OIL GENERATION, 2020
| Used oil generated | Lubricant lost
Sales | 0.57 | 0.43
Total: 8,071.3 Kilotonnes
Chart: USED OIL COLLECTION, 2020
| Collected | Not collected
Sales | 0.726 | 0.274
Chart: USED OIL DISPOSAL, 2020
| Fuel | Re-refined | VGO/MDO + Regen.-a | All other-b
Sales | 0.38 | 0.35 | 0.25 | 0.02
Chart: USED OIL RE-REFINING, 2020
| Basestock | All other
Sales | 0.65 | 0.35
Total: 4,616.0 Kilotonnes
Total: 3,386.1 Kilotonnes
Total: 1,156.7 Kilotonnes
a- Includes used oil re-refined into VGO/MDO or regeneration of transformer oil.
b- Includes other application such as concrete demolding agents, blended into HSFO/ANFO, etc.
Continued…

## Slide 248: Material Balance 2020
There are numerous used oil generators in the region. These can be divided into two groups: Used motor oil generators (oil from an internal combustion engine crankcase) and industrial oil generators. The first group includes every person who drives a car and either changes their own oil or takes their car to a garage or oil change service location.
  Oil change services, also known as “quick-lube” or “fast lube” services are defined in the industry as businesses that derive the majority of their sales from quick, convenient oil changes and other automotive preventative maintenance services that can be done in 30 minutes or less. Within the industry, locations that have dual profit centers, such as a car wash/fast lube, auto repair garage, muffler shop, tire stores, or car dealerships with quick service lanes, are called “lube plus” shops.
  The second group includes a wide range of companies that use equipment that relies on a variety of oils as elements of manufacturing or production processes. These oils can include engine oils, compressor oils, electrical transformer oils, hydraulic oils, metal cutting or processing oils, as well as oily wastewaters associated with these processes.
The used oil generated by industrial generators is either used onsite in space heaters and furnaces as fuel or collected by collectors. The usage of used oil for burning as fuel is higher in the industrial segment than in the automotive segment, resulting in lower used oil collection from the industrial segment.
  In automotive, do-it-yourself (DIY) customers, who change lubricant on their own, take the used oil to collection centers or local recycling centers. In some cases, such consumers also use used oil for their own purposes.
There is a growing trend of do-it-for-me (DIFM) quick-lube operations in the region, where vehicle owners take their cars to oil change service locations for lube change because of the convenience that they offer both in terms of automobile maintenance and in avoiding the difficulties in disposing of their own used oil. The DIFM to DIY ratio has improved over the past 20 years to approximately 75% DIFM to 25% DIY for personal automobile oil changes. This has led to an increase in used oil collection in the past few years.
Continued…

## Slide 249: Material Balance 2020
USED OIL GENERATION AND COLLECTION BY COUNTRY IN WESTERN EUROPE, 2020 |  |  |  |  | 
COUNTRY | LUBRICANT CONSUMPTION (KT) | USED OIL GENERATED (KT) | USED OIL COLLECTED (KT) | GENERATION RATE | COLLECTION RATE (FROM USED OIL GENERATED)
United States | 7,373.3 | 4,155.3 | 2,996.7 | 56% | 72%
Canada | 698.0 | 460.7 | 389.4 | 66% | 85%
Total | 8,071.3 | 4,616.0 | 3,386.1 | 57% | 73%
The United States is the largest market for finished lubricants in North America and generates a larger amount of used oil than Canada. The United States accounted for 90% of used oil generated between the United States and Canada in 2020.
  The U.S. used oil generation rate is lower compared to Canada. However, the U.S. finished lubricant market is characterized by a large amount of process oils, which cannot generate used oil. Process oils such as rubber process oils and white oils, which do not generate used oils, accounted for close to 14% of the total lubricant demand in the United States. The corresponding share for Canada is around 10%.
  Since generation rates are higher in the automotive segment rather than the industrial segment, countries with higher lubricant demand from the automotive segment compared to the industrial segment have higher generation rates – as is the case in Italy, Spain, and Portugal.
  After the overhaul of the consortium overseeing used oil collection in Italy and public initiatives to promote collection, used oil collection in Italy increased to surpass 90%, the highest collection rate in Europe.
The collection rate is higher in Canada than the United States, mainly because the collection of used oil is managed by individual used oil associations in provinces in Canada.

## Slide 250: Material Balance 2021
Chart: USED OIL GENERATION, 2021
| Used oil generated | Lubricant lost
Sales | 0.57 | 0.43
Total: 8,147.5 Kilotonnes
Chart: USED OIL COLLECTION, 2021
| Collected | Not collected
Sales | 0.73 | 0.27
Chart: USED OIL DISPOSAL, 2021
| Fuel | Re-refined | VGO/MDO + Regen.-a | All other-b
Sales | 0.38 | 0.34 | 0.26 | 0.02
Chart: USED OIL RE-REFINING, 2021
| Basestock-a | All other
Sales | 0.65 | 0.35
Total: 4,662.0 Kilotonnes
Total: 3,419.2 Kilotonnes
Total: 1,167.2 Kilotonnes
The lubricant consumption increased an estimated 0.9%, to reach 8,147.5 kilotonnes in 2021. Total used oil generation shows a similar growing trend of finished lubricant demand in the region, increasing 1% to reach 4,662 kilotonnes in 2021.
Used oil collection is also expected to see slight increase of 1% in 2021.
Used oil disposal is expected to remain the same as 2020.
a- Includes used oil re-refined into VGO/MDO or regeneration of transformer oil.
b- Includes other application such as concerte demolding agents, blended into HSFO/ANFO, etc.

## Slide 251: Used Oil Generation
The used oil generation rate in the region was estimated at 57% in 2020. However, the used oil generated volume declined around 12% in 2020 compared to 2019. This is mainly due to a decline in lubricant demand due to COVID-19.
  The overall decline in lubricant demand was around 10.2% in 2020. However, the decline in used oil generation was around 2.5% higher than the decline in lubricant demand. This is because the decline in lubricant demand was higher in automotive lubricants – lubricant demand in the consumer and the commercial segments declined by around 14.6% and 10.1%, respectively, in 2020. This is due to COVID-19-induced restriction leading to lower movement and thus lower demand for automotive lubricants. Automotive lubricant accounted for around 67% of total used oil generated in 2020.
The COVID-19 outbreak is not considered to have greatly impacted used oil generation in the industrial segment in the region. There were strict closures of factories; however, most industries only saw a moderate decline in their production rate through the pandemic.
Automotive lubricants such as PCMO and HDMO generate most of the used oil in Canada and the United States.
  In the automotive segment, used oil is mainly generated during oil change services. These oil change services are performed in quick lube centers, workshops, dealerships, general repair garages, tire, brake, and muffler shops, and fuel stations.
  In 2020, the generation of used oil was less in the workshops, general repair garages, tire, brake, and muffler shops compared to lube centers and authorized service centers. During the pandemic, vehicle owners changed lube oil either at their places or at the authorized facility due to several movement restrictions.
  Currently, most of the volume loss in the HDMO, PCMO, MCO, and other automotive fluids occurs due to the inadequate disposal of drained oil in the few less developed parts of the United States and Canada
  While most of the regions of the United States and Canada have proper disposal policies in place, there are few areas in Mississippi, New Mexico, Alabama, and Louisiana, where used oil is not disposed of adequately, in the United States. This is due to the lack of a proper regulatory framework as these areas are less developed compared to other states in the United States. As a result, customer awareness regarding used oil is also low.
Continued…

## Slide 252: Used Oil Generation
Chart: USED OIL GENERATION RATES BY PRDOUCT IN THE UNITED STATES AND CANADA, 2020 AND 2021-a
| PCMO | HDMO | Hydraulic Fluid | Metalworking Fluids | Industrial Engine Oil | Process Oil | All Other-b
Series 1 | 0.85 | 0.8 | 0.75 | 0.45 | 0.45 | 0.12 | 0.61
Automotive was the largest segment with more than 67% of total used oil generation in 2020. Used oil generated in the automotive segment is usually stored in drums or tanks by service centers in dealerships, quick lube centers, or repair garages to ship it to collectors or re-refiners.
The industrial segment accounted for 33% of total used oil generation in the region. Hydraulic fluid is among the major contributor of used oil generated in the industrial segment.
  Per government regulations, used oil should be properly transported in licensed carriers. These countries have established rules and criteria for licensing carriers used for transporting used oil.
  In both countries, industries are subject to penalties if they dump used oil and contaminate the environment. Industries such as steel, mining, power, plastic, and automotive manufacturing, which consume lubricants in large quantities, have better used oil disposal policies in place compared to other industries. Very few industries, especially in Canada, are allowed to burn used oil.
In 2021, used oil generated in the region grew 1%, which is proportional to the 0.9% growth in the lubricant demand.
USED OIL GENERATION BY PRODUCT IN THE UNITED STATE AND CANADA, 2020 AND 2021 |  |  |  | 
LUBRICANT | KILOTONNES |  | % OF TOTAL USED OIL GENERATED | 
 | 2020 | 2021 | 2020 | 2021
PCMO | 1,498.8 | 1,510.3 | 32.5 | 32.1
HDMO | 1,015.9 | 1,033.8 | 22.0 | 22.0
Hydraulic Fluid | 476.4 | 479.3 | 10.3 | 10.2
Industrial Engine Oil | 288.2 | 288.6 | 6.2 | 6.1
MWF | 254.9 | 256.5 | 5.5 | 5.5
Process Oil | 223.3 | 225.4 | 4.8 | 4.8
MCO | 34.7 | 35.0 | 0.8 | 0.7
All other-a | 823.9 | 833.2 | 17.8 | 17.7
Total | 4,616.0 | 4,698.1 | 100.0 | 100.0
a- Includes ATF, compressor oil, refrigeration oil, turbine oil, among others. |  |  |  | 
a- Generation rates are same for 2020 and 2021. Therefore, only one bar chart is shown.
b- Includes ATF, compressor oil, refrigeration oil, turbine oil, among others.

## Slide 253: Used Oil Collection
Used oil collection in the United States and Canada is estimated at 3,386.1 kilotonnes in 2020.
  A majority of this volume is collected in the United States, the larger lubricant market. However, the collection rate is higher in Canada, mainly because the collection of used oil is managed by individual used oil associations in provinces in Canada.
  The automotive segment, which mainly includes HDMO, PCMO, and 4T MCO oils, represents nearly 67.5% of the total used oil collected in the United States and Canada.
In 2021, the used oil collection in the two countries was estimated at 3,419.2 kilotonnes, amounting to 73% of generated used oil. The increase is due to recovery in lubricant demand in 2021.
Chart: USED OIL COLLECTION RATES BY PRODUCT IN THE UNITED STATES AND CANADA, 2020 AND 2021-a
| HDMO | Hydraulic Fluid | PCMO | Metalworking Fluids | Industrial Engine Oil | Process Oil | All Other-b
Series 1 | 0.76 | 0.75 | 0.72 | 0.71 | 0.71 | 0.7 | 0.74
USED OIL COLLECTION BY PRODUCT IN THE UNITED STATES AND CANADA, 2020 AND 2021 |  |  |  | 
LUBRICANT | KILOTONNES |  | % OF TOTAL USED OIL COLLECTED | 
 | 2020 | 2021 | 2020 | 2021
PCMO | 1,074.3 | 1,082.0 | 31.7 | 31.6
HDMO | 774.6 | 788.0 | 22.9 | 23.0
Hydraulic Fluid | 358.9 | 361.2 | 10.6 | 10.6
Industrial Engine Oil | 203.4 | 203.7 | 6.0 | 6.0
MWF | 179.9 | 181.0 | 5.3 | 5.3
Process Oil | 157.1 | 158.6 | 4.6 | 4.6
MCO | 21.2 | 21.3 | 0.6 | 0.6
All other-a | 616.6 | 623.5 | 18.2 | 18.2
Total-b | 3,386.1 | 3,419.2 | 100.0 | 100.0
a- Includes ATF, compressor oil, refrigeration oil, turbine oil, among others. b- Does not include imports of 80 KT. |  |  |  | 
a- Collection rates are same for 2020 and 2021. Therefore, only one bar chart is shown.
b- Includes ATF, compressor oil, refrigeration oil, turbine oil, among others.
Continued…

## Slide 254: Used Oil Collection
Automotive is the major contributor to the used oil collection business. This segment has diverse points of collection, which differ in terms of volume of used oil collected from them.
  It includes small independently owned garages, large operators of commercial fleets, automotive services chains, DIY, and large commercial operations.
  In recent years, the used oil collection rate has significantly increased due to the growing awareness of proper disposal of used oil among lubricant consumers. Moreover, the set up of used oil collection centers, lube centers, and door-to-door pickup facilities has made the collection process more convenient.
  In 2018 and 2019, DIY accounted for a significant share of the overall used oil collection. As consumers changing oil at their places have facilities to dispose of used oil either at the collection facility or lube centers. However, in 2020, it declined sharply due to COVID-19.
  In 2020, most of the used oil is collected from commercial facilities such as service stations, lube shops, fuel stations, car dealers (franchised workshops), quick lubes as well as industrial operations such as forestry, agriculture, and mining operations. This is because these facilities are typically serviced by a registered collector that has a service agreement with that facility.
  In 2020, commercial facilities accounted for 85% of the total used oil collection in the automotive segment.
  Approximately 15% of the total used oil collected comes from consumers that change their own oil or small commercial operators that choose to use the free consumer drop-off system.
In 2020, both countries initially noticed a decrease in the oil collection volume due to COVID-19. During government-mandated lockdowns, associations and regulatory authorities in both countries played a major role in managing the used oil collection.
  Guidelines and awareness programs focused on the safe storage of used oil were being launched by authorities to help consumers safely store products until they could be returned to a registered facility.
  For instance, British Colombia Used oil Management Association launched a “top collector award program” to support the used oil collection business.
  Other programs such as Most Improved Location as well as Long Time Service Award Program were launched by the British Colombia Used Oil Management Association to support the used oil collection during the pandemic.
AUTOMOTIVE USED OIL COLLECTION BY SOURCES, 2020 |  | 
SOURCE | KILOTONNES | % OF USED OIL COLLECTED
Commercial facilities such as service stations and lube shops; and large commercial operations such as mining, forestry, and agriculture | 1952.8 | 85.0
Consumers (DIY)/Small operators | 344.6 | 15.0
Total | 2,297.4 | 100.0
Continued…

## Slide 255: Used Oil Collection
In the United States and Canada, some re-refiners have done backward integration to also perform used oil collection as it reduces collection cost and ensures the quality of the used oil collected.
  For example, Clean Harbor, which owns Safety-Kleen, has over 200 locations for dropping used oil in the United States and Canada. It offers the facility of dropping used oil at its centers if the volume is less than 5.0 gallons or approximately 20.0 kgs. It is the largest used oil collector in the United States and Canada.
  Safety-Kleen has also enhanced its closed-loop program by launching the OilPlus program, through which any automotive or industrial lubricant consumer can buy the company’s Performance Plus-branded lubricants in exchange of used oil generated. Performance Plus-branded lubricants product line includes PCMO, HDMO, HTF, ATF, automotive and industrial greases, hydraulic fluids for industrial applications, and gear oils. Any consumer with less than 10 gallons of used oil can contact Safety-Kleen’s representative to become a member of the OilPlus program. It helps Safety-Kleen to increase product sales and expand its customer base.
  Another example of backward integration by re-refiners is Heritage Crystal Clean, a leading re-refiner in the United States, which acquired the collection fleet and collection centers of FCC Environmental Services to enter the business of oil collection. As of 2020, Heritage Crystal Clean had more than 85 service branches across the nation, including multiple waste recovery centers. It also has a re-refinery, regional antifreeze recovery centers, and several wastewater treatment facilities.
  Similarly, other re-refiners such as Avista Oil have presence in about 12 states of the United States to collect used oil directly from generators. Terrapure, one of the major re-refiners in Canada, has a well-established network of used oil collection facilities located in Western Canada. The company handles used oil collection services under its Oil Recycling Services group.
The pricing of used oil depends on the levels of supply and demand for used oil. Collectors may either charge generators to pick up their used oil or pay them for the oil. These charges mainly depend on the value they receive for their used oil from the aggregators/re-refiners/re-processors, which, in turn, are constrained by the value they can charge for their products. It is primarily influenced by the impact on competitive products of the price of crude oil.
Re-refiners have a mix of long-term contracts and spot purchases for sourcing used oil.
  Most of the used oil requirement is tied up in long-term contracts of one-year to five-year durations.
  The long-term contracts provide low-cost collection, as well as lower logistics cost as re-refiners can optimize collection frequency and routes.
  Spot purchases allow used oil re-refiners to fine-tune the average quality of used oil that is fed to the plants as all the used oil supply that the re-refiners are obliged to accept during the tenure of the long-term contracts may not be suitable for re-refining.
  Some small used oil collectors and re-refiners also engage in closed biddings, where they sell surplus used oil to other collectors or re-refiners.

## Slide 256: Used Oil Disposal 2020
Chart: USED OIL DISPOSAL IN THE UNITED STATES AND CANADA, 2020
| Fuel | Re-refining | VGO/MDO + Regen.-a | All other-b
Sales | 0.38 | 0.35 | 0.25 | 0.02
Total: 3,386.1 KT
Disposing of used oil in the environment is an illegal act in all parts of the United States and Canada, with penalties that vary from financial fines to prison terms.
  Safely storing the used oil is highly recommended to not only adhere to the laws in both countries but also protect the environment from hazardous materials.
  Enforcement is stringent in the United States and Canada due to which used oil is mostly disposed of in an environment-friendly way in these countries.
Out of the used oil collected in North America, approximately 60% is re-refined. This includes re-refining to basestocks, VGO/MDO, and regeneration of transformer oils.
  Approximately two-thirds of the re-refined used oil (1,156.7 KT) is re-refined to basestocks in the United States and Canada.
  Approximately, 815.6 KT of used oil is re-refined into VGO/MDO in the United States and Canada.
  The remaining used oil (around 80 KT) is regenerated. This is mainly transformer oils that are regenerated.
38% of used oil disposed of as fuel, while the remaining 2% of used oil is used as concrete demolding agents, blended into HSFO/ANFO, etc.
To promote a circular economy, used oil associations and other public bodies prefer used oil to be either re-refined into basestocks or reprocessed and regenerated into VGO/MDO or lubricants.
  However, the blending of used oil into heavy fuel has declined significantly in recent years due to the prospective and actual impacts of IMO 2020.
USED OIL DISPOSAL BY PRODUCT TYPE, 2020 |  |  | 
LUBRICANT TYPE | KILOTONNES |  | 
 | RE-REFINING-a | FUEL | ALL OTHER-b
Automotive Engine oils | 1,382.7 | 468.2 | 19.1
All Other-c | 669.6 | 821.8 | 24.5
Total | 2,052.3 | 1,290.0 | 43.6
a- Includes used oil re-refined into basestocks or re-refined into VGO/MDO or regeneration of transformer oil. |  |  | 
b- Includes other application such as concrete demolding agents, blended into HSFO/ANFO, etc. |  |  | 
c- Includes industrial oils and fluids, greases, and automotive oils such as MCO, ATF, etc. |  |  | 
Continued…
a- Includes used oil re-refined into VGO/MDO or regeneration of transformer oil.
b- Includes other application such as concrete demolding agents, blended into HSFO/ANFO, etc.

## Slide 257: Used Oil Disposal
In 2020, in the United States:
  Re-refined to basestocks: 1,020 KT
  Re-refined to VGO/MDO: 732.1 KT
  Regeneration of transformer oil: 50 KT
  Exports: 30 KT to Canada
In 2020, in Canada:
  Re-refined to basestocks: 136.7 KT
  Re-refined to VGO/MDO: 101.8 KT
  Regeneration of transformer oil: 11.8 KT
  Imports: 30 KT (included in 136.7 KT of used oil re-refining)
USED OIL DISPOSAL AND END-USE IN THE UNITED STATES AND CANADA IN KILOTONNES, 2020 |  |  | 
COUNTRY | RE-REFINING-a | FUEL | ALL OTHER
United States | 1,802.1 | 1,164.6 | -
Canada | 250.3-b | 125.4 | 43.6
Total-c | 2,052.3 | 1,290.0 | 43.6
a- Includes re-refining to VGO/MDO and transformer oil regeneration. b- Includes imports of 30 KT. c- Total do not add due to rounding. |  |  | 

## Slide 258: Used Oil Disposal 2021
Chart: USED OIL DISPOSAL IN THE UNITED STATES AND CANADA, 2021
| Fuel | Re-refining | VGO/MDO + Regen.-a | All other-b
Sales | 0.38 | 0.34 | 0.26 | 0.02
Total: 3,419.2 KT
In 2021, the used oil disposal remained the same in the United States and Canada. There was slight increase in used oil disposal volume due to an increase in lubricant demand.
USED OIL DISPOSAL BY PRODUCT TYPE, 2021 |  |  | 
LUBRICANT TYPE | KILOTONNES |  | 
 | RE-REFINING-a | FUEL | ALL OTHER-b
Automotive Engine oils | 1,398.6 | 473.8 | 19.0
All Other-c | 675.3 | 828.1 | 24.5
Total | 2,073.9 | 1,301.9 | 43.5
a- Includes used oil re-refined into basestocks or re-refined into VGO/MDO or regeneration of transformer oil. |  |  | 
b- Includes other application such as concrete demolding agents, blended into HSFO/ANFO, etc. |  |  | 
c- Includes industrial oils and fluids, greases, and automotive oils such as MCO, ATF, etc. |  |  | 
a- Includes used oil re-refined into VGO/MDO or regeneration of transformer oil.
b- Includes other application such as concrete demolding agents, blended into HSFO/ANFO, etc.

## Slide 259: Used Oil Re-refining
In 2020, re-refined Group II/II+ basestocks are the major re-refined basestock produced in the United States. Other basestock types such as Group I and III are produced in low quantities in the United States and Canada.
  There is only one re-refined, Universal Environmental Services, of re-refined Group III basestocks, with a basestocks capacity of around 27 killotonnes.
There are currently 15 registered used oil re-refining companies in the United States and Canada that are producing re-refined basestocks.
  The six largest companies accounted for about 80% of the total used oil capacity in both these countries in 2020.
  Clean Harbors acquired Safety-Kleen in 2012 and Evergreen Oil in 2013. In February 2015, Clean Harbors acquired Bango Refinery from Vertex Energy for a total purchasing price of USD 35.0 million. In 2021, the company signed a definitive agreement with Vertex Energy, Inc. to acquire certain assets related to Vertex’s used motor oil collection and re-refinery business.
  The company also owns Universal Lubricants’ used oil re-refining facility. Therefore, Clean Harbors has a total used oil capacity of 960.0 kilotonnes, amounting to almost 61% of the total re-refined used oil capacity in the United States and Canada. Sales of re-refined basestock are concentrated in the United States, where most re-refiners are located.
The United States also exports a small quantity of used oil to Eastern Canada. It was estimated around 30 KT in 2020.
  Safety-Kleen has a large captive market in its Breslau, ON re-refinery (which is only 100 miles from the U.S. border).
  Safety-Kleen Breslau processed 146 kilotonnes of used oil in 2019, of which Kline estimates about 50 kilotonnes was imported from the United States. The imports were estimated at around 30 KT in 2020. This is because used oil generation plummeted due to a decline in lubricant demand in 2020, leading to a decreased availability of used oil for re-refineries in the United States.
  Other than Breslau, Canadian re-refineries are small and geographically widespread.
Beyond the large volumes of used oil exported by Safety-Kleen to Canada, other cross-border movements of used oil from the United States to Canada are believed to be small.
Continued…

## Slide 260: Used Oil Re-refining
The total re-refined basestock capacity in the United States and Canada was estimated at 1,022 kilotonnes in 2020.
  Re-refined group II/II+ basestocks are the most produced re-refined basestocks in the United States, followed by re-refined Group I and Group III basestocks. Canada, on the other hand, consumes re-refined Group II/II+ basestocks for producing finished lubricants.
Presently, on account of the increasing demand for lighter grades in the automotive segment, demand for Group II/II+ and Group III basestocks is increasing. As a result, the production of re-refined Group II/II+ and Group III basestocks is also expanding, leading to a decline the demand for Group I basestocks.
  OEM recommendations and stringent fuel specifications that encourage the usage of lighter lubricant grades for vehicles are also leading to a decline in demand for Group I basestocks, due to which the production of re-refined Group I basestocks has also declined in both countries.
  Most of the re-refineries producing both Group I and Group II/II+ have either stopped producing Group I basestocks or reduced Group I basestocks production. They are mostly focusing on producing Group II/II+ basestocks.
  At present, re-refined Group I basestock are consumed for producing heavier grades of automotive lubricants and industrial oils.
MAJOR USED OIL RE-REFINERS IN UNITED STATES AND CANADA, 2020 |  |  |  | 
COMPANY | LOCATION | USED OIL FEED CAPACITY (KT) | RE-REFINED BASESTOCK CAPACITY (KT) | KEY PRODUCT
Safety-Kleen (Clean Harbors) | East Chicago, U.S | 403 | 255 | Group II/II+
Safety-Kleen (Clean Harbors) | Breslau, ON | 300 | 190 | Group II/II+
Heritage-Crystal Clean | Indianapolis, U.S | 259 | 160 | Group II/II+
Universal Environmental Services | Peachtree City, U.S | 190 | 133 | Group II/II+/III
Bango Refining (Clean Harbors) | Fallon U.S | 110 | 70 | Group II/II+
Heartland Petroleum (Clean Harbors) | Columbus, U.S | 69 | 62 | Group II/II+
Universal Lubricants (Clean Harbors) | Wichita, U.S | 62 | 40 | Group II/II+
Terrapure (GFL) | Vancouver, BC | 40 | 20 | Group II/II+
Olein Recovery | Yabucoa, U.S | 34 | 23 | Group II/II+
Ecolube Recovery | Portland, U.S | 26 | 18 | Group II/II+
Rock Canyon Oil | American Fork, U.S | 17 | 15 | Group I
Rational Resource | Plymouth, U.S | 17 | 13 | Group I
Green View Technologies (Clean Harbors) | Rollinsford, U.S | 16 | 10 | Group I
Rock Oil Refining | Stratford, U.S | 14 | 5 | Group I
Como Lube | Duluth, U.S | 11 | 8 | Group I
Total |  | 1,568 | 1,022 | 
Note: This does not include two re-refineries that are not operating currently. Evergreen Oil, which is owned by Clean Harbors. It has 93 KT used oil feed capacity and 60 KT Group II/II+ re-refined basestock capacity. Southeastern Petroleum. It has 47 KT used oil feed capacity and 30 KT Group I re-refined basestock capacity. |  |  |  | 
Continued…

## Slide 261: Used Oil Re-refining
In 2020, re-refiners were greatly impacted by less automotive-related travel and temporary customer shutdowns caused by the spread of COVID-19 in the first half of the year.
  Declining demand in the primary sectors impacted the re-refining business including the overall automotive sector, as consumer activity lags historical levels across the United States and Canada. Lower lubricant demand and price declines in the global oil market, exacerbated by COVID-19 impacts, reduced revenues for re-refiners.
  Re-refiners were compelled to operate at lower utilization rates due to the reduced availability of used motor oils as lubricant demand declined in 2020.
  Safety-Kleen temporarily shut down nearly half of the total production capacity of its used oil re-refineries in April 2020. However, by the end of 2020, re-refinery production capacity returned to mid-2019 levels.
The volume of re-refined basestocks available is driven by the overall finished lubricants demand. This is because finished lubricant demand affects the used oil generation and availability.
Crude oil prices also impacted the re-refining market. As crude oil prices increase, so do the prices of virgin basestocks; consequently, re-refined basestocks become more attractive.
  In the first half of 2020, crude oil prices plummeted that in turn adversely impacted the demand for re-refined basestocks. In April 2020, the monthly price of West Texas Intermediate (WTI), the North American benchmark price, sunk to a low of about USD 19 as markets reacted to higher inventories.
  In the months following, WTI prices partially recovered, albeit at an uneven pace, supported by production cuts and gradual reopening for some economies. This helped bring back some demand for oil. In 2020, WTI prices averaged USD 38.6, down from an annual average of USD 57.1 in 2019.
By the end of 2020, crude oil prices recovered to pre-pandemic levels of USD 58 per barrel, which in turn, led to an increase in the price of virgin basestocks. Moreover, tightening in the supply of virgin basestocks in the second half of 2020 due to lower utilization rate of refineries and halt in production pushed the prices up again at the end of 2020. Several plants halted production before Hurricane Laura hit the Gulf Coast in August 2020, including the 22,000 b/d API Group II Excel Paralubes plant in West Lake, Louisiana, and Motiva’s 40,300 b/d Group II plant in Port Arthur, Texas. Motiva was back online within two weeks, but Excel Paralubes was unable to restart until October.
Growing prices of virgin basestocks in recent years have resulted in an increase in the price of re-refined basestocks in recent years. This is because the quality of re-refined basestocks has improved and supply has increased over the years. As a result, re-refined basestocks are competing with virgin basestocks.
  Re-refiners selling finished lubricants usually take into consideration crude oil prices and finished lubricants prices produced using virgin basestocks to estimate their product prices.
Re-refiners sell basestocks on a contract basis or through tenders to blenders. Once a tender is final, a purchase order is placed by the blender mentioning the quantity of basestock needed, and then a call-off order is placed by the blender for the continuous supply of basestocks.

## Slide 262: Used Oil Re-refiner Profiles
Safety-Kleen
It is a wholly owned division of Clean Harbors (CLH), a public company, headquartered in Norwell, MA (Clean Harbors)/Richardson, TX (S-K), U.S.A.
Safety-Kleen was acquired by CLH in 2012 for $1.25 billion. Since that time, the company has pursued an aggressive policy of acquiring U.S. competitors. S-K is now the largest used oil collector and re-refiner in the world, fully integrated across the used oil value chain. Its assets and operations are predominantly located in the United States and Canada, with minor activities in Puerto Rico, Mexico, and India.
S-K produces a combination of base oils and heavy distillates at its re-refineries, plus recycled fuel oil (RFO) at more remote locations. It formulates finished lubricants at five blending plants and sells branded Performance Plus® packaged lubes. It also operates a branded closed-loop recycling system (OilPlusTM) with U.S. federal agencies, including the Post Office and the U.S Army, as well as with state and municipal entities.
Key Re-refinery Assets
Annual Volumetrics (incl. Vertex/Heartland):
Used Oil Collected: 686,000 Tons (2020)
Used Oil Processed: 739,000 Tons (2020)
Base Oil Produced: 377,000 Tons (2020)
Used Oil Value Chain Acquisitions:
Vertex Energy (incl. Heartland/H&H) (2021)
Green View Technologies (GVT) (2019)
Universal (2016)
Bango (from Vertex) (2016)
Emerald Services (2016)
Thermo Fluids (TFI) (from Nuverra) (2015)
Evergreen (2013)
Planned Investments:
S-K has been assessing a new base oil re-refinery project in TX for several years, but this project is on hold.
KEY RE-REFINERY ASSETS |  |  | 
OWNER | LOCATION | UO CAPACITY (KTONS/YEAR) | KEY PRODUCTS
Safety-Kleen | E. Chicago, IN | 403 | Gp. II/II+
Safety-Kleen | Breslau, ONT | 300 | Gp. II/II+
Bango | Fallon, NV | 110 | Gp. II
Heartland | Columbus, OH | 69 | Gp. II/II+
Universal | Wichita, KS | 62 | Gp. II
GVT | Rollinsford, NH | 16 | Gp. I
Vertex Energy | Marrero, LA | 238 | VGO
Emerald Svcs. | Tacoma, WA | 53 | MDO
Continued…

## Slide 263: Used Oil Re-refiner Profiles
Heritage Crystal Clean
It is a publicly owned subsidiary (NASDAQ:HCCI), of the Heritage Group, headquartered in Indianapolis, IN, U.S.A.
Initially formed as a wholly owned division of the Heritage Group in the 1980s, it focused on used oil collection in the Midwest, expanding to TX/LA in the 1990s. After the IPO in 2008, HCCI growth accelerated. It started up the Indianapolis re-refinery in early 2012, with an initial capacity of 172 KTA.
It has grown its used oil collection business through organic growth and M&A of three used oil collectors. It now handles used oil collection through 82 branches in 40 states.
The Indianapolis re-refinery capacity was expanded by 50% in 2015 (from 50 to 75 million gallons/year). Base oil production is about 90% Group II/10% Group I.
In addition to the re-refinery, HCCI operates 12 RFO plants and several antifreeze recovery operations. HCCI owns no blending plant; it sells all its base oil output to independent lube blender/marketers.
Key Re-refinery Assets
Annual Volumetrics (incl. Vertex/Heartland):
Used Oil Collected: 186,000 Tons (2020)
Used Oil Processed: 206,000 Tons (2020)
Base Oil Produced: 145,000 Tons (2020)
Used Oil Value Chain Acquisitions:
FCC Environmental (2014)
RS Used Oil Services (2013)
Crystal Flash (2011)
Planned Investments:
None. HCCI's used oil value chain business underperforms the industry. Several suitors have approached Heritage with carve-out proposals for the Oil Business division (used oil collection and re-refining). To-date, these approaches have been rejected, on the grounds of the necessity for a significant book asset write-down.
KEY RE-REFINERY ASSETS |  |  | 
OWNER | LOCATION | UO CAPACITY (KTONS/YEAR) | KEY PRODUCTS
Safety-Kleen | E. Chicago, IN | 403 | Gp. II/II+
Continued…

## Slide 264: Used Oil Re-refiner Profiles
Universal Environmental Services
It is private-owned with 86% owned by Avista Oil AG of Germany, headquartered in Peachtree City, GA, U.S.A.
Avista entered the U.S. used oil market in 2011 by gaining control over Universal Environmental Services’ (UES) used oil collection business in the Southeast. Since that time, through organic growth and acquisitions, UES has doubled its collection business.
The company now handles used oil collection from 48 locations in 24 states. Its assets include the Peachtree City re-refinery and 8 RFO plants.
The re-refinery was brought on-stream in mid-2013, at an original feed capacity of 90 KTA, which has been doubled by 2021. The plant produces mainly Group II/II+ base oils, and occasional volumes of solvent-extracted Group III, when economics support it. UES has no lube blending plants, but it contract-blends small volumes of finished lubricants
Key Re-refinery Assets
Annual Volumetrics (incl. Vertex/Heartland):
Used Oil Collected: 168,000 Tons (2020)
Used Oil Processed: 164,000 Tons (2020)
Base Oil Produced: 116,000 Tons (2020)
Used Oil Value Chain Acquisitions:
Enterprise Oil (Collector/Aggregator) (2021)
Avista acquires MidMark Capital and Navigator Partners’ equity in UES, raising its ownership stake to 86% (2017)
Metro Environmental (2015)
Private investor acquires McPherson equity (2017)
McPherson Oil (Collector) (2011)
Avista acquires 50% of UES (2011)
Planned Investments:
Avista was exploring a second re-refinery in the United States in the early 2010s, but this concept is on hold.
KEY RE-REFINERY ASSETS |  |  | 
OWNER | LOCATION | UO CAPACITY (KTONS/YEAR) | KEY PRODUCTS
UES | Peachtree City, GA | 190 | Gp. II+/III
Continued…

## Slide 265: Used Oil Re-refiner Profiles
World Oil Corporation
World Oil Corporation is private-owned by the Roth family.
The company was founded in 1938 and is headquartered in Compton, CA, U.S.A.
The company operates in seven divisions, including recycling, terminals, refining, and environmental services, in California.
World Oil Recycling (WOR, formerly Demenno-Kerdoon) is a sister company of World Oil Environmental Services (WOES, formerly Asbury Environmental Services). It is the largest used motor oil, coolant, and fuel recycling company in the Western U.S.
The WOES performs used-oil collection through its 13 collection centers and transportation to the WOR facilities for further recycling.
The recycling facility, located in Compton, CA, has a total used oil feed capacity of 344 kilotons per year, producing VGO/MDO, but operates below capacity. The plant mainly produces MDO for the LA/Long Beach marine bunker fuel market, while asphalt flux is sold to Mexican roofing asphalt producers.
Key Re-refinery Assets
Annual Volumetrics (incl. Vertex/Heartland):
Used Oil Collected: ~170,000 Tons (2020)
Used Oil Processed: ~185, 000 tons (2020)
VGO/MDO Produced: ~125 000 tons(2020)
Used Oil Value Chain Acquisitions:
Pan Pacific Petroleum
DeMenno-Kerdoon recycling
Ribost Marine Terminal
Asbury Environmental Services
Planned Investments:
NA
KEY RE-REFINERY ASSETS |  |  | 
OWNER | LOCATION | UO CAPACITY (KTONS/YEAR) | KEY PRODUCTS
World Oil Recycling | Compton, CA | 344 | VGO, MDO, Asphalt flux

## Slide 266: Used Oil Processors
In addition to basestocks re-refineries, both the United States and Canada have VGO/MDO re-refineries and industrial oil regenerating facilities.
  There are about 12 registered VGO/MDO re-refineries and industrial oil regenerating facilities in the United States and Canada, out of which eight are VGO/MDO re-refineries, while the remaining four facilities are industrial oil regenerating facilities.
VGO/MDO are largely being used as a source of fuel in various industrial applications. Apart from industrial application VGO/MDO are also significantly used in the marine industry.
  Recent implementation of the International Maritime Organization (IMO) regulations for a 0.50% global sulfur cap for marine fuels—which began on January 1, 2020, and is known as IMO 2020—is expected to significantly impact the used oil re-refining business.
  With the implementation of IMO 2020 regulations, there is expected a shift in the demand for marine fuel to low sulfur content fuel, such as distillate gas oils and VGOs, from high sulfur heavy fuel. This is expected to increase the demand for VGO in the future.
Used oil processors use sequences of dehydration, gas oil recovery/separation, and fractionation to regenerate used oil to produce VGO and MDO. These fuels are then used by oil companies to produce new lubricating oils or go for marine fuel.
Processors sell final products to industries on a contract basis specifying the quantity of VGO/MDO required for specific periods. Generally, these contract are of three to five years depending on companies.
VGO/MDO PROCESSORS CAPACITY IN THE UNITED STATES AND CANADA, 2020 |  | 
COMPANY | LOCATION | USED OIL FEED CAPACITY (KT)
Demenno-Kerdoon (World Oil) | Compton, U.S. | 344
Omega Refining (Clean Harbors) | Marrero, U.S. | 238
Noble Oil | Sanford, U.S. | 148
Synergy Hydrocarbon Recovery | Kingsland, U.S. | 83
Aaron Oil (Tradebe) | Saraland, U.S. | 66
Veolia | St. Hyacinthe, QB. | 63
Emerald Services (Clean Harbors) | Tacoma, U.S. | 53
Intergulf Corporation | La Porte, U.S. | 28
ORRCO | Portland, U.S. | 26
HD petroleum | Winnipeg, MB | 11
Total |  | 1,060
Note: This does not include Vertex Energy’s plant of 103 KT capacity as it is not operating currently. |  | 
INDUSTRIAL OIL REGENERATING CAPACITY IN THE UNITED STATES AND CANADA, 2020 |  | 
COMPANY | LOCATION | TRANSFORMER OIL PROCESSING CAPACITY (KT)
Hydrodec | Canton, U.S. | 39
Aevitas | Brantford, ON | 23
EPS Industries | Wheeling, U.S. | 9
Environmental Management Systems (EMS) | Phoenix, U.S. | 8
Total |  | 79

## Slide 267: Re-refined Lubricants
In 2020, total lubricants consumption in both the United States and Canada is 8,132.0 kilotonnes.
  The production of re-refined basestocks is less than 10% of the total basestocks (both virgin and re-refined) produced in the countries. This implies that the production of re-refined basestocks, which are mostly used for producing PCMO, HDMO, and hydraulic fluid, is extremely low compared to the production of virgin basestocks.
  This situation is not expected to change in the future. Due to less production of re-refined basestocks, re-refiners are unable to create demand among customers, especially vehicle operators, as an increase in demand will create an imbalance between demand and supply. Earlier, a few major re-refined lubricant suppliers tried to introduce their re-refined lubricants in the market but failed to cater to the demand of customers due to low production levels.
  As a result, they had to remove their re-refined lubricant product lines from the market due to increasing demand and low supply, which created an imbalance in the market. As a result, the re-refining business is mostly dominated by the closed-loop business, which means a collector collects used oil from customers, re-refines it into finished lubricants, and sells the re-refined finished lubricant back to the same customers. There is a need to increase used oil collection rates in both countries to increase re-refined basestocks production and avoid a situation of demand–supply imbalance in the market.
It is estimated that 1,156.7 kilotonnes of used oil re-refined to produce nearly 751.8 kilotonnes of re-refined basestocks in 2020.
Automotive accounted for 65% of the consumption of re-refined basestocks in the United States and Canada.
  PCMO led the consumption in automotive with 35% of the total re-refined basestocks consumed.
  Lower prices of re-refined lubricants compared to virgin basestock-based lubricants make them preferable among consumers.
  The commercial segment followed closely at 30% of the total lubricants demand.
CONSUMPTION OF RE-REFINED BASESTOCKS BY PRODUCT CATEGORY IN UNITED STATES AND CANADA, 2020 | 
LUBRICANTS | SHARE (%)
PCMO | 35
HDMO | 30
Hydraulic oil | 15
All other-a | 20
Total | 100
a- Includes other oils such as gear oils and industrial engine oils | 
Continued…

## Slide 268: Re-refined Lubricants
Lubricant suppliers, such as Safety-Kleen, are trying to educate customers that their product is derived from re-refined basestocks.
  They have asked local garages, workshops, and quick lubricants to inform customers visiting them that their lubricants are derived from re-refined basestocks. However, the local garages, workshops, and quick lube facilities that were interviewed said that customers still perceive lubricants made from re-refined basestocks to be lower in quality compared to lubricants made from virgin basestocks. However, the situation is improving as customer perception toward lubricants made from re-refined basestocks has improved.
  A few customers have some idea about re-refined basestocks and lubricants. However, most customers still prefer virgin basestock-based lubricants. Customers, especially the ones visiting local garages, workshops, and quick lubes, want their lubricants to meet product specifications. They want the highest-quality lubricants at the lowest possible price.
  Finished lubricants made from re-refined basestocks are lower in price compared to lubricants made from virgin basestocks; however, customers believe that the lower price of lubricants is due to lower quality, leading to low demand for lubricants made from re-refined basestocks.
A few re-refiners have lubricant-blending facilities to produce finished lubricants. These companies are selling finished lubricants to automotive and industrial customers. At present, the most preferred re-refined PCMO grades are SAE 10W-30 and SAE 5W-30, and the most preferred re-refined HDMO grade is SAE 15W40.
BASESTOCK RE-REFINERS AND THEIR LUBRICANTS BLENDING PLANTS IN THE UNITED STATES AND CANADA, 2020 |  |  | 
RE-REFINERS | LUBRICANT BLENDING PLANT | BRAND NAME | PRODUCT TYPE/VISCOSITY GRADE
Safety-Kleen (Clean Harbors) | Yes | EcoPower | Automotive 5W-20, 5W-30, 10W-30, 10W-40, 20W-50, 10W, 30, SAE 30 Gear Oil: GL-5 80W-90, GL-5 85W-140 Industrial Industrial engine oil: Railroad diesel engine oil Hydraulic oil: ISO 22, ISO 32, ISO 46, ISO 68, ISO 100, ISO 150
Universal Lubricants | Yes | Eco Ultra | Automotive HDMO: SAE 15W-40, SAE 10W-30, PCMO: SAE 10W-30, SAE 5W-20, SAE 5W-30 Industrial Hydraulic oil: ISO 32, ISO 46, ISO 68
Terrapure | Yes | Advanta ECO (basestocks brand) | Selling basestock grades under the brand name “Advanta ECO” Basestocks grades 100N, 150N, 450N Also selling white label recycled automotive lubricants and industrial oils
Continued…

## Slide 269: Re-refined Lubricants
The attitude of the U.S. and Canadian population toward proper disposal of used oil has slightly improved over the past five years because of environmental safety awareness. This has led to a slight increase in the re-refined basestocks production in recent years. However, government authorities, used oil generators, and re-refiners need to be more aggressive to educate customers and increase re-refined basestock production.
  For instance, Jiffy Lube’s official website provides information on the benefits of collection and re-refining of used oil. It also explains that Jiffy Lube is properly collecting its used oil after its signature oil change services.
  Similarly, the California Department of Resources Recycling and Recovery has tied up with the California State University-Long Beach Foundation to provide guidance to fleet managers about the benefits of using re-refined lubricants.
  Some quick lube channels are also selling finished lubricants derived from re-refined basestocks. Eco Lube Express, an oil change service provider in the United States, sells Safety-Kleen’s EcoPower engine oil brand, along with other virgin basestock-based finished lubricant brands, such as Mobil 1, Kendall, and Castrol.
  EcoPower is Safety-Kleen’s engine oil brand that is produced from re-refined basestocks It is available in various viscosity grades, such as SAE 15W-40 (HDMO), SAE 10W-30 (HDMO), semi-synthetic SAE 5W-20 (PCMO), SAE 5W-30 (PCMO), and SAE 10W-30 (PCMO). Eco Lube Express is an authorized dealer of EcoPower products.
  Additionally, Safety-Kleen is the official sponsor of the National Association for Stock Car Auto Racing program and runs various educational programs to increase customer awareness about re-refined lubricants in the United States and Canada.

## Slide 270: Finished Lubricant Market Outlook
Total demand for finished lubricants, including process oils, in North America will augment from 8,071.3 kilotonnes in 2020 to 8,465.7 kilotonnes in 2025. The United States is the major contributor, accounting for 91% of the total lubricant demand in North America in 2020, and is expected to continue its dominance over the forecasted period. Canada accounted for 9% of the demand.
  The outlook for U.S. lubricant demand during 2020 to 2025 will be greatly impacted by the COVID-19-related restrictions and trade barriers.
Chart: PROJECTED FINISHED LUBRICANT MARKET IN UNITED STATES AND CANADA, 2020-2030
| Industrial | Consumer | Commercial
2020 | 4233.3 | 1998 | 1840
2021 | 4262.2 | 2013.3 | 1872
2025 | 4376.2 | 2078.8 | 2010.7
2030 | 4349.5 | 1963 | 1902
Continued…

## Slide 271: Finished Lubricant Market Outlook
  As the United States resumed economic activities in the latter part of 2020 and in 2021, the country’s GDP recovered. According to the International Monetary Fund’s forecasts, the U.S. GDP recovered quickly and accounted for 6.4% growth in 2021 and is projected to account for an average of about 2.0% until 2025.
The overall lubricants demand in the United States is expected to reach an estimated volume of 7,545.8 kilotonnes in 2030.
  Lubricants consumed by the consumer automotive market segment are expected to grow at a slow rate of 1.0% annually during 2020-2025. After 2025, the lubricant demand in the consumer segment is expected to decline at an annual rate of 1.1% during 2025-2030. The increased consumption of synthetic oils in the segment, growing penetration of EVs, and better maintenance practices are some of the key factors resulting in a slow and declining growth in the consumer automotive lubricant segment.
  In the commercial automotive segment, growing construction, and trucking activities in the country are expected to drive the demand.
The Canada finished lubricant market is expected to decline over the forecast period and reach 668.7 kilotonnes in 2030 from 698 Kilotonnes in 2020.
  After a drop in lubricant demand in 2020 due to COVID-19, the market witnessed some recovery in 2021. However, it will eventually decline through the forecast period 2021 to 2030.
  This decline will largely be because of widening ODIs for PCMO and a proportionate decline in its demand.
  As new vehicles are added to Canada’s consumer automotive parc, older vehicles will continue to be scrapped. Moreover, the growing penetration of electric cars will further limit the demand for PCMO over the long term.

## Slide 272: Used Oil Industry Outlook
With a growth rate of 1% in the overall lubricant consumption from 8,071.3 kilotonnes in 2020 to 8,465.7 kilotonnes in 2025, the total used oil generated in the United States and Canada in 2025 is expected to increase at a very slow pace during 2020 through 2025. In percentage terms, the used oil generation rate is expected to increase from 57% in 2020 to 59% in 2025. This will be due to improving vehicle technology, leading to fuel efficiency and, subsequently, to more generation of used oil.
The percentage of used oil collected is expected to increase to 74% of the generated volume, as collectors are expected to expand their collection network to improve collection.
  The share of re-refining in the disposal of used oil is expected to reach 61% as the re-refining capacity increases. The production of re-refined basestocks is expected to increase with the addition of new re-refining capacities by four re-refiners—Regen III, Puraglobe, Rational Resource, and Mesa Oil Recycling—by 2025. The average yield rate of re-refining is expected to remain at 65%.
  The percentage of collected used oil usage as fuel is expected to remain stable at 38%.
  The used oil usage in other activities is expected to decrease to 1%. Share of other applications is expected to decrease to 1% because of increasing awareness of hazardous implications of disposing used oil in an environmentally friendly way.
Chart: USED OIL GENERATION, 2025
| Used oil generated | Lubricant lost
Sales | 0.59 | 0.41
Chart: USED OIL COLLECTION, 2025
| Collected | Not collected
Sales | 0.74 | 0.26
Chart: USED OIL DISPOSAL, 2025
| Fuel | Re-refining | VGO/MDO + Regen.-a | All other-b
Sales | 0.38 | 0.37 | 0.24 | 0.01
Chart: USED OIL RE-REFINING, 2025
| Basestock-a | All other
Sales | 0.65 | 0.35
Total: 4,994.8 Kilotonnes
Total: 3,696.1 Kilotonnes
Total: 1,352.8 Kilotonnes
Total: 8,465.7 Kilotonnes
Continued…
a- Includes used oil re-refined into VGO/MDO or regeneration of transformer oil.
b- Includes other application such as concrete demolding agents, blended into HSFO/ANFO, etc.

## Slide 273: Used Oil Industry Outlook
Chart: USED OIL GENERATION, 2030
| Used oil generated | Lubricant lost
Sales | 0.6 | 0.4
Chart: USED OIL COLLECTION, 2030
| Collected | Not collected
Sales | 0.75 | 0.25
Chart: USED OIL DISPOSAL, 2030
| Fuel | Re-refining | VGO/MDO + Regen.-a | All other-b
Sales | 0.38 | 0.37 | 0.24 | 0.01
Chart: USED OIL RE-REFINING, 2030
| Basestock-a | All other-c
Sales | 0.65 | 0.35
With the growing focus on circular solutions to support sustainability targets, the re-refining sector in North America is expected to grow over the coming decade.
  By 2030, re-refining, reprocessing, and regeneration of used oil is expected to remain stable at 61% of total used oil collected. The re-refining capacity as shown on slide 52 is expected to remain stable during 2025-2030. Therefore, no change in the share of re-refining is expected after 2025.
  The collection of used oil is expected to increase to 75% in 2030 supported by the growing footprint of re-refiners in the collection business. As of now, the majority of used oil is collected through lube centers and drop-off facilities. However, in the future, it is expected that most of the re-refiners would backward-integrate to make their operations more efficient.
Total: 8,214.5 Kilotonnes
Total: 4,928.7 Kilotonnes
Total: 3,696.5 Kilotonnes
Total: 1,352.9 Kilotonnes
a- Includes used oil re-refined into VGO/MDO or regeneration of transformer oil.
b- Includes other application such as concrete demolding agents, blended into HSFO/ANFO, etc.

## Slide 274: Re-refined Basestocks Capacity Outlook
The re-refined basestock capacity is expected to grow 26% during 2020 to 2025 as new players enter re-refining in the United States and Canada to cater to the growing demand for re-refined basestocks.
At present, no re-refiner has announced to close its re-refining facility in the countries in the near future. It is expected that Evergreen Oil, operating its re-refining facility in Irvine, CA, will close its plant in 2021. However, there has been no official announcement. Currently, Evergreen Oil is producing Group II/II+ basestocks in the United States.
As the demand for virgin Group I basestocks is declining and shifting toward Group II and Group III basestocks, the re-refining basestocks market is also following the same trend. Most of the re-refiners currently operating in the United States and Canada are producing Group II/II+ basestocks. Demand for re-refined Group I basestocks will be mainly accounted for by finished industrial lubricants over the next five years.
In 2020, there are only four re-refiners producing re-refined Group I basestocks.
  Few re-refiners, which are producing re-refined Group I basestocks, are expected to upgrade themselves to produce Group II basestocks, leading to a decline in the production of re-refined Group I basestocks.
  For instance, Rational Energies plans to double its re-refining capacity of Group I basestocks and upgrade itself to produce Group II basestocks in 2022. Currently, the company has the capability to produce re-refined Group I basestocks. The remaining Group I basestocks re-refiners will continue to operate to meet the demand for finished industrial lubricants and heavier grade automotive oils. This is because the demand for Group I-based industrial lubricants and heavier grade automotive oils will not completely vanish over the next 5-10 years.
RE-REFINED BASESTOCK CAPACITY, 2020, 2021, 2025, AND 2030 |  |  |  |  | 
 | KILOTONNES |  |  |  | 
Company | LOCATION | 2020 | 2021 | 2025 | 2030
Safety-Kleen (Clean Harbors) | East Chicago, U.S | 255 | 255 | 255 | 255
Safety-Kleen (Clean Harbors) | Breslau, ON | 190 | 190 | 190 | 190
Heritage-Crystal Clean | Indianapolis, U.S | 160 | 160 | 160 | 160
Universal Environmental Services | Peachtree City, U.S | 133 | 133 | 133 | 133
Bango Refining (Clean Harbors) | Fallon U.S | 70 | 70 | 70 | 70
Heartland Petroleum (Clean Harbors) | Columbus, U.S | 62 | 62 | 62 | 62
Universal Lubricants (Clean Harbors) | Wichita, U.S | 40 | 40 | 40 | 40
Olein Recovery | Yabucoa, U.S | 23 | 23 | 23 | 23
Terrapure (GFL) | Vancouver, BC | 20 | 20 | 20 | 20
Ecolube Recovery | Portland, U.S | 18 | 18 | 18 | 18
Rock Canyon Oil | American Fork, U.S | 15 | 15 | 15 | 15
Rational Resource | Plymouth, U.S | 13 | 13 | 29 | 29
Green View Technologies (Clean Harbors) | Rollinsford, U.S | 10 | 10 | 10 | 10
Como Lube | Duluth, U.S | 8 | 8 | 8 | 8
Rock Oil Refining | Stratford, U.S | 5 | 5 | 5 | 5
Regen III-a | Texas U.S. | - | - | 192 | 192
Puraglobe-a | Tampa, FL, U.S. | - | - | 49 | 49
Mesa Oil Recycling-a | Belen, NM, U.S. | - | - | 11 | 11
Total |  | 1,022 | 1,022 | 1,290-a | 1,290-a
a– These projects are in financing or construction stage and will open in the near future. Their basestock capacity is calculated with the 65% yield rate for the re-refineries. Note: This does not include two re-refineries that are not operating currently. Evergreen Oil, which is owned by Clean Harbors. It has 93 KT used oil feed capacity and 60 KT Group II/II+ re-refined basestock capacity. Southeastern Petroleum. It has 47 KT used oil feed capacity and 30 KT Group I re-refined basestock capacity. |  |  |  |  | 
Continued…

## Slide 275: Re-refined Basestock Capacity Outlook
It is expected that the demand for Group III basestocks is likely to increase in the consumer segment due to stringent fuel specifications that are driving demand for SAE 0Ws, such as SAE 0W-16 oils.
  Extended drain intervals are achieved with oils having better thermal and oxidative stability, which is offered by Group III basestocks. Additionally, OEM push in the passenger car segment is aiding in demand growth for premium low viscosity basestocks. Also, there is no major producer of Group III basestocks in the United States, and this demand is mostly fulfilled by imports coming from Asia-Pacific and the Middle East.
  Such factors are expected to offer huge growth opportunities to re-refiners to invest or upgrade themselves to produce re-refined Group III basestocks. At present, only Universal Environmental Services produces re-refined Group III basestocks, with a total Group III basestocks capacity of about 26.5 kilotonnes per year.
In terms of upcoming re-refined Group III basestocks projects, Regen III is expected to commission its re-refinery most probably in 2022 in Alberta, Canada, and Texas. Currently, the company is looking for financing, and once the project is funded, the facility will be operational within 18 months. in September 2021, the company completed work on the Pre-FEED/Front-end loading (FEL-2) validation.
  The company’s major focus is to produce re-refined Group III basestocks using its proprietary technology, known as ReGen, to produce synthetic lubricants. Its ReGen process is a three-step process, which involves a contaminant separation unit, a molecular separation unit, and a molecular treatment unit.
  Through this ReGen technology, Gen III Oil Corporation has the capability to produce significant volumes of Group III basestocks at a lower cost, using the solvent extraction process. The technology was patented in 2005. Another re-refinery, Avista, is expected to set up a hydrotreater unit to upgrade its refinery from Group II basestocks to Group III basestocks by the end of 2020.
  Similarly, Rational Resource is in the process of expanding its operational and executive teams and is expanding the capacity of its Plymouth, MN, plant to generate 12 million gallons per year of UMO processing. The expansion is expected to be completed by the first quarter of 2022.

## Slide 276: Market Evaluation
Opportunities and Challenges
The re-refining scenario in the United States and Canada may not witness any drastic changes in the forecast period because lubricant demand is expected to decline slightly, due to increasing use of synthetic and semi-synthetic oils and a flat automotive market. Also, no major change in used oil generation, collection, and re-refining is expected to happen in these two countries. However, the existing situation does provide an opportunity for consolidation as well as forward or backward integration to companies in the industry.
There will be some transition within the industry, such as a production shift from re-refined Group I basestocks to re-refined Group II and Group III basestocks. The growing preference for lighter-grade PCMOs is expected to provide opportunities for re-refiners to enter or upgrade themselves to produce re-refined Group III basestocks. This will increase the production of Group III basestocks over the next 10 years.
IMO 2020 regulations will also have an impact on the re-refining business as re-refiners have to invest in technology to comply with the regulations for marine fuels. It is an expensive decision for re-refiners; however, they will have to invest in the technology as, otherwise, they will be unable to sell their products in the market, which is not a viable business model. Therefore, re-refiners have to upgrade themselves to produce products meeting IMO 2020 regulations.
Few companies such as HD-Petroleum, headquartered in Canada, are producing MDOs that are already meeting the requirements of IMO 2020 regulations. Technology providers, including Pragmatic Environmental Solutions Company, mentioned that the regulation is providing additional business to engineering companies and technology providers as re-refiners have to upgrade themselves to meet the requirements of the regulation before 2020.

## Slide 277
Western Europe

## Slide 278: Western Europe Market Synopsis
Chart: USED OIL MATERIAL BALANCE IN WESTERN EUROPE, 2021-2030 (MILLION TONS)
| Finished Lube Demand | Used Oil Generated | Used Oil Collected | Used Oil Re-refined | RRBO produced
2021 | 3281.6 | 1902.7 | 1596.1 | 877.3 | 570.2
2025 | 3562.8 | 2066.4 | 1694.4 | 995.6 | 647.1
2030 | 3472.4 | 1979.3 | 1642.8 | 1008 | 655.2
Used Oil Regulations
In Europe, the individual countries are allowed to frame their own regulations under the framework provided by the European Waste Framework Directive, 2008/98/EC, amended by Directive (EU) 2018/851.
Countries such as Italy and Portugal regulate the collection and disposal of used oil through consortiums. Taxes are also levied such as in Italy to fund this consortium.
On the other hand, countries such as Germany follow free market policies for the used oil industry.
Used Oil Material Balance
The identity of the collector and the type of company varies from country to country, depending on the type of regulatory system within the country.
In countries in Southern Europe such as Italy, Spain, and Portugal, there are national used oil collection agencies which oversee collection companies and regulate used oil collection and distribution on a national scale.
The choice on whether to allocate collected used oil toward re-refining or fuel depends on re-refining capacity, the type of lubricant, and public priorities, among other factors.
In most of the countries, most of the used oil is re-refined either into basestocks or VGO/MDO except in the UK, where is it mostly disposed as fuel due to lack of re-refining capacity.
Disposal is not expected change during the forecast period.
MAJOR USED OIL RE-REFINERS IN USA AND CANADA, 2021-2030 |  |  | 
 | RE-REFINED BASESTOCKS CAPACITY (KILOTONNES) |  | 
COMPANY | 2021 | 2025 | 2030
Avista | 155.0 | 155.0 | 155.0
Itelyum | 131.0 | 131.0 | 131.0
Puraglobe-a | 100.0 | 150.0 | 150.0
Eco Huile | 60.0 | 60.0 | 60.0
Sertego | 60.0 | 60.0 | 60.0
STR Tecoil | 40.0 | 40.0 | 40.0
Whelan | 35.0 | 35.0 | 35.0
Cator | 25.0 | 25.0 | 25.0
Enviroil | 15.0 | 15.0 | 15.0
Egeo Oil | 15.0 | 15.0 | 15.0
R.A.M. Oil | 10.0 | 10.0 | 10.0
Total | 646.0 | 696.0 | 696.0
a- The re-refinery is a re-refined Group III basestock re-refinery with 100 KT capacity to produce re-refined Group III basestocks since April 2021. In 2020, it had a 50 KT production capacity for Group II basestock and 50 KT capacity for Group III basestock. |  |  | 
Used Oil Re-refining
In Western Europe, the trend is towards producing re-refined Group II and III basestocks, however, it is not as strong as the US. In Western Europe, most of the capacity is still focused on producing re-refined Group I absestocks.
However, this trend is changing as re-refiners such as Avista and Puraglobe are moving towards producing re-refined Group II and III basestocks. Itelyum has recently expanded its re-refined Group II basestocks capacity in the region.
Opportunities
The quantity of used oil feedstock available for re-refining in Western Europe is increasing thanks to regulatory and fiscal incentives to improve collection and generation rates, encouraged by the EU’s interest in promoting a circular economy.
The amount of re-refining with suitable quality for basestocks production is also rising as the quality of used oil improves. Used oil feedstocks in Western Europe are more often likely to be made from group III basestocks that has a superior quality.
Challenges
In some countries, there is insufficient feedstock to cover the whole of the re-refining capacity and feedstock needs to be imported from abroad to make up the shortfall. There are logistical and administrative difficulties in importing waste oil, since they are classified as a hazardous waste.

## Slide 279: Economic Background
Western Europe includes Germany, France, Italy, Spain, and the United Kingdom, among other countries situated in Western and Central Europe. All the countries taken into consideration in this chapter are members of the European Union (EU), with the exception of the United Kingdom, which has exited the European Union in the aftermath of the 2016 Brexit referendum. The exit has, however, has been in effect only in January 2021, with the end of the Brexit transition period. During the transition period, lasting through 2020, the United Kingdom remained a member of the EU.
SELECTED ECONOMIC CHARACTERISTICS OF COUNTRY, 2020 AND 2021 |  | 
KEY INDICATOR | 2020 | 2021
Population (Million) | 424.7 | 425.9
GDP at current prices (USD Billion) | 17,400 | 19,700
GDP per capita, current prices (USD) | 40,900 | 46,280
GDP growth rate, constant prices (Annual % change) | -6.9 | 4.5
Inflation, average consumer prices (Annual % change) | 0.3% | 1.4%
Current account balance (% Of GDP) | 2.2 | 2.5
Share in Real GDP-a |  | 
Services (%) | 70.9 | 70.9
Industry (%) | 25.1 | 25.1
Agriculture (%) | 1.6 | 1.6
a- Figures for the European Union (EU), estimates from 2017. |  | 
Source: CIA World Factbook, International Monetary Fund World Economic Outlook 2021 |  | 
Continued…

## Slide 280: Economic Background
Western Europe includes several highly developed economies, such as Germany and France, although levels of economic growth vary across the continent. The region has been struck by the 2008 global financial crisis and the Eurozone sovereign bond crisis, which started in 2010. Most countries have embarked on a course of policies dictated by the need to reduce unbalanced public accounts and high debt levels. Governments have pursued fiscal austerity and reduced public expenditure in the interest of reducing budget deficits and increasing debt repayment. Italy, with its high levels of public debt, has been one of the most affected countries, together with Spain.
The situation improved from the end of 2014, aided by the long-running quantitative easing program launched by the European Central Bank (ECB), which saw the bank intervening on markets to mass purchase sovereign bonds of the most affected countries, reducing yields. The economic outlook improved, and GDP growth levels recovered terrain lost during the crisis years. The recovery, after slowing down to an annual GDP growth of 1.3% in 2019, was arrested by the onset of the 2020 COVID-19 pandemic. European governments imposed nationwide lockdowns for several periods during 2020 and early 2021, curtailing economic activities and freedom of movement in order to contain the spread of the virus. GDP in Western Europe fell by 6.9% in 2020.
The health situation has improved markedly with the introduction of mass vaccination programs in the region and the continued easing of virus containment measures has contributed to an economic recovery. Upbeat survey results among both consumers and businesses in Western Europe show that a rebound in consumption is underway and is set to strengthen during 2021.
After a marginal contraction of GDP in the first quarter of 2021, GDP in both the Eurozone and the wider EU is forecast to grow by 4.8% in 2021 and 4.5% in 2022 in both the EU and the euro area, according to estimates by the European Commission. The volume of output across the bloc is projected to return to its pre-crisis level in the last quarter of 2021. In the United Kingdom, GDP is estimated to have grown by 4.8% in the second quarter of 2021 following the easing of COVID-19 restrictions.
Rising energy and commodity prices, production bottlenecks due to the shortage of components and raw materials, and capacity constraints in the face of rising demand are expected to exert upward pressure on consumer prices. Inflation in the Eurozone is expected to reach 1.9% at the end of 2021 and go back to 1.4% in 2022. Inflation may turn out higher than forecast if supply constraints are more persistent and price pressures are passed on to consumer prices more strongly.
Rising commodity prices and supply chain constraints also represent a risk to economic growth. The economic recovery in the United Kingdom is particularly vulnerable, due to the introduction of customs checks on its borders with the EU, the legacy of pandemic measures. and the shortage of specialized staff such as heavy good vehicle (HGV) truck drivers which are exacerbating the effects of supply chain disruptions, ensuing in shortages of critical goods such as fuel. The consumer price index in summer 2021 averaged inflation growth of 2.4%.

## Slide 281: Vehicle Production
Million units
Chart: LIGHT COMMERCIAL VEHICLE PRODUCTION BY COUNTRY IN WESTERN EUROPE, 2019-2021
| Germany | France | UK | Italy | Spain and Portugal | Others
2019 | 0.2 | 0.5 | 0.1 | 0.3 | 0.4 | 0.1
2020 | 0.1 | 0.4 | 0.1 | 0.3 | 0.3 | 0
2021 | 0.1 | 0.5 | 0.1 | 0.3 | 0.4 | 0
Million units
The commercial vehicle population in Western Europe in 2020 stood at 32.7 million.
Passenger vehicle production in Europe fell by 25% in 2020, mostly due to assembly plant closures effected by OEMs in response to national efforts to combat the spread of the pandemic. Production levels are expected to rebound by 26% in 2021, returning to close to 2019 levels. Similar patterns can be observed in commercial vehicle production.
Supply chain disruptions have ensued in a global shortage of critical raw materials and components, such as electronic chips for vehicle electronic systems, and this is affecting automotive manufacturing output.
Chart: PASSENGER VEHICLE PRODUCTION BY COUNTRY IN EUROPE, 2019-2021
| Germany | France | UK | Italy | Spain and Portugal | Others
2019 | 4.7 | 1.6 | 1.3 | 0.6 | 2.4 | 1.3
2020 | 3.5 | 0.9 | 0.9 | 0.5 | 2 | 1.1
2021 | 4.5 | 1.2 | 1.3 | 0.6 | 2.5 | 1.1
Chart: HEAVY COMMERCIAL VEHICLE PRODUCTION BY COUNTRY IN WESTERN EUROPE, 2019-2021
| Germany | France | UK | Italy | Spain and Portugal | Others
2019 | 158 | 56 | 20 | 31 | 27 | 192
2020 | 105 | 39 | 13 | 24 | 19 | 139
2021 | 123 | 45 | 16 | 27 | 24 | 158
Thousand units

## Slide 282: Vehicle Population
Chart: PASSENGER VEHICLE SALES BY VEHICLE TYPE IN WESTERN EUROPE, 2019-2021
| Germany | UK | France | Italy | Spain and Portugal | Others
2019 | 3.6 | 2.3 | 2.2 | 1.9 | 1.5 | 2.8
2020 | 2.9 | 1.6 | 1.6 | 1.4 | 0.9 | 2.3
2021 | 3.2 | 2 | 1.9 | 1.6 | 1.2 | 2.6
Million units
Million units
In 2020, passenger vehicles sales in Western Europe amounted to 10.7 million, registering a fall of 25.4% compared to 2019. Passenger vehicle sales are expected to recover to 12.5 million in 2021. The passenger vehicle population stood at 234.0 million in 2020.
Light commercial vehicle sales in Western Europe amounted to 1.6 million units in 2020, registering a fall of 18% compared with 2019. Light commercial vehicle sales are expected to recover to 1.8 million units in 2021.
Heavy commercial vehicle sales in Western Europe amounted to 249,000 in 2020, registering a fall of 26% compared to 2019. The heavy commercial vehicle population is expected to partially recover and rise to 279,000 in 2021.
Chart: LIGHT COMMERCIAL VEHICLE SALES BY COUNTRY IN WESTERN EUROPE, 2019-2021
| Germany | UK | France | Italy | Spain and Portugal | Others
2019 | 0.3 | 0.4 | 0.5 | 0.2 | 0.2 | 0.4
2020 | 0.3 | 0.3 | 0.4 | 0.2 | 0.1 | 0.3
2021 | 0.3 | 0.3 | 0.4 | 0.2 | 0.2 | 0.4
Chart: HEAVY COMMERCIAL VEHICLE SALES BY COUNTRY IN WESTERN EUROPE, 2019-2021
| Germany | UK | France | Italy | Spain and Portugal | Others
2019 | 95 | 52 | 62 | 26 | 32 | 69
2020 | 71 | 34 | 48 | 21 | 24 | 51
2021 | 80 | 38 | 53 | 23 | 28 | 57
Thousand units
Continued…

## Slide 283: Vehicle Population
Germany has the largest vehicle parc in Europe, comprising primarily compact class and small passenger vehicles. In 2020, an estimated 59.0 million vehicles operated in Germany, registering an increase of approximately 3.0% over 2019.
  The passenger vehicle parc numbered 48.8 million and increased by 1.1% in 2020 compared with 2019.
  The German automotive industry is recognized as the largest in Europe and is one of the most important economic sectors in the country. The industry’s turnover accounts for approximately one quarter of Germany’s domestic industry revenue. Almost three quarters of passenger vehicles manufactured in Germany are destined for export markets. Germany boasts the largest concentration of OEM plants in Europe. There are currently 43 automotive plants located in Germany.
  When the supply chain is included, there are almost 1,000 businesses involved in the automotive industry in Germany. Major German OEMs include the Volkswagen Group (VW), Daimler AG, and BMW, while Opel is part of the PSA Group, in turn part of Stellantis. Bosch, the ZF Group, and the Schaeffler Group are important auto-component OEMs.
  In 2020, German vehicle production stood at approximately 4.0 million units . Passenger vehicles accounted for approximately 90% of total production. The German automotive industry has entered a period of decline which started in 2016 and continued through 2020, exacerbated by factory closures during the COVID-19 pandemic.
  Passenger vehicle sales fell by 19% in 2020. Electric vehicles (EVs) recorded significant increases once again in 2020, driven by subsidies and growing consumer preferences for sustainable mobility solutions. The share of battery electric vehicles (BEVs) in the passenger vehicle parc rose from 0.3% (136,617 vehicles) in 2019 to 0.6% (309,083 vehicles) in 2020, and that of hybrid electric vehicles (HEVs) from 1.1% (539,383 vehicles) to 2.1% (1,004,089 vehicles). The share of plug-in hybrid vehicles (PHEVs) tripled to 0.6%.
Italy has the second largest passenger vehicle parc in Europe, amounting to approximately 40.2 million in 2020. Italy has a strong automotive tradition and a well-established motoring culture.
  Approximately 94% of households either own or have access to a passenger vehicle, and there are 655 motor vehicles per 1,000 inhabitants. The country is home to Fiat, an automobile manufacturer now part of the Stellantis Group.
  Italy saw some of the strictest lockdown measures implemented to contain the COVID-19 pandemic, including limits on personal mobility. Dealerships were closed and vehicle sales plummeted by 26% in 2020.
  Alternative-fuel vehicles, such as electric, hybrid, and LPG-powered, still make up only a negligible amount of the overall passenger vehicle parc in the country. Government-backed financial incentives for electric vehicle (EV) purchases were introduced only in 2018.
Continued…

## Slide 284: Vehicle Population
The United Kingdom has the third largest passenger vehicle population in Western Europe, with a passenger vehicle parc estimated at 35.4 million in 2019, according to estimates by LMC Automotive.
  A total of 1.6 million passenger vehicles were registered in 2020. Registrations for new passenger vehicles grew at a CAGR of approximately 1.5% between 2012 and 2019, before declining by 30% in 2020.
  The United Kingdom has been seeing a decline in passenger vehicle sales since 2016, as general consumer spending fell due to the climate of economic uncertainty following the May 2016 Brexit referendum. These downward pressures were exacerbated by dealership and factory closures during 2020.
  Despite the fall in new registrations, ultra-low-emission vehicles (ULEVs) saw large year-on-year increases in the United Kingdom, reaching 432,000 units at the end of 2020. The government has made ULEVs a key part of its efforts toward curbing carbon emissions and has put in place generous incentives toward ULEV purchasing, in addition to announcing a ban on new ICE vehicle sales beginning in 2030 which has contributed toward prompting the British automotive industry to invest in ULEV development.
  To support the United Kingdom’s EV manufacturing industry, the government has committed to spend nearly GDP 500 million in the next four years as part of the commitment to provide up to GDP 1 billion for the development and mass-scale production of electric vehicle batteries and associated EV supply chains.
France has a passenger vehicle parc of 33.6 million. An estimated 84% of households were motorized, with 47.5% owning one car, 31.1% with two cars, and 5.3% with three or more cars. The average age of the passenger vehicle parc was estimated at 9.2 years, 8.6 years for light commercial vehicles, and 7.6 years for heavy commercial vehicles.
  France is the tenth largest automotive manufacturing country in the world, and the second in Europe after Germany. The French automotive industry saw a period of increased output before 2018 when production flatlined. French OEMs include the PSA Group (now part of Stellantis), and the Renault Group.
  Sales of new vehicles fell by 27% in 2020.
  The French government is also dedicating a EUR 8 billion aid package to the automotive industry, which includes incentives for the purchase of new electric vehicles (EVs) and a scrappage program to remove heavily polluting vehicles from the vehicle parc. Drivers could get up to EUR 12,000 off the purchase price of a new EV. The scrappage programs aim to fund up to 200,000 new and used vehicle purchases.
  As a result of recent and strong government incentive measures, PHEVs and HEVs have recorded fast growth, particularly in the last two years. This trend seems to have accelerated in 2020. BEVs, PHEVs and HEVs accounted for 0.46%, 0.17%, and 1.39%, respectively, of the total passenger car population in 2019. By the end of 2020, BEVs are expected to reach 0.63% of the total passenger car population, while PHEVs and HEVs will account for 0.30% and 1.70%, respectively.
  Similar to other European countries and in an opposing tendency to the rest of the national market, the electric chargeable vehicle market increased by 36% in 2020.
Spain and Portugal have a combined passenger vehicle parc of 30 million vehicles. Sales of new passenger vehicles fell by 40% in 2020.

## Slide 285: Finished Lubricant Market Western Europe
Chart: OVERALL LUBRICANT DEMAND BY SEGMENT IN WESTERN EUROPE, 2020
| Industrial | Consumer | Commercial
Sales | 0.568 | 0.23 | 0.202
Total: 3,107.6 Kilotonnes
Chart: OVERALL LUBRICANT DEMAND BY PRODUCT TYPE IN WESTERN EUROPE, 2020 AND 2021
| PCMO | HDMO | Process Oils | Hydraulic fluids | Metalworking fluids | Industrial engine oils | All Other
2020 | 566.3 | 467.8 | 434.9 | 425.3 | 351 | 284.9 | 577.4
2021 | 596.6 | 482.4 | 467.2 | 450.5 | 372.7 | 301.1 | 611.1
KT
In 2020, total finished-lubricants demand in Western Europe amounted to 3,107.6 kilotonnes, down 14.1% over 2019. The large-scale decline in lubricant consumption is primarily due to the impact of COVID-19 and to the social distancing measures governments in the region to restrict movement and contain the spread of the disease.
Lubricant consumption in all market segments was negatively affected. Demand from the industrial and consumer segments both fell by 16%, because of factory and workshops closures and due to lowered demand for passenger automotive lubricants, since individual mobility was restricted. Demand from the commercial segment fell by only 7%, due to continued demand for goods fueled by a boom in e-commerce.
The finished lubricants market in Western Europe is characterized by a high synthetic penetration, particularly in the automotive segments, with lubricant formulations often based on Group II and Group III. It is also a relatively mature market, with low or declining growth rates.
Germany is the largest market, accounting for 24% of total finished lubricant in the region, followed by the United Kingdom with 19%, France and Italy with 16% each.

## Slide 286: Finished Lubricant Market Germany
Chart: OVERALL LUBRICANT DEMAND BY SEGMENT IN GERMANY, 2020
| Industrial | Commercial | Consumer
Sales | 0.597 | 0.238 | 0.165
Total: 748.3 Kilotonnes
Chart: OVERALL LUBRICANT DEMAND BY PRODUCT TYPE IN GERMANY, 2020 AND 2021
| Process Oils | PCMO | Metalworking fluids | HDMO | Hydraulic fluids | Industrial engine oils | All Other
2020 | 153.3 | 120.7 | 90.5 | 82.2 | 82 | 53.6 | 166
2021 | 169.2 | 126.5 | 94.9 | 84.2 | 86.2 | 58.3 | 178.1
KT
In 2020, Germany’s total finished-lubricants demand amounted to 748.3 kilotonnes, down 20% over 2019. The sudden, large-scale decline in lubricant consumption is an anomaly directly linked to the COVID-19 pandemic and the extraordinary prevention measures undertaken by the German federal government to combat the spread of the disease.
Lubricant consumption in all market segments was negatively affected. Demand from the industrial and consumer segments fell the most, by 22% and 21%, respectively, because of the restrictions on personal mobility and the forced factory closures.
In the consumer segment, trade channels operating in the passenger-vehicle lubricant sector experienced significant drops during the most stringent phase of lockdown. Kline estimates the sector operated only on 68% of its normal capacity. The consumer segment is characterized by a large passenger vehicle parc, a high synthetic lubricant penetration, and a preference for extended oil drain intervals (ODIs).
Continued…

## Slide 287: Finished Lubricant Market Germany
Germany has a large industrial base; industrial exports had seen strengthening demand up until 2020. Germany’s automotive industry is a major GDP contributor. Automotive production, however, was shut down for around five weeks during 2020. At the end of April 2020, automobile manufacturers gradually restarted operations, albeit at reduced volumes. The demand for vehicles during the COVID-19 lockdown was minimal and it is not expected to grow rapidly after the end of the outbreak. This could result in substantial reductions in demand for metalworking fluids, hydraulic fluids, industrial engine oils, and other lubricants.
    The metalworking industry was most affected by the lockdown, witnessing a (50%) decline during the period from April to June because of the lockdown of automotive OEMs in Europe. The automotive segment accounts for over half of national demand for metalworking fluids.
    All major OEMs in Germany including VW, Mercedes-Benz, and Porsche closed their assembly plants and engine manufacturing plants at the height of the pandemic.
  Machinery production has been falling at the same level as transportation equipment manufacturing. The German machinery manufacturing industry was already facing challenges since mid-2019, due to the deterioration in the global trade environment.
  Related sectors in the overall automotive supply chain were also affected by the downturn. Several companies supplying fabricated metal goods and primary metals, tire manufacturers, and machinery producers decided to reduce or suspend activities, opting for the temporary closure of facilities.
  The food-processing and pharmaceuticals industries worked at full capacity throughout the lockdown.
Commercial automotive lubricants was the least affected segment, with demand falling by 12% and was the first segment to recover, partially due to a boost in demand for goods through e-commerce.
  Heavy-duty and medium-duty fleets were operating at 60% above normal utilization rates, driven by the demand for food and other essential products as well as a surge in e-commerce sales.
  Distribution and urban logistics were working at close to full capacity. Private fleets and taxi fleets had much lower utilization rates.
  Inland shipping for industrial activity was stalled. Fuel and petrochemical industries were still operative.
  In the off-highway segment, demand from agriculture fleets and the public sector remained unchanged.
  Some public construction continued during the lockdown, as it was thought to present little risk for the spread of infection. Most private construction projects, however, were stopped or delayed.
  All mining activities in Germany were partly shut down.
The pandemic has not altered the balance of strength between the three segments, with industrial oils and fluids accounting for 60% of overall lubricant demand in Germany, the consumer segment accounting for 24%, and the commercial segment for 16%.

## Slide 288: Finished Lubricant United Kingdom
Chart: OVERALL LUBRICANT DEMAND BY SEGMENT IN UNITED KINGDOM, 2020
| Industrial | Commercial | Consumer
Sales | 0.581 | 0.229 | 0.19
Total: 593.2 Kilotonnes
Chart: OVERALL LUBRICANT DEMAND BY PRODUCT TYPE IN UNITED KINGDOM, 2020 AND 2021
| HDMO | Industrial engine oils | PCMO | Process Oils | Hydraulic fluids | All other-a
2020 | 106.5 | 101.8 | 95.4 | 84.6 | 79.1 | 125.8
2021 | 109.1625 | 106.4828 | 99.5976 | 88.407 | 82.5804 | 130.4546
KT
In 2020, total finished-lubricants demand in the United Kingdom amounted to 593.2 kilotonnes, down 14% over 2019. The United Kingdom also enforced several periods of lockdown during the pandemic: Non-essential retail businesses, excluding food and fuel stations, were closed, reducing the demand for transportation of goods. This affected negatively the economy which was already struggling to grow due to the global deterioration in the trade environment and policy uncertainty over the country’s exit from the EU. The market for finished lubricants in the United Kingdom is mature, growing at a slow pace.
  Demand for finished lubricants grew at a CAGR of less than 1% between 2012 and 2019.
The industrial lubricant segment in the United Kingdom is the largest segment in the lubricant market, accounting for about 60% of the total finished-lubricant market. Despite the trend toward de-industrialization which the country has experienced since the 1980s, The United Kingdom still retains of the world’s most technologically advanced manufacturing sectors, with particularly important civil and military aerospace and pharmaceutical industries.
  The industrial manufacturing sector accounted for a fifth of GDP. Some of the main manufacturing sectors include machine tools, transportation equipment, and chemicals.
Continued…

## Slide 289: Finished Lubricant United Kingdom
Demand for industrial lubricants experienced the largest decline, 16.6% in 2020 over 2019, due to the temporary shutdown of manufacturing sites in transportation-equipment manufacturing and related industries.
  Automotive manufacturing was one of the industries most severely affected by COVID-19. According to SMMT (The Society of Motor Manufacturers and Traders), United Kingdom’s passenger vehicle production fell by an approximate (20%) in the course of 2020 compared to 2019: even sharper falls were registered in the aviation and shipbuilding industries.
  This substantially affected supply chain segments, such as primary-metal products and fabricated metal products. Although these segments did not cease production during the lockdown, substantial contractions are still expected, because of the decrease in production in the transportation equipment manufacturing sector.
Demand for consumer vehicle lubricants fell by approximately 13.9%, with demand for routine oil changes decreasing due to reduced passenger vehicle travel in the lockdown period.
  Most lubricants for passenger vehicles in the United Kingdom are sold through the installed channel —essentially workshops, either franchised (FWS) or independent (IWS), which perform oil changes on behalf of their clients.
  Workshops were allowed to remain open but key annual maintenance operations were postponed and workshops concentrated on critical mechanical and safety repairs.
  Demand for consumer automotive lubricants is expected to rise by 3.5% in the next five years. In the longer term, lengthening ODIs and the impact of increasing EV sales are expected to negatively affect lubricant demand in the segment, and particularly on PCMO demand.
  Penetration of synthetics is higher in the consumer-automotive-lubricants segment, followed by penetration in the commercial-automotive-lubricants segment.
Commercial lubricant demand fell by 8.2%, with the off-highway segment experiencing the most decline, as construction and extractive industries had limits imposed on their activities.
  The construction sector was not restricted. It could continue business as usual, as long as social-distancing guidelines were maintained on construction sites. However, many construction sites decided to halt projects during the lockdown. An estimated 80% construction projects were put on hold during that period.
  The commercial automotive lubricant segment has been the least affected by the COVID-19 pandemic in terms of volumetric demand, and therefore it is forecast to have the slowest CAGR compared to the other categories. Demand from the commercial segment is expected to grow by 1.7% in the next five years, and then growth is expected to slow from 2025 to 2030.
The trend toward EV manufacturing in the automotive manufacturing is set to negatively affect demand for conventional industrial lubricants, such as hydraulic fluid, gear oil, and grease.
  Metalworking fluid demand will decline due to the electrification of passenger vehicles, as they require less lubrication during production.
  Demand for synthetic industrial lubricants is expected to gradually rise in certain applications, resulting in longer ODIs and a decrease in industrial lubricant demand over time.
  Demand for industrial oils and fluids is expected to grow by 3.4% between 2020 and 2025 but growth is expected to slow to 0.3% between 2025 and 2030.

## Slide 290: Finished Lubricant Market France
Chart: OVERALL LUBRICANT DEMAND BY SEGMENT IN FRANCE, 2020
| Industrial | Commercial | Consumer
Sales | 0.513 | 0.266 | 0.221
Total: 498.3 Kilotonnes
Chart: OVERALL LUBRICANT DEMAND BY PRODUCT TYPE IN FRANCE, 2020 AND 2021
| PCMO | Process Oils | Hydraulic fluids | HDMO | Metalworking fluids | Industrial engine oils | All other-a
2020 | 110.8 | 77.9 | 77 | 68.5 | 50 | 23.5 | 90.6
2021 | 115.232 | 80.3928 | 80.696 | 69.3905 | 51.45 | 23.9935 | 93.6804
KT
In the French lubricants market, industrial fluids were the largest segment accounting for 51.3% of the total lubricants market, followed by consumer at 26.6% and commercial automotive at 22.1%.
The finished lubricants market volume in France in 2020 was estimated at 498.3 kilotonnes, registering a 16% fall since 2019.
  This sharp decline observed in 2020 is due to the COVID-19 pandemic.
  Vehicle maintenance and repair workshops were allowed to operate during the lockdown period. However, many of them decided to close for several reasons, like limiting the spread of COVID-19, scarcity of customers or supply issues.
  All of this led to a loss in the number of passenger cars serviced during 2020, and consequently, in consumer lubricant demand in France, which fell by 18%.
  Demand volume decreased for the last six years due to the switch from conventional PCMO to synthetic and semi-synthetic PCMO oil with gradual extension of drain intervals due to longer lifespan of products, and the growing use of electrical and hybrid passenger vehicles.
Continued…

## Slide 291: Finished Lubricant Market France
The French economy has been in recovery mode since 2016. However, the lubricant market did not show growth, but a constant slow decline in volume. The market is affected by stringent regulations related to pollution and air quality which in turn is changing consumer and industrial practices and accelerating a switch from conventional to semi-synthetic and synthetic lubricants. The decline was strengthened by the advent of the COVID-19 pandemic.
The automotive manufacturing industry was disrupted by COVID-19. Some of the large original equipment manufacturers (OEMs) in France, such as Alstom and Bombardier, temporarily stopped production; Chantiers de l'Atlantique temporarily closed some of its workshops; and Airbus stopped production for few days. The National Institutes of Statistics and Economic Studies of France (Insee) estimated an overall loss of activity of 50% for industries other than food processing. Demand for industrial lubricants fell by 10% in 2020 compared with 2019, while in the previous four years, demand had been falling by 1.3% due to the introduction of synthetic industrial lubricants which enable a longer oil drain interval and to the adoption of technical processes such as minimum quantity lubrication or dry machining which requiring fewer amounts of lubricants.
The plants of several key automotive OEMs in France remained closed for a period of four to nine weeks during April and May.
    Toyota’s site in Valenciennes reopened in April after five-week shutdown.
    PSA’s plants in Mulhouse, Poissy, Rennes, Sevelnord, and Sochaux remained closed for different periods between March and May. This constitutes a potential vehicle-production volume loss estimated at about 146,000 units
Demand for commercial automotive lubricants has been decreasing over the last eight years, and it is forecast to continue decreasing in volume for the next 10 years at an annual rate of 0.4%. The switch from conventional to synthetic and semi-synthetic lubricants in commercial automotive is influenced by the Euro 6 standards.
    Within industries consuming commercial-vehicle-lubricants, agriculture and related food processing activities operated at nearly full capacity in order to secure the supply of first-priority items, such as food, during the lockdown.
    The use of light and medium commercial vehicles varied depending on the segment. Medical supplies, groceries, and other first-priority goods were in demand at higher levels than usual.
Demand for consumer automotive lubricants has been decreasing since 2011, and despite an improvement of the domestic economy, the segment is forecast to continue decreasing in the next 10 years, at an annual rate of 1.0%.
    Independent and franchised are the leading trade channels for passenger vehicle lubricant sales in France. Considered to be essential activities, these channels were fully operational during the lockdown. Although workshops remained open, the level of service was low and was limited to addressing critical issues with a car if the car had to be used for the professional reasons.
    According to the National Committee of Automobile Professionals, diesel, fuel, and gasoline consumption was 70% to 85% below the usual level because of restrictions on movement, which affected the consumption not only of fuel, but also of other products sold in fuel stations, including lubricants.

## Slide 292: Finished Lubricant Market Italy
Chart: OVERALL LUBRICANT DEMAND BY SEGMENT IN ITALY, 2020
| Industrial | Consumer | Commercial
Sales | 0.58 | 0.233 | 0.187
Total: 470.4 Kilotonnes
Chart: OVERALL LUBRICANT DEMAND BY PRODUCT TYPE IN ITALY, 2020 AND 2021
| PCMO | Hydraulic fluids | Process Oils | HDMO | Metalworking fluids | Industrial engine oils | All other-a
2020 | 85.3 | 73.6 | 73 | 70.5 | 54.6 | 35.7 | 77.7
2021 | 95.8772 | 83.3152 | 82.344 | 77.1975 | 61.4796 | 40.1982 | 87.1794
KT
The demand for finished lubricants in Italy in 2020 was estimated at 470.4 kilotonnes in 2020, registering a decrease of 12% compared with 2019.
Industrial oils and fluids is the largest segment by finished lubricant demand, accounting for 59% of total finished lubricant demand in Italy. Italy has a rich heritage of manufacturing industry and the economic importance of manufacturing is reflected in the large amounts of industrial oils and fluids consumed each year.
Consumer automotive lubricants is the second-largest segment, accounting for 24% of total finished lubricant demand. Italy has a large passenger vehicle parc, the second-largest in Europe, requiring large amounts of PCMO. In addition, being a vehicle manufacturing hub, lubricants are also used for factory fill. The segment includes motorcycle oil (MCO) used in two-wheelers, a popular vehicle type in Italy.
Continued…

## Slide 293: Finished Lubricant Market Italy
Commercial automotive lubricants is the smallest segment by finished lubricant consumption, accounting for 18.7% of the total. Italy has a large on-highway fleet, but there are relatively few off-highway vehicles used in mining, as Italy has a small mining and resource extraction sector. However, Italy has a large fleet of agricultural machinery which uses commercial automotive lubricants.
The fall in demand in 2020 was mostly due to the COVID-19 pandemic and the government measures that were imposed to curb its spread.
    Under the strict lockdown measures, valid from mid-March to early June, mobility was heavily curtailed, with residents often unable to leave the commune of residence. Personal vehicle utilization plummeted.
    Workshops in the installed segment were among the few businesses allowed to remain open. Most, however, chose to close, both for health and safety reasons and due to the unprecedented fall in demand. The ones that remained open chose to service only emergency vehicles or perform only emergency repairs, not including oil changes. Lubricant demand from the installed channel fell by over 75% during the first lockdown period.
    Mass merchandisers remained open, as did some auto parts stores. In the absence of oil changes provided by workshops, some motorists chose to perform oil changes themselves or purchased their own PCMO to refill oil levels as a temporary measure before workshops reopened.
    Demand for consumer lubricants during the lockdown period was estimated to be only 34% of the normal demand. The lockdown was lifted gradually, but mobility did not fully recover before the end of 2020. Several workshops and auto parts stores have gone out of business or reduced their service offer. However, many motorists returned to workshops to service their vehicles by the end of the year, and there was a sharp rise in demand in the second half of the year. In 202, demand fell by 12% in both the consumer and industrial segments, while it was stagnant in the industrial segment.
    The on-highway commercial segment was less affected than the consumer segment. Logistics fleets are critical for the supply chain and delivery of essential goods. On the one hand, demand from the segment increased as a result of the boom in e-commerce; on the other, there was a shortfall in industrial lubricant demand since many factories were shut during the lockdown period.
    Demand from the transportation channel also fell, as buses and coaches operated at a tenth of the normal capacity during the lockdown period. In the off-highway segment, there was a drastic fall in demand from the construction segment as all construction activity was put on hold. However, demand from agriculture was close to normal levels.
    Demand for commercial lubricants during the lockdown period was estimated to be only 70% of the normal.
    All factories providing non-essential goods were closed by law. In particular, automotive assembly plants, other transportation equipment manufacturing plants, and factories in the automotive supply chain closed down in the period. This had substantial implications for industrial lubricant demand as transportation equipment manufacturing alone contributes more than 30% of industrial lubricant consumption. Demand from steel mills and power plants also fell as a consequence of the automotive stop.
    Demand for industrial lubricants during the lockdown period was estimated to be only 36% of expected, with demand for only food grade lubricants and from the chemical industry holding up. The lag in demand is expected to be felt well beyond the end of the lockdown period as industrial production will struggle to recover in the face of depressed demand.

## Slide 294: Finished Lubricant Market Iberia (Spain and Portugal)
Chart: OVERALL LUBRICANT DEMAND BY SEGMENT IN SPAIN AND PORTUGAL, 2020
| Industrial | Commercial | Consumer
Sales | 0.523 | 0.268 | 0.208
Total: 375.2 Kilotonnes
Chart: OVERALL LUBRICANT DEMAND BY PRODUCT TYPE IN SPAIN AND PORTUGAL, 2020 AND 2021
| HDMO | Hydraulic fluids | PCMO | Industrial engine oils | Metalworking fluids | All other-a
2020 | 90.1 | 76.9 | 66.2 | 45.3 | 27.2 | 69.5
2021 | 92.0822 | 80.3605 | 69.7086 | 47.0667 | 28.3968 | 72.28
KT
Demand for finished lubricants in Spain and Portugal was registered at 375.2 Kilotonnes in 2020, a decrease of 11% over 2019.
  Demand for finished lubricants in Spain amounted to 330.5 kilotonnes, or 88% of the total for the Iberian peninsula.
  Demand in Portugal amounted to 44.7 kilotonnes, or 12% of the total.
Industrial oils and fluids comprise the leading segment in the market, accounting for 52.3% of the total. The commercial automotive segment accounts for 26.8% of the total market, followed by consumer automotive at 22%. The market has been witnessing a modest growth since 2014 when the economic recovery from the global financial crisis began in the region.
The strict measures introduced in order to control the spread of COVID-19 have been the primary cause of the significant contraction in lubricant demand in Spain and Portugal in 2020. The damage inflicted by the lockdown and social-distance measures caused the collapse of consumer spending in the first half of 2020. Real GDP contracted by approximately 20% in the second quarter of 2020 compared with the second quarter of 2019, according to IMF figures.
Continued…

## Slide 295: Finished Lubricant Market Iberia
The COVID-19 crisis has had a dramatic impact on the industrial sector. In March 2020, industrial production in Spain contracted by (11%) compared to February 2020.
Automotive manufacturing is one of the industries most affected by COVID-19 in Europe in general and in Spain in particular. The automotive industry generates around 10% of the Spanish GDP and employs about 650,000 people in the country. A large portion of Spain’s manufacturing activity is linked to the automotive industry, and vehicle-production plants were closed for several weeks. Consequently, demand for related products, such as metalworking fluids, hydraulic fluids, and industrial engine oils, registered the most significant decreases.
    All major OEMs in Spain, including Seat, PSA, Ford, VW, Mercedes-Benz, and Nissan were closed for a period in March and April.
    Nissan decided to shut down its plant in Barcelona.
Independent workshops and franchised workshops are leading channels for consumer automotive lubricant sales. They were considered essential services by both governments and hence could operate, but most of them operated at much lower rates. The lockdown resulted in a reduction of personal mobility. In Spain, franchised workshops posted a (95%) drop in operational activity during the lockdown period. Most franchised workshops were closed to the general public, and they would serve only vehicles that were transporting food, pharmaceuticals, and other essential goods. Independent workshops were affected by the lockdown as well.
Because of the lockdown, retailers had to shut down physical shops and promote online shopping. Online shopping and demand for transporting medical and essential supplies both increased throughout the lockdown. Therefore, lubricant demand from heavy-duty vehicle fleets and light- and medium-duty commercial fleets by logistics companies remained relatively strong.
    The collapse in economic activity was reported in March 2020, when retail sales declined by (15%) compared to February 2020.
The demand in the consumer automotive sector will decrease over the forecast period. The volume of lubricants for consumer automotive is expected to decrease in volume at an average rate of 0.8%. The consumer segment has seen the largest switch from conventional lubricants to synthetic lubricants, especially in the last five years. This is due to the increase of registrations of new passenger vehicles in the Spanish vehicle parc.
In the commercial automotive lubricant market, the demand for lubricants for commercial automotive consumers is expected to decrease at an annual average rate of 0.1% in the five-year forecast period. Euro VI emission standards drive consumption to a higher demand for synthetics and semi-synthetic lubricants. Despite efforts from OEMs, lubricant suppliers, and the government, the older vehicle parc is still a high consumer of conventional lubricants. Depending on targets adopted by the EU and the Spanish government, in a positive scenario, environmental policies will accelerate the switch from conventional lubricants to synthetics, increasing the value of the market but reducing its volume.

## Slide 296: Finished Lubricant Market Other Countries in Western Europe
Chart: OVERALL LUBRICANT DEMAND BY SEGMENT IN OTHER COUNTRIES IN WESTERN EUROPE, 2020
| Industrial | Consumer | Commercial
Sales | 0.587 | 0.247 | 0.165
Total: 422.2 Kilotonnes
Chart: OVERALL LUBRICANT DEMAND BY PRODUCT TYPE IN OTHER COUNTRIES IN WESTERN EUROPE, 2020 AND 2021
| Metalworking fluids | PCMO | HDMO | Hydraulic fluids | Process oils | Industrial engine oils | All other-a
2020 | 92.8 | 87.9 | 50 | 36.7 | 34.9 | 25 | 94.9
2021 | 98.9248 | 89.658 | 50.25 | 37.2872 | 35.249 | 24.975 | 98.5062
KT
Demand for finished lubricants in other countries in Western Europe amounted to 422.2 kilotonnes in 2020, registering a fall of 14% compared to 2019.
  Other countries in Western Europe include Belgium, the Netherlands, Switzerland, Norway, Sweden, Denmark, Finland, Iceland, and Luxembourg.
  The fall in demand in 2020 is largely due to the COVID-19 pandemic. Governments in these countries, similarly to other governments in the region, introduced curbs on mobility and on economic activity to facilitate the eradication of the pandemic from the region.
  Finished lubricant demand in the Netherlands amounted to approximately 30%, in Belgium for 20%, and in Switzerland for 10% of the total lubricant demand of other countries in western Europe.

## Slide 297: Lubricant Blenders
The market for finished lubricants in Europe has been primarily driven by the strict emission norms prevalent in the region and OEMs’ focus on fuel efficiency.
  In 2020, the region continued to have one of the highest penetration levels of high-performance, low-viscosity grades of lubricants in the world, particularly in the consumer market segment.
  The market for finished lubricants in Western Europe is mature and relatively fragmented, with several dozens of blenders holding small shares of the market.
  The leading blenders in Western Europe include Shell, which holds the largest market share (14%), followed by Total and ExxonMobil with approximately 11% each, BP with 10%, and Fuchs Petrolub SE with 5%.
  There are differences in lubricant blender market shares across country markets, with blenders with a local base typically holding leadership positions in their home markets.
  For example, Total is the leading supplier in France, holding a 31% share. Repsol, a Spanish blender, is the leading finished lubricant supplier in Spain, while ENI, the Italian national oil company, is the leading lubricant supplier in Italy.
Shell is the leading supplier in Germany and the United Kingdom and is the second leading supplier in France and Italy.
  The Anglo-Dutch major is strong across automotive and industrial segments.
  In the automotive segments, Shell benefits with partnerships with influential OEMs such as BMW, SDF, and Scania.
  The company devolves significant resources to research and development and is a leader in synthetic lubricant technology, developing gas-to-liquid basestocks.
  Shell is a leading supplier of compressor fluid, refrigeration oil, turbine and circulations oils, natural-gas-engine oil, fire-resistant hydraulic fluid, synthetic gear oil and lubricants used in marine applications.
TotalEnergies, formerly Total, has a strong position across all major European markets. The French major has commercial agreements with leading OEMs such as PSA Group, part of Stellantis, Renault-Nissan-Mitsubishi, KIA, and Mazda. Total is a leading supplier in diverse industries such as energy, chemicals, cement, food, paper, steel, textiles, metalworking, and automotive manufacturing.
BP is particularly strong in the United Kingdom and Germany.
  In the automotive segments, the British major has supply agreements with key OEMs, such as Volkswagen Group, Ford, Volvo, and Honda.
  BP is a leading supplier of consumer automotive lubricants thanks to its Castrol and Aral brands, which benefit from excellent brand reputations.
  In the commercial segment, BP is particularly strong in the light on-highway vehicle fleet. Castrol is more used in the on-highway segment while Aral is prevalent in agriculture and public transportation fleets.
  The company is also a leading supplier of metalworking fluids and synthetic industrial oils.
ExxonMobil is strong across all segments. The US major maintains a close cooperation in development and first-fill with Porsche and Daimler and is also a strong supplier in the automotive aftermarket. ExxonMobil is a significant supplier of most types of industrial lubricants and is also a major process oil and basestock producer.
Continued…

## Slide 298: Lubricant Blenders
Fuchs is a German-based independent lubricant supplier. In the automotive segment, the family-owned company is mostly active in the factory-fill business and has suffered since 2016 due to sluggish production figures. After acquiring Pentosin-Werke, the company has stepped up development of ATF and synthetic gear oil. In the industrial segment, Fuchs is a leading supplier of metalworking fluids and synthetic industrial fluids, holding one of the most comprehensive product portfolios in the industry.
There are several independent suppliers operating in Western Europe, typically with smaller market sizes and specialized in high-quality specialty market niches. Notable other companies include:
  Liqui Moly in Germany, producing synthetic PCMO.
  Blaser Swisslube in Switzerland, producing metalworking fluids
  Klueber lubrication in Germany, producing greases and specialty industrial fluids
  Hansen und Rosenthal (HuR) in Germany producing process oils
  Sonneborn (now part of HollyFrontier) in the Netherlands producing white oils
Over the last two decades, there has been a sizeable shift away from Group I basestocks toward Group II and Group III basestocks in the Western European market.
  No new API Group I formulations have been issued in five years.
  The logistics and storage cost benefits of using fewer basestocks has made Group II a preferred choice among blenders.
  Demand for Group I basestocks has been restricted to applications in which the need for high viscosity and solubility could not be met with other API groups.
  Group I basestocks are gradually exiting the automotive segment, especially in the engine oil category, for the consumer automotive segment.
  Lubricant blenders have shifted away from Group I basestocks to Group II basestocks in several industrial applications, such as hydraulic fluids and some gear oils.
  Solubility, aromatic content, and higher viscosity continued to be required in some industrial applications, such as metalworking fluids, rubber process oils, and marine oils.
  Lubricants used in EV are mostly all based on synthetic technology.
In the automotive segment, premium basestocks are now demanded by most European OEMs as API Group I formulations see no further approvals. Western European industrial demand is sophisticated, requiring a broad range of basestocks depending on functionality and technical requirements.
  Western European OEMs are very active on the market through their approvals, exerting pressure on the lubricants industry by require high-performance lubricant products with long oil drains and
  OEMs will only use lubricants that meet their approvals for factory fill and recommend only lubricants with approvals for service fill.
  Major OEMs in Western Europe include the Volkswagen Group (VW), Stellantis (created from the merger of PSA and FCA), Renault, BMW, and Daimler.
Group I API basestocks account for approximately 40% of regional basestock demand, Group III basestocks for 25%, Group II basestocks for 18%, and naphthenics for 9%, with all others accounting for the balance.

## Slide 299: Regulations
SUMMARY OF REGULATIONS | 
QUESTION | ANSWER
1. Do regulations exist specifically for used oil? | Yes. European Regulation 1013/2006 and EU Directive 2018/851 are the main legislative instruments at a European level specifically regulating used oil.
2. How is used oil classified i.e., hazardous waste, special waste etc.? | Hazardous
3. Are there any requirements on who can collect used oil? | Yes. They have to either apply for a license or become part of a public consortium.
4. Does country have an association(s) managing the collection and disposal of used oil? | In Italy, Portugal, Spain, and Denmark.
5. Is a levy charged on sales of lubricants to support used oil collection associations? | In Italy and Portugal.
6. Are there any requirements for how used oil generators manage used oil? | Yes. Used oil is classified as a hazardous waste and needs to be collected and stored separately.
7. Are there requirements for oil manufacturers, marketers or retailers to take back used oil? | Yes. There are requirements for all collectable used oil to be collected.
8. Do any requirements / legislation exist around different types of used oil? | Yes. There is a hierarchy of waste oil.
9. Does the country have requirements or regulations regarding the export or import of used oil? | Yes. Importers-exporters have to follow the requirements for the export and import of used oil.
10. Does the country have any legislation that requires used oil to be re-refined? | Yes. Re-refining is encouraged by EU legislation.
11. Does the country have legislation that requires lubricating oil to contain a percentage of re-refined basestock? | No.
12. Does the country allow used oil to be burned as a fuel (cement kilns, industrial boilers or furnaces, power plants, etc.)? | Yes.
Continued…

## Slide 300: Regulations
SUMMARY OF REGULATIONS |  | 
QUESTION |  | ANSWER
13. If used oil can be burned as a fuel, is the fuel burner subject to a different and more stringent set of air emissions requirements (relative to operating without burning used oil as a fuel) or must the fuel burner install additional pollution control equipment or energy recovery equipment before it can burn the used oil? |  | The fuel burner is subject to the same carbon emission requirements for burning used oil as for using fuel.
14. Is used oil allowed to be placed in a landfill? |  | No.
15. Does the country have legislation that gives incentives, financial subsidies or priority to any particular used oil disposition e.g., re-refining, fuel for burning, landfill etc. |  | Yes. For re-refining.
16. Please indicate whether used oil can be legally used (i.e., regulations do not prohibit) for the following purposes ( assuming that used oil is not being mixed first with a hazardous waste): | i. Burning in space heaters | Yes.
 | ii. Blending with crude oil at a refinery | Used oil can be blended with virgin basestock in a refinery.
 | iii. Dust suppressant | No.
17. Are there companies / associations advocating in used oil category? |  | Yes. GEIR is the main trade association for the re-refining industry at a European level advocating for the recycling of used oil.

## Slide 301: Regulations: Germany
Key Used Oil Regulations
The European Waste Oil Directive which governed waste oil disposal and recovery has been integrated into the amended European Waste Framework Directive, 2008/98/EC, amended by Directive (EU) 2018/851.
Directive 2018/851 was adopted by Germany’s legislation, making minor changes to the legislative language:
  Requiring waste oils to be collected separately, using good practices
  Prioritize waste oil treatment and regeneration over other recycling forms
  Waste oils with different characteristics are not to be mixed to improve the environmental outcome
  Examine data on waste oils provided by Member States to consider feasibility of adopting treatment measures and quantitative targets on waste oil regeneration. Commission shall submit report to the European Parliament.
The National Waste Oil Ordinance (WO) has been in force since 1987 and has been updated in 2002. The WO aims to regulate all aspects of A review process for the WO came to an end in October 2020.
Disposal, storage, and transportation have to comply with the German Federal Emission Control Act.
i. Generation
WO establishes that lubricant sales are tied to used oil generation and collection.
Separate storage and prohibition of mixing with other waste
ii. Classification (ABC)
Waste oil is classified as hazardous waste in four different categories.
Category One is dedicated to reprocessing and comprises waste oils from hydraulic, engine and gear lubricants
iii. Collection
Lubricant sales tied to a commitment to ensure collection.
Collectors need a standard waste collection permit. Mixing of waste oil categories is prohibited if it impedes reprocessing
iv. Transportation and Storage
Same rules as for collection
v. Disposal – Re-refining
Reprocessing has priority, but technical, organizational and economical constraints allow deviations
vi. Disposal – Fuel
Key points about regulations for used oil usage as fuel in short.
vii. Disposal – Other
Burning of untreated waste oil and distillation to heavy or medium fuels is allowed.
Waste oil that cannot be recycled may be reused as fuel or must be disposed of at dedicated special waste plants.
Regulatory Enforcement
i. Responsible Agencies
Federal Ministry of Environment
Federal Agency of Environment
ii. Enforcement Mechanisms
Local authorities efficiently monitor that waste oil is properly stored and handled
iii. Effectiveness of Regulations Enforcement
Priority of re-refining is only “written” in legislation. Deviations are possible. Private sector (OEMs) demands re-refining
Key Influencers
i. Public Sector
Federal Ministry of Environment
ii. Private Sector
BVA (waste oil organization, mainly re-refiners)
BVSE-Hazardous waste section in favor of keeping existing legislation (mainly collectors)
UNITI-independent lubricant association supports re-refining
Impact of Current Regulations
Low-Moderate
Separate collection supports waste oil quality. No mandatory re-refining.
Probable Future Regulations
Low: Depending on EU assessment
Continued…

## Slide 302: Regulations: Germany
Used Oil Regulations
Generation
The Waste Oil Directive stipulates that the sale of engine oil and gear oil is only permitted if a waste oil collection point exists at or in the immediate vicinity of the point of sale.
Packaged lubricants must be labelled, listing how and where waste oil is taken back for free from private users.
Commercial waste oil generators are subject to rules for storage, record keeping, electronic register, separate disposal and mixing prohibitions of different categories especially PCB containing oils. Several exemptions may apply.
Classification
In Germany, four collection categories of waste oil are defined in accordance with their suitability for reprocessing.
Category One includes mineral and synthetic (non-chlorinated) hydraulic, engine, gear and lubricating, mineral-based isolating and heat transmission oil. Category One is suitable for reprocessing.
Category Two comprises mineral-based machining oils free of halogens (except emulsions) synthetic machining and hydraulic oils.
Category Three comprises chlorinated oils and PCB containing oils up to 50ppm.
Category Four comprises biodegradable oils, synthetic insulation and heat transmission oils.
Disposal – Re-refining
Article 21 of the waste framework directive gives “priority to regeneration or alternatively to other recycling operations delivering an equivalent or better overall environmental outcome than regeneration”.
Article 2 Reprocessing Priority:
(1)“The reprocessing of waste oils shall be given priority over other disposal methods insofar as no technological and economical restraints including those of an organizational kind preclude this”.
Federal Agency speaks of a “relative” priority and sees the priority fulfilled if more than 50% of waste oil is reprocessed.
Re-refiners have to buy waste oil at a (free) market at market price. Thus, waste oil imports are necessary to utilize capacities
Waste oil re-refiners oppose this practice and are lobbying via their waste oil organization BVA for a strict priority or mandatory quota of waste oils to be re-refined.
Disposal – Fuel and Others
Direct burning as fuel is allowed, and cement kilns are the main outlet for waste oils deemed unsuitable for further processing.
Distillation of waste oil to heavy or medium fuel is allowed and finds an outlet in the bunker industry.
Collection
Collectors need a permit granted from the ministry for the environment and are obliged to take a sample of waste oil at the point of collection
According to the Waste Oil Directive, oils for machines, engines, turbines, and other equipment may only be sold to the end user if their packaging bears a stamp or label that states the oil is to be taken to a waste oil collection point after use.
If sellers of lubricating oils are unable to set up a collection point of their own for waste oil (for example department stores, hypermarkets, retail stores), they must enter into arrangements with third parties at their own expense in order to ensure there is a collection point in the vicinity.
Transportation and Storage
Same rules for collection apply for transportation.
Waste oils may only be reprocessed if they contain no contaminants or if any such contaminants are separated or destroyed by the reprocessing process. It is also prohibited to admix foreign substances such as solvents, brake fluids, and coolants to waste oils that could be reprocessed.
Federal Act of Emission Prevention Control regulates storage obligations to prevent emissions to air, water, soil and human health.
Different categories of waste oils, as defined under the Classification section, cannot be mixed together, but need to be stored separately.
Imports of used oil are strictly regulated. Re-refining companies are the only authorized importers.
Continued…

## Slide 303: Regulations: Germany
Regulatory Enforcement
Responsible Agencies
Federal Ministry of Environment (Bundesumweltministerium) sets the standards
Local authorities survey Generators, Collectors, Haulers, Regenerators , Fuel-Producers, Direct-Burners and Disposal Installations.
Enforcement Mechanisms
Local authorities are tasked with enforcement and oversight to make sure waste oil is properly handled, transported and stored..
Effectiveness of Regulations Enforcement
Low-Moderate
No effective enforcement of priority of regeneration as the law foresees, such that organizational, technical and economical constraints allow
Key Influencers
i. Public Sector
Bundesumweltministerium –Federal Ministry of Environment
Umweltbundesamt-Federal Agency of Environment
Bundesamt für Außenwirtschaft-
ii. Private Sector
BVA-waste oil association (mainly re-refiners, with Puraglobe and Avista as the key influencers)
BVSE-Hazardous waste section in favor of keeping existing legislation (mainly collectors)
UNITI -independent lubricant association supports re-refining
Probable Future Regulations
Low: Depending on EU assessment
The WO ordinance has been reviewed only in 2020. Further national changes to waste oil legislation are unlikely but are dependent on the EU assessment process.
Additional legislation based on Directive 2018/851 concerning waste management is pending, while the European Commission concludes it assessment process regarding setting recycling targets for waste oils.
A reporting template has been sent to all member states, who are tasked with assessing the lubricant consumption, collection, and utilization of waste oils by the end of 2021. The federal environment ministry is taking care of this process in Germany.
The assessment process will enable the European Commission to implement coordinated waste oil collection targets for all EU member states.
The process is expected to be complete by 2022.
On the basis of the assessment process, the European Commission will consider the feasibility of adopting treatment measures and quantitative targets on waste oil collection and re-refining. The Commission shall then submit report to the European Parliament for implementation into European law.

## Slide 304: Regulations: United Kingdom
Key Used Oil Regulations
EU Legislation
European legislation, such as the European Regulation 1013/2006, the waste framework directive 2018/85, and the waste (Circular Economy) (Amendment) Regulations of 2020, and the EU’s Industrial Emissions Directive (2010/75/EU). continue to apply to British law after the withdrawal of the United Kingdom until the end of the transition period. United Kingdom legislation originating in the EU before Brexit has been temporarily converted into British legislation.
English and Welsh law was updated on 1 October 2020 to include changes to the Waste Framework Directive (WFD) made in 2018. This was done through the Waste (Circular Economy) (Amendment) Regulations 2020.
Article 21 of the Waste Framework Directive is particularly relevant toward used oil generation:
  1. Without prejudice to the obligations related to the management of hazardous waste laid down in Articles 18 and 19, Member States shall take the necessary measures to ensure that:
    (a) waste oils are collected separately, where this is technically feasible;
    (b) waste oils are treated in accordance with Articles 4 and 13;
Article 4 of directive 2008 establishes a waste hierarchy as a priority order in waste prevention and management legislation and policy. The waste hierarchy goes from most desirable approach to less desirable approach, with disposal being the least desirable, and prevention the most desirable:
Prevention:
  Re-use
  Recycling
  Other recovery, e.g., energy recovery
  Disposal
Article 13 establishes the principles of taking all the necessary measures to ensure that waste management is carried out without endangering human health, without harming the environment and, in particular:
  (a) without risk to water, air, soil, plants or animals;
  (b) without causing a nuisance through noise or odors; and
  (c) without adversely affecting the countryside or places of special interest.
  (d) where this is technically feasible and economically viable, waste oils of different characteristics are not mixed and waste oils are not mixed with other kinds of waste or substances, if such mixing impedes their treatment.
  2. For the purposes of separate collection of waste oils and their proper treatment, Member States may, according to their national conditions, apply additional measures such as technical requirements, producer responsibility, economic instruments or voluntary agreements.
  3. If waste oils, according to national legislation, are subject to requirements of regeneration, Member States may prescribe that such waste oils shall be regenerated if technically feasible and, where Articles 11 or 12 of Regulation (EC) No 1013/2006 apply, restrict the transboundary shipment of waste oils from their territory to incineration or co-incineration facilities in order to give priority to the regeneration of waste oils.
National Legislation
The Control of Pollution (Oil Storage) regulations 2001 regulating storing waste oils.
The Environmental Waste (England and Wales) Regulations 2011 for regulating collection and trading of waste oil
the Environmental Permitting Regulations of 2010 regulate collection and disposal, including re-refining
The Waste Incineration Directive (WID) enforced in December 2005 regulates the fuel application of used oil in the United Kingdom
Impact of Current Regulations
Low-Moderate. There is no mandatory re-refining of waste oils.
Continued…

## Slide 305: Regulations: United Kingdom
Key Used Oil Regulations (continued)
i. Generation
Separate storage and prohibition of mixing with other waste
ii. Classification
Waste oil is classified as hazardous waste in the United Kingdom. It is illegal to mix hazardous with non-hazardous waste.
iii. Collection
Collecting companies must be registered as being certified by the Environment Agency to collect used oil
iv. Transportation and Storage
Companies disposing of waste must complete a waste transfer note and the transporting company must be registered to be able to transfer hazardous waste. Specific Oil Storage regulations must be followed.
v. Disposal – Re-refining
Re-refining must be carried out in line with guidelines for handling hazardous waste and the oil storage regulations.
vi. Disposal – Fuel
Installations must hold a permit and control for pollution. The Waste & Resources Action Programme has developed a program for guaranteeing quality.
Regulatory Enforcement
i. Responsible Agencies
Environment Agency
Department for the Environment, Forestry, and Agriculture
ii. Enforcement Mechanisms
Local authorities or ministerial inspections
iii. Effectiveness of Regulations Enforcement
Enforcement is not very effective. Given the low capacity for re-refining in the country, re-refining is given a low priority.
Key Influencers
i. Public Sector
Department for the Environment, Forestry, and Agriculture
ii. Private Sector
UKLA (United Kingdom Lubricant Association)
ORA (Original Recycling Association)
Impact of Current Regulations
Low-Moderate: There is no mandatory re-refining of waste oils.
Probable Future Regulations
Low: Depending on EU assessment
There is an expectation that the British government will implement new legislation to supplement expiring EU legislation but given the small size of the United Kingdom’s re-refining industry, this is treated as a low priority.
Used Oil Regulations
Generation
Waste oil must be separated and stored in line with the Control of Pollution (Oil Storage) Regulations 2001 and the European waste framework directive.
Waste oil must be treated separately according to the waste hierarchy enshrined in the waste framework directive and to the hazardous substance classification.
The waste framework directive bans landfill disposal of waste oil.
Waste oil must be stored in accordance with the rules discussed under the transportation and storage heading.
Classification
Waste oil is classified as a hazardous substance by the waste framework directive and by the technical guidance WM3: waste classification issued by the Environment Agency.
Collection
Directive 2008/98/EC, which requires waste oil to be recovered and recycled whenever possible, has been transposed into EU law. Companies collecting oil must comply with the 2013 Environmental Permitting Regulations and 2007 pollution prevention and Control Regulations 2007, as well as Waste Management Licensing and exemptions schemes.
The Environment Agency also issues registration certification under The Waste (England and Wales) Regulations 2011 whereby it licenses companies to collect and trade used lubrication oil.
This license is typically valid for three years.
Continued…

## Slide 306: Regulations: United Kingdom
The WID enforces the prevention and control of pollution. Under this directive, each installation should operate only if it holds a permit.
The permit should include all the measures necessary to achieve a high level of protection of the environment as a whole and to ensure that the installation is operated in accordance with the general principles governing the basic obligations of the operator. The permit should also include emission limit values for polluting substances, or equivalent parameters or technical measures, appropriate requirements to protect the soil and groundwater.
Article 4.1 of the WID was added for small oil burners with respect to any mineral and synthetic lubricating oils. These plants require an environmental permit issued by the local authority
Disposal – Fuel and Other
Companies intending to use used oil as fuel must also abide by the WID.
the Waste & Resources Action Programme, along with the Environment Agency, has developed the quality protocol for processed fuel oil (PFO) produced from used oil.
The Quality Protocol lays out the criteria for and standards for methods and materials used as well as finished product quality. PFO producers are also required to maintain records of waste produced.
PFO users who meet the quality protocol do not need to follow WID requirements.
Impact of Current Regulations
There are no collection fees or consortia governing used oil collection and re-generation as in other countries. Collection is mostly voluntary.
The United Kingdom’s re-refined basestock industry is rather small, and there are no specific regulations mandating collection and re-generation. Most used oil is disposed as fuel due to the lack of re-refining basestock capacity and the absence of substantial fiscal incentives in the country to aid the re-refined basestock industry.
Probable Future Regulations
Companies in the United Kingdom are looking at the process of review of the 2018 Waste Framework Directive, and in particular the requirement to measure collection and regeneration rates.
Further changes in EU legislation would have to be separately incorporated into British law, and it is as of now, unclear whether there is an appetite for this.
Key Influencers
i. Public Sector
Department for Environment, Food and Rural Affairs (DEFRA)
Department for Business, Energy and Industrial Strategy (BEIS)
ii. Private Sector
UKLA (United Kingdom Lubricants Association)
ORA (Original Recycling Association)
GEIR (European Re-refining Association)
Transportation and Storage
Companies must comply with the Control of Pollution (Oil Storage) Regulations 2001, when storing and transporting oil products, including waste oil.
The United Kingdom government adopted stricter regulations on oil storage following the high level of water pollution due to leakage of oil and oil-derived products from unbounded tanks and inadequate storage.
The regulation requires that the container must be strong enough not to burst or leak in ordinary use.
Fixed tanks that meet the design standard are any made to British Standard 5410 or a similar acceptable standard, or drums marked with UN for United Nations. The regulation gives other recommendations on container positioning and pipe attachments.
The United Kingdom government is also required to prevent pollution of water with List I substance presented under the EC Directives on Dangerous Substances (76/464/EEC).
Disposal – Re-Refining
Companies must follow the waste management framework WM3 and oil storage regulations, 2001, as well as existing European legislation for re-refining.

## Slide 307: Regulations: France
Key Used Oil Regulations
The EU’s waste framework directive applies in France as well and requires used oil to be collected, separated, treated, and, whenever technically feasible, regenerated, with priority given to regeneration as baseoils.
International transportation and import and export of used oil are regulated by Articles 11 or 12 of Regulation (EC) No 1013/2006, restricting the transboundary shipment of waste oils from their territory to incineration or co-incineration facilities in order to give priority to the regeneration of waste oils.
Disposal, transportation, and treatment of waste oils is regulated by articles R and L., 541-2, 541-3, and 541-8 of the Environmental Code.
The 2007 Finance Act imposed a regeneration levy of EUR 0.04 per kg on the sales of finished lubricants, used to finance the collection and management of used oils.
Directive 2010/75/EU on industrial emissions (Industrial Emissions Directive) regulates the operation of refineries, including re-refineries.
i. Generation
Used oil is expected to be generated wherever possible. Any producer of original waste must either manage it or use a third party to treat it. Waste producers are responsible for their waste until it is disposed of or recovered.
ii. Classification
Waste oil is classified as hazardous waste by the environmental code. It is illegal to mix hazardous with non-hazardous waste.
iii. Collection
Collecting companies must obtain a permit from the relevant agency to collect waste oil.
Collection is partially financed by the General Tax on Polluting Activity (TGAP)
iv. Transportation and Storage
Used oil must be transported and stored separately in line with the safety guidance outlined in the Energy Code and Environmental Code.
v. Disposal – Re-refining
Used oil must be treated in a safe way that enables to protect the environment, safety and public health, guidelines in the Environmental Code. Local authorities can impose additional requirements.
vi. Disposal – Fuel
Installations must hold a permit and control for pollution, conforming with the Environmental Code and Energy Code.
vii. Disposal – Other
Untreated waste oil must be treated according to the waste framework directive and the waste (Circular Economy) (Amendment) Regulations 2020 of 2020
Regulatory Enforcement
i. Responsible Agencies
Ministry of Ecology, Sustainable Development and Energy
Agency for the Environment and Energy Management (ADEME)
ii. Enforcement Mechanisms
If waste oil is abandoned, companies can suffer a range of penalties from finding a remedy to the imposition of a fine
iii. Effectiveness of Regulations Enforcement
Enforcement is relatively effective. There are sanctions tied to non-compliance and dispute settlement mechanisms.
Key Influencers
i. Public Sector
Ministry for the Economy and Finance
Local Authorities ((Préfet)
ii. Private Sector
Union Française des Industries Petrolières (UFIP)
National Trade Union Chamber of the Lubricants Industry (CSNIL)
Probable Future Regulations
High: New Law to be introduced
The anti-waste law for a circular economy, implementing the EU circular economy directive, is expected to be implemented soon, and is expected to make used oil re-refining to produce basestocks mandatory whenever feasible.
Continued…

## Slide 308: Regulations: France
Used Oil Regulations
Generation
The EU’s Waste Framework directive requires used oil to be collected, separated, and, whenever technically feasible, treated and generated. The 2007 Finance Act finances regeneration through a levy on every finished lubricant sale.
Classification
Waste oil is classified as hazardous waste by the environmental code. It is illegal to mix hazardous with non-hazardous waste.
Collection
The Environmental Code prescribes the obligations that collection companies must follow and gives ADEME the power to oversee their organization.
Transportation and Storage
Companies must comply with articles R and L., 541-2, 541-3, and 541-8 of the Environmental Code, which stipulates that transportation and storage of oil must be conducted in a way that protects the environment, safety, and public health.
Disposal – Re-refining
Used oils must be treated according to articles R543‐3 to 16 of the Environmental Code. Re-refiners need to operate in compliance with Directive 2010/75/EU on industrial emissions (Industrial Emissions Directive), which regulates the operation of refineries.
Due to their potentially harmful effects, refineries are considered to be installations classified for the protection of the environment under the Industrial Emissions Directive.
Under the directive, an emission limit value (EVT)is calculated on ad hoc basis that is prescribed for a site that a refinery should not exceed in the course of its operation.
Re-refineries are required to undergo an environmental impact assessment that must be satisfactory for the re-refiner to receive continued permission from the ministry to operate. The environmental impact assessment is carried out by an authorized consulting firm.
If the re-refinery is found to have exceeded its EVT or failed its environmental impact assessment, the re-refinery’s permit to operate can be revoked from the ministry. Local authorities participate in monitoring the operation of re-refineries.
Disposal – Fuel
Used Oil processors must follow the same regulatory processes as re-refiners. Installations hold a permit and control for pollution, conforming with the Environmental Code and Energy Code.
Disposal – Other
Untreated waste oil must be treated according to the waste framework directive and the waste (Circular Economy) (Amendment) Regulations 2020 of 2020
Regulatory Enforcement
Responsible Agencies
Ministry OF Ecology, Sustainable Development and Energy
Agency for the Environment and Energy Management (ADEME)
Enforcement Mechanisms
If waste oil is abandoned, companies can suffer a range of penalties from finding a remedy to the imposition of a fine
Effectiveness of Regulations Enforcement
Enforcement is relatively effective. There are sanctions tied to non-compliance and dispute settlement mechanisms.
Key Influencers
i. Public Sector
Ministry for the Economy and Finance
Local Authorities ((Préfet)
ii. Private Sector
Union Française des Industries Petrolières (UFIP)
National Trade Union Chamber of the Lubricants Industry (CSNIL)
GEIR (European Re-refining Association)
Impact of Current Regulations
Moderate to high. Untreated waste disposal is forbidden, and regeneration is strongly encouraged.
Probable Future Regulations
The anti-waste law for a circular economy, implementing the EU circular economy directive, is expected to be implemented soon, and is expected to make oil regenerating mandatory.

## Slide 309: Regulations: Italy
Key Used Oil Regulations
The EU’s waste framework directive applies in Italy as well and requires used oil to be collected, separated, treated, and, whenever technically feasible, recycled, with priority given to re-refining to produce basestocks
International transportation and import and export of used oil are regulated by Articles 11 or 12 of Regulation (EC) No 1013/2006, restricting the transboundary shipment of waste oils from their territory to incineration or co-incineration facilities in order to give priority to the regeneration of waste oils.
Legislative Decree No. 152/April 3, 2006 and Legislative Decree No. 95/27 January, 1992 are the main regulations at the national level regulating used oil in Italy.
The Italian government levies a tax on the consumption of finished lubricants (EUR 787.8 per KT in 2019). The excise duty is applicable in its entirety to lubricants with over 70% of mineral oil content, while it is applied proportionally according to its mineral content below the 70% figure.
Lubricant purchasing agreements are also required to include a mandatory contribution to the Italian used oil consortium toward recycling the oil, a fee quantified at 0.12 EUR per Kg in 2020.
In 2017, a decree was passed establishing a consortium for the collection, disposal, and regeneration of used oil (CONOU).
Since 2016, under the EU’s Green Public Procurement (GPP) policies, public sector bodies must ensure that only re-refined or biodegradable oils are used for public sector work.
i. Generation
Used oil is expected to be generated wherever possible. Any producer of original waste must either manage it or use a third party to treat it. Waste producers are responsible for their waste until it is disposed of or recovered
ii. Classification
Waste oil is classified as hazardous waste in Italy. It is illegal to mix hazardous with non-hazardous waste.
iii. Collection
Used oil is collected and managed by a consortium which has representation from the various manufacturers of lubricants, used oil collectors, and re-refiners
iv. Transportation and Storage
The same consortium is responsible for transportation and storage.
Disposal – Re-refining
Used oil must be treated in a safe way that enables to protect the environment, safety and public health, guidelines in the Environmental Code. Local authorities can impose additional requirements
vi. Disposal – Fuel
Installations which use used oil as fuel have to be authorized by the ministry for the environment.
vii. Disposal – Other
Untreated waste oil must be treated according to the waste framework directive and the waste (Circular Economy) (Amendment) Regulations 2020 of 2020
Regulatory Enforcement
i. Responsible Agencies
Ministry OF the environment
National Consortium for the management, collection, and treatment of used oil (CONOU)
ii. Enforcement Mechanisms
If waste oil is abandoned, companies can suffer a range of penalties from finding a remedy to the imposition of a fine
iii. Effectiveness of Regulations Enforcement
Enforcement is relatively effective. There are sanctions tied to non-compliance and dispute settlement mechanisms.
Key Influencers
i. Public Sector
Ministry for Economic Development
Ministry of the Environment
ii. Private Sector
Unione Petrolifera (UP)
Italian Lubricant Industry Association (GAIL)
Impact of Current Regulations
Moderate to high. Untreated waste disposal is forbidden, and regeneration is strongly encouraged.
Probable Future Regulations
High: New Law to be introduced
The anti-waste law for a circular economy, implementing the EU circular economy directive, is expected to be implemented soon, and is expected to make oil regenerating mandatory.

## Slide 310: Regulations: Iberia 1
Key Used Oil Regulations
The EU’s waste framework directive applies in Spain and Portugal as well and requires used oil to be collected, separated, treated, and, whenever technically feasible, regenerated, with priority given to re-refining to produce basestocks.
International transportation and import and export of used oil are regulated by Articles 11 or 12 of Regulation (EC) No 1013/2006, restricting the transboundary shipment of waste oils from their territory to incineration or co-incineration facilities in order to give priority to the regeneration of waste oils.
Royal Decree 679/2006 set up the regulatory framework governing used oil collection and regeneration in Spain and establishing the non-profit entities to oversee the used oil collection business.
The same royal decree established a levy of EUR 0.06 per kg on the marketed lubricant which finances the system.
In Portugal, Decree No. 153/2003 governs the management of used oils, taking into account production, regeneration, and re-refining.
There is only association approved in Portugal dealing with the collection and management of used oils (SOGILUB). It is financed by a levy of EUR 63.00 per cubic meter of lubricant sales.
i. Generation
In Spain, there is a system established by law through a non-profit entity which guarantees that used oil is collected at the generation point. In Portugal, an industry consortium is also tasked with overseeing oil generation and collection.
ii. Classification
Waste oil is classified as hazardous waste in both Spain and Portugal and must be handled and treated according to the relevant laws governing waste product treatments.
iii. Collection
In Portugal, the consortium is directly responsible for collection, storage, and quality control of used oil re-refining. In Spain, the collection stage is more autonomous from government entities. Collectors operate independently in an open market where used oils are bought and sold freely, although collectors have to be authorized by SIGAUS.
iv. Transportation and Storage
In Portugal, the same consortium is responsible for transportation and storage of collected used oil. In Spain, collectors or authorized third party service providers are responsible for transportation and storage. Re-refiners are also authorized collectors in Spain.
v. Disposal – Re-refining
The public-private partnership overseeing the industry in Spain has a stated target of re-refining 65% of the collected used oil enshrined in its statute. The Portuguese consortium has a similar target.
vi. Disposal – Fuel
Installations which use used oil as fuel have to be authorized. As Spanish authorities want to recover 95% of generated oil, disposal as fuel is encouraged for all collected used oil that cannot be re-refined.
vii. Disposal – Other
Untreated waste oil must be treated according to the waste framework directive and the waste (Circular Economy) (Amendment) Regulations 2020 of 2020.
Regulatory Enforcement
i. Responsible Agencies
Spanish Ministry of Energy and Environment
Spanish Used Oil observatory
Portuguese Ministry of Economy
National Entity for the Energy Sector (ENSE) in Portugal
ii. Enforcement Mechanisms
The Ministries of Energy and the Environment and the CNMC all have specific powers to issue regulations and decisions, and to supervise and enforce obligations under the law. In Spain, regional authorities also have broad powers in the energy sector.
iii. Effectiveness of Regulations Enforcement
Enforcement is relatively effective. In Spain the authorities mentioned above have the power to impose penalties and sanctions
There are sanctions tied to non-compliance and dispute settlement mechanisms.
Key Influencers
i. Public Sector
Ministry for economic development
Portuguese National Environmental Agency (APA)
ii. Private Sector
Sistema Integrado de Gestion de Aceites Usados (SIGAUS)
Sociedade De Gestao Integrada de Oleos Lubrificantes Usados (SOGILUB)

## Slide 311: Regulations: Iberia 2
Used Oil Regulations
Generation
The EU’s Waste Framework directive requires used oil to be collected, separated, and, whenever technically feasible, treated and generated. In Spain, SIGAUS, the organization tasked with overseeing the used oil sector, has a stated target of regenerating 65% of the collected used oil enshrined in its statute. Decree No. 153/2003 governs the management of used oils, taking into account production, regeneration, and re-refining possibilities. The hierarchy of operations as prioritized by the decree is re-refining, recycling, and disposal.
Classification
In Portugal, under the legal framework on waste management (approved by Decree-Law No. 178/2006 of 5 September as amended, and Decree-Law No. 152-D/2017 as amended), waste products must be transported and managed by licensed entities. A waste producer must also register on an electronic database and provide information on the quantities of waste delivered and entities responsible for its treatment.
In Spain, Royal Legislative Decree 1/2016 on integrated pollution prevention and control and Law 22/2011 on waste and contaminated soils are the main laws regulating used oil classification, and they require an integrated environmental authorization.
Collection
In Spain, the Royal Decree 679/2006 has set up SIGAUS which oversees and regulates the collection of used oil at a national level. In Portugal, Decree No. 153/2003 established SOGILUB, a public-private consortium which is the only authorized used oil collection and distribution company.
Transportation and Storage
The same decrees governing collection are valid for transportation and storage. In Portugal, SOGILUB takes care of used oil transportation and storage. In Spain, collectors must receive an authorization by SIGAUS. Several re-refiners are also authorized collectors in Spain.
Disposal – Re-refining
Re-refiners need to operate in compliance with Directive 2010/75/EU on industrial emissions (Industrial Emissions Directive), which regulates the operation of refineries, including re-refineries. In Spain, companies have to conform with the Revised text of Law 16/2002 on integrated pollution prevention and control and Royal Decree 815/2013 approving the Regulation on industrial emissions and developing Law 16/2002. In Portugal, re-refiners are subject to the legal framework for industrial emissions and the prevention and control of pollution (as set out under Decree-Law No. 127/2013) and require an environmental license.
Disposal – Fuel
Used Oil processors must follow the same regulatory processes as re-refiners. Sites utilizing recycled oil for fuel must be authorized. Regenerating takes priority in the hierarchy of used oil priority.
Disposal – Other
Untreated waste oil must be treated according to the waste framework directive and the waste (Circular Economy) (Amendment) Regulations 2020 of 2020
Probable Future Regulations
Any future regulations will depend on the EU assessment process which is expected to conclude in 2022.
Regulatory Enforcement
Responsible Agencies
Spanish Ministry of Energy and Environment
Spanish Used Oil observatory
Portuguese Ministry of Economy
National Entity for the Energy Sector (ENSE) in Portugal
Enforcement Mechanisms
The Ministries of Energy and the Environment and the CNMC all have specific powers to issue regulations and decisions, and to supervise and enforce obligations under the law. In Spain Regional authorities also have broad powers in the energy sector.
Effectiveness of Regulations Enforcement
Enforcement is relatively effective. In Spain, the authorities mentioned above have the power to impose penalties and sanctions
There are sanctions tied to non-compliance and dispute settlement mechanisms.
Key Influencers
i. Public Sector
Ministry for Economic Development
Portuguese National Environmental Agency (APA)
ii. Private Sector
Sistema Integrado de Gestion de Aceites Usados (SIGAUS)
Sociedade De Gestao Integrada de Oleos Lubrificantes Usados (SOGILUB)
Impact of Current Regulations
Moderate to high. Untreated waste disposal is forbidden, and regeneration is strongly encouraged. The consortium is effectively financed through the imposition of the used oil collection levy and the regulatory framework has enabled the development of a re-refining industry. The public procurement policies under GPP (Green Public Procurement Policies) are strong incentives for using re-refined lubricants in public sector procurement.

## Slide 312: Material Balance 2020
Chart: USED OIL GENERATION, 2020
| Used oil generated | Lubricant lost
Sales | 0.58 | 0.42
Total: 3,107.6 Kilotonnes
Chart: USED OIL COLLECTION, 2020
| Collected | Not collected
Sales | 0.8 | 0.2
Chart: USED OIL DISPOSAL, 2020
| Re-refined-a | Fuel | All other
Sales | 0.63 | 0.36 | 0.01
Chart: USED OIL RE-REFINING, 2020
| Basestock | All other
Sales | 0.65 | 0.35
Total: 1,809.1 Kilotonnes
Total: 1,523.2 Kilotonnes-b
Total: 966.3 Kilotonnes-a
Total finished lubricants consumption in the Western Europe was estimated at 3,107.6 kilotonnes in 2020.
  Out of the total volume, 1,809.1 kilotonnes or 58% of the lubricant demand the region is generated as used oil. Used oil generation has seen a slight increase due to technological improvements in the automotive segments and to regulatory pressures discouraging on-site reclamation of used oil.
  The remaining 42% of total lubricants demand in 2020 is lost in consumption, during handling, or through leakages. Lubricants such as process oils such as rubber process oils and white oils do not generate used oil since they become part of the final product. Generation is technically unfeasible for other industrial lubricant products such as greases.
  Western European countries have made major in-roads in promoting collection rates in recent years thanks to fiscal incentives, improved organization, better regulatory enforcement, and information campaigns. The collection rate has risen from 75% in 2018 to an estimated 80% in 2020.
  Generation, collection, and re-refining rates differ across Europe according to the regulatory system used, to the make-up of the lubricant market, and to the re-refining capacity of the country, among other factors.
a- Includes re-refining for VGO/MDO and transformer oil regeneration.
b- Includes 80 KT of imports of used oil from other regions such as Eastern Europe and Africa that is re-refined. Total domestic used oil collection is 1,443.2 KT.
a- Includes 80 KT of imports of used oil from other regions such as Eastern Europe and Africa that is re-refined.
Note: Includes re-refining to VGO/MDO and transformer oil regeneration.
Continued…

## Slide 313: Material Balance 2020
USED OIL GENERATION AND COLLECTION BY COUNTRY IN WESTERN EUROPE, 2020 |  |  |  |  | 
COUNTRY | LUBRICANT CONSUMPTION (KT) | USED OIL GENERATED (KT) | USED OIL COLLECTED (KT) | GENERATION RATE | COLLECTION RATE (FROM USED OIL GENERATED)
Germany-a | 748.0 | 449.0 | 375.0 | 60% | 83%
United Kingdom | 593.2 | 340.2 | 285.6 | 57% | 81%
France | 498.3 | 266.3 | 198.3 | 53% | 74%
Italy | 470.4 | 282.2 | 215.3 | 60% | 76%
Iberia (Spain and Portugal) | 375.2 | 236.4 | 181.0 | 63% | 76%
All other-b | 422.2 | 235.0 | 188.0 | 56% | 80%
Total | 3,107.6 | 1,809.1 | 1,443.2-c | 58% | 79%
a- Germany also imported around 219 KT over and above 375 KT collected domestically in 2020. So, total used oil disposed was 594 KT in Germany in 2020. b- includes Belgium, the Netherlands, and Switzerland, among others. c- Does not include 80 KT of used oil imports. |  |  |  |  | 
Germany is the largest market for finished lubricants in Europe and generates the largest amount of used oil in Western Europe, accounting for 26% of used oil generated in the region, followed by the United Kingdom and Italy, who respectively account for a share of 19.8% and 14.9%.
  Germany’s used oil generation rate is lower compared to other countries, however, since the German finished lubricant market is characterized by a large amount of water-miscible metalworking fluids and process oils which cannot generate used oil. The same is true about the United Kingdom which is a large consumer of metalworking fluids and white oils, as well as marine engine oils for deep sea vessels, which is another category of industrial lubricants that typically does not generate used oil.
  Since generation rates are higher in the automotive segment rather than the industrial segment, countries with higher lubricant demand from the automotive segment compared to the industrial segment have higher generation rates, as is the case in Italy, Spain, and Portugal.
  After the overhaul of the consortium overseeing used oil collection in Italy and public initiatives to promote collection, used oil collection in Italy have increased to surpass 90%, the highest collection rate in Europe.

## Slide 314: Material Balance 2021
Chart: USED OIL GENERATION, 2021
| Used oil generated | Lubricant lost
Sales | 0.58 | 0.42
Total: 3,281.6 Kilotonnes
Chart: USED OIL COLLECTION, 2021
| Collected | Not collected
Sales | 0.8 | 0.2
Chart: USED OIL DISPOSAL, 2021
| Re-refined-a | Fuel | All other-b
Sales | 0.63 | 0.36 | 0.01
Chart: USED OIL RE-REFINING, 2021
| Basestock | All other
Sales | 0.65 | 0.35
Total: 1,902.7 Kilotonnes
Total: 1,596.1 Kilotonnes-b
Total: 1,009.2 Kilotonnes-a
Used oil generated in Western Europe is expected to change from 1,809.1 kilotonnes in 2020 to 1,902.7 KT in 2021, a growth of 5.2%. The growth is in line with 5.6% growth seen in lubricant consumption in 2021.
Used oil collected in Western Europe is expected to increase from 1,443.2 kilotonnes in 2020 to 1,516.1 kilotonnes in 2021, growing by 5.1%. This excludes 80 KT of imports for 2020 and 2021.
The amount of used oil re-refined in Western Europe is expected to increase from 958.5 kilotonnes in 2020 to 1,009.2 KT in 2021.
The used oil industry in Western Europe will not witness any significant change in 2021 compared with 2020. The increases in used oil generation, collection, and re-refined are a direct result of the recovery in the lubricants industry in 2021.
a- Includes re-refining for VGO/MDO and transformer oil regeneration.
b- Includes 80 KT of imports of used oil from other regions such as Eastern Europe and Africa that is re-refined. In 2021, imports have been taken at 80 KT, same as 2020. Total domestic used oil collection is 1,463.2 KT.
a- Includes 80 KT of imports of used oil from other regions such as Eastern Europe and Africa that is re-refined.
Note: Includes re-refining to VGO/MDO and transformer oil regeneration.

## Slide 315: Used Oil Generation
Chart: USED OIL GENERATION RATES BY PRDOUCT IN WESTERN EUROPE, 2020 AND 2021-a
| PCMO | HDMO | Hydraulic Fluid | Metalworking Fluids | Industrial Engine Oil | Process Oil | All Other-b
Series 1 | 0.89 | 0.85 | 0.9 | 0.4 | 0.34 | 0.1 | 0.42
In 2020, used oil generated in western Europe amounted to 1,809.1 KT, equivalent to approximately 58% of finished lubricant consumption. In 2021, used oil generated in western Europe amounted to 1,902.7 KT, equivalent to approximately 58% of finished lubricant consumption.
  Not all used oil can be generated, and the balance of 42% accounts for oil lost to technical losses evaporation, combustion, leakages, and handling losses. Certain lubricant categories, including white oils, water-miscible metalworking fluids, marine engine oils, rubber process oils and other process oils, and greases cannot be recycled or regenerated. Process oils and 2-stroke engine oils are mostly lost in operation.
USED OIL GENERATION BY PRODUCT IN WESTERN EUROPE, 2020 AND 2021 |  |  |  | 
LUBRICANT | KILOTONNES |  | % OF TOTAL USED OIL GENERATED | 
 | 2020 | 2021 | 2020 | 2021
PCMO | 504.0 | 531.0 | 27.9 | 27.9
HDMO | 397.6 | 410.0 | 21.8 | 21.6
Hydraulic fluid | 382.8 | 405.5 | 21.2 | 21.3
MWF | 140.4 | 149.1 | 7.8 | 7.8
Industrial engine oil | 96.9 | 102.4 | 5.4 | 5.4
Process oil | 44.6 | 47.9 | 2.5 | 2.5
MCO | 12.7 | 13.1 | 0.7 | 0.7
All other-a | 230.1 | 243.8 | 12.7 | 12.8
Total | 1,809.1 | 1,902.7 | 100.0 | 100.0
a- Includes ATF, compressor oil, refrigeration oil, turbine oil, among others. |  |  |  | 
a- Generation rates are same for 2020 and 2021. Therefore, only one bar chart is shown.
b- Includes ATF, compressor oil, refrigeration oil, turbine oil, among others.

## Slide 316: Used Oil Collection
Used oil collection in Western Europe was estimated at 1,431.3 kilotonnes in 2020, amounting to 79% of generated used oil and close to 50% of total lubricant demand in the region.
  The amount of collected used oil has decreased by approximately 10% from the 1,597.6 kilotonnes recorded in 2018, largely due to the fall in annual lubricant demand linked to the COVID-19 pandemic.
  The decline is lower due to increase in collection rates in the region. Collection rates for used oils have been rising from an average of 75% in 2018 to 79% in 2020, due to the rise in PCMO demand due to the increase in vehicle sales and in the passenger vehicle parc. Awareness of proper disposal has also been rising among the public, highlighted by incentives and information campaigns. The increase in the quantity of available used oil has made collection more profitable, lowering transportation rates per volume.
In 2021, the used oil collection in Western Europe is estimated at 1,463.2 kilotonnes, amounting to 81% of generated used oil. The increase is due to recovery in lubricant demand in 2021.
Chart: USED OIL COLLECTION RATES BY PRODUCT IN WESTERN EUROPE, 2020 AND 2021-a
| PCMO | HDMO | Hydraulic Fluid | Metalworking Fluids | Industrial Engine Oil | Process Oil | All Other-b
Series 1 | 0.9 | 0.9 | 0.79 | 0.55 | 0.55 | 0.8 | 0.67
USED OIL COLLECTION BY PRODUCT IN WESTERN EUROPE, 2020 AND 2021 |  |  |  | 
LUBRICANT | KILOTONNES |  | % OF TOTAL USED OIL COLLECTED | 
 | 2020 | 2021 | 2020 | 2021
PCMO | 453.6 | 477.9 | 31.4 | 31.5
HDMO | 357.9 | 369.0 | 24.8 | 24.5
Hydraulic fluid | 302.4 | 320.3 | 21.0 | 21.1
MWF | 77.2 | 82.0 | 5.3 | 5.4
Industrial engine oil | 53.2 | 56.3 | 3.7 | 3.7
Process oil | 35.7 | 38.3 | 2.5 | 2.5
MCO | 9.5 | 9.8 | 0.7 | 0.6
All other-a | 153.6 | 162.4 | 10.6 | 10.7
Total-b | 1,443.2 | 1,516.1 | 100.0 | 100.0
a- Includes ATF, compressor oil, refrigeration oil, turbine oil, among others. b- Does not include imports of 80 KT. |  |  |  | 
a- Collection rates are same for 2020 and 2021. Therefore, only one bar chart is shown.
b- Includes ATF, compressor oil, refrigeration oil, turbine oil, among others.
Continued…

## Slide 317: Used Oil Collection
AUTOMOTIVE USED OIL COLLECTION BY SOURCES, 2020 |  | 
SOURCE | KILOTONNES | % OF USED OIL COLLECTED
Workshops and other installed segment facilities (dealerships, fuel stations, quick lubes) | 735.3 | 80.0
Commercial operations (mining and construction sites, large farms, public sector organizations) | 137.9 | 15.0
DIY | 45.9 | 5.0
Total | 919.1 | 100.0
All consumers of lubricating oil in the European Union are required to participate in the collection effort, and that includes industry, workshops, other installed automotive maintenance businesses, and private consumers who perform DIY oil changes. Lubricant users are forbidden from abandoning the used oil but are required to hand it to authorized collectors, or to workshop or other business in the sector which can, in turn, supply used oil to a collector.
The majority of the collected used oils are automotive engine oils and other automotive lubricants, which amount to approximately 950 kilotonnes, or 60% of the total used oil collected in Western Europe.
Most automotive engine oil in Western Europe is collected in workshops, since most motorists turn to workshops for oil changes. Countries in Western Europe are largely DIFM (Do-It-For-Me) markets, rather than DIY (Do-it-Yourself) markets.
As the majority of used oil collected is automotive engine oil, workshops represent the leading source of total collected used oil in Western Europe.
PCMO is typically collected in workshops dedicated to passenger vehicle servicing. Automotive gear oil, transmission oil, and grease are also collected from workshops.
HDMO is collected in-house workshops for larger fleets and in independent or franchised workshops for smaller fleets. HDMO for off-road vehicles and automotive hydraulic and transmission fluid used by mining, construction, and large agricultural businesses is typically collected on-site.
Continued…

## Slide 318: Used Oil Collection
Used oil collection rates within Western Europe differ by country.
  Collection rates have expanded in Western Europe driven by regulation, with many countries aiming to achieve the 95% collection rate aim as stated by the European Commission.
  As stated in article 21 of the Waste Framework Directive 2008/98/EC, member states are required to take all necessary measures to ensure that used oils are collected separately, where this is technically feasible, and are treated in accordance with the stated waste hierarchy and the protection of the environment and human health.
  While Germany has the largest amount of collected used oil, on account of its larger lubricant consumption
  Italy also has high collection rates. The consortium governing used oil collection in Italy, CONOU, has been re-organized and has been effective in a campaign to raise collection rates.
  Countries with a consortium regulating used oil collection, such as Italy, Spain, and Portugal, tend to have higher collection rates than countries operating an open, market-driven collection system, such as France and the United Kingdom.
Due to limited mobility and factory closures in Europe in 2020 as a result of the lockdowns introduce to combat the spread of the COVID-19 pandemic, used oil collection in Western Europe was adversely affected.
  The decrease was more marked in the aftermath of the first lockdown, when dealerships and factories were closed while curbs on personal mobility were most intense. Collection picked up again in summer and by the end of the year collection rates had recovered.
USED OIL COLLECTION BY COUNTRY IN WESTERN EUROPE, 2020 |  |  | 
COUNTRY | USED OIL GENERATED (KT) | USED OIL COLLECTED (KT) | COLLECTION RATE (%)
Germany-a | 449.0 | 375.0 | 83.0
United Kingdom | 340.2 | 285.6 | 81.0
France | 266.3 | 198.3 | 74.0
Italy | 282.2 | 221.3 | 78.0
Iberia (Spain and Portugal) | 236.4 | 175.0 | 74.0
All other-b | 235.0 | 188.0 | 80.0
Total | 1,809.1 | 1,443.2-c | 79.0
a- Germany also imported around 219 KT over and above 375 KT collected domestically in 2020. So, total used oil disposed was 594 KT in Germany in 2020. b- includes Belgium, the Netherlands, and Switzerland, among others. c- Does not include imports of 80 KT. |  |  | 
Continued…

## Slide 319: Used Oil Collection
The identity of the collector and the type of company varies from country to country, depending on the type of regulatory system within the country.
In countries in Southern Europe such as Italy, Spain, and Portugal, there are national used oil collection agencies which oversee collection companies and regulate used oil collection and distribution on a national scale.
  CONOU in Italy and SOGILUB in Portugal aggregate all the used oil collected in their respective country and the are the only authorized seller nationally of used oil to refineries.
  From a regulatory point of view, in countries governed by an Extended Producer Responsibility scheme (EPR) such as Italy and Portugal, collectors are part of a consortium that collects, transports, and manages used oil disposal.
  CONOU and SOGILUB essentially operate as collection agencies with several branches throughout the country. Re-refiners in Italy and Portugal are clients of the consortium and do not have a role in the collection effort.
In other countries with an open system, such as Germany, France, and the United Kingdom, collectors operate independently, and re-refiners also operate as collectors.
In Germany, the two largest re-refiners, Puraglobe and Avista, have their own collection arm with a large fleet of trucks. The two re-refiners are among the largest in Europe and have expanded their operation to neighboring countries such as Austria, Switzerland, Denmark, the Netherlands, and the Czech Republic. Other collecting companies with significant transnational clout in the area include Hans Schmidt, KS Logistic, and A.S.A., the leading used oil collection company in Austria. Germany has approximately 50 collection companies.
Hydrotec is the leading company for used oil collection in the United Kingdom, followed by Oakwood Fuels, and Oil Savage, while in France, the leading collector is Chimirec, followed by Veolia.
The two largest used oil collecting companies in Spain are the two leading re-refiners in Spain, Cator and Sertego. The collection market in Italy is very fragmented, with 72 collecting companies operating in the country.
The cost of used oil collection varies widely according to the regulatory system, whether incentives are used or not, on the type of lubricant, on the distance covered, and on local economic constraints.
  Variations in crude oil prices are also a key factor weighing on oil collection charges.
The price of used oil differs according to quantity, quality, geographic location, and type of contract.
  There is no fixed benchmark for deciding on a price: sometimes crude oil index prices are used, sometimes fuel prices are used, and sometimes, basestock index prices are used.
  Fluctuations in the price of crude oil and in currency exchanges also affect the price, as well as the presence of impurities, the most important of which is the presence of water in the oil.
  Every country has its own allowance limit for water in the oil, ranging from 1% to 10%, but over that limit the receiving party rejects the shipment.
Continued…

## Slide 320: Used Oil Collection
The type of contract depends often depends on the system used in the country:
  CONOU in Italy and SOGILUB in Portugal aggregate all the used oil collected in their respective country and are the only authorized seller nationally of used oil to re-refineries.
  In countries, where the consortium acts as a single seller, the contract is signed for long-term supply.
  In Portugal, annual supplies of used oil from the consortium, Sogilub, are awarded at an auction.
  In open market systems such as Germany, sales are negotiated in bilateral agreements between seller and buyer in a free market environment, and usually characterized by spot prices.
Used oil is usually stored by the generator into specifically assigned storage tanks, separate from other fluids, and appropriately labelled.
  Collectors generally prefer to handle collected used oil segregated into different product categories and stored in separate tanks.
  The segregation into separate tanks by product category is done in order to maximize revenue, since collectors obtain the highest prices for automotive engine and transmission oil because they are considered to be better re-refining feedstock.
  Collectors and generators adhere to strict storage and segregation practices which are designed to minimize the ingress of contaminants, such as water and antifreeze.
Generally, used oil generators have an agreement with a generator and develop standard protocols for collection with the collection company.
  The most common industry protocol is for the generator to contact the used oil collector when the storage tank reaches 90% of the capacity.
  Collection companies also have access to free drop-off points where DIY generators can safely dispose of their used oil for collection.

## Slide 321: Used Oil Disposal 2020
Chart: USED OIL DISPOSAL IN WESTERN EUROPE, 2020
| Re-refining | Fuel | All other-a
Sales | 0.63 | 0.36 | 0.01
Total: 1,523.2 KT
Out of the used oil collected in Western Europe, approximately 966.3 kilotonnes (including imports of 80 KT) are allocated to re-refining, 538.7 kilotonnes to fuel applications, and 18.2 kilotonnes to other uses, such as direct incineration or chemical neutralization.
The choice on whether to allocate collected used oil toward re-refining or fuel depends on re-refining capacity, the type of lubricant, and public priorities, among other factors.
  In the spirit of the European Union’s efforts to promote a circular economy, the preference for government agencies and other public bodies is for used oil to be re-refined as a basestock.
  Burning used oil as a fuel releases polluting contaminants into the atmosphere which contributes to increasing the carbon footprint of the emitter.
  In many countries, the feedstock allocated for re-refining is sufficient to cover re-refining capacity.
  In Italy and Spain, there is insufficient feedstock to cover the whole of the re-refining capacity and feedstock needs to be imported from abroad to make up the shortfall.
  There are logistical and administrative difficulties in importing waste oil, since they are classified as a hazardous waste. For this reason, imports are limited to Europe and are relatively small in most European countries, accounting for 1%-2% of total used oil, with the exception of Germany.
  Germany has a large re-refining industry and the domestic supply of used oil is insufficient. Germany is estimated to have imported as much as 219 kilotonnes in 2020, mostly from other European countries, but also from regions such as Africa.
  German used oil net imports surged in 2020, from the typical 120-170 KTA, in response to reduced domestic availability caused by lower COVID-19 induced lubricant consumption.
USED OIL DISPOSAL BY PRODUCT TYPE, 2020 |  |  | 
LUBRICANT TYPE | KILOTONNES |  | 
 | RE-REFINING | FUEL | ALL OTHER-a
Automotive Engine oils | 651.1 | 169.9 | -
All Other – b | 235.2 | 368.8 | 18.2
Imports | 80.0 | - | -
Total | 966.3 | 538.7 | 18.2
a- Includes direct incineration and chemical neutralization. |  |  | 
b- Includes industrial oils and fluids, greases, and other automotive oils such as MCO, ATF, HTF, and gear oil. |  |  | 
a- Includes re-refining for VGO/MDO and transformer oil regeneration.
b- Includes 40 KT of imports of used oil from other regions such as Eastern Europe and Africa that is re-refined. Total domestic used oil collection is 1,431.3 KT.
Continued…

## Slide 322: Used Oil Disposal
In the United Kingdom, there is a lack of re-refining capacity.
  Almost 80% of used oil collected in the United Kingdom is dedicated to fuel.
  In Germany and France, about 30% of used oil is allocated toward fuel applications.
  Italy has a policy of aiming to re-refine as much as possible of the collected oil into re-refined basestock. Currently 99% of used oil in Italy is dedicated to re-refining.
Re-refiners prefer working with automotive engine oils and hydraulic fluids and tend to avoid marine used oils, transformer oils, and metalworking fluids for re-refining. The higher viscosity, different additive packages, and higher metals and water contents of neat metalworking fluids and other industrial lubricants are often inconsistent with re-refinery process configurations.
Marine used oils tend to accumulate contaminants, making it difficult to treat them. Marine oils are also known to have the lowest prices due to the contamination levels.
The primary fuel applications for used oil in Western Europe are for the cement industry, steelworks, limestone works, marine bunkering, and on-site industrial cleaners. Neat metalworking fluids are mainly suited for heating in the cement industry.
Other disposal routes include direct incineration or chemical neutralization of the used oil that cannot be used as feedstock. This account only for 2% of the used oil collected and includes illegal disposal.
USED OIL DISPOSAL AND END-USE IN WESTERN EUROPE BY COUNTRY IN KILOTONNES, 2020 |  |  | 
COUNTRY | RE-REFINING-a | FUEL | ALL OTHER
Germany | 380.0 | 207.9 | 6.1
United Kingdom | 60.7 | 182.1 | 10.1
France | 113.1 | 66.2 | 1.6
Italy | 212.6 | 2.7 | -
All other-b | 200.0 | 79.8 | 0.4
Total | 966.3-c | 538.7 | 18.2
a- Includes re-refining to VGO/MDO and transformer oil regeneration. b- includes Denmark, Finland, Belgium, the Netherlands, and Switzerland, among others. c- Does not add due to rounding. |  |  | 

## Slide 323: Used Oil Disposal 2021
Chart: USED OIL DISPOSAL IN WESTERN EUROPE, 2021
| Re-refining | Fuel | All other-a
Sales | 0.63 | 0.36 | 0.01
Total: 1,596.1 KT
Out of the used oil collected in Western Europe, approximately 1,009.2 kilotonnes (including imports of 80 KT) are allocated to re-refining, 567.7 kilotonnes to fuel applications, and 19.2 kilotonnes to other uses, such as direct incineration or chemical neutralization.
In 2021, the volume of used oil disposal has increased as the lubricant demand recovered in the region.
USED OIL DISPOSAL BY PRODUCT TYPE, 2021 |  |  | 
LUBRICANT TYPE | KILOTONNES |  | 
 | RE-REFINING | FUEL | ALL OTHER-a
Automotive Engine oils | 679.5 | 177.2 | -
All Other - b | 249.7 | 390.5 | 19.2
Imports | 80.0 | - | -
Total | 1,009.2 | 567.7 | 19.2
a- Includes direct incineration and chemical neutralization. |  |  | 
b- Includes industrial oils and fluids, greases, and other automotive oils such as MCO, ATF, HTF, and gear oil. |  |  | 
a- Includes re-refining for VGO/MDO and transformer oil regeneration.
b- Includes 40 KT of imports of used oil from other regions such as Eastern Europe and Africa that is re-refined. Total domestic used oil collection is 1,431.3 KT.

## Slide 324: Used Oil Re-Refining
The stated used oil feed capacity in Western Europe is estimated approximately 1,405 kilotonnes including VGO/MDO and transformer oil regeneration facilities. Re-refineries in Europe received approximately 966.3 kilotonnes of used oil in 2020.
The average re-refined basestock yield rate in Europe is roughly 62% in 2020. The basestock re-refineries received 872 KT of used oil in 2020, producing around 540 KT of re-refined basestocks.
Currently, there are 17 re-refineries in Western Europe (excluding Greece and including transformer oil re-refiners).
  COVID-19 has had an impact on the ability of re-refiners to procure used oil feedstocks on local market. Major re-refiners have solved the supply issue by turning to import markets.
  This has been particularly the case in Germany.
  German used oil net imports surged in 2020, reaching 219 kilotonnes per year from the typical 120 to 170 KT used oil imported in previous years, in response to reduced domestic availability caused by lower COVID-19 induced lubricant demand.
  Imports of used oil feedstock have risen by smaller amounts in Italy and Spain too.
The quantity of used oil feedstock in Western Europe has increased thanks to regulatory incentives and governmental campaigns to improve collection rates, encouraged by the EU’s active interest in promoting a circular economy. The Italian consortium, CONOU, has made it its mission to raise awareness through digital information drives and events to reach all sectors of the economy and raise awareness of the obligation of businesses toward ensuring used oil collection. Consortia in Spain and Portugal have followed a similar route.
The amount of used oil allocated to basestock production has also risen to 63% of used oil available for re-refining, thanks to the increase in re-refined basestock production capacity and to the superior quality of used oil feedstock available on the market.
  Selling re-refined basestock is more profitable than other re-refined products from used oil, such as vacuum-gas oil (VGO), marine diesel oil (MDO), and other side-products.
  Consequently, when presented with used oil feedstock of sufficient quality, re-refiners choose to produce re-refined basestocks rather than other products.
  As the quality of available used oil feedstock in Western Europe improved, the quantity of re-refined basestock produced has improved too.
The quality of re-refined feedstocks is steadily improving due to the changing composition of the used oil re-refiners receive. A significant share of automotive used oil feedstock in Western Europe is made from synthetic, group III basestocks which have a better viscosity index and a superior quality.
Itelyum, Puraglobe, and Avista are the largest re-refiners in Western Europe, based on their basestock production capacity.
  These companies, together with STR Tecoil in Finland, are the only European re-refiners that produce premium basestocks (basestocks classified as Group II and above).
  Puraglobe is the only re-refiner producing Group III basestocks.
Perceptions of quality regarding re-refined basestocks have improved and major re-refiners such as Itelyum, Avista, and Puraglobe have earned a reputation for high quality on the wider market.
The larger re-refiners in Northern Europe have expanded vertically by acquiring international and domestic collectors and forging partnerships with blenders.
  Südöl have a partnership where they supply their parent company, Zeller + Gmelin.
Continued…

## Slide 325: Used Oil Re-Refining
USED OIL RE-REFINERS IN WESTERN EUROPE, 2020 (EXCLUDING INACTIVE PLANTS) |  |  |  |  | 
 |  | KILOTONNES |  |  | 
COUNTRY | COMPANY | USED OIL FEED CAPACITY | GROUP I BASESTOCK CAPACITY | GROUP II BASESTOCK CAPACITY | GROUP III BASESTOCK CAPACITY
Germany | Puraglobe-a | 160.0 | - | 50.0 | 50.0
 | Avista | 125.0 | 80.0 | - | -
Italy | Itelyum-b | 195.0 | 88.0 | 43.0 | -
 | R.A.M. Oil | 20.0 | 10.0 | - | -
France | Eco Huile | 120.0 | 60.0 | - | -
Spain | Sertego-c | 120.0 | 60.0 | - | -
 | Cator | 40.0 | 25.0 | - | -
Denmark | Avista | 120.0 | 75.0 | - | -
Finland | STR Tecoil | 60.0 | 40.0 | - | -
Portugal | Enviroil | 25.0 | 15.0 | - | -
 | Egeo Oil | 25.0 | 15.0 | - | -
United Kingdom | Whelan | 50.0 | 35.0 | - | -
Total |  | 1,060.0 | 503.0 | 93.0 | 50.0
a- This re-refinery is now completely Group III re-refinery as of April 2021. b- Itelyum has two re-refineries in Italy. One is in Pieve Fissiraga and other is in Ceccano. The re-refinery in Pieve Fissiraga produces both re-refined Group I and II basestocks. c- Sertego has four re-refineries in Spain. They are at Fuenlabrada, Palos de la F, Alfaro, and Cartagena. All of them have 30 KT feed capacity and 15 KT re-refined basestocks capacity. |  |  |  |  | 
Continued…

## Slide 326: Used Oil Re-Refining
VGO/MDO RE-REFINERS IN WESTERN EUROPE, 2020 (EXCLUDING INACTIVE PLANTS) |  |  | 
 |  | KILOTONNES | 
COUNTRY | COMPANY | USED OIL FEED CAPACITY | VGO/MDO CAPACITY
Germany | Baufeld | 100.0 | 70.0
 | Petro Plus | 40.0 | 20.0
 | Horst Fuhse Mineralölraffinerie | 20.0 | NA
 | Kurt Schmidt KS Recycling | 50.0 | 30.0
 | Südöl | 15.0 | 10.0
France | Osilub-a | 120.0 | 75.0
Total |  | 280.0 | 205.0-b
a- It is not clear if Osilub is producing VGO/MDO or processing further to produce re-refined basestocks. Kline understand that this re-refinery produces VGO/MDO, which is processed further in other plants to produce basestocks. b- Excluding Horst Fuhse Mineralölraffinerie’s plant. |  |  | 
TRANSFORMER OIL RE-REFINERS IN WESTERN EUROPE, 2020 (EXCLUDING INACTIVE PLANTS) |  |  |  | 
 |  | KILOTONNES |  | 
COUNTRY | COMPANY | USED OIL FEED CAPACITY | TRANSFORMER OIL CAPACITY | PRODUCTION
Germany | Starke & Sohn | 20.0 | 20.0 | 15.0
 | Trafolube | 15.0 | 15.0 | 8.0
United Kingdom | EOS | 30.0 | 30.0 | 25.0
Total |  | 65.0 | 65.0 | 48.0
Continued…

## Slide 327: Used Oil Re-Refining
The global basestock market is shifting away from API Group I basestocks in favor of higher quality basestocks, such as API Group II and Group III basestocks. The larger re-refiners are adapting to the changing demand landscape.
  Puraglobe is planning to add further production capacity for re-refined Group III basestocks at its Zeitz site which could yield a further 50 kilotonnes re-refined Group III basestock per year. The upgrade should be complete by 2023.
  Avista Oil is planning to convert its plant in Dollbergen from producing Group I+ basestocks to Group II basestocks.
  Osilub is reportedly planning to construct a third plant in France. Parent companies Veolia and Total have invested 55 million euros in a used oil regeneration plant in Le Havre (Seine-Maritime). The new re-refinery is on track to begin operations by the end of 2021 and will have a total used oil feed capacity of 120 kilotonnes.
  Itelyum has recently expanded its Group II basestock production capacity. Smaller re-refiners are considering whether to reconfigure their plants toward Group II basestock production.
  Smaller refiners include Tecoil in Finland and Südöl in Germany.
The price of basestocks is correlated with the price of crude oil, although basestock index prices and fuel prices are also used as benchmarks.
Basestocks are sold on the open to market to blenders, either through contracts or through competitive tenders.
The price of crude oil has been volatile throughout 2021. A key benchmark used in oil and petroleum products, the West Texas Intermediate (WTI), fell to as low as USD 20 dollars in Spring 2021, due to the global repercussions of the pandemic and to the price wars between Saudi Arabia and Russia, before recovering partially at the end of the year to overtake the USD 50 mark.
  Prices of re-refined basestock have been on a rising trend due to the improvement in quality of re-refined basestocks and to the corresponding increase in the price of virgin basestocks. The gap in price between virgin and re-refined basestocks has been closing. The typical price premium for a virgin basestock compared to a re-refined basestock is, on an average, less than 5% and in certain cases, can be close to 0.
  API Group II and Group III re-refined basestocks typically command a 1%-5% price premium over API Group I re-refined basestocks.

## Slide 328: Used Oil Re-Refiner Profiles: Avista Oil
Avista Oil (AO), was founded in 1951 and was formerly known as Mineralölraffinerie Dollbergen, headquartered in Germany.
The company is privately owned, with major stakes owned by Bitburger Holding GmbH (45%), Skion GmbH (45%), Dr. Weinberger Management & Consult GmbH (10%). Its CEO is Marc Verfürth.
The company is integrated through the used oil value chain, including collection, re-refining, and production and international marketing of lubricants.
The company’s current total used oil equity processing capacity is 348 Kilotonnes per annum, including two re-refining plants in Europe (Germany and Denmark) and one in the U.S.
Avista sells about 80 KTA (50 KTA re-refined) of marketable lubricants developed for various applications (PCMO, gear oils, lubricants for agricultural vehicles and construction machinery, as well as for various industrial uses).
Re-refined products are offered under brands AVISTA Kernsolvat, Motor Gold, Pennasol, AVISTA Flux, and AVISTA Fuel.
Avista is a closed-loop re-refiner in Europe.
Annual volumetrics for the year 2020:
  Used Oil Collected: 335,000 Tons, including Europe and U.S.
  Used Oil Processed (total): ~313,000 Tons
  Base Oil Produced (total): >200,000 Tons
Used oil value chain acquisitions:
  Universal Environmental Services LLC, US (2011)
  Large collectors in Belgium and the Netherlands
  How does the company operate? Closed loop vs. open loop re-refining?
Planned investments:
  Second re-refinery in the United States is on hold
  Avista Oil is planning to convert its plant in Dollbergen from producing Group I+ basestocks to Group II basestocks.
OVERVIEW OF USED OIL FEED CAPACITY AND KEY PRODUCTS BY LOCATION |  | 
LOCATION | USED OIL FEED CAPACITY (KILOTONNES PER YEAR) | KEY PRODUCTS
Dollbergen, Germany | 125 | Group I, I+
Kalundborg, Denmark | 120 | Group I
Peachtree City, GA,U.S. | 160 | Group II+. III

## Slide 329: SWOT Analysis: Avista Oil
STRENGTHS | WEAKNESSES
Avista Oil is one of the largest re-refiners in Europe, with one of the largest used oil feedstock processing capacities. The company has re-refining operations in several countries in Europe and in the United States, giving it a global reach and ready access to different markets. The company is vertically integrated. Avista has its own collection business and is able to secure raw material procurement in its home country, Germany, with large source of used oil feedstock. The company also has a finished lubricant product line and does toll blending for other companies, diversifying its import sources. The company has a diversified product base, producing Group II and III basestocks in the United States and Group I basestocks in Europe. | The company faces fierce competition in Germany for raw material and customers. Its German re-refinery cannot rely entirely on feedstock sourcing from its domestic market but has to import feedstock from abroad, which can be a problematic process and results in additional charges. The collection rate in its home country, Germany, is lower than in other countries in the region. The company produces only Group I basestocks in Europe. Avista is not active in supply Group III basestocks, which have seen rising demand in recent years.
OPPORTUNITIES | THREATS
Rising collection rates and interest in regenerated oil leave the company in a good position to cement its market leadership. The company is well-positioned to expand production of Group I and begin production of Group II basestocks also in Europe. Avista has expanded its collection business internationally, giving it additional access to raw material. There is potential to expand re-refining capacity in other countries. As the European leader, Avista is in a good position to enter new markets such as France, where currently only two re-refineries operate. | Demand for Group I basestocks in Europe is falling, which could translate into falling demand for Group I re-refined basestocks. The dwindling supply of used oil from Group I basestocks in Europe could exacerbate the used oil supply shortage. If the company expands into producing Group III basestocks, it could face difficulties entering the Group III basestock market in Europe, where there is already an established competitor.

## Slide 330: Used Oil Re-Refiner Profiles: Puraglobe
The company was founded as Puralube Inc. in 1995. Following the acquisition of the waste oil collection and two German VGO re-refineries of the Baufeld Group, the company entered the basestock re-refining business and started operations at the Group II Zeitz re-refinery in Eastern Germany in 2002, supported by public investment subsidies covering 50% of operating expenditure.
The company rebranded as Puraglobe in 2017. when it acquired the assets of Nexlube in Tampa, FL, United States.
Puraglobe has since divested its Chemnitz VGO plant, has increased operating capacity at its Zeitz plant, and has added additional hydrotreating units to be able to produce Group III re-refined basestocks.
The company is privately owned, with significant holdings by PE firms Allied Resource Group, Junction Energy Capital, and Ara Partners. Its CEO is Andreas Schüppel.
Puraglobe is the only producer of high-quality re-refined Group III basestocks in the world, employing the advanced UOP HylubeSAT process.
Puraglobe now owns a major used oil collection business in Germany (Baufeld), owns a two-train Group III re-refinery at Zeitz, and a lubricant blending plant in Tampa, FL.
Puraglobe is one of the largest importers of high-quality used automotive engine oil into Germany from other European countries.
The company ships a portion of its Group III production from Zeitz to Tampa for blending, and blends and markets finished lubricants under the SYNTAINICS® brand.
Annual volumetrics:
  Used Oil Collected: 40,000 Tons (2020), including Europe and U.S.
  Used Oil Processed (total): ~145,000 Tons (2020)
  Base Oil Produced (total): ~ 95,000 Tons (2020)
OVERVIEW OF USED OIL FEED CAPACITY AND KEY PRODUCTS BY LOCATION |  | 
LOCATION | USED OIL FEED CAPACITY (KILOTONNES PER YEAR) | KEY PRODUCTS
Zeitz, Germany | 160 | Group III
Used oil value chain acquisitions
  Nexlube, US (2017)
  Several collectors were acquired from 1990 to 2010
Planned investments:
  Puraglobe has recently announced its intention of adding a third Group III train at Zeitz, expected to start operations in 2023. The new train should have a used oil feed capacity of 80 kilotonnes, like the other two trains.
  Puraglobe also intends to re-start production at the Nexlube Tampa Group III re-refining plant in the near future.

## Slide 331: SWOT Analysis: Puraglobe
STRENGTHS | WEAKNESSES
Puraglobe is an established market player in Germany, which gives it access to the largest source of high-quality used oil feedstock in the region. The company has access to the most advanced re-refining technology in the region and is the only producer of higher quality re-refined Group III basestocks in Europe. The company has a global presence and an established importing network, which enables it to source feedstocks internationally. As a result, the company is not as reliant as others on the used oil collection market in Germany. The company has its own collection arm, giving it more control over its raw material supply chain. Puraglobe also has a finished lubricants business, selling motor oils under its own brand. Its integration gives it the ability to control costs and margins. | Puraglobe faces strong competition on its home market, which lowers the ready availability of used oil feedstock. The collection and re-refining rates in Germany are not as high as in other countries. The company needs to rely heavily on imports to fulfil procurement needs and importing comes with extra costs. Puraglobe only has one re-refining site in Germany and does not have re-refineries currently on-stream in other countries. The company does not have any Group I or Group II re-refining anymore.
OPPORTUNITIES | THREATS
The collection rate in Germany still has room to increase, leaving the company with potentially higher used oil feedstocks. Its position as the only producer of Group III re-refined basestocks in the region puts it in a good position in the face of rising demand for Group III basestocks in Europe. Completion of the Tampa re-refinery could give the company with privileged access to international markets, since Puraglobe will be able to directly supply the US market without having to import product from its Europe. Its finished lubricants business presents the company with a constant outlet for its product. Toll blending could represent an added revenue stream. | The concentration of production at one site leaves it vulnerable to shortages in case of technical failures or accidents at that site. Puraglobe has chosen to focus exclusively on Group III basestock production, without product diversification, leaving it vulnerable in case of changing market conditions. The delays in construction of the Tampa re-refinery could result in the company lagging behind its major competitors.

## Slide 332: Used Oil Re-Refiner Profiles: Itelyum
Itelyum was established in 1963 in Italy as Viscolube from the union of 16 companies operating in the used oil sector.
Over the years Viscolube has concentrated on the production of re-refined API Group I basestocks at its refinery of Pieve Fissiraga, near Milan, becoming the leading producer of re-refined basestocks in the country.
In 2001, the company strengthened its re-refining business through the acquisition of the Cerccano re-refinery from ENI.
In 2015, Viscolube started a new production unit at its Pieve Fissiraga plant capable of producing Group II basestocks.
In 2019, Viscolube rebranded as Itelyum after taking over Bitolea, an Italian company active in the purification of solvents. The resulting entity has three business units: regeneration (where re-refining falls under), purification, and environmental services.
The company is privately owned. The single largest shareholder is the private equity fund Stirling Square Capital Partners. Its CEO is Marco Codognola.
Itelyum has developed its own proprietary regeneration technology, together with the French company Axens, which includes hydrofinishing and deasphalting, and enables Itelyum to produce high quality regenerated basestock with a yield of over 65%. Itelyum markets its Group I and Group II basestocks as Group I+ and Group II+.
Annual volumetrics:
  Used Oil Collected: N/A. The company has an agreement with CONOU for the regular procurement of used oils and imports small quantities of used from neighboring countries
  Used Oil Processed (total) <200,000 Tons
  Base Oil Produced (total): >100,000 Tons
Used oil value chain acquisitions
  Castiglia Srl, Italy (2021)
  Bitoles (2021)
Planned investments:
  The company is considering whether to increase production of Group II basestocks, but operational expanse plans are on hold.
OVERVIEW OF USED OIL FEED CAPACITY AND KEY PRODUCTS BY LOCATION |  | 
LOCATION | USED OIL FEED CAPACITY (KILOTONNES PER YEAR) | KEY PRODUCTS
Pieve Fissiraga, Italy | 130 | Group I, II
Ceccano | 65 | Group I

## Slide 333: SWOT Analysis: Itelyum
STRENGTHS | WEAKNESSES
Itelyum can rely on a highly efficient collection network in its home country, Italy, under the auspices of CONOU. Itelyum also benefits from governmental incentives and subsidies from the Italian government. There is a regulatory drive toward incentivizing the use of regenerated oils in the public sector. The company does not have face significant competition in its own country. Itelyum is one of the few re-refiners with hydrofinishing units in their plants, enabling them to produce API Group II basestocks. The feedstock of available used oil has increased in quality in recent years. | Itelyum is mostly reliant on used oil collected in Italy, since the process of importing used oil is cumbersome. Consequently, its feedstock supply is limited. While the feedstock of used oil has been increasing in quality, large amounts of inferior quality feedstocks are generated as used oil in Italy, including monograde engine oil. This leaves the company with limited amounts of feedstock necessary to produce re-refined Group II basestocks. The centralized used oil procurement process in Italy leaves Itelyum without flexibility to negotiate autonomously with individual collectors. Since the acquisition of Bitolea in 2019, the company is not exclusively focused on used oil regeneration anymore.
OPPORTUNITIES | THREATS
Itelyum could be in a good position to increase production of Group II re-refined basestocks. The company is already producing re-refined Group II basestocks and the quality of its feedstock has been increasing, potentially enabling it to produce more re-refined Group II basestocks. The company already has international customers and, given its uncontested primacy in its country, could be able to expand its international operations in neighboring countries. | The recent rebranding and shift toward the solvent purification business could translate into a lack of focus on the regeneration market. The collection rate is very high in Italy, leaving the company unable to receive more feedstock given the importing difficulties. This could hurt the ability of the company to grow its output and keep pace with its international peers. The company would be particularly vulnerable if the generous public incentives toward re-refined basestocks are removed.

## Slide 334: Used Oil Processors
MAJOR USED OIL PROCESSORS IN WESTERN EUROPE, 2020 | 
COMPANY | COUNTRY
Italcementi | Italy
Lafargeholcim | France
Veolia | France
Heidelberger Cement | Germany
Märker Zement | Germany
Phoenix Zementwerke Krogbeumker | Germany
Schwenk Zement AG | Germany
In Western Europe, there are governmental incentives which privilege re-refined basestocks production as opposed to processing into fuel or other products such as VGO or MDO. As a result, the proportion of used oil allocated to processing as fuel or to other re-refined products other than basestocks has been falling.
  Re-refining into basestocks is the most profitable activity for used oil re-refiners. Re-refiners always prefer to re-refine used oil into basestocks, if presented with feedstock of required quality.
Processing operations and uses for collected used oil not destined to regeneration in Europe include the following:
  Processed fuel oil (equivalent to fuel oil or gas oil). This is particularly common in the United Kingdom, where major collectors such as Hydrodec, Oakwood Fuels, and Oil Salvage also engage in PFO production. PFO is typically used in asphalt plants, quarries, and in as start-up fuel in power stations.
  Fuel for the cement industry. This is common in France and Germany.
  Heavy oil for the marine industry.
  Fuel for heating stoves.
  Gas oil for off-road gas-powered vehicles.
  Waste incineration.
The cement industry is one of the largest industrial sectors purchasing used oil in Europe for processing.
  Used oil is used by the cement industry in very large quantities without any treatment
  It is usually used as a secondary or start-up fuel for the cement kilns
  In the United Kingdom and Germany, the cement industry pay only nominal amounts for the used oil. In the United Kingdom, the collector might even pay the cement-maker to take ownership of the low quality used oil.
Processors use a sequence of various processes to treat the used oil. The severity and complexity of the processing involved depends on the end-use.
  Contaminants need to be removed
  In the case of heavy distillates such as VGO. marine diesel oil and heating fuel the used oil needs to be demetallized
  For replacement fuel oil (RFO), used in Road stone plants, cement kilns, large marine engines, processing can be minimal: for this reason, several of the largest suppliers of RFO are used oil collectors
  Used oil burned in the cement industry requires no processing
  Direct burning in waste incinerators is usually only undertaken when the oil is so heavily polluted there is no other use for it.
Used oil processed as MDO needs to comply with the International Maritime Organization (IMO) regulations for a 0.50% global sulphur cap for marine fuels which began on January 1, 2020. Under the regulation, MDO cannot contain more than 0.5% sulphur content.
Note: Details of companies producing VGO/MDO from used oil is mentioned on slide 48.

## Slide 335: Re-Refined Lubricants
Re-refined basestocks make up a small share of the overall basestock market in Western Europe.
There is little clarity on how much re-refined basestock is used to manufacture finished lubricants in Europe.
  There is no requirement for finished lubricants in Western Europe to indicate whether they are manufactured from a re-refined basestocks or virgin basestocks.
  There is no requirement either for finished lubricants to be manufactured solely from virgin basestocks or re-refined basestocks.
  It is very common in Western Europe for blenders to use mixed feedstock made up of virgin and re-refined basestocks.
  The API basestock Group is more useful for blenders as a selection criteria, rather than whether the basestock is re-refined or not.
Re-refined basestocks tend to be sold at a discount on average compared with virgin basestock (less than 5%), but that is mostly due to the fact that the majority of re-refined basestocks in Europe are API Group I basestocks while the majority of basestocks used in the automotive segment are Group II or Group III.
For the same reason, the majority of re-refined basestocks are used for the production of industrial oils and fluids rather than automotive engine oils
Since the majority of automotive engine oils in Western Europe are synthetic, they are manufactured with Group III basestocks. This leaves the bulk of Group I basestocks demand to the industrial segment.
Major basestock re-refiners such as Avista and Puraglobe also blend their own finished lubricant lines, which would be manufactured with 100% re-refined basestocks.
Re-refined lubricant brands include Avista Pace, a consumer automotive products brand, Avista Pure, a commercial automotive products brand, and Puraglobe’s Syntainics, a motor oil brand.
Only in specific cases a blender will explicitly require that a lubricant be made from re-refined basestocks and label it accordingly. For example, commercial enterprises working a public sector project in Italy, such as construction work, are required to use re-refined lubricants.
Re-refined basestocks can still carry the stigma of being associated with inferior performance, particularly in Northern European countries. This is one of the factors driving mixed blending; a blender can purchase re-refined basestocks at a lower cost and blend them together with virgin basestocks to maintain the quality at lower costs.
Global majors, particularly vertically integrated majors with their own upstream operations, are more likely to use virgin basestocks rather than re-refined basestocks. There is still a lingering perception among some European majors that lubricants made from re-refined basestocks are unlikely to provide the same levels of performance as lubricants made from virgin basestocks.
In Italy, re-refined basestocks are largely free of the stigma, and are even perceived as yielding superior performance than virgin basestocks.

## Slide 336: Finished Lubricant Market Outlook
Chart: PROJECTED FINISHED LUBRICANT MARKET IN WESTERN EUROPE, 2020-2030
| Industrial | Consumer | Commercial
2020 | 1764.6 | 715.6 | 627.4
2021 | 1817.9 | 736.7 | 636.4
2025 | 2058.3 | 831.4 | 673.1
2030 | 2050.8 | 766.1 | 655.5
The outlook for finished lubricant market in Western Europe is positive. Total finished lubricant demand is forecast to grow by 5.6% in 2021, by a CAGR of 2.8% by 2025, and by a CAGR of 1.1% during 2020-2030.
  The high rate of growth registered in 2021 is mostly due to the rebound in lubricant demand following the pandemic-induced retrenchment recorded in 2020. Demand in 2020, in fact, fell by approximately 15% in Western Europe.
Demand for finished lubricants from the industrial segment is outpacing demand for automotive lubricants. There are several potential developments which may influence the supply and demand of used oil over the next decade, which include:
  The slowdown is most seen in the consumer automotive segment. Demand for consumer automotive lubricants is forecast to grow by a CAGR of 3% by 2025 and at a CAGR of 0.7% during 2020-2030, while demand for industrial lubricants is forecast to grow at a CAGR of 3.1% by 2025 and at a CAGR of 1.5% during 2020-2030.
  The increasing penetration of electric passenger vehicles is expected to result in a sharp fall in demand for PCMO and other automotive lubricants. A battery electric vehicle consumes less than half the amount of transmission fluid as an internal combustion engine-powered vehicle, and no engine oil or gear oil.
  Electrification is expected to affect commercial vehicles, but not to the same extent or within the same timescale as the passenger vehicles. Growth for commercial lubricant demand is expected at a CAGR of 1.4% by 2025 and at a CAGR of 0.4% during 2020-2030.
  Demand for all kinds of lubricants is expected to slow down in the longer term, even in the industrial segment. The manufacturing of electric vehicles, for example, requires less metalworking fluids.

## Slide 337: Used Oil Industry Outlook
Chart: USED OIL GENERATION, 2025
| Used oil generated | Lubricant lost
Sales | 0.58 | 0.42
Total: 3,562.8 Kilotonnes
Chart: USED OIL COLLECTION, 2025
| Collected | Not collected
Sales | 0.82 | 0.18
Chart: USED OIL DISPOSAL, 2025
| Re-refined-a | Fuel | All other
Sales | 0.64 | 0.35 | 0.01
Chart: USED OIL RE-REFINING, 2025
| Basestock | All other
Sales | 0.65 | 0.35
Total: 2,066.4 Kilotonnes
Total: 1,694.4 Kilotonnes
Total: 1084.4 Kilotonnes
Used oil generated in Western Europe is expected to change from 1,902.7 kilotonnes in 2021 to 2,066.4 in 2025, growing at a CAGR of 2.1%.
Used oil collected in Western Europe is expected to increase from 1,516.1 kilotonnes in 2021 to 1,694.4 kilotonnes in 2025, growing by a CAGR of 2.8%
The amount of used oil re-refined in Western Europe is expected to increase from 929.2 kilotonnes (excluding imports of 80 KT) in 2021 to 1,084.4 kilotonnes (excluding imports) in 2025, growing by a CAGR of 3.9%.
The amount of used oil generated and collected in Western Europe is forecast to increase between 2020 and 2025. This development is influenced by the following factors:
  Reductions in lubricant loss volume, due to improved lubricant formulations and the adoption of smart lubrication systems
  A renewed focus, stemming from European Union regulations, on creating a circular economy, which encourages the lubricant industry to allocate as much of finished lubricant consumption as possible toward re-refining.
  Efforts by collectors to maximize the amount of generated used oil available for collection, thereby maximizing profits.
  Greater focus on collection and processing of used industrial oils in line with over-arching environmental goals.
a- Includes re-refining for VGO/MDO and transformer oil regeneration.
Note: Includes re-refining to VGO/MDO and transformer oil regeneration.
Continued…

## Slide 338: Used Oil Industry Outlook
Chart: USED OIL GENERATION, 2030
| Used oil generated | Lubricant lost
Sales | 0.57 | 0.43
Total: 3,472.4 Kilotonnes
Chart: USED OIL COLLECTION, 2030
| Collected | Not collected
Sales | 0.83 | 0.17
Chart: USED OIL DISPOSAL, 2030
| Re-refined | Fuel | All other
Sales | 0.67 | 0.32 | 0.01
Chart: USED OIL RE-REFINING, 2030
| Basestock | All other
Sales | 0.65 | 0.35
Total: 1,979.3 Kilotonnes
Total: 1,642.8 Kilotonnes
Total: 1,067.8 Kilotonnes
Used oil generated in Western Europe is expected to change from 2,066.4 KT in 2025 to 1,979.3 KT in 2030 as lubricant demand declines during 2025-2030.
Used oil collected in Western Europe is expected to decline from 1,694.4 KT in 2025 to 1,642.8 KT in 2030. The collection rate is expected to increase from 82% in 2025 to 83% in 2030 due to which the decline in used oil collection is expected to be lower than the decline in used oil generation volume.
The amount of used oil re-refined in Western Europe is expected to remain stable at increase slightly from 1,084.4 KT in 2025 to 1,100 KT in 2030. The reasons are given below:
  Regulatory and market-based pushes for reducing burning of used oil.
  Continuing state-sponsored efforts to raise national collection rates.
  Changes in the business models of key industry players.
  Entry of the majors and supermajors as indirect sponsors of used oil collection and/or re-refining.
  Enhanced focus of all used oil value chain players on sustainability/CO2 reduction.
a- Includes re-refining for VGO/MDO and transformer oil regeneration.
Note: Includes re-refining to VGO/MDO and transformer oil regeneration.

## Slide 339: Re-Refined Basestock Capacity Outlook
The European Commission sponsored effort, in cooperation with UEIL, to build a common framework for data sources, regulations. and tools for companies by 2022. This is expected to generate clarity on collection and re-refining data, adding to the focus on sustainability in the lubricants industry and to the perception of regeneration as a key pillar in the circular economy. The new framework is expected to spur collection and re-refining in western Europe.
  Major European OEMs such as Daimler are interested in lowering the carbon footprint of the lubricants they consume and using re-refined basestocks is one way of achieving that aim.
  Re-refining is expected to recover from the impact from COVID-19 by the end of 2021.
Sustainability is expected to play a larger role in the re-refining industry and to drive demand for re-refined basestocks in future.
  Shell’s new carbon neutral lubricants program is one of the most notable developments in sustainability in the industry promoting recycling and re-refining.
Re-refiners are however confronted by several challenges, particularly on the supply side. While the temporary supply disruption brought on by the COVID-19 pandemic is expected to be resolved within the next two years, the industry is faced with a structural fall in supply, brought on by lengthening oil drain intervals and by increasing EV penetration. Re-refiners are already struggling to work near full capacity.
Re-refiners also need to adapt to evolving demand for basestocks in Europe. The current trend is for demand to grow for Group III and Group II basestocks while demand for Group I basestocks is falling. Currently, most re-refineries in Western Europe are producing Group I re-refined basestocks.
  Avista is likely to produce Group II re-refined basestocks by 2030.
  Puraglobe will add a third 50 KT Group III train by 2023.
  Smaller Group I re-refiners will face the choice of closure or upgrading to producing Group II basestocks.
  Group III production capacity, thanks to the upgrade to the Puraglobe plant, is expected to increase to 150 kilotonnes. Group II production is also expected to increase by the same amount.
  Osilub is reportedly planning to construct a third plant in France. Parent companies Veolia and Total have invested 55 million euros in a used oil regeneration plant in Le Havre (Seine-Maritime). The new re-refinery is on track to begin operations by the end of 2021 and will have a total used oil feed capacity of 120 kilotonnes. It is not clear if it will produce re-refined basestocks or VGO/MDO.
Continued…

## Slide 340: Re-Refined Basestock Capacity Outlook
RE-REFINED BASESTOCK CAPACITY IN WESTERN EUROPE, 2020, 2021, 2025, AND 2030 (EXCLUDING TRANSFORMER OILS) |  |  |  | 
 | KILOTONNES |  |  | 
COMPANY | 2020 | 2021 | 2025 | 2030
Avista | 155.0 | 155.0 | 155.0 | 155.0
Itelyum | 131.0 | 131.0 | 131.0 | 131.0
Puraglobe-a | 100.0 | 100.0 | 150.0 | 150.0
Eco Huile | 60.0 | 60.0 | 60.0 | 60.0
Sertego | 60.0 | 60.0 | 60.0 | 60.0
STR Tecoil | 40.0 | 40.0 | 40.0 | 40.0
Whelan | 35.0 | 35.0 | 35.0 | 35.0
Cator | 25.0 | 25.0 | 25.0 | 25.0
Enviroil | 15.0 | 15.0 | 15.0 | 15.0
Egeo Oil | 15.0 | 15.0 | 15.0 | 15.0
R.A.M. Oil | 10.0 | 10.0 | 10.0 | 10.0
Total | 646.0 | 646.0 | 696.0 | 696.0
a- The re-refinery is a re-refined Group III basestock re-refinery with 100 KT capacity to produce re-refined Group III basestocks since April 2021. In 2020, it had a 50 KT production capacity for Group II basestock and 50 KT capacity for Group III basestock. |  |  |  | 
Note: Osilub has a re-refinery in France. However, it is not clear if the re-refinery is producing VGO/MDO or processing further to produce re-refined basestocks. Kline understand that Osilub’s re-refinery produces VGO/MDO, which is processed further in other plants to produce basestocks. Osilub is expected to add another re-refinery of 120 KT used oil feed capacity by the end of 2021. However, it is not clear if it will produce re-refined basestocks or VGO/MDO.

## Slide 341: Market Evaluation
Opportunities
Basestock suppliers or companies intending to enter the re-refining market in Western Europe are faced with many opportunities.
The quantity of used oil feedstock available for re-refining in Western Europe is increasing thanks to regulatory and fiscal incentives to improve collection and generation rates, encouraged by the EU’s interest in promoting a circular economy. The collection rate has risen from 73% in 2018 to an estimated 80%, thanks to fiscal incentives, improved organization, better regulatory enforcement, and information campaigns. The increase in the quantity of available used oil has made collection more profitable, lowering transportation rates per volume. The amount of collected used oil is set to increase further, with many countries adhering to the 95% collection rate aim as stated by the European Commission.
In the spirit of the European Union’s efforts to promote a circular economy, the preference for government agencies and other public bodies is for used oil to be re-refined as regenerated oil. In countries with an EPR system, re-refiners who regenerate used oil into re-refined basestocks receive fiscal incentives.
The amount of re-refining with suitable quality for basestock production is also rising, due to the changing composition of the used oil re-refiners receive. Used oil feedstocks in Western Europe are more often likely to be made from synthetic, group III basestocks which have a better viscosity index and a superior quality.
Perceptions of quality regarding re-refined used oil are improving and the leading re-refiners in Western Europe have earned a reputation for high quality on the wider market.
Prices of re-refined basestock have been on a rising trend due to the improvement in quality of re-refined basestocks and to the corresponding increase in the price of virgin basestocks. The gap in price between virgin and re-refined basestocks is closing.
Challenges
There are several challenges confronting companies operating in the Western European re-refining market or wishing to enter it.
In some countries, there is insufficient feedstock to cover the whole of the re-refining capacity and feedstock needs to be imported from abroad to make up the shortfall. There are logistical and administrative difficulties in importing waste oil, since they are classified as a hazardous waste.
Not all lubricants generate sued oil. Approximately 37% of all lubricants consumed in the region are lost in consumption, during handling, or through leakages. While collection rates are set to increase, there is limited room to improve generation rates. Lubricants such as process oils such as rubber process oils and white oils do not generate used oil since they become part of the final product. Generation is technically unfeasible for other industrial lubricant products such as greases.
Countries with high collection rate, such as Italy, could reach peak collection capacity within the next 10 years.
The cost of used oil collection varies widely according to the regulatory system, whether incentives are used or not, to the type of lubricant, to the distance covered, and to local economic constraints.Variations in crude oil prices are also a key factor weighing on oil collection charges.
Some product categories, such as marine used oils, transformer oils, and metalworking fluids are not suitable for re-refining. These products make up a substantial amount of collected oils.
The global basestock market is shifting away from API Group I basestocks in favor of higher quality basestocks, such as API Group II and Group III. This represents a challenge for the used oil re-refining industry, as most re-refineries are geared toward Group I basestocks production and may not have enough suitable feedstock for Group III basestock production.